## Slide 1
Digital Archives for Nuclear Emulsion Data
- past experiments in cosmic-ray and accelerator physics -
HTS runs at ~0.5m2/h read-out speed.
All tracks in past experiments’ emulsion can be read-out. for minimum bias re-analysis. Share those emulsion data for educational use etc. → Digital Archives
Emulsion plates read-out by HTS so far are …
  All two blocks of RUNJOB 1997 flight
  Part of top 9 plates of JACEE-13 ( Antarctic circumpolar fight in 1994 )
  1 module of DONUT ( neutrino experiment )
K. Kodama : Aichi Univ. of Edication
M. Ichimura : Hirosaki Univ.
M. Nakamura : Nagoya Univ.
This presentation

## Slide 2
NETSCAN data obtained so far
RUNJOB
  Two blocks of 1997 flight ( 16.4 m2 ) were read-out.
  Total 10 flight campaigns ( 20 blocks ) had been done.
  Slips among emulsion plates were observed.
JACEE-13 ( Antarctic flight )
  1/4 of upper 9 plates ( 0.45 m2 ) were read-out.
  No slip observed.
DONUT
  Module #1 ( 11.5 m2, largest  Interactions expected ) were read-out.
  Total 7 modules were exposed to neutrino beam at Fermilab.

## Slide 3
RUNJOB
RUssia-Nippon JOint Balloon-program
10 successful flights ( 19951997,1999 )
  Each flight was 140 hours at mean altitude of  10g/cm2 ( 3035km )
HTS scanning done for 2 blocks of 1997 flight.

## Slide 4
0.7mm
Microscope view of a RUNJOB emulsion plate

## Slide 5
Selected vertices/interactions in RUNJOB target module
Look into 16 emulsion plates of 50cm×40cm size
Target module

## Slide 6
JACEE
Japanese-American Cooperative Emulsion Experiment
JACEE-13(1994) is Antarctic circumpolar flight
This flight was intended to study high energy cosmic ray flux.
It would be interesting to observe low energy anti-protons,
because of low rigidity cut off of this flight.
JACEE-13
flight path
https://stratocat.com.ar/fichas-e/1994/MCM-19941221.htm
Anihilation of an anti-proton in emulsion
The Study of Elementary Particles by the Photographic Method
Powell, Fowler and Perkins

## Slide 7
0.76mm
Microscope view of a JACEE-13 emulsion plate
high Z nucleus

## Slide 8
Selected vertices in JACEE-13 data
Look into 9 emulsion plates of 25cm×20cm size
2.1104 vertex candidates

## Slide 9
>105 tracks were read-out
In 2.6mm x 3.5mm x 10plate
by UTS
an interaction vertex
was found
close look at
the vertex
remove
penetrating tracks
NETSCAN method succeeded
to identify tau neutrino
charged current nteractions.
Physics Letters B504(2001)218-224
tau neutrino interaction vertex was found
tau decay
vertex
200 micron

## Slide 10
Nuclear Instruments and Methods A493(2002)45-66
Summary of  beam exposures in DONUT
3.54×1017 protons of 800GeV/c were used to create neutrino beam
and exposed to emulsion targets
Module #1 were read-out.
No swelling ( i.e. expand emulsion layer )
not to damage emulsion plates

## Slide 11
Ghost
MicroTrack Read-out
MicroTrack, DONUT mod-01 pl048 face=1 ph≥7 ( test scan )
Position and angle difference
of any two MicroTracks
tanθ
MicroTrack density = 1.6×106/cm2

## Slide 12
BaseTrack production
BaseTrack, DONUT mod-01 pl048 ph≥7 ( test scan )
MicroTrack angle resolution
evaluated with BaseTracks.
BaseTrack angle dependent
Tight cut ( ∆𝜃≤0.04 )
in lateral angle difference
to increase BaseTrack purity.
BaseTrack condition
where

## Slide 13
BaseTrack angle distibution
BaseTrack, DONUT mod-01 pl048 ph≥7 ( test scan )
BaseTrack density = 1.5×105/cm2

## Slide 14
Positon alignment between plates
DONUT mod-01 pl46–pl47 ph≥7
( test scan )
プレート間でつながる飛跡の
位置ズレ分布
No obvious slip observed
Slips observed in
RUNJOB-97A
RUNJOB-97A pl02–pl03

## Slide 15
BaseTrack recognition efficiency
DONUT mod-01 pl47 ( test scan )
■ : ph≥7
□ : ph≥8

## Slide 16
24 HTS scan areas were needed to read-out one emulsion plate.
5mm overlap between scan areas
01
02
03
05
06
07
09
10
11
13
14
15
17
18
19
21
22
23
04
08
12
16
20
24
ラベル
24 HTS scan data were joined to read-out one plate
DONUT plate
500mm x 500mm

## Slide 17
BaseTrack position distribution of one emulsion plate
(50cm x 50cm in DONUT)
BaseTrack, DONUT mod-01 pl045 ph≥7

## Slide 18
Linklet
- a pair of BaseTracks connected on two plates -
Linklet between pl045 and pl046
Position difference
Angle difference

## Slide 19
Track reconstruction and vertex search
group ⇒ chain ⇒ m-file ⇒ vertex
BaseTrack : 1.5x103/mm2, 3.6x108 tracks/plate
Linklet : 0.5x103/mm2, 1.3x108 linklets/plate-pair (1x)
Group : total 0.45x106 Groups, 14.8 tracks/Group
Chain : 13.2 chains/group, total 6.0x109 Chains
  make Chains for Groups with < 1x106 tracks
M-file of largest chains in each Group only.
  Reject passed-through (tusukinuke) tracks.
  definition : dxy=100m, dz=1plate
Pickup vertex candidates.
  ttv : same-plate, dr<3m, dt>20mrad, 0<dz<2.3mm
  vtx : bin-volume = 20x20x100m, #-of-ttv>10
Fe
emulsion plate 47
emulsion plate 48
Fe
emulsion plate 46
Fe
Fe
Fe
emulsion plate 45
emulsion plate 44

## Slide 20
Track reconstruction and vertex search
group ⇒ chain ⇒ m-file ⇒ vertex
BaseTrack : 1.5x103/mm2, 3.6x108 tracks/plate
Linklet : 0.5x103/mm2, 1.3x108 linklets/plate-pair (1x)
Group : total 0.45x106 Groups, 14.8 tracks/Group
Chain : 13.2 chains/group, total 6.0x109 Chains
  make Chains for Groups with < 1x106 tracks
M-file of largest chains in each Group only.
  Reject passed-through (tusukinuke) tracks.
  definition : dxy=100m, dz=1plate
Pickup vertex candidates.
  ttv : same-plate, dr<3m, dt>20mrad, 0<dz<2.3mm
  vtx : bin-volume = 20x20x100m, #-of-ttv>10
Fe
emulsion plate 47
emulsion plate 48
Fe
emulsion plate 46
Fe
Fe
Fe
emulsion plate 45
emulsion plate 44
vertex in this region
in next slide

## Slide 21
Selected vertex candidates
62.1mm < vz < 63.5mm ( between pl047 and pl048 ) … still preliminary

## Slide 22
Summary
Full surface read-out of all emulsions in past experiments is being possible.
It will be valuable to read out emulsions in past experiments and make them public in some way, such as a Digital Archives of emulsion data.
  Minimum bias re-analysis for physics purpose.
  Real data for educational use.
Data obtained so far …
  All two blocks of RUNJOB 1997 flight ( 16.4 m2 )
  Part of JACEE-13 flight ( 0.45 m2 )
  1 module of DONUT ( 11.5 m2 )