## Slide 1
OTR as possible detector for high intensity electron beam profile of T2K's MUMON-EMT test at ELPH
22.02.2023 29. ICEPP Symposium
Oderich Ferdinand Auersperg-Castell University of Vienna
Exchange semester at High Energy Physics Tohoku (Tohoku U)

## Slide 2
From Austria
At end of Physics Master at University of Vienna
Exchange semester at Tohoku University (winter semester 2022/23)
At High Energy Physics Group Tohoku (HEP Tohoku)
  Led by Prof. Atsuko Ichikawa (Spokesperson of T2K for last 4 years)
  Part of T2K Collaboration
  Other Projects: HyperK, ILC, Search for Neutrinoless Double Beta Decay with AXEL
Odi
オディ

## Slide 3: T2K experiment
MUMON
Tokai
Kamioka

## Slide 4: MUMON
MUon MONitor  measures muons that are produced alongside neutrinos
Located 118m downstream from the target,
Used to determine the neutrino beam direction

## Slide 5: MUMON
Monitor muons in real time. Indispensable monitor to reduce beam loss Si is main sensor for monitor. IC is for cross-check and backup.
Scintillator and Iron plates. It takes about 1 day to see the profile.
SuperK

## Slide 6: MUMON
150x150cm detector area
Primary sensor array
7x7 Si PIN Photodiodes
Half of them have to be replaced every ~100 days due to radiation damage
Secondary sensor array
7x7 Ionisation chambers

## Slide 7: Proton beam upgrade and EMT
Proton intensity will be upgraded
This will increase the muon (and neutrino) flux
 from 1.5 x 106 muons/cm2/s to 4.2 x 106 muons/cm2/s
Si PIN Photodiodes will need to be replaced after a month!  new kind of MUMON sensor needed!
with
High radiation tolerance!
Real time measurement
EMT – Electron Multiplier Tube
Same as PMT, but with aluminium cathode instead of photocathode
Expected to be more radiation tolerant!
Currently tested outside of J-PARC
Tested in MUMON during next beam time
EMT sensor
Bleeder circuit

## Slide 8: EMT performance test at ELPH
Why 4th MUMON-EMT test?
evaluate degradation of aluminium cathode
To evaluate degradation of the bleeder circuit
Temperature Dependence
Where?
At 90 MeV electron linear accelerator of ELPH (Tohoku U) in Sendai
How?
Low intensity 7pA (7Hz, 1pC/pulse) electron beam to check the EMT signal
High intensity 140nA (7Hz, 20nC/pulse) electron beam to test EMT‘s radiation tolerance
  EMT cell is moved through electron beam to irradiate it evenly
   a detector is needed for the test that can be used for beam monitoring during high intensity  OTR
at ELPH

## Slide 9: OTR detector– General concept
Optical Transition Radiation - When charged particles (like electrons) pass through the boundary between two media with different electrical properties photons are emitted.
Photons – visible light
Electron beam
Aluminum foil
-> to camera
EMT cell
Aluminum foil
Filter – to prevent over saturation of camera

## Slide 10: OTR Development
# | Component | Description
1 | CT holder* | Also supports OTR tube
2 | OTR tube* + Foil Top* + Cross Top* | Light tight connection between beamline and mirror
3 | Mirror | Thorlabs CCM1-E02/M, 45°
4 | Adapter* | Between Mirror and Filter slider
5 | Filter Slider | Thorlabs CFS1 Filter Mount
6 | Black Sheet holder* | Close gap with black sheet
7 | Lens | Ricoh FL-BC7528-9M - F2.8/75mm
8 | Camera | Thorlabs CS165MU/M
9 | Aluminium Frame | 25cm, 30x30mm
* In house 3D print
1
2
3
4
5
6
7
8
9

## Slide 11: OTR - Foil top and Cross top
OTR tube
OTR Foil Top
OTR Cross Top
2 Foil Tops -> prepare new foils while measurement is running
To be able to do focussing calibration of camera fast
  -> just change the Top

## Slide 12: OTR Implementation
3rd MUMON-EMT test Nov. 2021
With simple former OTR setup
4th MUMON-EMT test Nov. 2022
With advanced OTR setup

## Slide 13
OTR EXECUTION - Implementation at ELPH
4th MUMON-EMT test
3rd MUMON-EMT test

## Slide 14: OTR Execution - Intensity adjustment
Neutral density filters:
2x ND-2 (50% Transmission)
ND-4 (25% Tranmission)
ND-10 (10% Transmission)
ND-2 (lower, black) filter and
ND-4 (upper, silver) filter
ND-2 (transparent, fits into the
filter slider Insert) filter and
ND-10 (smaller, dark) filter

## Slide 15: OTR Execution - Data taking
Beam coordinates
in the
OTR pictures:
x
y
-x
-y
High intensity beam
All filters used except in first case (no ND-10)
On 15. and 16.11.2023 OTR with 2 foils
On 17. OTR with 1 foil.
15.11.2022
2 foils
16.11.2022
2 foils
16.11.2022
2 foils
17.11.2022
1 foil

## Slide 16: OTR Execution – Results and Evaluation
Camera resolution:
Camera X-Axis: 1440 pixels
Camera Y-Axis: 1080 pixels
Readout Values:
X-Axis:
Y-Axis:
Beam coord.
in the
OTR pictures:
x
y
-x
-y

## Slide 17: OTR Execution – Results and Evaluation
Preliminary result for beam width:
x
y
Camera screen size:
- X-AxisBeam: 12.50 mm
- Y-AxisBeam: 16.75 mm
x
y
Calibration picture
 Pixel size: (0.0116 mm)2
Camera resolution:
- X-AxisBeam: 1080 pixels
- Y-AxisBeam: 1440 pixels
Beam profile picture
Camera pictures transformed into Beam coordinates

## Slide 18: OTR Execution – Results and Evaluation
We want to irradiate the EMT cell evenly
Electron beam is narrow -> move EMT through beam
Step size of EMT actuator movement
16x16mm area
20x20 locations
Step size = 16 mm/19 = 0.85 mm
This result indicates that the EMT cell was successfully irradiated evenly
…
…
…
0.85 mm
19 steps
Beam Size

## Slide 19: OTR - Additional measurements
Open questions for me
  What influence does the flatness of the foils have
    Measurements with different tilts
  Does the beam cause a radiation damage on the foils? If yes, does it affect the performance of the detector?
    Measurements with same beam intensity over longer time
  Why is there a camera saturation despite using so many filters and despite the change to single foil? Is the range the filters are effective on wrong?
    Filter on different positions.
    Change to single foil on 17.11.22
Observed damage on 1. foil (replaced after 1 day on 16.11.23 at 17:30, )

## Slide 20: まとめ – Summary
Muon monitor is measuring the beam direction in the T2K experiment. → indispensable for T2K beam operation
Upgrade of proton intensity for T2K neutrino production → new MUMON sensor with better radiation robustness
EMT cells are developed as new sensors.
EMTs are tried in MUMON-EMT tests. Recently 4th test in November 2023 at ELPH (Sendai) for
  Degradation of cathode aluminium and the bleeder circuit.
  Temperature dependence.
High intensity e- beam → Use OTR for beam profile monitoring
First analysis shows satisfactory beam behaviour (diameter and position)  OTR works well
  Further data evaluation for exact beam profile
     Short exposure measurement series
  Determine reliability of OTR results with additional measurements
Master Thesis

## Slide 21
Thank you very much for your Attention!
4th MUMON-EMT test at ELPH

## Slide 22: Back Up

## Slide 23: OTR Calibration
Focusing for two foils setup (length of foiltop is chosen to represent distance to inbetween the foils.)
Focusing for single foil setup
(cross is put where the foil would be.)
Alignment and height correction (done with laser)
Focusing

## Slide 24: OTR – Exchange Semester tasks
Only 1 semester time  OTR development very fitting task
Develop construction which
fits on the experiment table with the rest of the instruments
allows to have the camera be focused on the foil/the point in between the foils which is/are located in the beamline
can be used for high and low intensity beam -> be able to exchange filters
is simple and easy to set up
is completely dark on the inside (to minimize noise on the camera)
ideally is easily accessible to do calibration and exchange foils

## Slide 25: OTR version at last test (Nov. 2021, 2. MUMON Test)
Single Foil
Rather spontaneous set up idea
Camera was put on tripod next to experiment table
Setup had to be wrapped in black foil since it was open
It was hard to keep camera focused because the setup was only loosely connected to the rest of the experiment
Old OTR  Motivation for new OTR

## Slide 26: OTR - physics

## Slide 27: OTR - physics

## Slide 28: OTR EXECUTION - Implementation ELPH
ELPH Accelerator Hall and Beam Dump
without MUMON setup
Beam Dump with MUMON setup but without CT and OTR (except for Aluminum Frame)

## Slide 29: MUMON – project timeline
MUMON upgrade is proposed
1. test -> Linearity for high intensity is OK
2. test -> Radiation tolerance of EMT is much better than that of SI
3. test ->
4. test