Planned optimization of RF structures
for HALHF
HALHF Workshop,
Oslo, April 4th-5th, 2024
Kyrre Sjobak
Department of Physics, University of Oslo

---
Conventional RF linacs for HALHF
B. Foster et al, 2023 New J. Phys. 25 093037
The high energy colliding electron beam in HALHF comes from a plasma-accelerator,
but all the beam energy is provided via or directly from the RF linacs
Much of the construction cost, operation complexity, and energy use at HALHF comes from the RF linacs
The RF linacs are used to accelerate several beams, with different parameters:
The electron drive beams for the plasma-accelerator (31 GeV, 4.27nC x 16 bunches)
The colliding positron beam (31 GeV, 6.4 nC x 1 bunch)
The colliding electron beam (5 GeV, 1.6 nC x 1 bunch)
Design from 2023 paper assume a 25 MV/m L-band (1.5 GHz) using 21 MW/m at 50% efficiency, in bursts of 8-10µs.
Combining plasma linac drivers and colliding positron beam
→ Very important to optimize and to understand!

---
https://cds.cern.ch/record/2655160
CLIC optimization
CLIC, the Compact Linear Collider, also being
a drive-beam powered linear accelerator,
share many design challenges
This was (re-)optimized taken into account several
parameters, models, and constraints;
Exploring the design space to find a range of
potentially feasible designs
Parameters was varied, such as the number of cells,
beam aperture radius&thickness, and accelerating gradient,
of the main linac accellerating structures, and luminosity and √s
Model outputs such as construction cost and energy consumption
Models for beam dynamics connecting e.g.
luminosity and √s to requirements for beams
Constraints such as wake-fields and
RF structure break down (vacuum arcing) rates
This relied on a detailed fast model for main linac RF structure performance
See CLIC collaboration, 2016, “Updated baseline for a staged Compact Linear Collider”, https://cds.cern.ch/record/2210892
Power consumption
relative to best case
as function of aperture a
and number of cells Nc
Cost and power consumption
for machines with different
luminosities L [1034 cm-2s-1]

---
Fast model for traveling wave RF structures
Input
Output
CLIC uses traveling wave RF structures
Highly optimized structures for the main beam linac
≈100 MV/m, X-band (12 GHz),
very strong wake field damping
Made with stacks of cells, powered from input coupler
Can apply power flow model from A. Lunin et al, 2011, PRAB 14, 052001
to predict power requirements, wake fields, power transients,
from overall structure geometry parameters (length, frequency, apertures),
cell performance (R/Q, vg, Q, …), and required gradient & beam current
Gives gradient profiles
linked to power and loading:
RF pulse shapes with beam loading compensation
(all bunches see the same voltage and gradient profile)
(Beam between t2 and t3)
G_0 = \sqrt{\frac{\omega \frac{R'}{Q}(0) P_0 }{v_g(0)}}

---
Estimation of gradient limits
Plots from K. Sjobak, “Avoiding vacuum arcs in high gradient
normal conducting RF structures”, PhD thesis, UiO, 2016
and also from my talk from HG2013 in Trieste
Starting from the normalized peak surface fields such as of the structure design,
and the gradient profile G(z), we can calculate the peak fields Ê(z) or ŜC(z)
Break down rates (BDR) scales as Ê30τ5, proportional to G30τ5. Equivalent scaling for Ŝc
Can re-scale data from experimentally tested structures to find limits for break down constraints
@ standard conditions: τ0 = 200ns, BDR0 = 10-6 breakdowns/pulse/meter
The modeled structure can then be compared to this,
giving an estimate for the BDR or maximum pulse length at the given operating conditions.
Pulsed surface heating can also be estimated analytically
and compared to fatigue limit (ΔT=50K)
Examples:
Allowed pulse length from different constraints
for CLIC_G “reference structure” as function
of number of cells, with strict breakdown constraints
RF→beam energy efficiency as a function of taper
\bar E(z) = \hat E / G
=
*
GL=100MV/m, I=1.92A, L free
GL=100MV/m, I=1.92A, L=216mm

---
Estimation of long range wake field
Long range wake field can be estimated
from vector sum of first dipole mode in each cell
This model can be compared to wakefield limits
set by beam dynamics, and used for
Finding minimum bunch separation
Go/no-go for a structure
W_\perp(s) = \frac{1}{N_\mathrm{cells}} \sum_{i = 0}^{i < N_\mathrm{cells}} W_i(s)
W_i(s) = - A_i ~ \exp\left(\frac{-\omega_i ~s/c }{2 Q_i}\right) ~ \sin\left(\omega_i ~ s/c ~ \sqrt{1-\frac{1}{4Q_i^2}} ~ \right)

---
The cell database
Calculation is based on knowing the local properties of the RF structure – R’/Q, Q, vg, …
Also break-down relevant quantities such as
and wakefield mode quantities
This is interpolated from “cell database” of carefully optimized accelerator cells, with various combinations of aperture radius a and thickness d
Current cellDB has cells using the CLIC main beam design,
described in CLIC-NOTE-1026 (2014)
Highly damped, breakdown rate optimized cells
Can be scaled in frequency
As a first step, can scale CLIC main beam accelerator cells
Should give a reasonable estimate
CLIC drive beam accelerator type cells would be interesting to test
CLIC drive beam accelerator structure design
could be the ideal “template” to use
Described in CLIC-NOTE-945 (2012)
\bar E(z) = \hat E / G
a/λ
a/λ
d/h
d/h

---
Existing implementation
This method is implemented in the CLICopti
RF structure parameter estimator
Available from
https://gitlab.cern.ch/clic-software/clicopti
Modular C++ library with Python and Octave front-end,
created for use in optimization of traveling wave linacs
Implements cell database interpolation,
gradient profile calculation, gradient limits,
and long-range wake fields as discussed above;
Calculates power requirements, pulse length limits,
wakefields, and efficiencies
Used for re-optimization of CLIC main beam linac
References:
K.Sjobak et al., CLIC-NOTE-1031
J. Ögren et al, "Toolbox for optimization of RF efficiency for linacs", IPAC19
K. Sjobak, “Avoiding vacuum arcs in high gradient normal-conducting RF structures", PhD thesis, UiO, 2016

---
Implementation in
Bayesian optimizer
and integrated simulation
Will provide an accurate “calculator” for power requirements etc.
for drive beam and positron linac
Scan structure lengths and gradients with
requirements for beam currents and bunch distance
Remove configurations that won’t work due to gradient limits or wake fields
Find optimum for cost and efficiency
Start with CLIC main linac type cells (cell database);
Will try to have limited implementation of CLIC drive beam type structures
Python library wrapping C++ →
Will also be able to flag configurations breaking gradient limits
or with problematic wake fields
This can then be used for selecting RF linac design and layout with higher confidence
Important element of the overall size and cost of HALHF
Will help answer whether to combine or separate the driver and positron acceleration RF linacs
To be implemented in start-to-end framework AND Bayesian optimization

---
Conclusions and Outlook
The conventional RF linacs for creating the various beams are a very important part of HALHF
Good models for performance of traveling wave RF linacs
were developed and used for the optimization of CLIC
Based on RF power flow and energy conservation
Predict well the gradient profiles, power requirements, and efficiencies
Can estimate gradient limitations and long range wake fields
We will re-use these models for calculating the performance of the HALHF RF linacs for optimization

---
Acknowledgments
Oslo accelerator group:
Erik Adli, Kyrre N. Sjobak,
J.B. Ben Chen, Gevy Cao,
Ole Gunnar Finnerud, Daniel Kalvik,
Carl A. Lindstrøm, Pierre Drobniak
Funding:
The Research Council of Norway

---
Breakdown Limit Data

---
Heading
Subheading
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Diam vulputate ut pharetra sit amet aliquam id diam.
qwertyuiop
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Diam vulputate ut pharetra sit amet aliquam id diam.
Lorem ipsum dolor sit amet, consectetur adipiscing elit.