## Slide 1
FCC
PS
SPS
LHC
Status Report on FCC Accelerator Science and Technology
Michael Benedikt, CERN
Austrian FCC Meeting,
11 October 2021
photo: J. Wenninger
Work supported by the European Commission under the HORIZON 2020 projects EuroCirCol, grant agreement 654305; EASITrain, grant agreement no. 764879; ARIES, grant agreement 730871, FCCIS, grant agreement 951754, and I.FAST, grant agreement 101004730.
http://cern.ch/fcc

## Slide 2
Double ring e+ e- collider
Common footprint with FCC-hh, except around IPs
Asymmetric IR layout and optics to limit synchrotron radiation towards the detector
2 IPs, large horizontal crossing angle 30 mrad, crab-waist collision optics (alternative layouts with 4 IPs under study now)
Synchrotron radiation power 50 MW/beam at all beam energies
Top-up injection scheme for high luminosity Requires booster synchrotron in collider tunnel
FCC-ee basic design choices

## Slide 3
parameter | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45 | 80 | 120 | 182.5
beam current [mA] | 1390 | 147 | 29 | 5.4
no. bunches/beam | 16640 | 2000 | 393 | 48
bunch intensity [1011] | 1.7 | 1.5 | 1.5 | 2.3
SR energy loss / turn [GeV] | 0.036 | 0.34 | 1.72 | 9.21
total RF voltage [GV] | 0.1 | 0.44 | 2.0 | 10.9
long. damping time [turns] | 1281 | 235 | 70 | 20
horizontal beta* [m] | 0.15 | 0.2 | 0.3 | 1
vertical beta* [mm] | 0.8 | 1 | 1 | 1.6
horiz. geometric emittance [nm] | 0.27 | 0.28 | 0.63 | 1.46
vert. geom. emittance [pm] | 1.0 | 1.7 | 1.3 | 2.9
bunch length with SR / BS [mm] | 3.5 / 12.1 | 3.0 / 6.0 | 3.3 / 5.3 | 2.0 / 2.5
luminosity per IP [1034 cm-2s-1] | 230 | 28 | 8.5 | 1.55
beam lifetime rad Bhabha / BS [min] | 68 / >200 | 49 / >1000 | 38 / 18 | 40 / 18
FCC-ee collider parameters (stage 1)

## Slide 4
Marica Biagini
B-factories: KEKB & PEP-II:
double-ring lepton colliders,
high beam currents,
top-up injection
DAFNE: crab waist, double ring
S-KEKB: low by*, crab waist
LEP: high energy, SR effects
VEPP-4M, LEP: precision E calibration
KEKB: e+ source
HERA, LEP, RHIC: spin gymnastics
combining successful ingredients of several recent colliders → highest luminosities & energies
FCC-ee design concept
based on lessons and techniques from past colliders (last 40 years)
Marica Biagini

## Slide 5
FCC-ee RF staging scenario
three sets of RF cavities to cover all options for FCC-ee & booster:
high intensity (Z, FCC-hh): 400 MHz mono-cell cavities (4/cryom.)
higher energy (W, H, t): 400 MHz four-cell cavities (4/cryomodule)
ttbar machine complement: 800 MHz five-cell cavities (4/cryom.)
installation sequence comparable to LEP ( ≈ 30 CM/shutdown)
WP | Vrf [GV] | #bunches | Ibeam [mA]
Z | 0.1 | 16640 | 1390
W | 0.44 | 2000 | 147
H | 2.0 | 393 | 29
ttbar | 10.9 | 48 | 5.4
“Ampere-class” machine
“high-gradient” machine
Notes: “Continuous flow” operation: succession of 8 months operation, 4 months installation shutdown (LEP-like)
Three sets of cavities to cover all options (+ booster):
  high intensity (Z, FCC_hh): 400 MHz mono-cell cavities, ≈1MW RF source
  high energy (H, t): 400 MHz four-cell cavities -> will be used for the W machine
  booster and t machine complement: 800 MHz four-cell cavities (400 MHz would do the job as well)
High energy set for the W-machine not optimal (20-30% reduction of beam current) – building & installing 48 specialized CM would impact more (>>1 year delay)
Optimize the re-use of the 100MW, 400MHz RF power & controls hardware installed for the ‘Z-machine’
  design an easily adaptable and modular RF power distribution system

## Slide 6
Cavity Studies
Optimized Cavity Shape, Technology and Operating Temperature (complexity, power consumption, Qo, Eacc)
Design 1- & 4-cell Cavities
Beam-Cavity Interaction
Cavity Control System (LLRF)
SRF & Substrate Technologies
Improved Cavity Engineering: New SC Materials, Novel Fabrication Methods, Substrate Surface Preparation, Coating Techniques
Fabrication & Testing of 1-l & 4-cell cavities for new cryomodule
Collaboration with international Partners
Cryomodule Development
Engineering design of 400 MHz cryomodule including ancillaries
Building a 2 cavity CM which can host 1-/4-cell 400 MHz cavities
R&D Collaboration with int’l Partners (e.g. JLAB)
800 MHz CM: Profit from Ongoing Development @ PERLE in Paris
FPC & HOM RF Couplers
Improved design, fabrication and testing of 400 MHz Fundamental Power Coupler (FPC)
FPC R&D towards 1MW CW fixed/movable FPC
‘Adjustable’ FPC (external large adaptation of Qext)
HOM coupler production
FCC SRF R&D Program Structure in a Nutshell
RF Power Sources
novel klystron bunching methods
LHC klystron retrofit as proof of principle
prototype design, fabrication and testing

## Slide 7
Prototypes of FCC-ee low-power magnets
Twin-dipole design with 2× power saving
16 MW (at 175 GeV), with Al busbars
Twin F/D arc quad design with 2× power saving
25 MW (at 175 GeV), with Cu conductor
prototype
prototype

## Slide 8
by* = 0.8 mm achieved in both rings – using the
FCC-ee-style “virtual” crab-waist collision scheme
Design: double ring e+e- collider as B-factory at 7(e-) & 4(e+) GeV; design luminosity 8 x 1035 cm-2s-1; by* 0.3 mm; nano-beam – large crossing angle collision scheme (crab waist w/o sextupoles); beam lifetime5 minutes; top-up injection; e+ rate up to 2.5 1012 /s ; under commissioning
Y. Funakoshi, Y. Ohnishi, K. Oide
SuperKEKB is demonstrating FCC-ee key concepts
M. Tobiyama, K. Oide
SuperKEKB – pushing luminosity and b*
new world record L = 3.12 x 1034 cm-2s-1 on 22 June ‘21

## Slide 9
FCC-ee complete arc half-cell mock up
including girder, vacuum system with antechamber + pumps, dipole, quadrupole + sext. magnets, BPMs, cooling + alignment systems, technical infrastructure interfaces.
key beam diagnostics elements
bunch-by-bunch turn-by-turn longitudinal charge density profiles based on electro-optical spectral decoding (beam tests at KIT/KARA) ; ultra-low emittance measurement (X-ray interferometer tests at SuperKEKB, ALBA) ; beam-loss monitors (IJCLab/KEK?) ;
beamstrahlung monitor (KEK); polarimeter ; luminometer
FCC key deliverables: prototypes by 2025
bunch electric field at the crystal
changes the laser pulse polarization
A.-S. Müller

## Slide 10
FCC-ee Machine Detector Interface
Lumical
Compensating solenoid
screening
solenoid
FF quads
100 mrad
IP
prototype Q1
canted cosine theta
with fringe field
correction,
using LHC SC cable
field measurement
at warm
challenging integration:
2 T detector solenoid,
luminosity monitor
(Bhabha scattering),
compensation &
shielding solenoids
narrow central chamber
with 1 cm radius,
also avoids trapped modes
M. Koratzinos
M. Boscolo,
A. Novokhatski,
M. Sullivan
M. Dam,
A. Bogomyagkov,
E. Levichev,
M. Koratzinos

## Slide 11
FCC hh basic design choices
dual aperture superconducting magnets
two high-luminosity experiments (A & G)
two other experiments (L & B) combined with injection upstream of experiments
two collimation insertions
  betatron cleaning (J)
  momentum cleaning (F)
extraction/dump insertion (D)
RF insertion (H)
Injection from LHC (~3 TeV) or scSPS (~1.2 TeV)
Alternative layouts under study

## Slide 12
parameter | FCC-hh |  | HL-LHC | LHC
collision energy cms [TeV] | 100 |  | 14 | 14
dipole field [T] | 16 |  | 8.33 | 8.33
circumference [km] | 97.75 |  | 26.7 | 26.7
beam current [A] | 0.5 |  | 1.1 | 0.58
bunch intensity [1011] | 1 | 1 | 2.2 | 1.15
bunch spacing [ns] | 25 | 25 | 25 | 25
synchr. rad. power / ring [kW] | 2400 |  | 7.3 | 3.6
SR power / length [W/m/ap.] | 28.4 |  | 0.33 | 0.17
long. emit. damping time [h] | 0.54 |  | 12.9 | 12.9
beta* [m] | 1.1 | 0.3 | 0.15 (min.) | 0.55
normalized emittance [mm] | 2.2 |  | 2.5 | 3.75
peak luminosity [1034 cm-2s-1] | 5 | 30 | 5 (lev.) | 1
events/bunch crossing | 170 | 1000 | 132 | 27
stored energy/beam [GJ] | 8.4 |  | 0.7 | 0.36
FCC-hh (pp) collider parameters (stage 2)

## Slide 13
worldwide FCC Nb3Sn program
Main development goal is wire performance increase:
Jc (16T, 4.2K) > 1500 A/mm2 50% increase wrt HL-LHC wire
Reduction of coil & magnet cross-section
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
~10% margin
FCC ultimate
5400 mm2
After 1-2 years development, prototype Nb3Sn wires from several new industrial FCC partners already achieve HL-LHC Jc performance
FCC conductor development collaboration:
Bochvar Institute (production at TVEL), Russia
Bruker, Germany, Luvata Pori, Finland
KEK (Jastec and Furukawa), Japan
KAT, Korea, Columbus, Italy
University of Geneva, Switzerland
Technical University of Vienna, Austria
SPIN, Italy, University of Freiberg, Germany
2019/20 results from US, meeting FCC Jc specs:
Florida State University: high-Jc Nb3Sn via Hf addition
Hyper Tech /Ohio SU/FNAL: high-Jc Nb3Sn via artificial pinning centres based on Zr oxide.

## Slide 14
16 T dipole design activities and options
Cos-theta
Blocks
Common coils
Short model magnets (1.5 m lengths) will be built until 2025
Swiss contribution
Canted
Cos-theta
H2020
INFN
CEA
CIEMAT
PSI
LBNL
FNAL

## Slide 15
US – MDP: 14.5 T magnet tested at FNAL
15 T dipole demonstrator
Staged approach: In first step pre-stressed for 14 T
Second test in June 2020 with additional pre-stress reached 14.5 T
60-mm aperture
4-layer graded coil
84% on the laodline at 1.9 K
92% on the loadline at 4.2 K

## Slide 16
High Field Magnet program goals until 2027
    1. Develop Nb3Sn magnets for collider-scale production, through robust design, industrial processes and cost reduction
    2. Demonstrate Nb3Sn full potential in terms of ultimate performance (short model programs)
  3. Provide a proof-of-principle for HTS magnet technology

## Slide 17
FCC-ee is first stage of FCC integrated programme; first physics ~2040
FCC-ee design incorporates many lessons from recent & present e+e- colliders, and goes further! SuperKEKB demonstrates key concepts
FCC-ee = efficient and sustainable collider at the e+e- energy frontier: highest luminosity per input power, highest luminosity per construction cost, most precise energy calibration, and ultimate upgrade potentials (ERL-based FCC-ee, 100 TeV FCC-hh, …)
Prototypes of FCC-ee key components by 2025
Superconducting cable & high-field magnet programme prepares for 100 TeV proton-proton collider, FCC-hh, in the same tunnel, to begin operation around ~2060
Take home messages