## Slide 1: Hardware Activities at HEPHY
Austrian FCC Meeting

## Slide 2
HEPHY
Institut für Hochenergiephysik
Nikolsdoerfer Gasse 18
Österreichische Akademie der Wissenschaften
Hauptgebäude, Ignatz Seipel Platz
Institute for High Energy Physics (HEPHY)
  Founded 1966 to take advantage of Austria’s CERN membership (1959)
  Situated in Vienna, two locations
  Staff: ~80 people
Belongs to
Austrian Academy of Sciences (ÖAW/OEAW)
  Founded 1847 as “scientific club”
  Nowadays the largest non-university institution for basic research in Austria
  28 Institutes with around 1450 staff
    Humanities
    Natural sciences

## Slide 3
Intensity Frontier
Energy Frontier
Astroparticle
(non-accelerator)
Frontier
Frontiers in HEP @ HEPHY
CMS @ CERN
Belle @ KEK
CRESST @ LNGS
Medical Imaging @ MedAustron

## Slide 4
Experimental Expertise @ HEPHY
Electronics
Semiconductor
Sensors
Detector Modules

## Slide 5
We are operating high level equipment for sensor characterization and module construction
  Several probe stations for sensor tests (own developments)
  Semi-automatized module assembly (CMM, glue robot)
  Fully automatic thin-wire bonding machine
  Microscopes for optical measurements
  Radioactive sources and Lasers for signal stimulation (TCT)
  Software frameworks for sensor design and simulation (TCAD)
  Chip design Workflow (Cadence, Mentor, SOS,….)
Infrastructure at HEPHY
QTC/SQC Setup
HGCCal Setup
Laser Setup
PQC Setup
Probe station 3
Climatic Chamber
Thin-wire bonding machine
Coordinate Measurements

## Slide 6
The Energy Frontier
CMS @ CERN

## Slide 7
LHC Long Shutdown 3 (LS3) in 2025-2027
Accelerator upgrade to High-Luminosity (HL)-LHC
Upgrade of experiments necessary
  Existing systems reach end of life (radiation damage)
  Increase in luminosity at HL-LHC: 300  3000 fb-1  More radiation hard material necessary
  Increase in pile-ups  new techniques necessary
    “Track trigger” in Tracker
    Timing layer as complete new subdetector of CMS
Phase-II Upgrade of CMS:
Complete exchange of Outer Tracker  200 m2 Si Sensors needed
New Highly Granularity Calorimeter (HGCal)  600 m2 Si Sensors (8 inch)
New Timing Layer  Ultra-Fast detectors to enable “4D” tracking”
CMS Phase-II Upgrades
Layout of HGCal
Big responsibility and commitments in both projects as institute members are convenors of working groups for sensor development in both subdetectors

## Slide 8: Completely replace Outer tracker for Phase II
Maintain physics performance
  Track trigger concept
Increase radiation hardness
  2.3 ⨉ 1016 neq/cm2  Pixel
  1 ⨉ 1015 neq/cm2  Strips
Reduce material budget
Extend tracking acceptance
  .4 ➔
Increase granularity
  Keep channel occupancy below 1 % at high pile-up
CMS Tracker Upgrade
Notes: Low material budget is essential for precise track reconstruction, Coulomb scattering deflects path

## Slide 9
Calorimeter Endcap or High Granularity CALorimeter
CALICE-inspired imaging calorimeter optimized for particle ﬂow analysis
Covers 1.5 < η < 3.0
215 tons per endcap, full system at -35°C
Silicon part:
∼620 m2 of silicon sensors, 8” (200mm wafers)
∼6M channels in
~30k modules, two cell sizes 0.5 and 1.1 cm2
Scintillator part:
∼400 m2 of scintillator,
∼240k tiles + SiPMs in ∼4000 boards, two tile size 4–30 cm
El.-mag. section CE-E: Si, Cu, CuW, Pb absorbers, 28 layers, 25X0 & ∼1.3λ
Hadronic section CE-H: Si+scintillator/SiPM, steel absorbers, 22 layers, ∼ 8.5λ
High Granularity Calorimeter
“disc”
“Si module”

## Slide 10
Wafer layouts for both strip sensors of Tracker and HGCal sensors is fully driven by us at HEPHY
  Main sensor, test structures
Using self-developed framework based on open source tools
Needs negotiations with vendors on details (e.g. design rules, dicing precision,..)
Supported by TCAD simulations for optimizing different aspects
  E.g. periphery simulation
Sensor Design
2S Wafer layout
HGCal full wafer LD layout

## Slide 11
Goal: fully reproduce strip-sensor measurements
Better understanding on Electric field, currents, breakdown behavior, interstrip characteristics,..
Performed tasks at HEPHY:
Improved/tuned sensor mesh and design
Improved physics models
Includes “real” doping profiles as result of scanning resistance profiling (SRP)
Added additional traps, revealed by DLTS (deep level transient spectroscopy) in unirradiated sensors
Further improvements by determining the correct charge carrier lifetime through GCD measurements
Sensor Simulation

## Slide 12
We worked with Infineon to find a “second source” for large-area planar Si sensors
2009: Project started by private contacts as a bottom-up approach
2012-2014: production of 6” p-on-n sensors
  Goal: re-produce the current CMS tracker sensors
  Production workflow: design by HEPHY, production at IFX, characterization (lab, beam tests,…) by HEPHY (mostly done in the framework of Bachelor’s and Masters’ theses)
2015: First AC-coupled sensor on 8” wafer
2015-2017: production of first Si strip sensors on 8-inch FZ p-type wafers
2016/17: production of pad sensors for HGCal and 6-inch p-type sensors for CMS Tracker
2018 program stopped due to economic reasons
12
6“ p-on-n
Wafer:
Former CERN DG Heuer with Infineon manager and M. Dragicevic
Sensor Production
8” p-type
strips
6” CMS PS-S
prototypes
Infineon CEO together with HEPHY and CERN representatives
8” CMS HGCal
prototypes

## Slide 13
Characterizing sensors with several custom probe stations in our clean rooms
  ”custom” refers to develop both hardware and software to our own needs by help of our large electronics and mechanics groups
Tracker and HGCal in different status at the moment:
  “Series production” of Tracker sensors require quality control of tracker sensors using full sensors and process control on dedicated test structures (PQC)
  R&D of HGCal sensors to qualify 8” process of HPK
    Bulk irradiation tests (neutrons)
    Gamma/X-Ray irradiations for Oxide studies
    Full wafer characterization
    Backside fragility
Sensor Testing
PQC Setup
HGCal Setup

## Slide 14: Medaustron
Medical Imaging at

## Slide 15
MedAustron: Austrian hadron cancer therapy center
Based on CERN PIMMS study
Became operational end of 2016
Patient treatment using proton and carbon beams utilizing Bragg peak
  Protons: 60 MeV to 800 MeV, Clinical energies ≤ 250 MeV
  Carbon ions: 120 MeV/u to 400 MeV/u
Dedicated non-clinical irradiation room (IR1) for research
We perform regular beam tests there and collaborating with a group of TU Wien to establish an Ion-CT system
medAustron

## Slide 16
“Ion CT” by measuring stopping power in object per voxel needs
Tracker (similar beam telescope)
  Currently DSSDs
Calorimeter to measure residual energy
  Sandwich calo using scintillator planes and SiPM readout
Image Reconstruction
Ion Imaging
Phantom
Reconstructed image

## Slide 17: pCT Tracker Upgrade: Monolithic
Depleted Monolithic Active Pixel Sensor combines both active sensing element and readout electronics into one device
  Sensor development becomes chip development
  Generally agreed that this technology will be the future of Si sensors in HEP
  Deep wells fully shield CMOS electronics from active volume and allows full CMOS electronics
DMAPS (a.k.a. HV-CMOS)

## Slide 18
Ion Imaging Tracker Upgrade
MALTA HV CMOS
TowerJazz 180nm
512×512 square pixels, pitch 36.4 µm -> 1.82 cm2
asynchronous readout
Tested in beam time at MedAustron in summer 2019:
4 sensor planes of MALTA-C with Epi substrate used as „proof of principle“ as high-rate replacement
Due to small chip size no “phantom”
Plot below shows hitmap of not fully centered beam

## Slide 19
Current Projects:
  RD50-MPW (2|3)
  OBELIX (Belle-II Upgrade)
  HiBPM Readout chip
Available foundries/processes
  Lfoundry 150nm (LF15A)
  Towerjazz 180 nm CMOS Imaging Process (TS18IS)
  STM BiCMOS Bipolar/CMOS combination
Setups/Readout systems
  Chip design Software infrastructure (Cadence, Mentor,… tools)
  FPGA design (Xilinx, Altera) and test stands
DMAPS/CMOS at HEPHY
Current periphery of RD50-MPW3
RD50-MPW2 as seen
through confocal 3D microscope

## Slide 20
Use Time-of-flight (ToF) concept to reconstruct residual energy
Precision timing based on Low Gain Avalanche Detectors (LGAD) a.k.a. UFSD needed
  LGAD have an additional deep implant layer to create locally a high electric field to initiate an avalanche
First tests performed successfully at MedAustron reaching 40ps
  System concept currently studied
  Taking advantage of developments of MTD layer of CMS Upgrade (and FCC later)
pCT calorimeter upgrade

## Slide 21
HEPHY is very active detector development and well prepared for future detectors at FCC
Current projects:
  CMS Phase-II Upgrades: Tracker and HGCal
  Belle II:
    Silicon Vertex Detector (installed 2019) with key contributions to electronics, mechanics, readout
    Belle-II Upgrade (DMAPS-based currently starting)
  Dark Matter
    CRESST (with COSINUS, NUCLEUS)
    DANAE: DEPFET Silicon sensor based
  Medical application
    Ion Imaging: Hardware setup and image reconstruction
    Ideal test bed for new concepts (DMAPS, LGAD sensors,…)
Rich expertise in all aspects of detector development
  Sensor Design, Simulation, Implementation
  Detector Module design, assembly
  Electronics & FPGA design, hardware and firmware
  Cleanroom laboratories with several test stands
  Most recently: ASIC and DMAPS Sensor Design, Precision Timing
Conclusion

## Slide 22
The End.

## Slide 23
LHC Roadmap
Most of our work is now for Phase-II Upgrades (LS3)
What is the next European project after HL-LHC?
  HE-LHC, FCC, CLIC, ILC,…
  Development for detector technologies need to start well in advance
European Strategy for Particle Physics Update 2020~2030
  Scheduled for approval in 2020
    Open Symposium May 2019 Granada (Spain)
FCC

## Slide 24
is a CERN R&D collaboration with currently 63 institutes (370 authors)
Initially focused on radiation hardness of silicon
  widened its scope, e.g. towards timing detectors (LGADs)
  Recently started also HV-CMOS developments
Covers now all Si development paths we see important for future HEP detectors
  Thus we joined RD50 in Dec 2017
CERN RD50 collaboration
Weightfield2 (1st version created at
HEPHY):

## Slide 25
CMS is planning to build a High Granularity Calorimeter for Phase-II at HL-LHC
Covering 1.5 < η < 3.0
Features unprecedented transverse and longitudinal segmentation
  Silicon in high radiation areas
  Scintillating tiles in the low-radiation region of CE-H (Mixed Silicon-Scintillator cassettes)
Cassettes
Silicon
Scintillator
Silicon
Scintillators
CMS High Granularity Calorimeter

## Slide 26
Fluence is n-dominated w.r.t. charged hadrons (90%/10%)
  No validated irradiation model in TCAD up to fluence of 1016 neq
Deployment of thinner sensors in the higher ﬂuence regions of the calorimeter
  improved charge collection
  reduced leakage current
Typical signals in calorimeter much higher than MIPs
  MIP sensitivity needed for energy calibration (e.g. isolated muons)
Radiation Hardness
300 μm
120 μm
200 μm

## Slide 27
Access to Triga Mark II nuclear reactor at TU Vienna
  Similar to JSI Ljubljana, but only 2x10 cm wide samples possible (no larger irradiation channel
  Distance to HEPHY 30 minutes by car or public transport
Cold Chuck available at HEPHY for characterization of irradiated sensors
  Self-made Peltier-based system
  6”, to be upgraded to 8” for HGCal
  Used for irradiation studies of Infineon sensors
  Study to understand Eeff as current has to be scaled to +20°
Sensor Irradiation

## Slide 28: PQC: Tracker & HGCal
PQC - Process Quality Control: Use test structures to asses the quality (stability) of the production process
  6” AC coupled (Tracker 2S and PS-s)
  6” DC coupled (Tracker PS-p)
  8” DC coupled (HGCal)
Same set of test structures on all wafers
Use standardised pattern of 20 connection pads: flute
  Connect using standardised probe cards
  Use switching to access all structures on one flute
  Automatic movement to next flute
PS-s
2S
HGC HD
PQC Flutes

## Slide 29
DD with Industry
Silicon is a key detector technology for future HEP experiments
All LHC experiment upgrades will use Silicon detectors
But Silicon detectors are a major cost driver
Silicon detector areas used in HEP
From a few cm2 at NA11 up to 200 m2 (CMS)
Tracker Upgrades of CMS and ATLAS (~200 m2 each)
Significant increase for CMS Highly Granular Calorimeter (HGCal) by ~ 600 m2
Wafer Sizes used for HEP detectors
NA11 started with 2-3 inches (1980)
Today 6 inch (150 mm) is standard (used by LHC Experiments)  Introduced in the industry in the 80ies
Producers
Only one high-quality high-volume producer available during LHC construction

## Slide 30
Currently using Double-sided strip sensors and FADC readout very similar to Belle-II SVD
Sensors:
  Size: (2.56 × 5.12) cm2
  Thickness: 300 µm
  Pitch 50 / 100 µm (Strips: 512)
DAQ:
  Readout chain APV  FADC  VME
  Max. event rate: 500Hz  90 minutes to record one image with 1E6 tracks  11 days for full iCT 3D reconstruction (many images under different angles)
  Planned short-term upgrade: Gbit Ethernet instead of VME readout to increase speed (will also implemented into SVD for speeding up local runs)
Ion Imaging Tracker
Particle rates for clinical use (109 particles/s) are too high for both
  detectors (ghost, pile-up) and
  readout (trigger rate max 100kHz)

## Slide 31
CMS currently sees 32 pp collisions per event (pile-up) in average
CMS will suffer from a pile-up of ~200 collisions per event at HL-LHC
  Too many ambiguities for vertexing and track reconstruction
Tracking in 4D
Real event with pile-up of 78 in CMS

## Slide 32
„Tracking in 4D“ allows to reduce pile-up of HL-LHC area to current levels
Tracking in 4D
Simulation of pile-up of 200 and 30ps timing resolution of MTD:

## Slide 33: Tracking in 4D

## Slide 34
Circular collider with 80-100 km circumference
  Different flavors: FCC-ee, FCC-eh, FCC-hh
Detector concepts: scaled versions of ATLAS and CMS
  Forward detectors up to η<6
  Tremendous particle fluence of ~6x1017 neq cm-2 & TID ~0.4GGy  ultra-high radiation tolerant detectors
  Pile up of 1000 mitigated by timing  ultra-fast detectors
Future Circular Collider
Z.Drásal, Vertex 2017 Asturias Spain
Z.Drásal, Vertex 2017 Asturias Spain

## Slide 35
Depleted Monolithic Active Pixel Sensors became available due to availability of:
HV processes in CMOS foundries
high resistivity bulk material
At a couple of foundries
Examples:
MAPS: Mimosa Series
  Quite old, charge collection due diffusion only
  Different foundries and processes
DMAPS: ALPIDE, MALTA and Monopix
  TowerJazz Imaging process, 6 metal layers, small (180 nm) feature size, deep p-well
  Process modified to optimize charge collection
  RD50 Lfoundry and others
Still R&D issues to solve. E.g.:
Backplane metallization, biasing
Radiation hardness
Large sensors (stitching)
Thin, flexible silicon
DMAPS (HV/HR-CMOS)
Malta test at MedAustron
RD50-MPW1
Modified Towerjazz process:

## Slide 36
Demand of detectors/chips for HEP still vanishingly small compared to big industry
Access through and help by proxies (Europratice, CERN,..) mandatory
Europractice IC initiative:
Software services
  Provides all necessary software tools for ASIC / FPGA development, chip simulation, verification, versioning (Cadence,…)
  http://www.europractice.stfc.ac.uk/
Foundry access
  Multi-project wafer runs organized by Europractice: cost-effective way for prototyping
  https://europractice-ic.com/
Different other foundry/process options:
TSMC 65nm via CERN frame contract
STM, ONSemi, AMS,.. via CMP https://mycmp.fr/
Access to Foundries and Tools

## Slide 37
Typical setup consists of:
FPGA Evaluation board
  Xilinx, Trenz, Enclustra
ASIC-specific chip board
Custom FPGA firmware written in VHDL/Verilog
SoC-Mini Linux distribution
Typically an ethernet connection to PC
Setup used for
  R&D, debugging
  lab measurements
  beam tests at testbeam facilities, e.g. CERN, MedAustron
Hardware for Prototype tests
Caribou System
BDAQ readout board
Monopix2 chipboard
RD50 MPW2
chipboard
Main board
FPGA evaluation board

## Slide 38
The Intensity Frontier
Belle @ KEK

## Slide 39: SuperKEKB / Belle II
SuperKEKB: e-/e+ collider at KEK, Tsukuba, Japan  B factory
40-fold increase in peak luminosity to 81035 cm-2s-1  11010 BB / year
50-fold increase in integrated luminosity until 2023 w.r.t. Belle
Refurbishment of accelerator and detector required
  Nano-beams with cross-sections of ~10 µm x 60 nm
  10 mm radius beam pipe at interaction region
e- 7GeV 2.6 A
e+ 4GeV 3.6 A
Peak luminosity
[cm-2s-1]
Integrated luminosity
[ab-1]
Calendar year
Target of SuperKEKB / Belle II
Belle II

## Slide 40: Belle II Detector
electron (7GeV)
positron (4GeV)
KL and muon detector:
Resistive Plate Counter (barrel outer layers)
Scintillator + WLSF + MPPC (end-caps, inner 2 barrel layers)
Particle Identification
Time-of-Propagation counter (barrel)
Prox. focusing Aerogel RICH (fwd)
Central Drift Chamber
He(50%):C2H6(50%), Small cells, long lever arm, fast electronics
EM Calorimeter:
CsI(Tl), waveform sampling (baseline)
(opt.) Pure CsI for end-caps
Vertex Detector
2 layers DEPFET + 4 layers DSSD
Beryllium beam pipe
2cm diameter
Belle II Experiment @ KEK

## Slide 41: Belle II Silicon Vertex Detector
Four layers of double sided silicon strip detectors (made from 6” wafers)
Radii of SVD layers: 38 / 80 / 115 / 140 mm
2,3,4 or 5 sensors per ladder
Belle II Vertex Detector (VXD) = SVD + PXD
Ladders
End rings
Carbon fiber (CF) cone
End flange
Pixel Detector (PXD) (inside SVD  individual sub-detector)
Outer CF shell
Beam pipe

## Slide 42: SVD Ladder Design
L6 Ladder
L5 Ladder
L4 Ladder
L3 Ladder
FWD module
BWD module
Origami +z
Origami ce
Origami -z
BWD
FWD
Cooling pipe
Cooling pipe
Cooling pipe
BWD module
FWD module

## Slide 43: Double-sided strip sensors
Sensor Properties:
Double-sided with perpendicular strips
AC-coupled readout with poly-silicon resistor
N-bulk, 300/320 micron thickness
Three layouts only:
  Rectangular small for layer 3 (HPK)
  Rectangular large for layers 4-6 (HPK)
  Trapezoidal for forward layers 4-6 (Micron)
 | Readout strips(p/Rf) | Readout strips(n/z) | Readout pitch (p/Rf) | Readout pitch(n/z) | Sensors # (+ spares) | Active area (mm2)
Large | 768 | 512 | 75 μm | 240 μm | 120+18 | 122.90x57.72 =7029.88
Trapezoidal | 768 | 512 | 50-75 μm | 240 μm | 38+6 | 122.76x(57.59+38.42)/2=5893.09
Small | 768 | 768 | 50 μm | 160 μm | 14+4 | 122.90x38.55 =4737.80

## Slide 44: Sensors for Forward Region
Trapezoidal sensor for forward region
Designed completely in-house
  Production at Micron Inc.
  Testing again in-house
Double sided with orthogonal strips
  Special isolation measure necessary on ohmic side (p-stop)
  Different p-stop layouts on test sensors
  Testbeam and irradiation study to determine best structure
Atoll
Common
Combined
Sensor thickness = 300-320μm

## Slide 45
Design and construction of the Belle II Silicon Vertex Detector
  “Origami Module”: Highly integrated and lightweight module
    Carbon-fibre reinforced ribs
    6” DSSD, Kapton flex PCB
    CO2 cooling
    Material budget 0.55 X0 (averaged)
  Design developed at HEPHY starting in 2008
  Ladder assembly in-house finished 2017
Detector Module Assembly

## Slide 46: Half-Ladder Assembly
Sub Process
RS5 on assembly base
BW sub-assembly gluing
FW sub-assembly gluing
Completed half-ladder
2015: Assembly process at HEPHY Clean room:

## Slide 47: Belle II SVD Electronics
Belle II Electronics Chain:
48
8

## Slide 48: Belle II SVD – Activities and Status
October 2018
  Marriage of PXD+SVD = VXD
  Commissioning of VXD
  Outer cabling from dock boxes to FADC crates
November 2018
  Installation of VXD
  Inner cabling between detector and dock boxes
December 2018
  Completion of cabling and services
  Commissioning of installed Vertex Detector (VXD)
PXD + SVD marriage (+X)
VXD installation
installed FADC boards

## Slide 49
The Cosmic Frontier
CRESST @ LNGS

## Slide 50
Working group on “Rare Event Searches” is synergetically working on these projects:
DANAE: Search for very low-mass dark matter particles interacting with electrons
CRESST III: Search for low-mass dark matter particles interacting with atomic nuclei
COSINUS: Clarify the long-standing dark matter claim from DAMA
NUCLEUS: Precisely measure coherent, elastic neutrino nucleus scattering (CEvNS)
Rare Event Searches

## Slide 51: Synergy, more than a buzzword:
Experiment | Aim | Technology | Signal | Physics Case
DANAE | Search for very low-mass dark matter particles interacting with electrons | Silicon (DEPFET) | Electron recoil | Dark Matter
CRESST III | Search for low-mass dark matter particles interacting with atomic nuclei | Cryogenic | Nuclear recoil | 
COSINUS | Clarify the long-standing dark matter claim from DAMA |  |  | 
NUCLEUS | Precisely measure coherent, elastic neutrino nucleus scattering (CEvNS) |  |  | CEvNS
Rare Event Searches

## Slide 52
Nothing found in classic WIMP windows
  Also no candidate by SUSY
dark matter detection using ionization signal from Dark Matter- electron scattering
  inelastic nature of scattering and increased energy transfer possible due to lightness of electron
DANAE – Dark Matter Detection

## Slide 53
DEPFET: DEPleted Field Effect Transistor
  Charges are collected at internal gate  modulation of current in FET
  Well-established concept (e.g. BELLE-II)
RNDR-DEPFET
  Modified to host two internal gates
  Charge transfer between gates 1 & 2 with n transfers
  Noise scales with 1/sqrt(n)
  Minimum noise levels defined by leakage current
DANAE – Key Principle

## Slide 54
DANAE Test setup available at HLL Munich
  Stirling cooler & vacuum chamber
  To be transferred to Vienna
DEPFET Sensor prototype detector matrix
  64x64 pixels á 75x75x450µm
  Sensitive volume: 24mg
DANAE Implementation

## Slide 55
Cryogenic Rare Event Search with Superconducting Thermometers
  Direct detection of dark matter particles via their scattering off target nuclei
Scintillating CaWO4 crystals as target operated as
  Cryogenic calorimeter
  Cryogenic light detector to detect scintillation light
CRESST at LNGS Gran Sasso

## Slide 56
Cryogenic Detector with Phonons (>90%)
  Transition Edge Sensor (SQUID-type)
  Ultimate energy resolution is determined by how well you can measure T against thermodynamic fluctuations
Scintillation light (few %)
  Particle type dependent
CRESST Detectors

## Slide 57
CRESST-III
Run 1: 07/2016 – 02/2018
  30eV threshold reached
  Leading sensitivity over one order of magnitude: 160MeV/c2 – 1.8GeV/c2
Run 2: 12/2018 – 10/2019
  Upgraded detector modules with dedicated hardware changes to understand unexplained rise
Run 3: >01/2020
  2nd round with additional modifications
CRRESST-III Timeline

## Slide 58
COSINUS: Testing the DAMA signal with cryogenic NaI detectors
  Re-use technology of CRESST
  First data taking planned 2022
DAMA/LIBRA claimed DM signal with statistical significance of 11.9σ
COSINUS

## Slide 59
Study neutrino-induced nuclei recoil
  Using reactor neutrinos at high flux
  Challenges: recoil energies below 100eV  ultra-low thresholds required
Nucleus collaboration: 5 institutes with ~40 members
Scientific Goals:
  Measurement of weak mixing angle
  Approach neutrino floor
Nucleus