Developing an IoT System
IoT Air Quality System
Uli Raich (uli.raich@gmail.com)
Two lectures on Hardware and Software for
the Internet of Things applied to Air Quality measurement
Lecture 1: Introduction to the hardware
and development environment and access to the “things”
Presented online at the Seminar – Air Quality and
IoT based Air Sensors Nov. 2023

---
Resources
The slides and the code of all demo programs are available for download
at https://github.com/uraich/IoT4AQ

---
What is IoT?
Wikipedia:
The Internet of Things (IoT) describes physical objects (or groups of such objects) with sensors, processing ability, software and other technologies that connect and exchange data with other devices and systems over the internet or any other communication networks

---
IoT
The name “Internet of Things” already suggests that there are two distinct components to it:
- Things, which are represented by sensors and actuators. We therefore must have a means to read out these sensors and to control the actuators. Hardware interfaces are needed for this.
- Internet, we must be able to send data read from the sensors to the Internet and receive commands for the actuators from it. This means that we need a network interwork and the software to run the network protocols.

---
IoT system architecture

---
What is IoT
What is an IoT system composed of?
We need:
- Sensors and actuators
- A processor powerful enough to run the network protocol layers
- A network interface: either Ethernet of WiFi
- Interfaces to the sensors and actuators:
  - General Purpose I/O (GPIO) lines
  - I2C, I2S, SPI, serial interfaces
The cost for the controller should be in a good relation with the cost of the things

---
which micro-contoller?
Question of
- Needs (how much memory, which speed, which interfaces …)
- Budget
- Software environment and programming language
  - Most common: Arduino SDK
  - MicroPython
- Taste

---
… and today? for 10 Euros?
The micro-controller

---
ESP32 network connection
ESP32 network connection

---
The system with AQ sensors
From left to right:
The ESP32 CPU card with serial
connections to the
PlanTower PMS5003 dust sensor
The SGP30 air quality sensor
The SHT30 temperature and
humidity sensor

---
Programming the micro-controller
Depending on the processor used, several programming environments are available. For the ESP32 you have:
- esp-idf (ESP integrated development framework) provided by Espressif (not recommended for a beginner programmer)
- The Arduino SDK (Software Development Kit) originally developed for the Atmel Atmega chips but today available for many micro-controllers including the ESP32.
- MicroPython. A stripped down Python-3 interpreter with additional features needed by micro-controllers available for several chips including the ESP32.
In these lectures I use MicroPython

---
Communication tools
Communication tools
Serial communication (the PC :
minicom
Interaction with the file system:
ampy
IDE:
thonny
Flash Programming:
esptool
Several other tools are available, I listed only those that will be demonstrated during the presentation

---
How to interact with MicroPython
The MicroPython interpreter is installed on the ESP32 flash.
The Interpreter itself is written in C and available in OpenSource from github.
You can build MicroPython from source yourself and install it in the ESP32 flash using esptool.
You will need some infrastructure to accomplish this:
- xtensa-esp32-gcc cross compilation chain
- esp-idf
- cmake
- a dedicated Python virtual environment
- esptool to erase and program the flash memory
You can also pick up a firmware binary and flash it.

---
thonny
thonny
d

---
Interfacing to the “things”
Interfacing to the “things”
The ESP32 has a big number of interfaces implemented on the chip:
- GPIO pins
- PWM
- Capacitive touch sensor
- I2C (Inter Integrated Circuit) interface
- SPI (Serial Peripheral Interface) interface
- Analogue to digital converter
- Digital to analogue converter
- Timer

---
ESP32 pinout
ESP32 pinout

---
Checking the system
In C the ubiquitous “hello world” program checks if
- You can edit a program
- You can compile and link it
- You can run it
On embedded systems the simplest program possible is often the “blinking led” program
It shows that you can access the system and that interfacing works

---
IoT “Hello world”

---
Dust Sensors
The working principle:
Light from an LED or Laser is scattered by the dust particle and the scattered light is detected by a photo diode.
The air flow is maintained through a ventilator or through convection by a heater

---
Dismounted sensor

---
Different sensor types
Sharp GP2Y1051
PlanTower PME 5003
DMS 501A

---
Differences between the dust sensors
- Air flow (ventilator on convection)
- Light source (LED, laser, light wave length)
- Interface:
  - analogue output, needs an Analogue to Digital Converter (ADC)
  - PWM output signal
  - a micro-controller transforming the signal and sending a serial text string

---
PWM
The amount of dust particles is given by the time the output signal is low.
Very clean air results in a signal that is constantly high.
We will concentrate on the PMS 5003 because it is the easiest to read out.
More on the other sensor on the Twiki:
https://afnog.iotworkshop.africa/do/view/IoT_Course_English/DustSensors

---
The PMS5003 dust sensor
The PMS5003 sends its measurements to the micro-controller over a simple serial line.

---
Meaning of the serial message
Bytes	meaning
0,1	Magic word: ‘BM’
2,3	Frame length: data + checksum = 28
4,5	PM1.0 concentration [µg/m3]
]6,7	PM2.5 concentration [µg/m3]
7,9	PM10 concentration [µg/m3]
...
16,17	No of particles <0.3 µm in 0.1 L of air
...
30,31	checksum

---
Results from the dust measurement

---
Metal Oxide gas sensors
In clean air, donor electrons in metal oxide are attracted toward oxygen which is adsorbed on the surface of the sensing material, preventing electric current flow.
In the presence of reducing gases, the surface density of adsorbed oxygen decreases as it reacts with the reducing gases. Electrons are then released into the tin dioxide, allowing current to flow freely through the sensor. The current flow will give the equivalent readings of the measured gas.

---
The Sensirion SGP 30
The SGP30 is a MOS sensor providing output signals for volatile organic compounds (VOCs) and for the CO2 concentration.
It uses an I2C interface to
communicate with the
micro-controller

---
The I2C bus
The I2C bus
The Inter-Integrated Circuit (I2C) bus was invented by Philips in the early 1980. It is used by many sensors to communicate their data to the CPU.

---
The I2C protocol
The I2C protocol
Write to the bus
Read from the bus
7 bit device address + R/W bit

---
SHT30 and SGP30
In addition to dust concentration we want to measure
- eCO2: the CO2 concentration in the air in ppm
- TVOC: the total amount of volatile organic compounds in ppb
This can be accomplished with the SGP30 air quality sensor
The SGP30 needs to know the temperature and humidity in the air, which can be measured with an SHT30 temperature and humidity sensor.
We log these measurements as well.

---
I2C addressing
I2C addressing
The I2C bus uses the master/slave paradigm. The CPU acts as the master and the sensors as slaves.
The I2C bus uses 7 address bits (the 8th bit is the R/W line). A maximum of 128 slaves can therefore be connected to a single master.
The ESP32 has two hardware I2C buses, but MicroPython also provides a software I2C implementation using bit-banging on any GPIO line.
The pins for SCL (the I2C clock line) and SDA (the I2C data line) are
- SCL: GPIO 22
- SDA: GPIO 21
Control and readout of an I2C based sensor requires a driver accessing it using the MicroPython I2C driver calls. An example for the SHT30 temperature and humidity sensor is explained here.

---
MicroPython’s I2C driver
MicroPython’s I2C driver
From the MicroPython doc on the I2C bus for the ESP32
On the ESP32 CPU:
scl : GPIO 22
sda: GPIO 21

---
Scanning the I2C bus
Scanning the I2C bus
This is the code to read the I2C addresses of all modules connected to the bus
A list of all valid addresses is returned.
In our case we find:
- 0x45: SHT30
- 0X58: SGP30
d

---
How to get the driver?
There are several possibilities:
- It is already implemented in the interpreter: You are lucky! Just use it
- Somebody has published his driver in github: Clone it and install it on /lib of the ESP32
- There is a driver for CircuitPython (Adafruit’s version of MicroPython):
  You can easily port this to MicroPython
- You are unlucky and you will have to write the driver yourself!

---
Drivers are classes
Drivers are classes
Drivers are often implemented as Python classes
When an instance of a class is created the __init__ method its called
This method initializes the I2C bus and performs any initialization that the device may need.
The ESP32 has 2 hardware I2C interfaces and I2C bus 1 is reserved for users.
MicroPython includes a driver for the I2C bus whose methods are used to communicate with the I2C device.
The sensor functions and its control is provided through registers, which must be read and written. A typical sensor can have a big number of such registers (up to ~ 100) and each bit within the register may have a specific meaning. The sensor data sheet describes all register details.
Drivers are either frozen into the firmware binary or uploaded into the /lib folder in flash.
Usually a driver is provided with a few simple demo programs showing its use.

---
How to use the driver