## Slide 1
CEPC Beam Physics Issues
Chenghui Yu
for the CEPC accelerator team
Jan. 19, 2021

## Slide 2: Outline
Overview of CEPC collider ring
The DA optimization progress based on CDR
High luminosity scheme of CEPC
Summary

## Slide 3
Overview of CEPC collider ring
Double ring collider with 2 IPs
Compatible with the geometry of SPPC

## Slide 4
 | Higgs | W | Z
Number of IPs | 2 |  | 
Beam energy (GeV) | 120 | 80 | 45.5
Circumference (km) | 100 |  | 
Synchrotron radiation loss/turn (GeV) | 1.73 | 0.34 | 0.036
Crossing angle at IP (mrad) | 16.5×2 |  | 
Piwinski angle | 3.48 | 7.0 | 23.8
Number of particles/bunch Ne (1010) | 15.0 | 12.0 | 8.0
Bunch number (bunch spacing) | 242 (0.68s) | 1524 (0.21s) | 12000 (25ns+10%gap)
Beam current (mA) | 17.4 | 87.9 | 461.0
Synchrotron radiation power /beam (MW) | 30 | 30 | 16.5
Bending radius (km) | 10.7 |  | 
Momentum compact (10-5) | 1.11 |  | 
 function at IP x* / y* (m) | 0.36/0.0015 | 0.36/0.0015 | 0.2/0.001
Emittance ex/ey (nm) | 1.21/0.0024 | 0.54/0.0016 | 0.18/0.0016
Beam size at IP sx /sy (m) | 20.9/0.06 | 13.9/0.049 | 6.0/0.04
Beam-beam parameters x/y | 0.018/0.109 | 0.013/0.123 | 0.004/0.079
RF voltage VRF (GV) | 2.17 | 0.47 | 0.10
RF frequency f RF (MHz) (harmonic) | 650 (216816) |  | 
Natural bunch length z (mm) | 2.72 | 2.98 | 2.42
Bunch length z (mm) | 4.4 | 5.9 | 8.5
HOM power/cavity (2 cell) (kw) | 0.46 | 0.75 | 1.94
Energy spread (%) | 0.134 | 0.098 | 0.080
Energy acceptance requirement (%) | 1.35 | 0.90 | 0.49
Energy acceptance by RF (%) | 2.06 | 1.47 | 1.7
Photon number due to beamstrahlung | 0.082 | 0.050 | 0.023
Beamstruhlung lifetime /quantum lifetime* (min) | 80/80 | >400 | 
Lifetime (hour) | 0.43 | 1.4 | 2.5
F (hour glass) | 0.89 | 0.94 | 0.99
Luminosity/IP L (1034cm-2s-1) | 3 | 10 | 32
Physics goals
Performance
Construction cost
Operation cost
Fluctuation
Beamstruhlung
Flexibility
Robust
……
CDR beam parameters of collider ring

## Slide 5
Component | x (mm) | y (mm) | z (mm) | x (mrad) | y (mrad) | z (mrad) | Field error
Dipole | 0.10 | 0.10 | 0.10 | 0.1 | 0.1 | 0.1 | 0.01%
Arc Quadrupole | 0.10 | 0.10 | 0.10 | 0.1 | 0.1 | 0.1 | 0.02%
FF Quadrupole | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 
Sextupole | 0.10 | 0.10 | 0.10 | 0.1 | 0.1 | 0.1 | 
Higgs
Dipole | Quadrupole | Sextupole
B2/B0≤4×10-4 B3/B0≤0.8×10-4 B4/B0≤0.2×10-4 Bn(n>4)/B0≤0.8×10-4 | B2/B1≤4×10-4 B3/B1≤4×10-4 B4/B1≤2×10-4 Bn(n>4)/B1≤1×10-4 | B3/B2≤20×10-4 B4/B2≤3×10-4 B5/B2≤20×10-4 Bn(n>5)/B2≤10×10-4
RMS
R=12mm
89.1% of 1000 seeds
The DA optimization progress base on CDR
SAD is used
145 turns tracked
1000 samples
IR sextupoles + 32 arc sextupoles
(Max. free various=254)
Damping at each element
RF ON
Radiation fluctuation ON
Sawtooth on with tapering
Crab waist=100%
RMS close orbit distortions are smaller than 30 µm and 50 um in horizontal and vertical plane. Beta beatings < 7% , Coupling < 0.2%
KEK
Including FF

## Slide 6
Component | x (mm) | y (mm) | z (mm) | x (mrad) | y (mrad) | z (mrad) | Field error
Dipole | 0.10 | 0.10 | 0.10 | 0.1 | 0.1 | 0.1 | 0.01%
Arc Quadrupole | 0.10 | 0.10 | 0.10 | 0.1 | 0.1 | 0.1 | 0.02%
FF Quadrupole | 0.10 | 0.10 | 0.10 | 0.10 | 0.10 | 0.10 | 
Sextupole | 0.10 | 0.10 | 0.10 | 0.1 | 0.1 | 0.1 | 
Dipole | Quadrupole | Sextupole
B2/B0≤4×10-4 B3/B0≤0.8×10-4 B4/B0≤0.2×10-4 Bn(n>4)/B0≤0.8×10-4 | B2/B1≤4×10-4 B3/B1≤4×10-4 B4/B1≤2×10-4 Bn(n>4)/B1≤1×10-4 | B3/B2≤20×10-4 B4/B2≤3×10-4 B5/B2≤20×10-4 Bn(n>5)/B2≤10×10-4
RMS
R=12mm
72.4% of 1000 seeds
SAD is used
145 turns tracked
1000 samples
IR sextupoles + 32 arc sextupoles
(Max. free various=254)
Damping at each element
RF ON
Radiation fluctuation ON
Sawtooth on with tapering
Crab waist=100%
The DA margin shows we can expect more aggressive scheme for higher luminosity
KEK
The DA optimization progress base on CDR
Higgs

## Slide 7
 L*=2.2m, c=33mrad, βx*=0.36m, βy*=1.5mm, Emittance=1.2nm
  Strength requirements of anti-solenoids Bz~7.2T
  Enough space for the SC quadrupole coils in two-in-one type (Peak field 3.8T & 136T/m) with room temperature vacuum chamber & Iron yoke
Key parameters of CDR Higgs scheme
High luminosity scheme at Higgs energy

## Slide 8
 L*=1.9m, c=33mrad, βx*=0.33m, βy*=1.0mm, Emittance=0.68nm
  Strength requirements of anti-solenoids Bz~7.2T
  Two-in-one type SC quadrupole coils (Peak field 3.8T & 141T/m) with room temperature vacuum chamber & Iron yoke
Key parameters of high luminosity scheme
High luminosity scheme at Higgs energy
 L*=2.2m, c=33mrad, βx*=0.36m, βy*=1.5mm, Emittance=1.2nm
  Strength requirements of anti-solenoids Bz~7.2T
  Two-in-one type SC quadrupole coils (Peak field 3.8T & 136T/m)
Lower emittance and smaller beam pipe aperture within the region of SCQ
 L*=2.2m, c=33mrad, βx*=0.33m, βy*=1.0mm, Emittance=0.9nm

## Slide 9
High luminosity scheme at Higgs energy
For the part of cryostat inside the detector, the shape and size stay the same as CDR.
Under gravity, deformation=190m
Installation
Vacuum situation at the IP
High luminosity
We hope the length of cryostat can be as shorter as possible.
The design of detector won’t be affected.
Change of cryostat
CDR

## Slide 10
Change of IP chamber
Be: φ28mm
Al: φ28mm-> φ40mm
Cu: φ17mm
Be pipe: 28mm, SCQ Beam pipe:20mm
Be pipe: 28mm, Beam pipe:17mm
CDR
High luminosity
High luminosity scheme at Higgs energy

## Slide 11
HOM Power distribution | High luminosity Be pipe: 28mm SCQ Pipe:17mm |  | CDR Be pipe: 28mm SCQ Pipe:20mm | 
 | Higgs | Z | Higgs | Z
Be pipe | 3.46w | 52.1w | 2.66w | 40.74 w
Al | 22.62w | 335.4w | 21.32w | 317.2w
Y-shape crotch | 13.4w | 199w | 12.9w | 191.5w
Total power | 39.48w | 586.5w | 36.88w | 549.5w
Shrinking the SCQ pipe aperture from 20mm to 17mm, the power deposition will increase 10% which is acceptable.
Change of HOM deposition nearby the IP
High luminosity scheme at Higgs energy

## Slide 12
Q1a is the most challenging.
The design of quadrupoles and anti-solenoid is similar to that in CDR.
Iron yoke is adopted to eliminate the field crosstalk between the two apertures.
Coil | Central field gradient (T/m) | Magnetic length (m) | Width of GFR (mm) | Minimal distance between two aperture beam lines (mm)
Q1a | 141 | 1.21 | 15.21 | 62.71
Q1b | 84.7 | 1.21 | 17.92 | 105.28
Q2 | 94.8 | 1.5 | 24.14 | 155.11
Change of final focusing quadrupole coils
High luminosity scheme at Higgs energy

## Slide 13
Two layers cos2θ quadrupole coil using Rutherford cable with iron yoke. The inner diameter of the coil is 37mm. The width of the cable is 2.5mm, and there are 19 turns in each pole.
Each multipole field in single aperture is smaller than 1×10-4. The field crosstalk is smaller than 0.5×10-4. The dipole field in each single aperture as a result of field crosstalk is smaller than 5 Gs.
2D model
Magnetic flux density distribution
Change of final focusing quadrupole coils
High luminosity scheme at Higgs energy

## Slide 14
Shorter cell length to control the emittance from CDR 1.2nm to 0.7nm
Optimization of the quadrupole radiation effect
  Interaction region: longer FF quadrupoles
  ARC region: longer quadrupoles
  Reduction of dynamic aperture requirement from injection
  Straight section region: larger x at injection point
Optimization of high order chromaticity for arc region
Better correction of energy dependent aberration
Change of ARC region
High luminosity scheme at Higgs energy

## Slide 15
High luminosity scheme at Higgs energy
 | Higgs (CDR) | Higgs (high luminosity)
Number of IPs | 2 | 2
Beam energy (GeV) | 120 | 120
Circumference (km) | 100 | 100
Synchrotron radiation loss/turn (GeV) | 1.73 | 1.73
Crossing angle at IP (mrad) | 16.5×2 | 16.5
Piwinski angle | 3.48 | 4.87
Number of particles/bunch Ne (1010) | 15.0 | 16.3
Bunch number (bunch spacing) | 242 (0.68s) | 214 (0.70s)
Beam current (mA) | 17.4 | 16.8
Synchrotron radiation power /beam (MW) | 30 | 30
Bending radius (km) | 10.7 | 10.7
Momentum compact (10-5) | 1.11 | 0.73
 function at IP x* / y* (m) | 0.36/0.0015 | 0.33/0.001
Emittance ex/ey (nm) | 1.21/0.0024 | 0.68/0.0014
Beam size at IP sx /sy (m) | 20.9/0.06 | 15.0/0.037
Beam-beam parameters x/y | 0.018/0.109 | 0.018/0.115
RF voltage VRF (GV) | 2.17 | 2.27
RF frequency f RF (MHz) (harmonic) | 650 (216816) | 650 (216816)
Natural bunch length z (mm) | 2.72 | 2.25
Bunch length z (mm) | 4.4 | 4.42
HOM power/cavity (2 cell) (kw) | 0.46 | 0.48
Energy spread (%) | 0.134 | 0.19
Energy acceptance requirement (%) | 1.35 | 1.7
Energy acceptance by RF (%) | 2.06 | 2.5
Lifetime (hour) | 0.43 | 0.35
F (hour glass) | 0.89 | 0.88
Luminosity/IP L (1034cm-2s-1) | 2.93 | 5.0

## Slide 16
Achieved (without errors):
Goal (with errors):
We are developing more powerful methods for the DA optimization
High luminosity scheme at Higgs energy
Dynamic aperture
Notes: 11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 17
Difficulties:
  Vacuum chamber connection
    Longitudinal space: bellows should absorb deformation when baking. Add Z-direction support, length has been decreased to 83mm.
    Transversal space: all the structure should be within detection angle.
  Hardware protection
    Avoid SR
High luminosity scheme at Higgs energy
IR Mechanical Design

## Slide 18
The installation design nearby the IP
High luminosity scheme at Higgs energy
IR assembly

## Slide 19
High luminosity scheme at Higgs energy
IR assembly

## Slide 20
Standard TME cells are chosen for lower booster emittance to relax the DA requirement of collider ring.
1.4nm is expected. (CDR: 3.6nm)
High luminosity scheme at Higgs energy
Booster ring
Uniform distribution of quadrupoles
Combined magnet: B+Q, B+S

## Slide 21
Parameter | Symbol | Unit | Designed
e- /e+ beam energy | Ee-/Ee+ | GeV | 10
Repetition rate | frep | Hz | 100
e- /e+ bunch population | Ne-/Ne+ |  | > 9.4×109 / >9.4×109
 |  | nC | > 1.5
Energy spread (e- /e+ ) | σe |  | < 2×10-3 / < 2×10-3
Emittance (e- /e+ ) | εr | nm rad | 10
Bunch length (e- /e+ ) | σl | mm | 1 / 1
e- beam energy on Target |  | GeV | 4
e- bunch charge on Target |  | nC | 10
In order to relax the DA reqirement of booster the beam emittance of Linac should be controlled as 10 nm with the damping ring of energy 1.1GeV. (CDR: 40nm)
1.1GeV
1200m
High luminosity scheme at Higgs energy
LINAC

## Slide 22
The possibility of other energies base on high luminosity Higgs scheme
Normal Z mode: Q1a=Vertical focusing quadrupole, Q1b+Q2=Horizontal focusing quadrupole
W & H mode: Q1a+Q1b=Vertical focusing quadrupole, Q2=Horizontal focusing quadrupole
Higher than Higgs energy: Q1a+Q1b+Q2=Vertical focusing quadrupole
High luminosity Z: HOM at SCQ Pipe will be one of the dominant constraint. Replacing the whole cryostat is the best option. The shape and size of cryostat stay the same and the inner aperture of SCQ beam pipe can be made large enough since Z beam energy is low enough.

## Slide 23
CEPC high luminosity Parameters
 | tt | Higgs | W | Z | 
Number of IPs | 2 | 2 | 2 | 2 | 
Energy (GeV) | 180 | 120 | 80 | 45.5 | 
Circumference (km) | 100 | 100 | 100 | 100 | 
SR loss/turn (GeV) | 8.53 | 1.73 | 0.33 | 0.036 | 
Half crossing angle (mrad) | 16.5 | 16.5 | 16.5 | 16.5 | 
Piwinski angle | 1.16 | 4.87 | 9.12 | 24.9 | 
Ne/bunch (1010) | 20.1 | 16.3 | 11.6 | 15.2 | 
Bunch number (bunch spacing) | 37 (4.45s) | 214 (0.7us) | 1588 (0.2s) | 3816 (86ns) | 11498 (26ns)
Beam current (mA) | 3.5 | 16.8 | 88.5 | 278.8 | 839.9
SR power /beam (MW) | 30 | 30 | 30 | 10 | 30
Bending radius (km) | 10.7 | 10.7 | 10.7 | 10.7 | 
Phase advance of arc cell | 90/90 | 90/90 | 90/90 | 60/60 | 
Momentum compaction (10-5) | 0.73 | 0.73 | 0.73 | 1.48 | 
IP x/y (m) | 1.0/0.0027 | 0.33/0.001 | 0.33/0.001 | 0.15/0.001 | 
Emittance x/y (nm) | 1.45/0.0047 | 0.68/0.0014 | 0.28/0.00084 | 0.27/0.00135 | 
Transverse IP (um) | 37.9/0.11 | 15.0/0.037 | 9.6/0.029 | 6.36/0.037 | 
x/y/IP | 0.076/0.106 | 0.018/0.115 | 0.014/0.13 | 0.0046/0.131 | 
VRF (GV) | 9.52 | 2.27 | 0.47 | 0.1 | 
f RF (MHz) (harmonic) | 650 (216816) | 650 (216816) | 650 (216816) | 650 (216816) | 
Nature bunch length z (mm) | 2.23 | 2.25 | 2.4 | 2.75 | 
Bunch length z (mm) | 2.66 | 4.42 | 5.3 | 9.6 | 
HOM power/cavity (kw) | 0.45 (5cell) | 0.48 (2cell) | 0.79 (2cell) | 2.0 (2cell) | 3.02 (1cell)
Energy spread (%) | 0.17 | 0.19 | 0.11 | 0.12 | 
Energy acceptance requirement (DA) (%) | 2.0 | 1.7 | 1.2 | 1.3 | 
Energy acceptance by RF (%) | 2.61 | 2.5 | 1.83 | 1.48 | 
Lifetime (hour) | 0.59 | 0.35 | 1.3 | 1.7 | 1.4
Lmax/IP (1034cm-2s-1) | 0.5 | 5.0 | 18.7 | 35.0 | 105.5
Beamstrahlung Lifetime
Beam-beam simulation

## Slide 24: Summary
The design of high luminosity scheme with 51034cm-2s-1 & 30MW has been designed. It doesn’t meet strong limitation and also won’t affect the current mechanical design of detector.
The L* can be set as 1.9m from IP with lower emittance and smaller beam pipe within the region of SCQ.
For the consideration of high luminosity Z, if it’s a strong limitation from local HOM heating problem due to the narrow SCQ beam pipe, replacing the whole cryostat is the best option. The shape and size of cryostat stay the same and the inner aperture of SCQ beam pipe can be made large enough.
More detailed studies will be done. Such as DA optimization with errors, detector background evaluation, etc.