## Slide 1: New Accelerator Physics and Technology Trends
Ralph W. Aßmann, DESY
IHEP 2021
Virtual, Hongkong, China
20 January 2020
An 18 Minute Glimpse at a Very Rich Topic

## Slide 2: Slow-down in Energy Increase of Frontier Accelerators
Livingston plot leveling off – here our version, giving beam energy versus time
HiLumi
Hadron acc. project
Hadron acc. proposal
Lepton acc. project
Lepton acc. proposal
Advance of new colliders limited by practical constraints on required resources (budget, manpower) and size (does it fit on site?)
FCC-ee CEPC

## Slide 3: Why this slow-down? Part 1
Technical limitations in highly advanced and mature technologies
Hadron (p) circular collider
Limited by available bending field strength By (even super-conducting):
Increase momentum p by increasing radius R times bending field By
Lepton (e-,e+) circular collider
Limited by synchrotron radiation losses U0, to be fed back by RF voltage VRF:
Increase momentum p by increasing radius R and lowering bending field By
E.g. LEP2: 3% of energy lost per turn, 10,000 turns/second

## Slide 4: The End of LEP2
November 2nd, 2000, 7am
When we shut down LEP2 in 2000 we thought that it was the last e+e- circular collider due to synchrotron radiation limit!
Larger facility with innovative high luminosity design (realizing new ideas) will allow pushing the e+e- energy frontier (FCC-ee, CEPC).
Alternatively: going linear. This avoids synchrotron radiation limitation! But comes with its own challenges.

## Slide 5: Why this slow-down? Part 2
Technical limitations in highly advanced and mature technologies
Lepton (e-,e+) linear collider
Limited by achievable accelerating gradient (energy gain per length)
Increase momentum p by increasing gradient Gacc or length L
Achievable accelerating gradient limited by peak surface field, flashovers, surface damage and breakdown rate
Example shows a result from CLIC at a high RF frequency of 30 GHz
By now, some important progress made but gradients limited to 100 MV/m at max presently
Sketch Padamse, Tigner
“Runzelröhre”
20 MV per Meter
Flashover at too high voltages
Damaged location
30 GHz, 16 ns, 66 MV/meter
CLIC, W. Wuensch
W. Wuensch

## Slide 6: How to advance?
Looking for solutions
Hadron (p) circular collider
Increase radius = size (FCC-hh)
Increase bending field
SC bend magnet work (FCC-hh)
Increase supplied RF voltage
(FCC-ee, CEPC)
Increase radius = size (FCC-ee, CEPC)
Increase mass of acc. particle (muon)
Increase length (ILC, CLIC)
Increase accelerating gradient
Pushing existing technology (ILC, CLIC)
New regime of ultra-high gradients (plasma, dielectric accelerators)
Lepton (e-,e+) circular collider
Lepton (e-,e+) linear collider

## Slide 7: Many high tech activities ongoing in the big collider projects, pioneering new solutions, advancing technology and opening new possibilities! No time to go through in detail. Apologies! See the many talks on R&D and results presented at this conference! Affordability is a critical issue: cost of components, energy efficiency, OP costs! Here, just a few remarks on trends...

## Slide 8: Trend: Smart Manufacturing and Assembly
Can we bring down cost per meter of accelerator by a factor 2 – 10?
Halbach quadrupole using NdFeB, 3D printed, 23.6 T/m, R=34.7mm bore (0.82T max), 10-4 errors at R=10mm
Material cost: $1100. No alignment better than 0.25 mm required anywhere. Assembled with mallet.
Picture courtesy S. Brooks, BNL
Smart manufacturing and assembly (optimized as industrial process):
Factory: Instead of highly accurate pieces of permanent magnets (very expensive) accept non-perfect pieces with larger tolerances (cheap).
Measurement Lab: Measure those pieces accurately.
Computer: Solve for adequate positioning of pieces such required field on beam is achieved.
Computer: Calculate required mechanical custom support for pieces.
Factory: 3D print the optimized custom support.
Factory: Assemble permanent magnet that provides required fields.

## Slide 9: Trend: Energy Efficiency and Green Accelerators
Reduce energy consumption
For example, ERL (CBETA, PERLE, bERLinPro, ...), permanent magnets, novel klystrons:
ERL concept proposed in 1965: M. Tigner, “A possible apparatus for electron clashing-beam experiments”. Nuovo Cim 37, 1228–1231 (1965).
Re-use the energy stored in the beam – RF cavities for pumping energy into beam and for extracting it
PERLE: 1 GeV energy recovery demonstration of a recirculating SC linear accelerator.
We heard about CEPC related work on klystrons with improved efficiency, see also impressive CERN-driven advances on klystron efficiency  mature technologies but still considerable room for improvement!

## Slide 10: Trend: Machine Learning and Artificial Intelligence
Reduce energy consumption
Machine learning (SLAC, PSI, CERN), automated commissioning (ANL), and autonomous accelerators (DESY):
At DESY in the SINBAD/ARES accelerator a team from DESY & KIT is testing methods towards an autonomous accelerator
Exploits highly non-linear regime of ARES with limited number of degrees of freedom
https://scitechdaily.com/

## Slide 11: Trend: Accelerators and Gravity
New territory for large colliders
Can a large storage ring like LHC detect gravitational waves?
Rao et al, PRD 2020
https://journals.aps.org/prd/abstract/10.1103/PhysRevD.102.122006
https://arxiv.org/pdf/2012.00529.pdf
Thanks to Frank Zimmermann

## Slide 12: Trend: Accelerators and Gravity
New territory for large colliders
https://indico.cern.ch/event/982987/
Thanks to Frank Zimmermann

## Slide 13: Trend: The R&D on Compact Accelerators
Looking for solutions
Hadron (p) circular collider
Increase radius = size (FCC-hh)
Increase bending field
SC bend magnet work (FCC-hh)
Increase supplied RF voltage
(FCC-ee)
Increase radius = size (FCC-ee)
Increase mass of acc. particle (muon)
Increase length (ILC, CLIC)
Increase accelerating gradient
Pushing existing technology (ILC, CLIC)
New regime of ultra-high gradients (plasma, dielectric accelerators)
Lepton (e-,e+) circular collider
Lepton (e-,e+) linear collider
Factor 206.8 higher mass muon versus electron
BIG factors  Novel concepts pursue transformative concepts that can open new horizons in energy reach for HEP research

## Slide 14
Trend:

## Slide 15: Trend: R&D on Compact Accelerators
Looking for solutions
Hadron (p) circular collider
Increase radius = size (FCC-hh)
Increase bending field
SC bend magnet work (FCC-hh)
Increase supplied RF voltage
(FCC-ee)
Increase radius = size (FCC-ee)
Increase mass of acc. particle (muon)
Increase length (ILC, CLIC)
Increase accelerating gradient
Pushing existing technology (ILC, CLIC)
New regime of ultra-high gradients (plasma, dielectric accelerators)
Lepton (e-,e+) circular collider
Lepton (e-,e+) linear collider
Factor 206.8 higher mass muon versus electron
Factor 100 – 1000 higher accelerating gradient
BIG factors  Novel concepts pursue transformative concepts that can open new horizons in energy reach for HEP research

## Slide 16: Trend: High Gradient – High Frequency – Small Dimensions
Powering novel accelerators
Plasma Accelerator Laser- or beam driven Dynamic Plasma Structure
Plasma field calculations
High  High  Small Gradients Frequencies Dimensions (1 – 100 GV/m) (> 100 GHz) (< 1 mm)
No klystrons for high frequencies!
Use particle bunches or laser pulses as drivers.
Material limitations solved through “new cavities”: dielectric materials, plasma cavities, …
Two main directions:
Microstructure Accelerator Laser- or beam driven Vacuum accelerators Conventional field design
1
2

## Slide 17: Laser-Driven Micro Structures (Vacuum) – 1
Vacuum dielectric accelerator
1 GeV/m possible but low absolute energies achieved so far
AXSIS project (ERC synergy grant) at DESY/ Uni Hamburg: THz laser-driven accelerator with atto-second science  Kärtner/Fromme/Chapman/Assmann

## Slide 18: Laser-Driven Micro Structures (Vacuum) – 2
Vacuum dielectric accelerator
“Accelerator on a Chip” grant from Moore foundation for work by/at Stanford, SLAC, University Erlangen, DESY, University Hamburg, PSI, EPFL, University Darmstadt, CST, UCLA
Lasers drive structures that are engraved on microchips (e.g. Silicium)
Major breakthroughs can be envisaged:
  Mass production
  Implantable accelerators for in-body irradiation of tumors
  Accelerators for outer space

## Slide 19: Nano Structures...
Figure from Akash Sahai
Small dimensions with particular promises and challenges

## Slide 20: Trend: Laser Plasma-Acceleration
Internal injection

## Slide 21: Optimization: Phase Slippage Stability/Reproducibility
Maximize distances over which we can accelerate Hit the same phase every time

## Slide 22: Strong plasma focusing: Betatron motion and X rays
Wiggling electrons emit X rays  a plasma accelerator as accelerator and undulator at once
If an electron beam is injected mis-matched into a plasma, we expect strong beta mismatch oscillations of the beam size.
The oscillating electrons should radiate X rays.
This was seen in a SLAC experiment in 2001.
Plasma acts as undulator!

## Slide 23: Novel Acceleration R&D in Europe  Towards International Projects
How can we develop plasma accelerators towards usability?
European novel accelerator projects with international involvement
Funded by EU Horizon2020 as EU Design Study
CERN experiment collaboration under leadership of MPI (A. Caldwell)
Independent national projects*, funded by national states. About 16 major facilities for novel plasma acceleration R&D in Europe.
* See note on ELI
ERC Synergy Grant

## Slide 24: EuPRAXIA: A European Strategy for Accelerator Innovation
Do the required intermediate step between proof of principle and production facility – make one acc. unit!
PRESENT EXPERIMENTS
Demonstrating 100 GV/m routinely
Demonstrating GeV electron beams
Demonstrating basic quality
EuPRAXIA INFRASTRUCTURE
Engineering a high quality, compact plasma accelerator
5 GeV electron beam for the 2020’s
Demonstrating user readiness
Pilot users from FEL, HEP, medicine, ...
PRODUCTION FACILITIES
Plasma-based linear collider in 2040’s
Plasma-based FEL in 2030’s
Medical, industrial applications soon

## Slide 25: Conclusions
Long-term future
The long-term future is bright: there will be plenty of opportunities as technology advances!
Larger e+e- colliders are a future path, requiring affordable technology and good energy efficiency, both if circular or linear.
Advanced e+e- colliders (plasma/dielectric/laser) are another possible path forward. Energy very promising but beam quality insufficient:
  There are now near future science applications outside HEP, e.g. FEL. This can be the stepping stone towards a plasma linear collider.
  Major projects going on, all including HEP aspects.
Muon colliders and future ep machines are subject of intensifying R&D.
In Europe experts panels are being set up to propose accelerator R&D roadmaps in follow-up to European strategy of particle physics. Stay tuned...

## Slide 26: Thank you for your attention