## Slide 1: CEPC Injection/Extraction Hardware Design Towards TDR
Jinhui Chen, Lihua Huo , Yuwen Wu, Hua Shi , Guanjian Wu, Zilin Chen, Guanwen Wang, Lei Wang, X.H. Cui, D. Wang, Yiwei Wang
Injection group
2021-1-20
The IAS Program on High Energy Physics 2021 , Jan. 19-21, 2021 , Online

## Slide 2: Outline
1
Overview of CEPC Inj./Ext. systems
2
DR Inj./Ext. system hardware design towards TDR
3
BST LE inj. system hardware design towards TDR
4
BST HE ext. system hardware design towards TDR
5
Summary

## Slide 3
Overview of the CEPC injection and extraction systems

## Slide 4: Layout of the accelerator complex
The CEPC accelerator complex consists of a Linac, which including a small damping ring for positron beams, several transport lines, a booster ring and 2 storage rings, all of which are in a single tunnel.
1.2km
10-120GeV
120GeV
120GeV
e+
e-
100km
Damping ring
Dump
Dump

## Slide 5: CEPC injection and extraction systems
DR injection and Extraction system(e+)
Booster LE injection system (e+,e-)
Booster Extraction system1 (e+,e-)
Collider off-axis injection system (e+,e-)
Booster Extraction system2 (e+,e-)
Booster HE injection system (e+,e-)
Collider swap out injection system (e+,e-)
Collider swap out extraction system (e+,e-)
Collider beam dump system(e+,e-)
There are 9 injection and extraction sub-systems in CEPC accelerator complex, including:
Off-axis injection
(in W and Z mode)
On-axis injection
(only in Higgs mode)
Linac
DR
Booster
Collider
120GeV
1.1GeV
10~120GeV
dump
①
⑨
④
②
⑥
③
⑧
⑦
⑤

## Slide 6: Main types of inj.&ext. hardware
 | Sub-system | Kicker Type | Kicker waveform | Septa Type | Thickness of septum
1 | Damping ring inj./ext. | Slotted-pipe kicker | Half-sine/250ns | Horizontal LMS | ф22/3.5mm
2 | Booster LE inj. | Strip-line kicker | Half-sine/50ns | Horizontal LMS | ф55/5.5mm
3 | Booster ext. for CR off-axis inj. | Delay-line dipole kicker | Trapezoid /440-2420ns | Vertical LMS | Ф55/6mm
4 | Collider off-axis inj. | Delay-line NLK kicker | Trapezoid /440-2420ns | Vertical LMS | Ф75x56/2mm
5 | Booster ext. for CR on-axis inj. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS | Ф55/6mm
6 | Booster HE inj. | NLK or Pulsed sextupole | Half-sine/0.333ms | Vertical LMS | Ф55/6mm
7 | Collider swap out inj. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS | Ф75x56/6mm
8 | Collider swap out ext. | Ferrite core dipole kicker | Half-sine/1360ns | Vertical LMS | Ф75x56/6mm
9 | Collider beam dump | Delay-line dipole kicker | Trapezoid /440-2420ns | Vertical LMS | Ф75x56/6mm
10 | RF region beam separating | Delay-line dipole kicker | CW square / 165us,50% | Horizontal Copper septa | Ф75x56/10mm

## Slide 7
DR Inj./Ext. system hardware design towards TDR

## Slide 8: Damping ring injection and extraction system
Damping ring is dedicated to decrease emittance of positron beams
Double bunches are stored at the same time
On-axis bunch-by-bunch injection
Hardware：Vertical slotted-pipe kicker 、horizontal LSM
250ns
10ms
125ns
1.1GeV，75.4m
240mm
120mrad

## Slide 9: LSM requirements for DR
Septum=3.5mm
Stored beam
Inj. beam
11mm
5.5mm
11mm
Injected beam | X(mm) | Y(mm) | Z(mm)
LSM in | -30.0 | -23.75 | -500.0
LSM out | 0 | -20 | 0
x
z
Stored
beam
Injected
beam
Top view
-30.0
（mm）
y
z
Stored
beam
Injected
beam
septum
Side view
（mm）
Stored beam | X(mm) | Y(mm) | Z(mm)
LSM in | 0 | 0 | -500.0
LSM out | 0 | 0 | 0
Parameters | Unit | DR-LSM
Quantity | - | 2
Energy | GeV | 1.1
Horizontal deflection angle | mrad | 120
Insertion length | m | 0.5
Magnetic field strength for injected/extracted beam | T | 0.883
Min. Septum thickness（including septum board, inj./ext. beam pipe wall, installation gap) | mm | 3.5
Field uniformity | - | <±0.05%
Leakage field | - | ≤1×10-3
Clearance of stored beam at lambertson（HV） （refer to stored beam orbit） | mm | 36.422
Clearance of inj.&ext. beam at lambertson（HV）（refer to inj.&ext. beam orbit） | mm | 2211
Physical aperture of stored beam vacuum chamber | mm | 2222

## Slide 10: LSM physics design
Stored beam chamber
(VP,FeCoV,1J22)
Injected beam chamber
(SS, 316L)
Yoke (DT4)
Winding (96T)
Stored beam
Inj. beam
Exit of LSM
Stored beam pipe(VP) inner
diameter= ø22mm,
Thickness=2mm
Injected beam pipe (SS):
W=41mm, H=19mm,
Thickness=1mm
Septum
Thickness=2+1+0.5=3.5mm
Magnet gap: 22mm
Winding:
W=70mm,H=105mm,T=96
Exciting current=166A
Inductance=0.0228H
700×344×268mm
Injected beam
Stored beam
Magnet pole
Installation margin
Yoke
1mm
2mm
0.5mm
3.5mm
Φ22mm
1J22
316L
41×19mm
Contributed By Yuwen Wu

## Slide 11: 3D simulation
Stored beam vacuum chamber:1J22
Center magnetic field intensity：8836Gauss
Magnet effective length：542mm
Vertical Leakage field：2.81E-04
Horizontal Leakage field：1.79E-06

## Slide 12: DR inj./ext. kicker design parameters
parameter | Unit | DR-kicker
Quantity | - | 2
Type | - | Slotted-pipe kicker
Deflect direction | - | Vertical
Beam Energy | GeV | 1.1
Deflect angle | mrad | 10.7
Magnetic effective length | m | 1.4
Magnetic strength | T | 0.0281
Integral magnetic strength | T·m | 0.03934
Clearance region(H×V) | mm | 32.8×26.6
Good field region(H×V) | mm | 19.8×16
Field uniformity in good field region | - | ±1.5%
Repetition rate | Hz | 100
Amplitude repeatability | - | ±0.5%
Pulse jitter | ns | ≤5
Bottom width of half sine pulse(5%-5%) | ns | < 250

## Slide 13: Magnet physics design
2D simulation model
Max. voltage of coil: Umax=10622V
Max. exciting current: Imax=2400A
Magnet coil inductance=387nH
Good field region
19.8×16mm
x=±10, y=±8
Un.= -0.9%~1.5%
Good field region: 19.8×16mm
Field uniformity: -0.9%~1.5%
Contributed By Lihua Huo,Lei Wang

## Slide 14: Slotted-pipe kicker engineer design
Outer body (316L)
Busses (FOC)
insulation support (ceramic)
HV feedthrough
Cooling water pipe
+
-
To vacuum pump

## Slide 15: 250ns-fast kicker pulser design
Scheme: 20-stage inductive adder based on SiC-MOSFETs.
The co-axial transformer is configured as bipolar output.
The pulser is located outside tunnel and 10 cables with length of 30m are applied to connect to kicker.
Due to short end of the slotted-pipe kicker, the reflection energy should be return to the pulser.
A proper absorption circuit must be designed at pulser end.
20-stage inductive adder
920mm
510mm
564mm

## Slide 16
BST LE Inj. system hardware design towards TDR

## Slide 17: Booster LE injection system
On-axis bunch-by-bunch injection
Hardware：
  Kicker: vertical strip-line kicker driven by fast pulser
  Septa: horizontal Lambertson magnet
50ns,100Hz
Q
Q
22.5m
478.5m
1m
1m
ϴV=0.11mrad
454m
50mm
Side view
Q
Q
ϴH=22mrad
22mm
517mm
Top view
Lambertson
kicker
0.055mm
30.22mm
Q
Q
Q

## Slide 18: LSM requirements for BST LE inj. system
Injected beam | X(mm) | Y(mm) | Z(mm)
LSM in | -22.0 | -50 | -800.0
LSM out | 0 | -50 | 0
Stored beam | X(mm) | Y(mm) | Z(mm)
LSM in | 0 | 0 | -800.0
LSM out | 0 | 0 | 0
Parameters | Unit | DR-LSM
Quantity | - | 2
Energy | GeV | 10
Horizontal deflection angle | mrad | 22
Insertion length | m | 0.8
Magnetic field strength for injected/extracted beam | T | 0.9175
Min. Septum thickness（including septum board, inj./ext. beam pipe wall, installation gap) | mm | 5.5
Field uniformity | - | <±0.02%
Leakage field | - | ≤1×10-3
Clearance of stored beam at lambertson（HV） （refer to stored beam orbit） | mm | 3050
Clearance of inj.&ext. beam at lambertson（HV）（refer to inj.&ext. beam orbit） | mm | 1829
Physical aperture of stored beam vacuum chamber | mm | 5555
Septum=5.5mm
Stored beam
Inj. beam
27.5mm
14mm
27.5mm
x
z
Stored
beam
Injected
beam
Top view
-22.0
（mm）
y
z
Stored
beam
Injected
beam
septum
Side view
（mm）
-50.0

## Slide 19: LSM physics design
Stored beam chamber
(VP,FeCoV,1J22)
Injected beam chamber
(SS, 316L)
Stored beam pipe(VP) inner
diameter= ø55mm,
Thickness=4mm
Injected beam pipe (SS):
inner diameter=ø29mm,
Thickness=1mm
Septum
Thickness=4+1+0.5=5.5mm
Magnet gap: 32mm
Winding:
W=70mm,H=140mm,T=128
Exciting current=188A
Inductance=0.0682H
Yoke (DT4)
Winding (96T)
Stored beam
Inj. beam
1000×383×343mm
Exit of LSM
Injected beam
Stored beam
Magnet pole
Installation margin
Yoke
1mm
4mm
0.5mm
5.5mm
Φ55mm
1J22
316L
Φ29mm
Contributed By Yuwen Wu

## Slide 20: 3D simulation
Stored beam vacuum chamber:1J22
Center magnetic field intensity：9200Gauss
Magnet effective length：849mm
Vertical Leakage field： 4.41E-04
Horizontal Leakage field： 1.56E-04

## Slide 21: BST LE inj. kicker design parameters
parameter | Unit | Booster Low Energy injection kicker
name | - | BSTLEIK
Quantity | - | 2
Type | - | Strip-line kicker
Deflect direction | - | Vertical
Beam Energy | GeV | 10
Deflect angle | mrad | 0.11
Length of Strip-line kicker electrode | mm | 1000
Gap between two electrodes | mm | 44
Odd mode impedance |  | 50±1
Even mode impedance |  | <65
Clearance region(H×V) | mm | 22×44
Good field region(H×V) | mm | 12×22.6
Integral field uniformity | - | ±2.5%
Amplitude of electrical pulse（into 50Ω） | kV | ±12.25
Repetition rate | Hz | 100
Amplitude repeatability | - | <2% (RMS)
Pulse jitter | ns | ≤1
Bottom width of electrical pulse（3%-3%） | ns | < 50

## Slide 22: Strip-line kicker design for booster LE inj.
Kick strength
  Total kick angle: θ=0.11mrad
  E=10GeV, d=44mm, g=1 =>U*L>24.2kV∙m
  Total strip-line kicker electrode length L=1m =>U>24.2kV(or ±12.1kV)
Here, θ is kick angle(rad)；E is beam energy(eV)；U is applied pulse voltage for both electrodes(V)；l is strip-line length；d is the distance between the electrodes，g is the geometry factor, determined by the shape of the electrode. w is the strip-line width.
Kick speed
  Min bunch spacing - τ=25ns
    Electrode length l<3.75m => l= 1m
    Electrical pulse Width 6.7ns< tp <43.3ns =>Flat-top ttop >6.7ns, Rise/fall Time tr/tf <18.3ns
50ns,100Hz

## Slide 23: Kicker physics design
To achieve highest geometric factor(g=0.9866) the blade width should be w=70mm, when d=44mm.
Blade length=1m，thickness=10mm
Voltage between blades=24.5kV
Outer body: distance between vanes=60mm
Odd mode impedance Zodd=50Ω, even mode impedance Zeven=60.5Ω
blade
Outer body
2D-geometry
Contributed By Hua Shi

## Slide 24: 3D simulations
1000mm
50Ω co-axis feedthrough，d/D=7/16mm
1010mm
TDR
8mm
7mm
16mm
S-parameter
Pulse bandwidth：300MHz
Impedance mismatching
（from feedthrough to blade）

## Slide 25: 3D simulations
Field uniformity: ~0.52% in x=(-6, 6) mm, ~1.35% in y=(-11.3, 11.3)
Emax=9MV/m @ excited pulse peak=15kV
Emax=9MV/m

## Slide 26: Strip-line kicker engineer design
Outer body (316L)
HV feedthrough
electrodes(FOC)
Contributed By Lihua Huo,Lei Wang

## Slide 27: 50ns-fast puler design
Scheme: pulser based on DSRDs driven by 6-stage inductive adder;
The similar hardware was developed in HEPS-TF project.
4ns
V=17kV,
FWHM=5ns,
Tr(10-90%)<2.6ns,
Tf(90-10%)<3.2ns,
Bottom width(3%-3%)<10ns
PFL=0.3m
DSRDs circuit with 6-stage inductive adder driven
J.H. Chen, Strip-line kicker and fast pulser R&D for the HEPS on-axis injection system, NIMA 920(2019)1-6
Drift Step Recovery Diode

## Slide 28
BST HE Ext. systems hardware design towards TDR

## Slide 29: BST-HE-Ext. for CR off-axis injection
Train by train or bunch-by-bunch extraction
Kicker: horizontal out-vacuum delay-line dipole kicker(coating ceramic vacuum chamber) driven by PFN-based solid-state pulser
Septa: vertical Lambertson magnet
200ns
40~2000ns
200ns
1kHz
200ns
40~2000ns
200ns
1kHz
Booster
E- CR
Side view
Booster
E- CR
Top view
LMS
LMS
LMS
LMS
Kicker
NLK
NLK
Kicker
down
up
out
in
Septum Plate 6mm
Septum Plate 2mm

## Slide 30: BST-HE-Ext. for CR on-axis swap-out injection
1360ns,1kHz
Dipole kicker: horizontal ferrite core out-vacuum kicker+coating ceramic chamber+LC resonance pulser
Inj. NLK: horizontal NLK or Pulsed sextupole+coating ceramic chamber+LC resonance pulser
Septa: Vertical Lambertson magnet
0.333ms,1kHz
1360ns,1kHz
Septum Plate 6mm
Booster
E- CR
Side view
Booster
E- CR
Top view
LMS
LMS
LMS
LMS
LMS
LMS
LMS
LMS
Kicker
Kicker
Kicker
NLK
NLK
Kicker
down
up
down
up
out
out
in
Septum Plate 6mm
Bunch-by-bunch extraction

## Slide 31: BST EXT kicker design parameters
parameter | Unit | BST-EXT-kicker1 （for CR off-axis inj.） | BST-EXT-kicker2 （for CR on-axis inj.）
Quantity | - | 2 | 2
Type | - | In-air delay-line dipole kicker | In-air lumped parameter dipole kicker
Deflect direction | - | Horizontal | Horizontal
Beam Energy | GeV | 120 | 120
Deflect angle | mrad | 0.2 | 0.1
Magnetic effective length | m | 1.4 | 0.7
Magnetic strength | T | 0.06 | 0.06
Integral magnetic strength | T·m | 0.08 | 0.04
Clearance region(H×V) | mm | 55×55 | 55×55
Good field region(H×V) | mm | ? | ?
Field uniformity in good field region | - | ±1.5%？ | ±1.5%？
Repetition rate | Hz | 1k | 1k
Amplitude repeatability | - | ±0.5% | ±0.5%
Pulse jitter | ns | ≤5 | ≤5
Bottom width of pulse(5%-5%) | ns | Trapezoid：440~2420 | Half-sine：1360
Tr/Tf(5%-95%) | ns | <200 | <680
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz

## Slide 32: Kicker magnet physics design
h=64mm
W=68mm
55mm
4mm
L=
I=
U=I
Lumped parameter kicker with shorted end : Tr（5%-95%）=3τ=561ns
Lumped parameter kicker with matched resistor : Tr（5%-95%）=3τ/2=280.5ns
Delay-line kicker with matched resistor : Tr（5%-95%）=τ=187ns
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz

## Slide 33
Lumped parameter dipole kicker magnet
Features:
Out-vacuum kicker with metallic coating ceramic vacuum chamber
Pulser: Inductive adder based on IGBTs.
<1360ns,1kHz

## Slide 34: Distributed parameter (delay-line) dipole kicker
Features:
The structure of delay-line kicker is complicated, but helps to achieve ideal trapezoid waveform.
ceramic vacuum chamber with special pattern metallic coating
Pulser: adjustable pulse width inductive adder or Marx generator based on SiC MOSFET
PFN
Delay-line kicker magnet
200ns
40~2000ns
200ns
1kHz
Solid-state switches（SIC MOSFET）
C-type
Dual C-type
Marx generator
Or
Cap.
challenges

## Slide 35: Summary
There are 9 injection and extraction sub-systems in CEPC accelerator complex. The types of all inj./ext. components are figured out.
The hardware designs towards TDR are being carried out.
So far，the kickers and the Lambertson septas preliminary designs for the damping ring ， the booster low energy inj. system are completed. The kickers for high energy ext. sub-systems are being designed.

## Slide 36
END
Thank you for attentions!!!

## Slide 37
Backup slides

## Slide 38: Booster Ring
Booster operating mode | Higgs |  |  | W |  | Z | 
Beam energy（GeV） | 10 | 120 |  | 10 | 80 | 10 | 45.5
Function | Injection （both） | Extraction （off-axis） | Inj./Ext. （on-axis） | Injection （off-axis） | Extraction （off-axis） | Injection （off-axis） | Extraction （off-axis）
Bunch number | 242（in half ring） |  | 7（in half ring） | 1524（uniform） |  | 6000 | 
Min. bunch spacing （ns） | 680 |  | 23800 | 220 |  | 25 | 
Bunch number per train× train number | - |  | - | - | - | 80×75 | 
Train spacing （ns） | - |  | - | - | - | 2460 | 
Injection（extraction）mode | Bunch by bunch |  |  | Bunch by bunch |  | Bunch by bunch | Train by train
Kicker repetition rate (Hz) | 100 | 1000 |  | 100 | 1000 | 100 | 1000
Kicker pulse width (ns) | 1360 |  |  | 440 |  | 50 | <6900
Kicker flat top（ns） | - |  |  | - |  | - | >1980
Kicker rise（fall）time (ns) | <680 |  |  | <220 |  | <25 | <2460
Timing delay(ns) | <680 |  | <23800 | <220 |  | <2460 | <4400
injection（extraction）period (s) | 2.42 | 0.242 | 0.007 | 15.24 | 1.5 | 60 | 0.075
Kick angle (mrad) | 0.11 | 0.2 | 0.1 | 0.11 | 0.2 | 0.11 | 0.2
Kick Integral field strength (Tm) | 0.004 | 0.08 | 0.04 | 0.004 | 0.05 | 0.004 | 0.03
Beam pipe aperture Φ（mm） | 55 |  |  |  |  |  | 
Considering the compatibility of three operating modes:
Function | LE-Injection （both） | HE-Extraction （off-axis） | HE-Inj./Ext. （on-axis）
Kicker repetition rate (Hz) | 100 | 1000 | 1000
Kicker pulse width (ns) | 50 | 440~2420(Adjustable) | 1360
Kicker flat top（ns） | - | 0~1980(Adjustable) | -
Kicker rise（fall）time(ns) | <25 | <220 | <680
injection（extraction）period (s) | 60 | 1.5 | 0.007
Kick angle (mrad) | 0.11 | 0.2 | 0.1
Kick Integral field strength (Tm) | 0.004 | 0.08 | 0.04
Beam pipe aperture Φ（mm） | 55 | 55 | 55
50ns,100Hz
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz

## Slide 39: Collider ring
Booster operating mode | Higgs |  |  | W |  | Z | 
Beam energy（GeV） | 120 |  |  | 80 |  | 45.5 | 
Function | Injection （off-axis） | Injection （on-axis） | Extraction （dump） | Injection （off-axis） | Extraction （dump） | Injection （off-axis） | Extraction （dump）
Bunch number | 242（in half ring）- 7 |  |  | 1524（uniform） |  | 12000 | 
Min. bunch spacing （ns） | 680 |  |  | 220 |  | 25 | 
Bunch number per train× train number | - |  |  | - |  | 80×150 | 
Train spacing （ns） | - |  |  | - |  | 245 | 
Injection（extraction）mode | Bunch by bunch |  |  | Bunch by bunch |  | Train by train | 
Kicker repetition rate (Hz) | 1000 |  |  | 1000 |  | 1000 | 
Kicker pulse width (ns) | 1360 |  |  | 440 |  | <2460 | 
Kicker flat top（ns） | - |  |  | - |  | >1980 | 
Kicker rise（fall）time (ns) | <680 |  |  | <220 |  | <245 | 
Timing delay(ns) | <680 | <23800 | <680 | <220 |  | <4400 | 
injection（extraction）period (s) | 0.242 | 0.007 | 0.242 | 1.5 |  | 0.15 | 
Kick angle (mrad) | 0.1 | 0.2 | 0.2 | 0.1 | 0.2 | 0.1 | 0.2
Kick Integral field strength (Tm) | 0.04 | 0.08 | 0.08 | 0.027 | 0.05 | 0.015 | 0.03
Beam pipe aperture HxV（mm） | 75×56 |  |  |  |  |  | 
Function | Injection （on-axis） | Injection （off-axis） | Extraction （dump）
Kicker repetition rate (Hz) | 1000 | 1000 | 1000
Kicker pulse width (ns) | 1360 | 440~2420(Adjustable) | 440~2420(Adjustable)
Kicker flat top（ns） | - | 0~1980(Adjustable) | 0~1980(Adjustable)
Kicker rise（fall）time(ns) | <680 | <220 | <220
injection（extraction）period (s) | 0.007 | 1.5 | 1.5
Kick angle (mrad) | 0.2 | 0.1 | 0.2
Kick Integral field strength (Tm) | 0.08 | 0.04 | 0.08
Beam pipe aperture HxV（mm） | 75×56 | 75×56 | 75×56
200ns
40~2000ns
200ns
1kHz
1360ns,1kHz
Considering the compatibility of three operating modes:
200ns
40~2000ns
200ns
1kHz