## Slide 1: A Perspective on Plasma Accelerators
Chan Joshi
University of California Los Angeles
Work supported by U.S. D.O.E. HEP , NSF
Electrons
Positrons
OSIRIS simulation by F. Tsung UCLA

## Slide 2
Special Thanks to
M. Hogan, T. Katsouleas, W. Lu, C.E. Clayton, K. Marsh, M. Litos , W. An, F. Tsung, F. Albert, B. Dangor
V. Yakimenko , R. Siemann, J.M. Dawson
All our former students, postdocs and Colleagues
C. Joshi, S. Corde, W.B. Mori, Phys. Plasmas 27, 070602 (2020)
Talk based on

## Slide 3
Accelerator based Experiments are necessary to address Important Science Questions in this Century
Are there additional dimensions of space?
Why is there matter-antimatter imbalance?
How did the universe begin?
What is dark matter?
How were heavy elements created?
Notes: The often quoted Turner report ‘Connecting Quarks with Cosmos” has outlined 11 Physics questions for the 21st century. Many of these will require different kinds of accelerators to help answer them.

## Slide 4
Particle colliders 21st Century
Electron
Source
Positron Source
Damping
Ring
Accelerator
Accelerator
500 GeV CM
30 km (<20 MeV/m)
$ 20+ B (DOE Estimate)
Energy Frontier of particle Physics
Very large
Very Expensive
Can we make accelerators at energy frontier smaller and cheaper?
International Linear e-e+ Collider
Other Contenders:
FCC : CERN e-e or p-p
CEPC: China e-e+
Notes: Here is the conceptual drawing of what the International Linear Collider might look like.It will collide 250 GeV beams of e-e+ against one another.The length of the machine is 31 KM and the cost is as yet unknown but will be in all likelyhood in the neighborhood of $10 billion.The ILC will enable us to find answers to some the most important puzzles confounding us today such as:
Are there extra dimensions of space?
Are there more fundamental particles to be found?
What gives particles their mass?
It is clear however that the ILC will be the last of these gargantun machines ever built.Pressumably we will run out of money before we run out of space . Even then the accelerator portion of these machines contributes approximately XX% of the total machine cost .Therefore this technology based on microwaves to accelerate particles is simply too inefficient adding roughly 50 million volts of energy to the accelerating particles every meter.
Is there a better way?

## Slide 5
Laser Acceleration of Particles Workshop Los Alamos 1982
Can high electric fields
of laser pulses or beams
be used to accelerate particles?
At ultra high gradients?
To very high energies?
SSC
Anyone?
Notes: In 1980 the Tigner subpanel of the HIPAP released it’s report on the state of “ Accelerator Research and Development” . In response to the Tigner subcomittee’s recommendations, the DOE in 1982 held a workshop at Los Alamos on Laser Acceleration of Particles with Andy Sessler as the Scientific Co-ordinator. The goal of this Workshop was to examine fresh ideas that might lead to accelerators beyond the “Next Linear Collider”..In particular there was interest in uncovering new ideas that might accelerate particles 100-1000 times more rapidly than did then current microwave powered accelerators.
Naturally the interest turned to lasers.

## Slide 6
Relativistic Wakes in Plasmas
as particle accelerators?
Leonardo deVinci
Study of Wakes:1509
Wake –disturbance left behind
By a piston moving thru fluid
Plasma Wake Field Accelerator
A high energy electron bunch
Laser Wake Field Accelerator
A single short-pulse of photons
Drive beam
vp~ c
Trailing beam

## Slide 7
Conventional
Plasma: Holographic Interferometry
1 m
TM mode in a SW Structure
Ez, Er and B𝜃
20 MeV/m
3-30 cm diameter permanent Cu structure
TM mode in Plasma
Ez, Er and B𝜃
20 GeV/m
30-300 um diameter transient structure
RF and Plasma Accelerators
z
r
Courtesy
M. Downer

## Slide 8: Multi-stage Plasma based Linear Collider (basic design follows the ILC collider concept)
E. Adli et al. Snowmass Proc. 2013
Seryi et al. 23rd PAC Conf. Proc.
W. Leemans et al Phys. Today 2009
Courtesy; S. Corde

## Slide 9: Why Use Wakes in Plasmas for Acceleration? 1D-Linear Plasma Wakefield Theory
For tpulse of order pwp-1 ~ 100fs (1017/no)1/2 and spot size c/wp
Large wake for a laser amplitude ao= eEo/mwoc ~ 1 or a beam density nb~ no
e-beam
Laser
Wakes are said to be linear when n1< no

## Slide 10: Linear Wakes can Accelerate both e- & e+
Linear Wake when n1 < no
Sinusoidal longitudinal electric field
Longitudinal and transverse field out of phase by
The e- and e+ can be accelerated in a region
PLASMA DENSITY
Longitudinal
Electric Field
Transverse
Electric Field

## Slide 11: What about positron driven wakes? Nonlinear dynamics of positron plasma interactions
e+
28 GeV Positron Beam at SLAC propagates through a dilute plasma
Plasma
electrons
Positron
beam
Focusing
force
Accelerating
field
Central core surrounded
By a halo
Initial beam at plasma
entrance
Beam exiting plasma
E 162 Collaboration
P. Muggli et al PRL 2008

## Slide 12
FULL/REDUCED PIC CODES VALIDATED BY NUMEROUS EXPTS and USED TO DESIGN EXPT.s AND CONFIRM NEW IDEAS

## Slide 13: Linear wake formation, energy loss and energy gain of a positron bunch in plasma
Experiment
PIC Simulation
Energy
Gain
Energy
Loss
Energy gain of 80 MeV in 1m
Typical e+ acceleration gradient < 20 MeV/m
Ref. B. Blue etal. PRL 2002
Expt. Done on FFTB
@ SLAC
e+ Bunch

## Slide 14: Nonlinear Wakes in the blowout regime driven by laser pulse or e-bunch
Concepts for linear wakes due to J.M. Dawson
Ref. T. Tajima and J,M, Dawson PRL 1979
P. Chen, J.M. Dawson et al. P.R.L. 1985
Nonlinear wakes: Rosenzweig, Katsouleas, Mori, Lu, etc.
Need < 100fs (FWHM) driver beams with a0 >2 0r a > 10 KA electron beam

## Slide 15
Longitudinal and transverse fields in blowout regime
(ideal for preserving emittance or beam quality)
Longitudinal Field
In direction of propagation
Longitudinal Field
In transverse direction
Transverse Field
In transverse direction

## Slide 16
BREAKING THE 1 GeV BARRIER
With 15 micron long bunches
ne≈3.51017 cm-3 L≈10 cm, N≈ 1.81010
Charge Fraction > E0 0.8% 25pC of charge
M. Hogan et al. PRL 2005
Ref. M. Hogan et al

## Slide 17
Ref. I. Blumenfeld et al. Nature 2007
C. Joshi, CERN Courier2007
E-167: Energy Doubling with a Plasma Wakefield Accelerator in the FFTB
422
85
Energy (GeV)
Drive Electron Beam 42 GeV
Particles in the tail gained 43 GeV in just 85 cm
Acceleration gradient of 50 GeV/m sustained over 85 cm
Beam head erosion limited the propagation of the beam to a distance less than pump depletion length.
Notes: Have been some remarkable results, most recently from the final E-167 run in April this year
This didn’t just spring from a vacuum - result of sustained effort over many years to develop the techniques and apparatus to do these experiments
That’s what this type of facility allows for.
Will come back to this point later when we discus the bypass line

## Slide 18
NAE Grand Challenges for Engineering
Engineer Tools of Scientific Discovery
“..engineers will be able to devise smaller, cheaper
but more powerful atom smashers, enabling physicists
to explore realms beyond the reach of current technology.”
Particle Physics Project Prioritization Panel (P5) Report 2014:
Building for Discovery
“A primary goal, therefore, is the ability to build
the future generation accelerators at dramatically lower cost.
…For e+e- colliders, the primary goals are improving the
accelerating gradient and lowering the power consumption”
Compact and Cheaper High-Energy Colliders a Grand
Challenge for Science and Engineering in the 21st century

## Slide 19
Propagation
Direction
Electric
Field
Drive Beam
Trailing
Beam
Electric
Field
Propagation
Direction
Acceleration of a distinct trailing bunch and
beam loading of the Wake
Drive Bunch
Trailing
Bunch
Blown Out Wake
Loaded Wake
Unloaded wake
M. Tzoufras et al. P.R.L. 2008

## Slide 20
Acceleration of Trailing Bunch of Electrons
M. Litos et al. Nature 2014
M. Litos et al. PPCF 2016
Max. Energy gain 9 GeV in 1.3m, energy spread <5%, 25% energy extraction efficiency

## Slide 21
Acceleration of positrons in nonlinear wakes
S. Corde et al. Nature 2016
e+ beam produces wake & a dense region of plasma electrons that traps e+
4 GeV in 1.3 m
1.8% energy spread
Low beam divergence
Simulation
EXPERIMENT

## Slide 22: Jet Age of Laser-wakefield Acceleration-LWFA Takes off RAL/IC, LBNL and LOA Expts show ~ 10% energy spreads
IC
Rutherford
LBNL
LOA

## Slide 23: Coming of age of Laser Wakefield Accelerators 2003-today
Maximum energy gain of 8 GeV seen at BELLA.
Percent level energy spreads
@4 hour operation of a LWFA in Germany
Numerous new ideas: colliding pulse injection, self beam loading,
Photon acceleration and deceleration, overcoming dephasing ,DLA
wake assisted relativistic guiding. Ionization injection
A phenomenological theory for nonlinear wakes, nonlinear
beam loading, beam matching, transverse beam instabilities
-essential to our understanding and charting a path forward.

## Slide 24
RAL
LBL Osaka
UCLA
E164X
ILC
ANL
Plasma Accelerator Progress
“Accelerator Moore’s Law”
E167
LBNL
Working Machines
Doing physics
Max.Energy in
Experiments
Electron beam driven
Laser beam driven
Machines
Doing Physics
PBA
Experiments
Maximum Energy Gain 43 GeV
C.Joshi and
T. Katsouleas
Physics Today 2003
2020

## Slide 25
U.S. Plasma Accelerator Scenario Big picture: R&D still Discovery Science
Can critical physics issues for a multi-stage e+e- collider be quantified via experiments and/or simulations in the next decade : 2017-2027?
Can the then remaining critical issue be solved by 2032 ?
Can an important enough first application of a plasma accelerator be identified?
Can a plasma accelerator built for this application (for << $1B) serve as a prototype for a LC by 2035?
Can the community come up with
a CDR for a Plasma-Based LC by 2035?
C. Joshi Scientific American

## Slide 26
Next big challenge for Plasma-Accelerators is demonstration of
All the necessary parameters for a single stage of a multi-stage collider
No single experimental facility is suitable such a demonstration
So must rely on a combination of experiments and 1:1 PIC simulations
Experiments Simulations
More than 90% energy extraction Generation and acceleration of
From the pump to the wake ultra-low emittance beams
Extraction of 90% of the energy from Generation and acceleration of
the wake by the accelerating beam highly polarized e- and e+ beams
Emittance preservation at 1um level Techniques for high quality beam
generation in linear wakes
Nearly 100% charge throughput
Less than 1% energy spread Staging, radiation loss
0.5 nC charge accelerated per shot Transverse beam instabilities
Do all this with both e- and e+

## Slide 27: Two-bunch PWFA
Plasma and beam density
with on-axis Ez line out
Beam Energy
Energy Doubling (10-20+ GeV) with <1% Energy Spread
,Pump Depletion and > 40% energy transfer efficiency
Drive Bunch
Trailing Bunch
Drive
Bunch
Trailing
Bunch
Energy Doubling
Simulations by W. An UCLA, .Joshi et al. PPCF 2018

## Slide 28: Two-bunch PWFA
Beam Matching in and out of plasma accelerator
And emittance preservation
Matched Beam in Plasma
Plasma
Ramp
Simulation Results: Weiming An

## Slide 29
Colliders and 5th Generation Light Sources both need Cheaper and more Compact Accelerators
COLLIDERS
e and e+
TeV beams
Spin polarization
Multiple stages
High Luminosity
-nC charge per beam
-nm emittance
-kHZ Rep. rate
->20 MW Average power
-> need 90% driver beam-
accelerated bunch energy extraction efficiency
5th Gen Light Source
e
1GeV beams
10 pC charge per beam
Single stage
High beam brightness
-Extremely low energy spread
-nm emittance
-kHZ Rep. rate
A true 5th Gen. Light Source that will compete with X-FELs
may be the 1st grand application of the advanced accelerator concepts technology.

## Slide 30
Deciphered by Venky Ramakrishnan’s
Team: Nobel in Chemistry 2009
Synchrotrons and X-FELs poised to be Breakthrough Tools of Discovery in 21st century
100,000 proteins in human body
75,000 enzymes
25,000 Genes in each cell

## Slide 31
Conclusions
Developing plasma accelerators that will disrupt an established technology is a long-term endeavor. Beautiful science but limited resources.
A team that has diverse expertise, bright young people eager to make their mark and good leadership is essential to success.
3) Long term funding and access to facilities is essential
4) Important to have goals to judge progress but must also have the freedom to pursue unexpected avenues as they open up.
5) The prognosticators must come up with a “killer app” such as
5th Generation Light Source to secure funding for continued R&D within 10 years.