## Slide 1: PID at EIC
Thomas K Hemmick

## Slide 2: Electron Ion Collider Future Collider
  What is the spatial mapping of quark and gluon fields in the nucleon AND nucleus.
  Is the missing spin to be found via quark orbital momentum?
  Are new phases of matter (Color-Glass Condensate) accessible at low x in nuclei?
Site Selected BNL !!

## Slide 3: Compelling EIC SCIENCE Questions
Does this saturation produce matter of universal properties in
the nucleon and all nuclei viewed at nearly the speed of light?
Is there a simple boundary that separates the region from the more dilute quark gluon matter? If so how do the distributions of quarks and gluons change as one crosses the boundary?
Where does the saturation of gluon densities set in?
How are sea quarks and gluons and their spin distributed
in space and momentum inside the nucleon?
How are these quark and gluon distributions correlated with the
over all nucleon properties, such as spin direction?
What is the role of the motion of sea quarks and gluons
in building the nucleon spin?
How does the nuclear environment affect the distribution
of quarks and gluons and their interaction in nuclei?
How does the transverse spatial distribution of gluons compare to that in the nucleon?
How does matter respond to fast moving color charge passing through it?
Is this response different for light and heavy quarks?
q
h
g*
e’
e

## Slide 4: Evolution In Our Understanding Of Nucleon “Spin”
Traditionally we treated proton as a 1D object  What are the quark, gluon intrinsic spin contributions to the nucleon’s spin?
Last 10+ years: Theoretical tools and experiments to view proton as a (2+1)D object became available.
What are the position & momentum correlations amongst partons? Do they contribute to nucleon’s spin?
Notes: Its not just understanding the nucleon spin sum rule. But a deeper quest to understand the nucleon as a many body object in QCD.

## Slide 5: Unified view of the Nucleon Structure
Wigner distributions:
EIC – 3D imaging of partons: Quarks (fixed target) , Gluons (collider)
TMDs – confined motion in a nucleon (semi-inclusive DIS)
GPDs – Spatial imaging of quarks and gluons (exclusive DIS)
5D
3D
1D
JLab12
COMPASS
for
Valence
HERMES
JLab12
COMPASS
(X. Ji, D. Mueller, A. Radyushkin)

## Slide 6: Physics at Low x?
See Ann. Rev. Nucl Part (60) 2010 F. Gelis et al., , arXiv:1002.0333)
Method of including non-linear effects (McLerran, Venugopalan)
Small coupling, high gluon densities
BK/JMWLK equations lead to a Saturation Scale QS(Y)
At QS gluon emission balances the recombination
Strongly correlated gluonic system at high energy (low-x)
Universal? Color Glass Condensate ??
Linear QCD
BFKL:
gluon
emission
Nonlinear QCD
BK/JMWLK gluon recombination
DGLAP
BFKL
BK/JMWLK
Need a higher energy e-p collider than HERA?
Large Hadron electron Collider (LHeC)
 Nuclei: naturally enhance the densities of partonic matter
Why not use Nuclear DIS at high energy?

## Slide 7: Gluon and the consequences of its properties:
Gluons carry color charge  Can interact with other gluons!
What could limit this indefinite rise?  saturation of soft gluon densities via ggg recombination must be responsible.
recombination
Apparent “indefinite rise” in gluon distribution in proton!
No unambiguously observation
Fundamental limiting state of matter
“Color Glass Condensate”
McLerran & Venugopalan et al
“…The result is a self catalyzing enhancement that leads to a runaway growth. A small color charge in isolation builds up a big color thundercloud….”
F. Wilczek, in “Origin of Mass”
Nobel Prize, 2004
Notes: Significant modification and simplification of this slide… may convert in to two….

## Slide 8: How to reach the high gluon density?
Enhancement of QS with A, not energy
Kowalski, Teany
PRD 68:114005
Alternatively,
Probe the nucleons in NUCLEI US Electron Ion Collider (EIC)

## Slide 9: EIC Basics and Timeline
Center of Mass Energies: 20 GeV – 141 GeV
Maximum Luminosity: 1034 cm-2s-1
Hadron Beam Polarization: 80%
Electron Beam Polarization: 80%
Ion Species Range: p to Uranium
Interaction regions: up to two

## Slide 10: Interaction Region
+/- 4.5 meters for detectors
Limited outside radius

## Slide 11
Generic All-purpose Detector
Asymmetric!!

## Slide 12: PID ~ Velocity
p = mgb E = mg velocity(b) measurement yields mass.
Direct measurement:
  Record signal time at multiple locations, calculate v.
  “Fast” detector = low transit time spread (most easily achieved at small transit time)
Velocity-dependent interaction(s) with detector:
  Specific Ionization (aka )
  Cherenkov Radiation:
    qC measured wrt track direction.
    Thus dependent upon deliverables from tracking
  Bremsstrahlung:
  Transition Radiation:
eID mechanisms
TOF covered well in prior presentations, not repeated here

## Slide 13: Available Space Depends Upon Tracking Options
Cylindrical defining volume
+/- ~ 1.2 meters
Outer radius:
  ~20 cm for hybrid
  ~50 cm for All-silicon
Hybrid Option allows for dE/dx
MUCH smaller than STAR or ALICE
LAURA GONELLA

## Slide 14: dE/dx w/ hybrid detector
Dots = STAR
Boxes = sPHENIX Test Beam
Specific ionization is a function of b.
PID bands vs momentum.
Crossing ~b = 0.7 (TOF can help)
Limitations from Landau tails:
  Primary ionization Statistics = Poisson
  Total ionization = Landau
  Traditional Approach:
    Lots of gas & lots of samples
  Forward thinking approaches:
    Gas choice to minimize Landau
    “Cluster Counting”
Goal: Achieve dE/dx performance with least gas volume

## Slide 15: Speculative Cluster Counting Concept
Scaling to our available length:
Using a 3s reference @ 40 cm gas:
Existing Concept (“Timepix”)
  Avalanche onto Silicon Pixels
  Tiny Pixels (smaller than cluster spacing)
  Sufficient gain for single electron
In principle can work
Expensive for large area.
Can we accomplish with conventional tech?

## Slide 16: Long Shadow Detector -- LSD
Drift leverages huge Lorentz angle as “magnifier”
Clusters spread across space and time.
Higher B = Lower Transverse diffusion
  Example: T2K(130 V/cm) has only
Detect (count) clusters with conventional means.
B-field
track
HV-
New Concept: Like a “Streak Camera”
Sensors
Bad for Tracking
Good for PID
Silicon Tracker
Multiple sections…
Early Conceptual Stage: Requires R&D

## Slide 17
Leading Barrel PID Technology: DIRC
17
:
Generic reference design: 1m barrel radius, 16 sectors
176 bars: synthetic fused silica,17mm (T) ´ 32mm (W) ´ 4200mm (L)
Photo sensors: MCP-PMTs -3x3mm2 pixels
DIRC in sPHENIX
hpDIRC ala eRD14
At normal incidence, Cerenkov light is internally reflected for
Cerenkov angle preserved if bars meticulously flat with 90 degree corners.
Spectacularly compact PID device with photon detection at end.

## Slide 18: hpDIRC Performance Simulations
Original BaBar DIRC was effectively “proximity focused”
hpDIRC section creates focused ring improving resolution.
Excellent match to EIC needs.
Strict requirements on “correlated terms”, (e.g. angular resolution of tracking)
Works with either standard tracking solution.

## Slide 19
Hadron End: Dual RICH
Cherenkov radiator
○ Refractive Index
n = 1.02 (aerogel) 1.0008 (C2F6)
○ Length of the radiator
L = 4 cm (aerogel) , 160 cm (C2F6)
Mirrors
Photon Detector
3 mm pixel size; 200-500 nm MAPMT
Particle Generation
Originate from the vertex
Exquisite detail in simulation.
AI-based optimization.
Uses constant external angular resolution assumption.
Similar external constraint assumed as deduced for separate gas & aerogel RICHes
Tracking maybe tolerates ~2X sim (0.5 – 1.0 mrad)
NOTE: PMTs to the side makes optical aberration (“Emission”) dominant

## Slide 20
Electron Arm: Modular RICH
Cherenkov radiator
(Aerogel) refractive index, n = 1.03
Length of the radiator, L = 3cm
lens with focal length, 𝑓= 6”
Photon Detector
3 mm pixel size
NOTE: Similar performance to aerogel in dRICH
Hadron ID requirements relaxed…aerogel only
Additionally require eID ~ 4GeV/c
Modular RICH focused by Fresnel Lens
  Sharp image improves resolution.
  Transmission of lens combats dispersion
Provides TOF with suitable readout device (LAPPD)

## Slide 21: eID by Transition Radiation (TRD)
“Threshold detector” (TR X-rays produced or not)
Pmin ~ 1 GeV (rejection ~constant at higher momentum)
1: Make TR photons:
Index, n, change
X-ray regime
Film, foam, fleece
2: Layered to get more photons
3: ID TR photons by energy/pos
4: Reject Pions
Balance between X0 and rejection

## Slide 22: eID by Hadron Blind Detector
PHENIX HBD optimized for 1e-vs-2e separation.
  20 photoelectrons vs 40 photelectrons
Non-zero hadron response.
Re-optimize for EIC??
electron
Unfocused Threshold
Cherenkov
Fractional Contribution to signal
Pion Signals Simulated
1st Gap Dominates!
Limited by 1st Gap
Garfield + Fast Monte Carlo

## Slide 23: Speculative HBD++ ??
microMEGAS provide the smallest gas length.
Gain from any or all of three layers:
  Gain from GEM
  Gain from m1
  Gain from m2
m1
m2
Conceptual Idea
G
HBD: Phenix
HBD+: Gem + 1-stage mM gain
HBD++: GEM _ 2-stage mM gain
Speculative! Requires R&D

## Slide 24: Time-of-Flight
Direct measurements of velocity require a fast charge collection device.
The time resolution is automatically helped by small devices:
  LGAD: Low Gain Avalanche Device. Instantly small.
  MCP: Micro Channel Plate  LAPPD (Large Area Picosecond Photon Detector)
MCP: Micro Channel Plate

## Slide 25: TOF @ EIC: Available space
PID from TOF requires:
  Time resolution.
  Maximum path length.
Known ring makes size restrictions!
  Civil construction already there.
  One ring outsize the detector.
Practical Implementation:
  Tempting to assume time resolution scales as
  Extreme care required to minimize or eliminate correlated errors (e.g. “start clock jitter”)

## Slide 26: Summary
Electron Ion Collider has passed “CD0” and will be built at BNL.
Detector challenges in PID are exacerbated by limited available space.
Asymmetric collisions lead to asymmetric requirements
Options exist to leverage
  TOF.
  Cherenkov
  dE/dx
Solutions seem to be in hand.
More R&D possible on alternative speculative avenues.

## Slide 27
BACKUP SLIDES

## Slide 28
Cherenkov Pointing:
  Parameterizations of gas Cherenkov indicate pointing required at 0.5-1.0 mrad level while inside the radiator.
  Calculations of aerogel devices indicate 0.5 -1.0 mrad level.
  Calculations of DIRC indicate 0.5 mrad level or better.
TOF:
  Path length can influence PID resolution at the best dt.
  Non-trivial influence of “material budget distribution”.
  Need deeper understanding of this issue.
PID requirements toughening with time:
  SIDIS group shown on right. Jets want even more.
  PID requirements are not symmetric in eta, driven by 0.8  1.0
  Is a symmetric barrel optimal at our asymmetric collider?
Summary
Old
New
Meta-materials: Game changer,
But we can’t assume these will work:

## Slide 29: What is the meaning of “Long Shadow”?
Camel
Satellite Photo

## Slide 30: Additional Integration Points
Gas RICH at highest momentum (hadron arm) does not enjoy an over-abundance of Cherenkov photons (love to have lots of Zed).
Angular resolutions required for Cherenkov-based PID detectors must be evaluated WITHIN the radiator:
  Services at Zed > 1.2 may scatter particle before hadron arm Cherenkov.
  DIRC bars scatter particles on their own (17 mm quartz)
  Must evaluate needs of a tracking layer behind Cherenkov devices.
Cherenkov detectors require photo-sensors
  Many technologies are sensitive to field strength and orientation.
  1 Tesla at the sensor is fine.
  Easy to achieve with central field = 1.5 Tesla.
  Very challenging but seems doable if central field = 3 Tesla…trade off with optical aberration as you move sensors back.
  SiPM sensors operate fine in the field, but radiation damage can lead to high rate of “false photons”
Need to minimize bending of tracks within the RICH.
Zed
Is this less than 1 mrad scattering

## Slide 31
High Momentum GEM RICH
1m of CF4 radiator at 1.003 bar (slightly overpressure)
CsI Photocathode on top GEM
Mirror in deep UV -> MgF2 coating
Single Photon Capability ->quintuple GEM stack with APV25-SRS
Particles ~perpendicularly incident on spherical mirror, focused onto a GEM stack directly
According to the parameterization, tracking is leading error contribution is worse than ~7 mrad, becomes negligible resolution factor around 2 mrad. Between 2 and 7mrad , more detailed investigation is required.
Plot shows viscerally the effect.
More detailed simulation required.
OK
hmm
Performance from Parameterized Test Beam Data
p
p
NOTE: High chromaticity = loose requirement on tracking

## Slide 32
Trivial (just math) Calculation:
  Assume photon measured perfectly.
  Tracker makes fixed error a.
  dqC depends on both and a!
Requirements depend upon performance
  Parameterizations:
    Wide range of assumptions possible.
  Full Monte Carlo
    Robust and Reliable results.
Ring Imaging Cherenkov (RICH) vs. Track Direction
We present both parameterizations and full Monte Carlo calculations

## Slide 33
Basic Coupling of Tracking to PID
Cherenkov Angle (qC):
  Centroid from n
  dqc from:
    Nphoto-electrons
    chromaticity (aka dispersion; n(l))
    pixel size
    optical aberration (aka “emission”)
    magnetic field
    Track Pointing
  dp from tracking
Time Of Flight (TOF):
  Calculates m2 using p, b.
  dm from:
    dt
    dp
    dL
Dominant
If dt is tiny, dL is significant
NOTE: Where PID is excellent, it can contribute to momentum resolution.
Dominant Term
Strongly reliant upon tracking
Weakly reliant upon tracking…discussed in backup slides
NOTE:
N independent TOF measurements,
Challenges exist to make independent
  Common clock
  Etc…

## Slide 34
FRANCOIS-XAVIER GIROD
SPENCER KLEIN
XUAN LI
XIN DONG
Håkan WENNLÖF
ASTRID MORREALE
Rey Cruz-Torres
RACHID NOUICER
Many presentations.
Similar themes:
Si as a vertex
All-Silicon

## Slide 35: Superb e/p Separation
Focused Gas RICH
Low index gas pushed the e/p out to 15 GeV or beyond.
Compromise parameter is Zed length:
  1-1.5 meters in Zed
  Under study:
    Move Zvertex toward –h exacerbating the space issue.
eRD6 RICH
prototype
eRD14 “dual RICH”
simulation
Notice:
eID needs met w threshold device
Optics maybe unnecessary

## Slide 36
psTOF
36
TOF needs a measurement of p and L
As dt➝5 ps, requires precision path length L ( c*dt~1.5 mm…tracking must exceed this.)
Multiple scattering might be the biggest worry, need to ensure low material budget and/or enough tracking layers to catch scattering.
Depends partly upon the material that does not provide position measurement:
Several technologies reviewed, no one chosen yet
AC-LGADs could provide a very good tracking layer (~100 um) + timing (20 ps)
External start time provided by forward detectors could be helpful
Study of Self-timing (Internal) using tracks

## Slide 38: More Compact Cherenkov eID Detectors
Close to 4 GeV.
Effective enough alone?
Complementary detector?
  TRD?
  dE/dx?
Modular RICH:
Fresnel-focused compact RICH
eRD14 “mRICH”
eRD14 “hpDIRC”
Useful at the lowest momenta.
Performance limited by Mult. Scattering.
Detailed simulations req’d and underway
Expectation:
  3-4s @ 1 GeV