## Slide 1: CEPC collective instabilities studies
Na Wang, Yudong Liu, Yuan Zhang, Yuting Wang, Haisheng Xu
1/14/2022
IAS mini-workshop on Accelerator Physics, Jan. 13-14, 2022

## Slide 2: Outlines
Impedance updates
Single bunch instabilities
Transverse resistive wall instability
Beam ion effects
Electron cloud effects

## Slide 3: Impedance updates
Impedance model is updated regarding the change of the chamber cross section (ellipticalcircular), as well as more impedance contributors included.
  Main impedance contributions are considered.
  Possible large contributors, including Inj./ext. elements, feedback kickers, absorbers, masks/collimators around the ring, are not included yet.
Element | Number | Element | Number
Resistive wall | / | BPMs | 1808
RF cavities | 60 | IR Collimators | 16
Flanges | 37714 | Electro separators | 20
Bellows | 15949 | IP chambers | 2
Gate valves | 500 | ES Transitions | 40
Vacuum pumps | 5316 | IP Transitions | 8

## Slide 4: Changes on Resistive Wall
Incoherent tune shift due to the quadrupolar impedance is derived from beam oscillation equations.
Yuting Wang
[y]frev
0.1Hz
DC value of the quadrupolar impedance dominates
Incoherent tune slope:

## Slide 5: Changes on Resistive Wall
Resistive wall impedance
  Form factor – Ratio of elliptical and circular chamber (infinite thick wall)
  RW_ Elliptical multilayer= Form factor * RW_Circular multilayer (, , dt)
Yuting Wang
Solid lines: Based on Lutman’s method
Dashed lines: Yokoya form factor
With frequency decreases, the skin depth increases and the background material outside the beam pipe should be considered.
Two impedance models:
Model A: Vacuum outside the chamber
3mm Cu + Vacuum (Infinite)
Model B: Magnet outside the chamber
3mm Cu + 100mm Magnet (=100) + Vacuum (Infinite)

## Slide 6: Changes on Resistive Wall
Yuting Wang
Model A: Vacuum outside the chamber
Model B: Magnet outside the chamber
Dependence on the thickness of the magnets
Dependence on the permeability and conductivity of the magnets
Consider that 80% of the collider is surrounded by the magnets, the tune shifts are 0.26/-0.25 (A-1)
Main different among different methods can be explained by the impedance model and the form factors used.
For circular chamber, unsymmetrical magnets (e.g. dipoles) can also generate incoherent tune shift.
[1]
[2]
[1] PRST-AB, 5, 111001 (2002), [2] PRE 66, 056501 (2002)

## Slide 7
Broadband impedances are mainly contributed by: resistive wall, flanges, bellows, RF cavities.
Narrowband impedances need to be further checked.
Ring longitudinal impedance

## Slide 8
Broadband impedances are mainly contributed by: resistive wall, flanges, bellows.
Narrowband impedances need to be further checked.
Ring transverse impedance

## Slide 9
Components | Number | Z¦¦/n, mΩ | kloss, V/pC | ky, kV/pC/m
Resistive wall | - | 6.2 | 363.7 | 11.3
RF cavities | 60 | 0.5 | 101.2 | 0.5
Flanges | 37714 | 5.2 | 37.3 | 5.2
BPMs | 1808 | 0.04 | 9.5 | 0.2
Bellows | 15949 | 2.9 | 87.4 | 3.9
Gate Valves | 500 | 0.2 | 14.5 | 0.4
Pumping ports | 5316 | 0.3 | 2.3 | 0.2
Collimators | 16 | 0.04 | 23.4 | 0.6
IP chambers | 2 | 0.004 | 0.3 | 0.05
Electro-separators | 20 | -0.1 | 34.5 | 0.1
Taper transitions | 48 | 0.04 | 2.5 | 0.09
Total |  | 15.3 | 676.6 | 22.5
CDR Total |  | 11.4 | 786.8 | 20.2
Longitudinal and transverse broadband impedances are dominated by the RW, flanges and bellows.
The loss factor is mainly contributed by the resistive wall, RF cavities and bellows.
Compare to the CDR budget, we have larger Z/n and ky, but smaller kloss.
Impedance budget @z=3mm

## Slide 10: Collective instabilities
Instability issues for high luminosity Z are investigated.
  High beam current and bunch intensity
  Low momentum compaction
  Short natural bunch length
  Slow radiation damping
  Large circumference (0, RW)
Key instability issues
  Single bunch effects
  Transverse resistive wall instability
  Electron cloud effect
  Beam ion instability
Parameter [unit] | Z-High Lumi
Beam energy [GeV] | 45.5
Lmax/IP (1034cm-2s-1) | 105.5
Emittance (H/V) [nm] | 0.27/0.00135
Beam current [mA] | 839.9
Bunch number | 11520
Bunch Population [1010] | 15.2
Momentum compaction [10-5] | 1.43
Natural bunch length z (mm) | 2.75
Natural energy spread | 3.7810-4
Betatron tune x/y | 319.10/317.22
Synchrotron tune | 0.032
Radiation damping [ms] | 849.5/849.5/425.0

## Slide 11: MWI instability & bunch lengthening
Rarely induce beam losses, but may reduce the luminosity due to the deformed beam distribution and increasing of the beam energy spread.
The instability threshold is about half of the design bunch intensity.
σl with ZL [mm] (σl/σl0-1) | 6.5 (140%)
e/e0-1 | 35%
Design
Design
Yuan Zhang

## Slide 12: Influence of impedance on beam-beam
Less stable region obtained with longitudinal impedance included in the beam-beam simulation consistently.
The beam-beam interaction gets more unstable with longitudinal impedance due to the X-Z coupling.
The stable region shrunk and shifted
CDR impedance is used in these plots
W/O ZL
W/ ZL
Yuan Zhang

## Slide 13: Influence of impedance on beam-beam
With the real/imaginary longitudinal impedance roughly multiplied by a factor, the influence of the impedance on the beam-beam interaction is further investigated.
ReZL (0.512), ImZL (1)
Distinct influence shown with the real part of the impedance increased by a factor of 2
Locations of the stable regions are mainly fixed.
CDR impedance is used in these plots
Yuan Zhang

## Slide 14: Influence of impedance on beam-beam
ReZL (1), ImZL (0.512)
Reasonable large stable region even with the imaginary part of the impedance increased by a factor of 2, only with shift of the stable region.
 To optimize the impedance to mitigate this effect, the real part of impedance should be well controlled, while the imaginary part can be more relaxed (NEG coating may not be necessarily less than 1m).
CDR impedance is used in these plots
Yuan Zhang

## Slide 15: Transverse mode coupling instability
Fast instability, normally with beam losses.
The instability threshold extends from 45A to 85uA when considering bunch lengthening due to the longitudinal impedance.
The instability will be further detuned when considering the bunch lengthening due to the beamstrahlung.
Design
Design
W/O ZL
W/ ZL

## Slide 16: Transverse resistive wall instability
The coupled bunch instability can be driven by the resonance at zero frequency of the transverse resistive wall impedance.
An efficient bunch by bunch feedback damping of ~3 turns is required.
  Multiple of feedback systems around the ring
  Single mode damping specially for the RW is under consideration
  A positive chromaticity tends to provide some extra damping
 | Z-High Lumi
Instability growth time [ms] | 2.0 (~6 turns)
Radiation damping [ms] | 840
Bunch by bunch feedback [ms] | 1.0 (~3 turns)
Growth of the most dangerous mode vs. damping factors

## Slide 17: Beam ion effects
Induce emittance blow-up and a positive tune shift along the bunch train.
Filling pattern: {Ntrain=144, Bunch spacing=23ns, Gap=492ns}
Beam size increase due to the beam ion interaction are foreseen.
Build-up of ions along the bunch train
Parameters | Z-30MW
Lsepωion/c0 | 0.8
ρion,ave[m-3] | 4.3E11
τe [ms] | 0.1
τH [ms] | 4.0
y | 0.016
Bunch by bunch feedback can be effective on damping this effect
PRAB, 23, 074401 (2020)

## Slide 18: Electron cloud effects
The electron density is increased due to the change of the chamber cross section. The SEY needs to be reduced to <1.2 by introducing NEG coating.
More detailed simulations as well as evaluation of its induced heating are under going.
Elliptical chamber: SEY<1.3
Round chamber: SEY<1.2
Yudong Liu

## Slide 19: Summary
Impedance model is updated regarding the change of the chamber cross section (ellipticalcircular), as well as more impedance contributors included
Key instability issues for high luminosity Z are investigated:
  Coupling of the longitudinal impedance and the beam beam effects results in reduce of the stable beam-beam interaction region, the real part of the impedance should be well controlled.
  TMCI is OK considering bunch lengthening induced by longitudinal impedance.
  Resistive wall instability needs an efficient feedback damping of ~3 turns
  Ecloud requires an SEY of less than 1.2 or adding antechambers.
  Beam size increase due to the beam ion effect are foreseen  feedback system is needed to damp this effect.

## Slide 20: Thank you for your attention!