## Slide 1: Klystrons and RF Power Sources for CEPC
Zusheng Zhou（周祖圣）
On behalf of CEPC RF power source team
Feb.15, 2023

## Slide 2: Outline
Klystron
  Design consideration
  R&D Status
    1st prototype
    2nd (HE klystron) conditioning
    3rd (MBK) design and fabrication progress
    C&S band klystron design
CEPC RF power sources
Summary

## Slide 3
Design consideration
Parameters | Value
Freq.(MHz) | 650
Klystron QTY. | 120
Klystron power(kW) | 800
1 to 2 SC cavity | 
P band klystron for CEPC Collider
C&S band klystron for CEPC Linac
Parameters | S | C
Freq.(MHz) | 2860 | 5720
Klystron QTY. | 33 | 236
Klystron power(MW) | 80 | 50
RF structure distribution | 1-to-2&1-to-4 | 1-to-2

## Slide 4
R&D Status

## Slide 5: RF Power source choice
 | Tetrodes | IOTs | Klystrons | SSA | Magnetrons
 | DC–400MHz | (200–1500)MHz | 300 MHz – 1 GHz | DC – 20 GHz | GHz range
 | 1 MW | 1.2 MW | 1.5 MW |  | < 1MW
 | 85% - 90% (class C) | 70% | 65% | 60% | 90%
Remark | Broadcast technology, widely discontinued |  |  |  | Oscillator, not amplifier!
RF power sources - efficiencies
High power klystrons are the more attractive choice because of their high eﬃciency, low cost and more stable than IOT and SSA for CEPC collider.
The Collider beam power is more than 60 MW. The increase in efficiency of RF power sources is considered a high priority issue.

## Slide 6: System overall efficiency
Wall to PSM power supply/modulator | 95%
Modulator to klystron | 96%
Klystron to waveguide | 75%
Waveguide to coupler | 95%
Coupler to cavity | ~100%
Cavity to beam | ~100%
Overall efficiency | ~65%
CEPC Collider SRF Wall Plug Efficiency
The critical factor is klystron efficiency
Much higher efficiency, less energy consumption.

## Slide 7: Cost consumption
Chart: 
| 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 576 | 460.8 | 384 | 329.1429 | 288 | 256 | 230.4
CEPC at 800 RMB/MWh and 6000 hours/year
Excessive electricity bill, M RMB
1 year
Efficiency, %
65 M RMB
84M RMB
Efficiency impact on operation cost (Only considering operation efficiency of klystrons)
NOW
1st tube
62%
COMING
2nd tube
75%
FUTURE
MBK
80%
Save Money

## Slide 8: R&D strategy and plan (2016 to 2021)
3 or more klystron prototypes
Step1
Step2
Step3
1st
2nd
3rd
more
Prototypes
Efficiency: 60%
70%
80%
2016 | 2017 | 2018 | 2019 | 2020 | 2021
2022
2023

## Slide 9: 1st prototype high power test results
High power test stand
Pulsed 800kW
Parameters | Design | Test
Operating frequency (MHz) | 650 | 650
Beam Voltage (kV) | 81.5 | 80
Beam Perveance (μA/V3/2) | 0.65 | 0.7
Efficiency(%) | 65 | 62
Saturation Gain(dB) | ≥45 | 47
Output power(kW) | 800 | 800
1 dB Bandwidth(MHz) | ≥1 | 1.8
  700kW CW and 800kW pulsed power with 62% efficiency

## Slide 10: HE Klystron Milestone
Jan., 2021: Klystron manufacture started
Jul., 2021: Parts fabrication completed
Nov., 2021: Gun processing and klystron baking out
Dec., 2021: Klystron delivered to IHEP
Mar., 2022: Klystron conditioning started
  Cold high voltage conditioning
  Cathode activation
  High voltage conditioning
  RF Conditioning(Pulsed and CW)
Jul., 2022: CW 630kW/Eff. 70.5%

## Slide 11
Electron gun
Fabrication processing
Cold test
Collector body

## Slide 12: Electron gun processing
Cathode Temp. 975 degree C @Fil. 27V/6A

## Slide 13: Klystron final assembly
Klystron final assembly

## Slide 14: Klystron baking out

## Slide 15: High power test preparation
Klystron is in place in IHEP PAPS site

## Slide 16: High power conditioning
On Jul.5, 2022
CW power: 630kW
Eff. : 70.5%
Chart: Power vs. High Voltage
| 70 | 75 | 80 | 85 | 90 | 95 | 100 | 103
 | 188.1 | 247.75 | 311.8 | 385.1 | 453.7 | 524 | 595 | 632.13
Chart: Power vs. Efficiency
| 70 | 75 | 80 | 85 | 90 | 95 | 100 | 103
 | 0.53422 | 0.59306 | 0.63789 | 0.68027 | 0.69725 | 0.70715 | 0.71087 | 0.70461

## Slide 17: MBK design and fabrication status

## Slide 18: MBK physical and mechanical design
Final physical and mechanical design was completed at the end of 2021.
Parameters | Value
Frequency | 650 MHz
Output Power | 800 kW
Efficiency | 80.5%
bandwith | ±0.75 MHz
Beam voltage | 54 kV
Beam current | 2.51*8 A
Beam number | 8
Parameters | Value
Frequency | 650 MHz
Output Power | 800 kW
Efficiency | 80.5%
 | ±0.75 MHz
Beam voltage | 54 kV
Beam current | 2.51*8 A
Beam number | 8

## Slide 19: MBK Fabrication Status
Fabrication of two types of output window prototype is completed.
The high power conditioning was been processed with solid state amplifier at PAPS site.
Test result | Alumina | Beryllium oxide
VSWR@651MHz | 1.048 | 1.089
VSWR@650MHz | 1.034 | 1.084
VSWR@649MHz | 1.052 | 1.096
  High power conditioning site

## Slide 20: MBK Fabrication Status
The experimental cavity is completely manufactured with mechanical tuning device.
Fabrication of MBK beam tester is completed(including electron gun, collector, focusing coil) and will be delivered to IHEP for high power test on next month.
MBK Coils and field value
MBK beam tester
Chart: MBK magnet test results on beam axis

## Slide 21: C band and S band klystron
Type | QTY | Freq.(MHz) | Structure type
S-band klystron | 33 | 2860 | 1 1-to-1，standard-bunch 3 1-to-2，standard acc. structure. 8 1-to-2，large aperture acc. structure 21 1-to-4, standard acc. structure.
C-band klystron | 236 | 5720 | 1-to-2，standard acc. structure.

## Slide 22
80 MW C-Band(5720 MHz) klystron
Beam optics design simulation
Chart: Z (mm)
Emax @Anode = 0.1546E+05 V/mm
% Ripple rate < 4.2%
Emax@ FE = 0.1864E+05 V/mm
Beam Current = 390 A
Beam Voltage = 410 kV
Perveance = 1.49 µP
8.5 A/cm^2
4.4 A/cm^2
Average = 6.5 A/cm^2
Cathode Loading
Cathode uniformity 1.9 : 1
Beam Trajectories
Beam Current

## Slide 23
GUN simulation result in CST
Chart: Beam Envelop
| 20 | 33.877552000000001 | 47.755104000000003 | 61.632652 | 75.510204000000002 | 89.387752000000006 | 103.26531 | 117.14286 | 131.02041 | 144.89795000000001 | 158.77551 | 172.65306000000001 | 186.53059999999999 | 200.40816000000001 | 214.28572 | 228.16327000000001 | 242.04080999999999 | 255.91835 | 269.79592000000002 | 283.67347000000001 | 297.55101000000002 | 311.42858000000001 | 325.30612000000002 | 339.18369000000001 | 353.06123000000002 | 366.93876999999998 | 380.81634000000003 | 394.69387999999998 | 408.57141999999999 | 422.44898999999998 | 436.32652999999999 | 450.20407 | 464.08165000000002 | 477.95918999999998 | 491.83672999999999 | 505.71429999999998 | 519.59181000000001 | 533.46938 | 547.34694999999999 | 561.22446000000002 | 575.10203000000001 | 588.9796 | 602.85717 | 616.73468000000003 | 630.61225000000002 | 644.48982000000001 | 658.36734000000001 | 672.24491 | 686.12248 | 699.99999000000003
 | 35.5062 | 25.9477 | 19.9269 | 15.959 | 13.628 | 12.1128 | 10.9589 | 10.0341 | 9.2502 | 8.5723 | 8.0739 | 7.7131 | 7.3005 | 6.7911 | 6.2931 | 6.1218 | 6.1342 | 6.0545 | 6.0401 | 5.7847 | 5.5436 | 5.6122 | 5.6007 | 5.6657 | 5.5432 | 5.4129 | 5.5278 | 5.491 | 5.5817 | 5.5122 | 5.4408 | 5.5474 | 5.4788 | 5.5823 | 5.5623 | 5.5471 | 5.5506 | 5.4814 | 5.6131 | 5.6423 | 5.6372 | 5.5516 | 5.4731 | 5.6676 | 5.7595 | 5.7511 | 5.5973 | 5.5001 | 5.7701 | 6.0018

Beam trajectories
Surface Gradient

## Slide 24
Solenoid Design
Magnetic Field at the Tube Body = 2540G
Magnetic Field at the Cathode = 32.67 G
Reverse Coil
Pole Pieces
Focusing Coils

## Slide 25
Chart: Electric field profile at the top of the Ceramic
Chart: Electric field at the lower surface of the Ceramic
21.84 kV/mm
4.47 kV/mm
18.39 kV/mm
@ FE 59.9832 18.0268 2.1844E+05
@lower ceramic; 96.0000, -96.7931, 2.9319E+04
@anode; 30.6698, 61.6178, 1.8394E+05
@ corona 85.803, -91.8242, 1.5702E+05
@upper ceramic; 106.000 -92.2877 4.4685E+04
Surface gradient at beam optic & ceramic

## Slide 26
Beam dynamic simulation of C band klystron
Parameters | Value
Frequency | 5720 MHz
Output Power | 80MW
Efficiency | 45%
Beam voltage | 420 kV
Beam current | 403 A
Beam number | 1

## Slide 27
Optimization in progres
Beam dynamic simulation of C band klystron

## Slide 28
S Band klystron parameters
Parameters | Value
Operating frequency | 2860MHz
Output power | 80MW
RF pulsed width | 4μS
Beam voltage | 350kV
Beam current | 414A
Beam μperveance | 2.0
Efficiency | 55%
The RF power source system of CEPC LINAC includes 33 sets of pulsed klystron operating at a frequency of 2860MHz. The power of these klystron are excepted to be 80MW.

## Slide 29
Efficiency improvement
The 1-D code AJDISK is suitable for the preliminary optimization of the interaction section parameters. Based on AJDISK, a 1-D automatic optimization code via NSGA-II was developed at IHEP.
The 1-D efficiency is about 64%.

## Slide 30
30
Efficiency improvement
The parameters obtained from AJDISK was checked by 2-D code EMSYS and 3D code CST.
Parameters | DGUN | CST
Beam μperveance | 1.978 | 1.997
Beam maximum radius | 8.54mm | 8.64mm
Beam minimum radius | 7.93mm | 8.02mm
Beam ripple | 3.7% | 3.6%

## Slide 31
RF power sources

## Slide 32: Collider transmission system

## Slide 33: Collider infrastructure
Collider Power Source Gallery
High voltage power supply are placed on the ground.
For space savings, transmission system in part are placed in RF tunnel.

## Slide 34: Booster RF power source
The Booster RF system consists of 1.3 GHz superconducting RF cavities. There are 12 cryo-modules for Higgs operation, each containing eight 9-cell superconducting cavities.
These cavities need 96 set 25kW power sources.
SSA, their capabilities extend from a few kW to several hundred kW, reasonable efficiency (~50%), high gain, and modular design provide high reliability.
So the SSA has been chosen for the Booster RF power source system.
Design consideration
Parameters | Values
Frequency | 1.3 GHz
Power | 25 kW
Gain | ≥65 dB
Bandwidth (1dB) | ≥ 1 MHz
Amplitude stability | ≤0.1% RMS
Phase stability | ≤0.1°RMS
Phase Variation | ≤10°
Harmonic | < -30 dBc
Spurious | < -60 dBc
Efficiency at 25kW | ≥45%
MTBF | ≥30000 h
Redundancy | 1 power module failure
1.3 GHz/25kW SSA Specifications

## Slide 35: Booster SSA cabinet
2120mm(H)×1326mm(W)×1300mm(L)

## Slide 36: Booster SSA parts
1:2 power divider
6:1 power combiner

## Slide 37: Booster RF transmission

## Slide 38: Damping ring RF power source
There are 2 RF stations, RF power is 650MHz/90kW/station.
Parameters | Values
Frequency | 650MHz
Power | 90 kW
Gain | ≥65 dB
Bandwidth (1dB) | ≥ 1 MHz
Amplitude stability | ≤0.1% RMS
Phase stability | ≤0.1°RMS
Phase Variation | ≤10°
Harmonic | < -30 dBc
Spurious | < -60 dBc
650MHz/90kW SSA Specifications

## Slide 39: Damping ring SSA cabinet
3210mm(H)×3220mm(W)×1800mm(L)

## Slide 40: Damping ring SSA key components
1:4 power divider
60kW 1:2 power divider

## Slide 41: Damping ring SSA key components
30kW 2:1 power combiner
60kW 2:1 power combiner
2 port directional coupler
4 port directional coupler

## Slide 42: Summary
HE klystron is being developed, efficiency of 60% and 70% has been achieved, 80% efficiency is expected to be reached by the end of this year.
Development of S and C band 80MW klystron for CEPC Linac is also in progress.
Design of RF power distribution system for collider, booster, damping ring and Linac is showed.
SSA mechanical design for booster and damping ring is also showed.

## Slide 43
Thanks for your attention!