## Slide 1: CEPC collective instability study status
Na Wang, Yuan Zhang, Haisheng Xu, Saike Tian , Yudong Liu, Yuting Wang
IHEP
IAS workshop, Feb. 12th-16th, 2023, Hong Kong

## Slide 2: Outline
Impedance modeling
  Resistive wall & geometrical impedance
Collective instabilities
  Bunch lengthening and microwave instability
  Transverse mode coupling instability
  Coupled bunch instabilities
  Beam ion effects
Summary and outlooks

## Slide 3: Impedance modeling
Impedance modeling of the key vacuum components has been performed since the beginning of the project.
Resistive wall impedance
  Generated from finite conductivity of the vacuum chambers
  Calculated with theoretical formulas considering the NEG coating
Geometrical impedance
  Generated by the discontinuity of the vacuum chambers
  Calculated individually with 2D/3D simulation codes

## Slide 4: Resistive wall impedance
Including main chamber, MDI chamber, collimators in the IR region and stainless steel chamber (flanges, bellows, BPMs)
Main chamber:
(L=97km)
SS chamber:
(L=3km)
3mm copper
0.2um NEG coating
3mm stainless steel
28mm
28mm
Collimator:
10 hori.+8 vert.
MDI chamber:

## Slide 5: Resistive wall impedance
The impedance contributed by the main vacuum chamber dominates both the longitudinal and transverse RW impedance. The impedance from stainless steel chambers also shows nontrivial contributions.
Components | Z¦¦/n, mΩ | kloss, V/pC | ky, kV/pC/m
Main chamber | 6.0 | 350.7 | 10.9
SS chamber | 0.7 | 73.4 | 1.6
MDI chamber | 6.9E-3 | 0.7 | 0.2
Collimators | 8.9E-3 | 0.9 | 0.3
RW Total | 6.7 | 425.6 | 13.8
Ring Total | 15.9 | 741.4 | 33.8
ReZL
ImZL
ReZy
ImZy
Broadband effective impedance @z=3mm

## Slide 6: Geometrical impedance
Main vacuum components considered in the impedance model
RF cavity
Flange
Bellows
Pumping port
BPM
Gate Valve
Electro separator
Collimator

## Slide 7: Impedance model
ReZL
ImZL
ReZy
ImZy
The longitudinal broadband impedance is dominated by the RW, flanges and bellows.
The transverse impedance is dominated by the RW, flanges, bellows and collimators.
Inj./ext. elements, feedback kickers, absorbers, masks and collimators outside the IR region are still missing.

## Slide 8: Impedance budget @z=3mm
Components | Number | Z¦¦/n, mΩ | L, nH | kloss, V/pC | ky, kV/pC/m
Resistive wall | - | 6.7 | 355.7 | 425.6 | 13.8
RF cavities | 60 | 0.5 | 24.8 | 101.2 | 0.5
Flanges | 37714 | 5.2 | 276.1 | 37.3 | 5.2
BPMs | 1808 | 0.04 | 2.0 | 9.5 | 0.2
Bellows | 15949 | 2.9 | 154.6 | 87.4 | 3.9
Gate Valves | 500 | 0.2 | 11.4 | 14.5 | 0.4
Pumping ports | 5316 | 0.3 | 18.4 | 2.3 | 0.2
Collimators | 16 | 0.04 | 1.8 | 26.4 | 4.8
IP chambers | 2 | 0.004 | 0.2 | 0.3 | 2.9
Electro-separators | 20 | -0.1 | -5.4 | 34.5 | 0.1
Taper transitions | 48 | 0.04 | 2.3 | 2.5 | 1.8
Total |  | 15.9 | 842.0 | 741.4 | 33.8

## Slide 9: Impedance evolution
The impedance model will be continuously updated along with the development of the hardware designs.
  The effective impedances varies along with the development of the impedance model => apparent increases on both Z/n and ky are shown.
Chart: 
| Z/n | kloss | ky
CDR-2018 | 1 | 1 | 1
IARC-2021 | 1.3421 | 0.8452 | 1.099
2023 | 1.3947 | 0.9423 | 1.6733
Evaluate with rms bunch length of 3mm
CDR-2018
IARC-2021
2023
Elliptical cross section
Circular cross section
More contributors included
More detailed chamber material, collimator updated and betatron function weighing is considered.

## Slide 10: Main beam parameters for the collider rings
Parameter [unit] | Higgs | W | Z | tt-bar
Beam energy [GeV] | 120 | 80 | 45.5 | 180
Lmax/IP (1034cm-2s-1) | 5 | 16 | 115 | 0.5
Emittance (H/V) [nm] | 0.64/0.0013 | 0.87/0.0017 | 0.27/0.0014 | 1.4/0.0047
Beam current [mA] | 16.7 | 84.1 | 803.5 | 3.3
Bunch number | 249 | 1297 | 11934 | 35
Bunch Population [1010] | 13 | 13.5 | 14 | 20
Momentum compaction [10-5] | 0.71 | 1.43 | 1.43 | 0.71
Bunch length z (natural/total) [mm] | 2.3/4.1 | 2.5/4.9 | 2.5/8.7 | 2.2/2.9
Energy spread (natural/total) [10-4] | 10/17 | 7/14 | 4/13 | 15/20
Betatron tune x/y | 445.10/445.22 | 317.10/317.22 | 317.10/317.22 | 445.10/445.22
Synchrotron tune | 0.049 | 0.062 | 0.035 | 0.078
Radiation damping [ms] | 44/44/22 | 156/156/78 | 850/850/425 | 14/14/7

## Slide 11: Collective instabilities in the collider rings
Rough estimations of the instability threshold based on analytical criterions.
Impedance budget | 
Z¦¦/n, mΩ | 15.9
ky, kV/pC/m | 33.8
 | Higgs | W | Z | ttbar
Single bunch (longitudinal) Z¦¦/n [m] | 6.5 | 4.1 | 0.7 | 14.4
Single bunch (transverse) ky [kV/pC/m] | 69.7 | 40.2 | 12.4 | 109.8
Multi-bunch SR(longitudinal) [GHzG] | 4.5 | 0.1 | 6.5E-4 | 171.2
Multi-bunch SR (transverse) [G/m] | 3.0 | 0.08 | 8.9E-4 | 72.7
 | Higgs | W | Z | ttbar
Single bunch (longitudinal) Z¦¦/n [m] | 6.5 | 4.1 | 0.7 | 14.4
Single bunch (transverse) ky [kV/pC/m] | 69.7 | 40.2 | 12.4 | 109.8
 | 4.5 | 0.1 | 6.5E-4 | 171.2
 | 3.0 | 0.08 | 8.9E-4 | 72.7
Although the criterion usually underestimates the threshold, we do observed its influence on the beam-beam interaction [PRAB 23, 104402 (2020); PRAB 25, 011001 (2022)].
TMCI unstable
Tight narrowband impedance requirements for Z (at least ~two orders higher for the other energies)

## Slide 12: Bunch lengthening and microwave instability
Considering single beam, variations of bunch length and beam energy spread with bunch intensity are calculated by particle tracking simulations.
Higgs
Higgs
Z
Z
Higgs:
Instability threshold is around 100 nC  far above the design bunch current.
At the design bunch intensity, the bunch will be lengthened by ~30% due to the impedance.
Z:
Instability threshold is about half of the design bunch intensity.
At the design bunch current, the bunch length and the beam energy spread are increased by ~140% and ~35%, respectively.

## Slide 13: Transverse mode coupling instability (TMCI)
Main constraint on the single bunch current for Z.
For the single beam, consistent studies with both transverse and longitudinal impedance show reduction of the instability from longitudinal impedance.
  TMCI threshold at =0 10nC (design value: 22.4nC, Impedance: IARC-2021)
  Threshold beam current decreases with increase of chromaticity
Head-tail phase shift over the bunch:
High order modes maybe excited with large chromaticity

## Slide 14: TMCI with lengthened bunch from BS and ZL
2023-ZT
2021-ZT
TMCI threshold: 21e10 (33.6nC)
TMCI threshold: 15e10 (24nC)
Simulations are performed, considering bunch lengthening and energy spread increase @14e10, with the beam-beam code developed by Yuan Zhang.
 Increase of the TMCI threshold due to the reduction of bunch density
 Threshold decreases dramatically due to the increase of impedance
Yuan Zhang’talk for detail

## Slide 15: Transverse resistive wall instability
Assuming the whole ring is made of copper with coating, the instability growth rate is much faster than the synchrotron radiation damping (=850ms).
n=11616
n=11615
n=11617
n=11618
f [kHz] | Mode index | Growth t [ms]
-2.338 | 11616 | 2.2 (7 turns)
-5.335 | 11615 | 3.2 (10 turns)
-8.332 | 11614 | 4.0 (12 turns)
-11.330 | 11613 | 4.6 (14 turns)
Tough requirement on feedback damping (broadband feedback + mode feedback)

## Slide 16: Transverse resistive wall instability (cont.)
With more detailed RW impedance model, the instability growth time can be further reduced by the stainless steel components. Contributions from the MDI and collimators are limited.
n=11616
n=11615
n=11617
n=11618
f [kHz] | Mode index | Growth t [ms]
-2.338 | 11616 | 2.2 (7 turns)
-5.335 | 11615 | 3.2 (10 turns)
-8.332 | 11614 | 4.0 (12 turns)
-11.330 | 11613 | 4.6 (14 turns)
1.7ms
Tough requirement on feedback damping (broadband feedback + mode feedback)

## Slide 17: Transverse resistive wall instability (cont.)
Stabilizing effect of chromaticity is checked according to the theory developed in [PRAB 24, 024402 (2021)]
 Limited damping from  for Z
Natural bunch length or energy spread
z=2.5mm, =410-4, kz=0.1
With impact of ZL and beamstrahlung
z=8.7mm, =1310-4, kz=0.4
Complex growth rate in terms of zero chromaticity growth rate
Head-tail phase shift over the bunch:
()/(c/t)
()/(c/t)
 =10
 =0
()/(c/t)
()/(c/t)
 =10
 =0
 = 2ms
 = 2ms

## Slide 18: RF HOMs
For the operation mode of Higgs, W and low luminosity Z (with total beam power of 10 MW), the 2-cell 650MHz RF cavities will be adopted.
  The longitudinal and transverse HOMs below the cutoff frequency are measured.
  The impedance is above the SR threshold for Z in both longitudinal and transverse planes. In the resonant case, the instability has a growth rate of 114 ms and 19 ms, respectively.
  The W operation mode will also be unstable in transverse when consider only SR damping. In the resonant case, the instability has a growth rate of 105 ms.
Courtesy of JiYuan Zhai

## Slide 19: RF HOMs (cont.)
For the high luminosity Z, the RF cavities will be replaced by the 1-cell cavities.
  HOMs can be well damped (loaded Q of 100 has been considered) below the threshold that determined by the SR damping.
Courtesy of JiYuan Zhai

## Slide 20: Beam ion effects
Trapped ions can induce bunch centroid oscillation and emittance growth.
The possibility of ion trapping and fast beam ion instability are investigated.
With vacuum pressure of 1nTorr, and CO has been considered as the only ion species
Consider multi bunch train filling pattern, the instability growth calculated by the analytical theory for W and Z are faster than SR damping.
Build-up of ions along the bunch train

## Slide 21: Macro-particle simulations for Z
Filling pattern: 144 bunch trains, each train contains 83 bunches with spacing of 23ns
Multi-train filling is effective in mitigating the beam ion instability. However, beam emittance growth is still foreseen bunch by bunch feedback is needed.
x/y=69/96m
Horizontal
Vertical

## Slide 22: Summary and outlooks
Main constraints from the beam collective effects are mainly focused on Z
  Transverse impedance restrict the single bunch current for single beam, as well as the stability of the beam-beam interaction.
  Tough requirement on feedback from TRWI  effective damping should be demonstrated.
Comprehensive or consistent studies considering coupling among different factors are needed for accurate estimate of the machine performance:
  impedance-beam beam, longitudinal-transverse, collective effect - feedback
Impedance model needs to be further evolved or optimized
  Constraint on the luminosity for the high performance Z.
  Kickers and machine protection collimators (or mask) can give nontrivial contributions, which are not included yet.
  HOM should be further checked for some key element, e.g. electro-separators.
Further investigation of the two-stream instability is still needed.

## Slide 23: Thank you for your attention!