## Slide 1: CEPC Polarization Study Status
Zhe Duan
On behalf of CEPC Beam Polarization Working Group
2023. 02. 15
IAS Program on High Energy Physics (HEP 2023)
Feb 14-16, 2023

## Slide 2: CEPC Beam polarization working group
Physics design:
  Tao Chen, Zhe Duan, Hongjin Fu, Jie Gao, Sergei Nikitin (BINP), Dou Wang, Jiuqing Wang, Yiwei Wang, Wenhao Xia(graduated)
Polarized electron source & linac:
  Xiaoping Li, Cai Meng, Jingru Zhang
Polarimeter:
  Shanhong Chen, Yongsheng Huang, Guangyi Tang
Discussions with D. P. Barber (DESY) on polarization theories and simulations are illuminating.
Helpful discussions with E. Forest (KEK) & D. Sagan (Cornell) on usage of Bmad/PTC are acknowledged.

## Slide 3: Motivation of CEPC polarized beam program
Vertically polarized beams in the arc
  Beam energy calibration via the resonant depolarization technique
  Essential for precision measurements of Z and W properties
  At least 5% ~ 10% vertical polarization, for both e+ and e- beams
Longitudinally polarized beams at IPs
  Beneficial to colliding beam physics programs at Z, W and Higgs
  Figure of merit: Luminosity * f( Pe+, Pe- )
  ~50% or more longitudinal polarization is desired, for one beam, or both beams
Supported by National Key R&D Program 2018-2023 to design longitudinally polarized colliding beams at Z-pole.
The study in this presentation is based on CEPC CDR lattice & parameters.
Will be included as a Chapter in the Appendix in the CEPC TDR.
L. Arnaudon, et al., Z. Phys. C 66, 45-62 (1995).

## Slide 4: Beam polarization in the collider rings
Colliding bunch: top-up injection
Non-colliding “pilot” bunch: decay mode
time
Polarization
Bunch charge
CEPC CDR parameters | 45.6 GeV (Z, 2T) | 80 GeV (W) | 120 GeV (Higgs)
Polarization build-up time w/o radiative depolarization (hour) | 256 | 15.2 | 2.0
Beam lifetime (hour) | 2.5 | 1.4 | 0.43
required to realize in top-up mode, if | 0.6% | 5% | 11%
CEPC CDR parameters | 45.6 GeV (Z, 2T) | 80 GeV (W) | 120 GeV (Higgs)
 | 256 | 15.2 | 2.0
 | 2.5 | 1.4 | 0.43
 | 0.6% | 5% | 11%
  If , then
Injection of polarized beams is required
  to achieve high-level longitudinal polarization without significantly sacrificing luminosity
  also benefits resonant depolarization measurements w/ pilot bunches.

## Slide 5: Preparation and injection of polarized beams
e- polarization >80%, SLC/ILC/EIC
[1] Z. Duan, talk on eeFACT 2022, FCC EPOL Workshop 2022;
[2] T. Chen, Z. Duan, D. H. Ji, D. Wang, arXiv:2302.05321v1 [physics,acc-ph]
[3] W. H. Xia, Z. Duan, D. P. Barber, Y. W. Wang, B. Wang, J. Gao, arXiv:2204.12718v1 [physics.acc-ph], submitted to PRAB
[4]W. Xia, Z. Duan, J. Gao and Y. W. Wang, RDTM (2022) doi: 10.1007/s41605-022-00344-2
Aspect | Key issue | Pages in this presentation
Polarized beam acceleration in booster | How serious is depolarization, possible mitigation? [1,2] | 6-10
Equilibrium beam polarization in collider rings | What are the mechanisms of radiative depolarization?[3] | 11
Resonant depolarization | How to generate polarized e+ beam?[1] | 12-14
Longitudinally polarized colliding beams | How to design spin rotators in the collider rings?[1,4] | 15

## Slide 6: Depolarization in the booster
The spin tune changes and could cross spin resonances
  The spin resonances are spaced by 440 MeV for e+/e-
The non-adiabatic crossing could vary and lead to depolarization [1]
  Spin resonance strength ε
  Acceleration rate [km]
Polarization is maintained (ΔP < 1%) for the regimes of fast crossing & slow crossing
[1] Froissart and Stora, NIM 7, 297 (1960) [2] A. K. Barladyan, et al., PRAB 22, 112804, (2019)
[3] S. Nakamura, et al., NIM A 411, 93 (1998) [4] T. Khoe et al., Part. Accel. 6, 213 (1975)
[5] Configuration Manual: Polarized Proton Collider at RHIC, 2006 [6] V. Ranjbar, et al., PRAB 21, 111003 (2018)
Fast crossing
Slow crossing

## Slide 7: Setup of CEPC booster lattice
Arc region covers ~ 80% of circumference
General structure of the CEPC booster lattice
  8 arcs each containing 140 FODO cells
  interleaved with 8 straight sections
60 imperfection lattice seeds
  Misalignment error & field error, scan BPM offset
  Closed orbit correction & tune correction
Multi-particle tracking in Bmad
  Energy and RF ramping in the whole process
  Element-by-element tracking with radiation damping & quantum excitation

## Slide 8: Spin resonance structure of CEPC Booster
Intrinsic resonances:
Super strong resonances:
Imperfection resonances:
Super strong resonances:
Strength of intrinsic & imperfection resonances can be approximated by[1]
Enhancement or cancellation occurs when specific conditions are met or not
Resonances are generally weak within working beam energies of CEPC.
due to P superperiods
due to M identical FODOs in each arc
[1] S. Y. Lee, Spin dynamics and snakes in synchrotrons (World Scientific, 1997).

## Slide 9: Estimation of depolarization with Froissart-Stora formula
Imperfection resonance
Intrinsic resonance
Assumption:
single crossing of imperfection & intrinsic resonances
there are no interference between resonance crossings

## Slide 10: Depolarization effects: simulation vs. estimation
Z-mode
W-mode
H-mode
In the acceleration to Z & W
  The spin resonances are generally weak
  Polarization is mostly maintained
  Estimations agree fairly well with simulations
In the acceleration H
  The spin resonances become stronger at higher energies
  Severe depolarization occurs
  Mitigation methods to be explored

## Slide 11: Radiative depolarization in the collider rings
Two distinct spin diffusion mechanisms were proposed in [1] in 1970s, regarding the regimes of spin resonance crossing, in the combined effects of synchrotron oscillation and synchrotron radiation
Regime | Correlated regime | Uncorrelated regime
Condition |  | is violated and
Theory | Non-resonant spin diffusion & perturbative treatment of | Resonant spin diffusion
Depolarization effect | Higher-order synchrotron sideband spin resonances | No dependence on , weaker depolarization
Regime | Correlated regime | Uncorrelated regime
Condition |  | 
Theory |  | Resonant spin diffusion
Depolarization effect | Higher-order synchrotron sideband spin resonances | 
Monte-Carlo simulations were compared with these theories[2], showing a gradual evolution from the correlated regime to the uncorrelated regime in parameter scan, suggesting existing theories are incomplete, requiring further development
Z
Higgs
Case A: dependence on beam energy
Case B: influence of harmonic RF cavity
optimal lengthening condition
Scan harmonic RF voltage
[1] Derbenev, Kondrantenko and Skrinsky, Part. Accel. 9, 247 (1979) [2] W. H. Xia, Z. Duan, D. P. Barber, Y. W. Wang, B. Wang, J. Gao, arXiv:2204.12718v1 [physics.acc-ph], submitted to PRAB

## Slide 12: e+ damping/polarizing ring
DR V4.0 | unpolarized e+ | polarized e+
Energy (Gev) | 1.542 | 
Circumference (m) | 144.2 | 
Number of trains | 2(4) | 
Number of bunches/trian | 1(2) | 
Total current (mA) | 12.4 | 
Bending radius (m) | 3.44 | 
Dipole strength B0 (T) | 1.07 | 
Wiggler strength B+ (T) | 1.8 | 
Wiggler cell length (m) | 1.5 | 
U0 (kev/turn) | 190.9 | 
Damping time x/y/z (ms) | 7.77/7.77/3.89 | 
Momentum compaction | 0.015 | 
Storage time | 20 ms | 10 min
0 (%) | 0.072 | 
0 (mm.mrad) | 138 | 
injection z (mm) | 6 | 
Extract z (mm) | 5.7 | 5.6
inj (mm.mrad) | 2500 | 
ext x/y (mm.mrad) | 151/15 | 138/14
inj /ext (%) | 0.18 /0.072 | 
RF acceptance (%) | 1.8 | 
fRF (MHz) | 650 | 
VRF (MV) | 3.95 | 
Longitudinal tune | 0.044 | 
Asymmetric wigglers
B+=1.8T=-5 B-
cell length=1.5m
16 such cells
+1(2)

## Slide 13: RD scenario & e+ damping/polarizing ring
bunches stay ~10 min to accumulate ~ 20% polarization, for RD
bunches stay ~ 20 msec without gaining beam polarization, for regular refill
Positron damping ring
Preparation and injection of polarized e+/e- bunches alternates with unpolarized bunches.

## Slide 14: What we can gain from injecting polarized beams for RD?
Scenarios of polarized beam generation |  | Self-polarization in the collider[1] | Injection of polarized beams[2]
Hardware | Polarized electron gun | None | Yes
 | Asymmetric wigglers | In the collider | In the positron damping ring
Polarization level |  | 5% ~ 10% | > 70% for e-, > 20% e+
Dead time for physics |  | Initial 1~2 hours in each fill | None
Frequency of RD measurements |  | Every ~10 min per beam | More frequent for e- beam
RD on colliding beams |  | None | Possible, especially at lower bunch charge
Horizontal polarization for free spin precession method |  | Strong spin flipper in the collider | Spin rotator in the transfer line; much higher polarization
[1] The FCC-ee Energy and Polarization Working Group, arXiv:1909.12245v1, 2019.
[2] Zhe Duan, talk on 2nd EPOL Workshop, Sep 29, 2022

## Slide 15: Spin rotators in the collider ring @ Z-pole
Solenoid-based spin rotators
  interleaved solenoid + quads [1] to cancel coupling effects
Anti-symmetric insertion just outside interaction region [2,3,4]
Influence[4]
  Increase of circumference ~ 2.8 km, can be optimized
  DA shrinks but still sufficient, can be further optimized
  Depolarization is relatively weak near 45.6 GeV, confirmed by simulations
    Cancellation of energy dependence with the anti-symmetric design
[1] D. Barber, et al., A solenoid spin rotator for large electron storage rings. Part. Accel. 17 (1985) 243.
[2] I. Koop, Longitudinally polarized electron in SuperB, eeFACT’08
[3] S. Nikitin, IJMPA 34, 1940004 (2019), IJMPA 45, 2041001 (2020).
[4] . W. Xia, Z. Duan, J. Gao and Y. W. Wang, RDTM (2022) doi: 10.1007/s41605-022-00344-2

## Slide 16: Summary
For polarized beam applications at CEPC, we’ve studied the possibility of generating polarized beams from the source and injecting into the collider rings. Some key issues have been addressed
  Beam polarization can be mostly preserved in the booster up to 45.6 GeV and 80 GeV.
  Polarized e+ beam can be generated in the e+ damping/polarizing ring, for RD measurements.
  Spin rotators have been implemented into the collider rings @Z-pole, with promising performance.
Mechanisms of radiative depolarization effect still require further investigation.

## Slide 17
Thank you for your attention!