## Slide 1
The Compact Linear Collider (CLIC)
Andrea Latina (CERN)
on behalf of CLIC
IAS HKUST
14-16 Feb 2023
Outline
CLIC project overview
CLIC at 380 GeV
Optimisation studies
Applications
Summary

## Slide 2: The Compact Linear Collider (CLIC)
  Timeline: Electron-positron linear collider at CERN for the era beyond HL-LHC
  Compact: Novel and unique two-beam accelerating technique with high-gradient room temperature RF cavities (~20’500 structures at 380 GeV), ~11km in its initial phase
  Expandable: Staged programme with collision energies from 380 GeV (Higgs/top) up to 3 TeV (Energy Frontier)
  CDR in 2012 with focus on 3 TeV. Updated project overview documents in 2018 (Project Implementation Plan) with focus 380 GeV for Higgs and top.
  Cost: 5.9 BCHF for 380 GeV (stable wrt 2012)
  Power: 168 MW at 380 GeV (reduced wrt 2012),
  corresponding to 60% of CERN’s energy consumption today
  Comprehensive Detector and Physics studies
Accelerating structure prototype for CLIC:
12 GHz (L~25 cm)

## Slide 3: Collaborations
CLIC accelerator
  ~50 institutes from 28 countries*
  CLIC accelerator studies
  CLIC accelerator design and development
  Construction and operation of CLIC Test Facility, CTF3
CLIC detector and physics (CLICdp)
  30 institutes from 18 countries
  Physics prospects & simulations studies
  Detector optimisation + R&D for CLIC
+ strong participation in the CALICE and FCAL Collaborations and in AIDA-2020/AIDAinnova
*Canada missing on map
Notes: Chec AIDA – Canada missing

## Slide 4: CLIC parameters

## Slide 5: CLIC Layout 380 GeV

## Slide 6: CLIC Luminosity Performance
Result of detailed simulations

## Slide 7: CLIC timeline
Ramp-up and up-time assumptions: arXiv:1810.13022, Bordry et al.
Technology Driven Schedule from start of construction shown above.
A preparation phase of ~5 years is needed before (estimated resource need for this phase is ~4% of overall project costs)

## Slide 8
  Drive beam accelerated to ~2 GeV using conventional klystrons
  Intensity increased using a series of delay loops and combiner rings
  Drive beam decelerated and produces high-RF
  Feed high-RF to the less intense main beam using waveguides
  Extend by extending main linacs, increase drivebeam pulse-length and power, and a second drivebeam to get to 3 TeV
CLIC can easily be extended
  What are the critical elements:
    Physics
    Gradient and power efficiency
    Costs

## Slide 9
3-volume CDR 2012
4 CERN Yellow Reports 2018
Updated Staging Baseline 2016
Two formal submissions to the ESPPU 2018
Available at:
clic.cern/european-strategy
Resources
Details about the accelerator, detector R&D, physics studies for Higgs/top and BSM
Several LoIs have been submitted on behalf of CLIC and CLICdp to the Snowmass process:
The CLIC accelerator study: Link
Beam-dynamics focused on very high energies: Link The physics potential: Link The detector: Link

## Slide 10: CLIC is a mature design/study
The CLIC accelerator studies are mature:
Optimised design for cost and power
Many tests in CTF3, FELs, lightsources and test-stands
Technical developments of “all” key elements

## Slide 11: Recent updates
After the European Strategy for Particle Physics Update (ESPPU)
  Immediate study of luminosity performance margins, gamma-gamma and Z-pole operation
  Timeline for further studies changed (slower implementation)
  Accelerator
  Resources too limited to move into TDR “proper”
  External projects using X-band technology very important and much increased
  Prioritize R&D type of studies and development of core technologies (will show later)
Physics and Detector:
  Less resources for dedicated CLIC studies, more “Higgs-factory” approach (i.e., CLIC, ILC, FCC-ee, CEPC) and continue linking to detector R&D collaborations

## Slide 12: CLIC acc. studies – luminosities
Further work on luminosity performance, possible improvements and margins, operation at the Z-pole and gamma-gamma
      Luminosity margins and increases:
    Z pole performance, 2.3x1032 – 0.4x1034 cm-2 s-1
    The latter number when accelerator configured for Z running (e.g., early or end of first stage)
    Baseline includes estimates static and dynamic degradations from damping ring to IP: 1.5 x 1034 cm-2 s-1, a “perfect” machine will give : 4.3 x 1034 cm-2 s-1, so significant upside
    In addition: doubling the frequency (50 Hz to 100 Hz) would double the luminosity, at a cost of +50 MW and ~5% cost increase
    CLIC note and paper about all these studies
Nanobeam workshop (summary by Nuria Catalan): LINK
Notes: Is this the last version of this slide, now published

## Slide 13: CLIC acc. studies – luminosities
Further work on luminosity performance, possible improvements and margins, gamma-gamma collider
      Gamma – Gamma spectrum (example)
Notes: Is this the last version of this slide, now published

## Slide 14: CLIC Project Readiness 2025-26
Project Readiness Report as a step toward a TDR – for next ESPP
Assuming ESPP in 2026, Project Approval ~ 2028, Project (tunnel) construction can start in ~ 2030.
Focusing on:
The X-band technology readiness for the 380 GeV CLIC initial phase
Optimizing the luminosity at 380 GeV
Improving the power efficiency for both the initial phase and at high energies
Goals for these studies by ~2025:
Improved 380 GeV parameters/performance/project plan
Push multi-TeV options/parameters

## Slide 15: Power and Energy
Design Optimisation:
The designs of CLIC, including key performance parameters as accelerating gradients, pulse lengths, bunch-charges and luminosities, have been optimised for cost but also increasingly focussing on reducing power consumption.
Technical Developments:
Technical developments targeting reduced power consumptions at system level high efficiency klystrons, and super conducting and permanents magnets for damping rings and linacs.
Running when energy is cheap:
CLIC is normal conduction, single pass, can change off-on-off quickly, at low power when not pulsed. Specify state-change (off-standby-on) times and power uses for each – see if clever scheduling using low-cost periods, can reduce the energy bill
Renewable energy (carbon footprint):
Is it possible to fully supply the annual electricity demand of the CLIC-380 by installing local wind and PV generators (this could be e.g., achieved by 330 MW-peak PV and 220 MW-peak wind generators, at a cost of slightly more than 10% of the CLIC 380 GeV cost)
Power estimate bottom up (concentrating on 380 GeV systems)
Very large reductions since CDR, better estimates of nominal settings, much more optimised drivebeam complex and more efficient klystrons, injectors more optimized, etc
Further savings possible, main target damping ring RF significantly reduced, L-band klystrons (target 110-130 MW)
Energy consumption ~0.8 TWh yearly (target 0.6)
CERN is currently (when) running at 1.2 TWh (~90% in accelerators)

## Slide 16
Optimisations – examples
Design Optimisation:
All projects aim to optimize – most often energy reach, luminosities and cost. Examples from all Higgs factories mentioned above.
Power is becoming at least as important, maybe even compromising ultimate performance for power saving.
Technical Developments:
Technical developments targeting reduced power consumptions at system level high efficiency klystrons and RF systems generally, and super conducting (traditional SC, and HTS in particular) including cryo, and permanents magnets.
Heat recovery:
Already implemented in point 8 for LHC
Tunnel heat recovery study by ARUP in 2022
The designs of CLIC, including key performance parameters as accelerating gradients, pulse lengths, bunch-charges and luminosities, have been optimised for cost and power

## Slide 17: Rings to Main Linac optimisation
BC2 RF new optimisation for cost and power consumption

## Slide 18: Main Linac
Long-range wakefields suppression
Experiment at FACET (SLAC)
Tests of Beam-based orbit correction at FACET

## Slide 19: Running on renewables and when electricity is cheap
Two studies in 2017:
Supply the annual electricity demand of the CLIC-380 by installing local wind and PV generators (this could be e.g. achieved by 330 MW-peak PV and 220 MW-peak wind generators) at a cost of slightly more than 10% of the CLIC 380 GeV cost.
  Study done for 200 MW, in reality only ~110 MW are needed
Self-sufficiency during all times can not be reached but 54% of the time CLIC could run independently from public electricity supply with the portfolio simulated.
Can one run an accelerator as CLIC in a mode where one turn “on” and “off” depending prices (fluctuating with weather, demand, etc) ?
Specify transition times (relatively fast for a LC) and the annual luminosity goal
Significant savings – but the largest saving is the obvious one, not running in the winter.
Flexibility to adjust the power demand is expected to become increasingly important and in demand by energy companies.
More information (link)
Victor Gleim CC-BY-SA-4.0
A real implementation:
A physical power purchase agreement (PPA) is a long-term contract for the supply of electricity at a defined, fixed price at the start and then indexed every year, negotiated between a producer of renewable electricity and a consumer for a defined period (generally 15 to 20 years).
Being considered for CERN initially at limited scale.
Advantages: price, price stability, green, renewable.
Nuclear energy remains very important, on the timescale of a future CERN facility: SMEs
Must be a goal to run future accelerator at CERN primarily on green and more renewable energy with very low carbon footprint. However, energy costs will remain a concern

## Slide 20: Sustainable Construction – some elements
Carbon Cost/Life Cycle Assessment LCA study 2023
Similar CO2 estimates made for the FCC tunnel in the framework of Snowmass.
Assume a small tunnel (~5.6m diameter) and that the equipment in the tunnel has the same carbon footprint as the tunnel itself, 20km acc. incl. tunnel corresponds to 240 kton. This is equivalent to 50-60 TWh of nuclear power.
Two final comments:
The work on-going for the FCC to “integrate” into the areas near CERN, including getting rid of spoil, is obviously also a crucial element on the way to a environmentally integrated collider.
Responsible purchasing – and understanding the impact on our supply chain, costs and potential for changes – will be essentials for future projects (information from E.Cennini)
Talk by B.List (link)

## Slide 21: Cost - I
Machine has been re-costed bottom-up in 2017-18
Methods and costings validated at review on 7 November 2018 – similar to LHC, ILC, CLIC CDR
Technical uncertainty and commercial uncertainty estimated

## Slide 22: Cost - II
Other cost estimates:
Construction:
From 380 GeV to 1.5 TeV, add 5.1 BCHF (drive-beam RF upgrade and lengthening of ML)
From 1.5 TeV to 3 TeV, add 7.3 BCHF (second drive-beam complex and lengthening of ML)
Labour estimate: ~11500 FTE for the 380 GeV construction
Operation:
116 MCHF (see assumptions in box below)
Energy costs

## Slide 23: X-band tests
EU projects: ARIES, I-FAST, new TNA
Structures and components production programme to study designs, operation/conditioning, manufacturing, industry qualification/experience
Industrial questionnaire:
Based on the companies feedback, the preparation phase to the mass production could take about five years. Capacity clearly available.

## Slide 24: Use in smaller linacs (C- and X-band)
SwissFEL: C-band linac
CompactLight Design Study 2018-21 (link)
Compact FEL based on X-band technologies
104 x 2 m-long C-band (5.7 GHz) structures (beam up to 6 GeV at 100 Hz)
Similar μm-level tolerance
Length ~ 800 CLIC structures
Being commissioned
X-band structures from PSI perform well
Photo: SwissFEL/PSI
CERN: eSPS study (3.5 GeV X-band linac)
26 academic and industrial partners: http://www.compactlight.eu/Main/HomePage

## Slide 25
CompactLight Design Studies 2018-21 (right)
INFN 1 GeV linac
Flash RT, at CHUV
“Design Studies” for ICS
AERES, IFAST and TNA project
Overview at LINK
Applications – injector, X-band modules, RF
X-band accelerating modules
Notes: Size of investments

## Slide 26: Beam Facilities using X-band technology
TU Eindhoven: SMART*LIGHT, ICS
Tsinghua: VIGAS, ICS
CERN: AWAKE electron injector
INFN Frascati: EuPRAXIA@SPARC_LAB, accelerator
DESY: SINBAD/ARES, deflector
CHUV/CERN: DEFT, medical accelerator
Daresbury: CLARA, linearizer
Trieste: FERMI energy upgrade
VIGAS

## Slide 27
High Eff. Klystrons
L-band, X-band (for applications/collaborators and test-stands
High Efficiency implementations:
New small X-band klystron, ordered
Large with CPI, work with INFN
L-band two stage, design done, prototyping for FCC
Also important, redesign of damping ring RF system (well underway) – no klystron development foreseen
Drivebeam klystron: The klystron efficiency (circles) and the peak RF power (squares) simulated for the CLIC TS MBK (solid lines) and measured for the Canon MBK E37503 (dashed lines) vs total beam power.
Publication: https://ieeexplore.ieee.org/document/9115885

## Slide 28
X-band linac
I-FAST – CompactLight Structure
10 MW, 1.5 μs @1 KHz
50 MW, 1.5 μs @100 Hz
High-energy module

## Slide 29
Accelerating structure RF operating parameters
Courtesy M. Diomede
Two structures being manufactured

## Slide 30: CLIC Detector
 High-performing detector optimized for CLIC beam environment  Full GEANT-based simulation, including beam-induced backgrounds, available for optimization and physics studies  Mature reconstruction chain allows detailed performance characterisation – e.g. for tracking: effect of busy environment; displaced track reconstruction
Software framework:
 Originally in iLCSoft, the simulation/reconstruction is now fully embedded in the Key4HEP ecosystem –> a common target for all future collider options – existing reconstruction algorithms “wrappered” for the new framework
NIM A956 (2020) 163304
CLICdet:

## Slide 31: Detector R&D for CLICdet
Calorimeter R&D => within CALICE and FCAL
Silicon vertex/tracker R&D:
Working Group within CLICdp and strong collaboration with DESY + AIDAinnova
Now integrated in the CERN EP detector R&D programme
A few examples:
 Successful sensor+ASIC bonding using Anisotropic Conductive Film (ACF), e.g., with CLICpix2, Timepix3 ASICs.
ACF now also used for module integration with monolithic sensors. https://agenda.linearcollider.org/event/9211/contributions/49469/
ACF conductor ball
Detailed simulations, Allpix2 transient Monte Carlo combined with electrostatic 3D TCAD.
Beam tests at DESY, e.g. 5.8 ns CLICTD time resolution achieved https://agenda.linearcollider.org/event/9211/contributions/49443/
CLICTD monolithic tracking sensor:
 Development of bump bonding process for CLICpix2 hybrid assemblies with 25 μm pitch https://cds.cern.ch/record/2766510
 Exploring sub-nanosecond pixel timing with ATTRACT FASTPIX demonstrator in 180 nm monolithic CMOS https://agenda.linearcollider.org/event/9211/contributions/49445/
 Now performing qualification of modified 65 nm CMOS imaging process for further improved performance
Hybrid assemblies:
Monolithic sensors:

## Slide 32: Physics Potential recent highlights 1: Initial energy stage
Higgs coupling sensitivity:
 Sensitivities under different integrated luminosity scenarios to complement accelerator luminosity studies
https://arxiv.org/abs/2001.05278 other sensitivities from Briefing Book https://arxiv.org/abs/1910.11775
Increased integrated luminosity at 380 GeV (4ab–1)
Baseline: 380 GeV (1ab–1) + 1.5 TeV
Top-quark threshold scan  Optimisation of scan points including beam spectrum; here optimising on mass and Yukawa coupling.  Expected top-quark mass precision of 25MeV can be improved by 25% without losing precision on width or Yukawa. https://arxiv.org/abs/2103.00522
 Ongoing studies on Higgs and top-quark precision physics potential

## Slide 33: Physics Potential recent highlights 2: Multi-TeV stages
 Ongoing studies on new physics searches
Dark matter using mono-photon signature at 3TeV, e+e- -> XXg  New study using ratio of electron beam polarisations to reduce systematics  Exclusions for simplified model with mediator Y and DM particle X  For benchmark mediator of 3.5TeV, photon energy spectrum discriminates different DM mediators & allows 1TeV DM particle mass measurement to ~1% https://arxiv.org/abs/2103.06006
CLIC 3TeV, geY=1
Search for heavy neutrinos  e+e- -> Nn -> qqln signature allows full reconstruction of N  BDT separates signal from SM; beam backgrounds included.  cross-section limits converted to mass (mN) coupling (VIN) plane
LHC analysis: [1812.08750], different assumption VeN = VmN ≠ VtN = 0

## Slide 34: Summary and thanks
CLIC studies focused on core technologies, X-band and nanobeam, for next ESU, well underway.
Keep focus on both 380 GeV and multi-TeV performance and R&D
Greatly helped by studies of smaller linacs and systems using X-band technology
Detector and physics studies continue at lower pace, also in many areas integrated or connected with ”Higgs-factory” studies, and wider Detector R&D efforts
Thanks to Steinar Stapnes and to many CLIC accelerator colleagues for slides and inputs, and to Aidan Robson for the CLICdp slides

## Slide 35: Luminosity of future colliders
Per IP, from Snowmass

## Slide 36: Personnel estimate and cost – and Higgs factories
One FTEy estimated to 200kUS$

## Slide 37: Higher energy projects – and costs

## Slide 38: Timelines in Snowmass Energy Frontier summary
Comments:
Timelines are technologically limited – except the CERN projects that are linked to completion of the HL-LHC
CEPC and ILC schedules are mature, but the projects need to pass approval processes in the near future to maintain these schedules
CCC and MC are less well defined but R&D and project development on the shown timescales is reasonable, CCC can also upgrade ILC
A clear wish to develop options for future US-sited EF colliders
US put emphasis on “fast” access to a Higgs factory
From Meenakshi Narain EF summary Snowmass

## Slide 39: Pushing the acc. technology – R&D
CLIC core studies:
Normal conducting accelerating structures are limited in gradient by three main effects (setting aside input power):
Field emission
Vacuum arcing (breakdown)
Fatigue due to pulsed surface heating
Studying these processes gives important input into:
RF design – Optimizing structures also coupled with beam dynamics
Technology – Material choice, process optimization
Operation – Conditioning and recovery from breakdown
Designs for CLIC steadily improving, but also RFQ, Muon collider, XFEL, ICS, etc
Important experimental support
Multi-TeV energies:
High gradient, high wall-plug to beam efficiency, nanobeam parameters increasingly demanding