## Slide 1: CEPC radiation protection (RP) study
Guangyi Tang on behalf of CEPC RP Group
IAS Program on High Energy Physics, 2023/2/14

## Slide 2: outline
Introduction
Synchrotron radiation shielding
Radionuclide production estimation
Collider ring dump design
Linac hot spots and beam losses shielding
Summary and outlook
Simulation Using FLUKA, Flair.

## Slide 3: RP concepts
Source:
  beam, target (hot spot), synchrotron radiation, ...
Radiations may damage equipment and health.
How to estimate the damage
  For material: absorbed dose, unit: Gray (Gy)
  For health: ambient dose equivalent, unit: Sievert (Sv)
How to reduce radiation damage:
  Shorten exposure time
  Increase distance
  Shield
    High Z: iron, lead, tungsten, ...
    Hydrogen-containing: water, paraffin wax, ...

## Slide 4: Radiological impact
Main consideration aspects
Impact factors | Characteristics
Synchrotron radiation | Radiation damage to magnets coils; Over heat load to ventilation system; Formation of ozone and nitrogen oxides in the air; Slightly activation to the material around;
Random beam loss | Cause secondary radiation inside the tunnel; Determine the bulk shielding thickness;
Hot spots | MDI, Collimation locations, collider/linac dumps, injection/extraction points;
Radiological impact on environment | Dose from stray radiation emitted during machine running Radionuclides in the cooling water, underground water, tunnel air, soil. Radioactivity analysis for the solid components and waste
Machine protection | Active/passive protection

## Slide 5: outline
Introduction
Synchrotron radiation shielding
Radionuclide productions
Collider ring dump system
Linac hot spots and beam losses
Summary and outlook

## Slide 6: Simulation setup
Tunnel geometry
Length: 100m;
  3 dipoles;
  2 quadrupoles;
  2 sextupoles;

## Slide 7: Simulation setup
Dipole
insulations, coils, leads
(epoxy resin)
Insulations is added in the model. Both beam-pipes are made of copper.
In the cross-section, area of lead:
Drift chamber
area of lead:

## Slide 8: Simulation setup
Quadrupole
insulations, coils, leads
(epoxy resin)
area of lead :
Sextupole
area of lead :

## Slide 9: booster
dipole ->drift chamber ->quadrupole -> sextupole ->drift chamber ->dipole …
Magnets

## Slide 10: Parameters: 50MW
Collider
The ramping simulation is more critical than reality.
  Overestimate dose to booster
Booster
Ramping simulation: example @Higgs
 | Higgs | WW | Z | ttbar
Beam energy/GeV | 120 | 80 | 45.5 | 180
Ne/bunch/ | 14 | 13.5 | 14 | 20
Number of bunches | 415 | 2162 | 19918 | 58
Number of photons/114m | 4.7e18 | 1.6e19 | 8.4e19 | 1.4e18
 | Higgs | WW | Z | ttbar
Beam energy/GeV | 120 | 80 | 45.5 | 180
 | 14 | 13.5 | 14 | 20
Number of bunches | 415 | 2162 | 19918 | 58
Number of photons/114m | 4.7e18 | 1.6e19 | 8.4e19 | 1.4e18
 | Higgs | WW | Z | ttbar
Current(mA) | 1 | 2.69 | 14.4 | 0.12
Injection duration(s) | 32.8 | 39.3 | 134.7 | 30
Injection interval(s) | 38 | 155 | 153.5 | 65

## Slide 11: Dose to insulations
Dose values are equal in middle of magnet, not in both ends of magnet.
“Hot spots” in insulation because:
  The shielding between magnets are not designed well.
  SR hits the iron close to beam pipe and bypasses lead.
Hot spots shielding will be considered in next stage.
Dose in uniform regions are summarized in the following pages.

## Slide 12: Dose vs lead thickness: 50MW
While running @Higgs/Z/WW (13 years),
  Possible to reduce 2cm lead if no ttbar run;
Lead thickness is constrained by the operation schedule.
While running another 5 years @ttbar ,
  2.5cm lead is needed for dipole and quadrupole, more for sextupole.

## Slide 13: dose to booster insulation: 50MW
While running @Higgs/Z/WW (13 years),
The dose to dipole and quadrupole is slightly higher than upper limit based on our simulation scheme.
Pay attention to sextupoles. We will simulate more precisely, with accurate time scheme and beam energy.
While running another 5 years @ttbar ,

## Slide 14: radionuclides simulation
Beam losses & SR photon of energy >6MeV
Simulate two critical cases:
  SR @ttbar and beam losses @Z
FLUKA options
Wall material:
  Case1: water as wall
  Case2: rock as wall
 |  | Higgs | WW | Z | ttbar
Beam energy/GeV |  | 120 | 80 | 45.5 | 182.5
Ne/bunch/ |  | 14 | 13.5 | 14 | 20
Number of bunches | 50MW | 415 | 2162 | 19918 | 58
Number of SR photons >6MeV | 50MW | 1.4e10 | 1e-7 | negligible | 1.3e15
Life time | 50MW | 0.33 | 0.91 | 1.33 | 0.30
Beam losses/114m | 50MW | 5.5e7 | 1.0e8 | 6.7e8 | 1.2e7
 |  | Higgs | WW | Z | ttbar
Beam energy/GeV |  | 120 | 80 | 45.5 | 182.5
 |  | 14 | 13.5 | 14 | 20
Number of bunches | 50MW | 415 | 2162 | 19918 | 58
Number of SR photons >6MeV | 50MW | 1.4e10 | 1e-7 | negligible | 1.3e15
Life time | 50MW | 0.33 | 0.91 | 1.33 | 0.30
Beam losses/114m | 50MW | 5.5e7 | 1.0e8 | 6.7e8 | 1.2e7

## Slide 15: Soil/rock
 |  | Soil | components of different rocks
density |  | 1.6g/cm^3 | 1.2~3.3g/cm^3
Major element (wt%) | C | 1.0 | ---
 | N | 0.12 | ---
 | O | 34 | 30~70
 | Na | 0.50 | 0.1~2.9
 | Mg | 0.52 | 0.4~3.7
 | Al | 8.0 | 3.5~9.7
 | Si | 40 | 26~39
 | P | --- | 0.02~0.16
 | K | 2.36 | 1.8~3.7
 | Ca | 2.26 | 0.2~4.8
 | Ti | 1.0 | 0.09~0.8
 | Mn | 0.24 | 0.02~0.12
 | Fe | 9.6 | 0.8~6.3
In previous study, use soil as tunnel wall.
Now use average components of rocks in each site candidate.
Simulate productions of residual nuclei after one year running in:
  Cooling water
  Air in tunnel
  Water outside tunnel
  Rock (leachable isotopes)
Compared with Chinese mandatory standard GB18871.

## Slide 16: Radionuclides production
 |  | Half-life | Cooling water | 
 |  |  | Specific activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | O15 | 122s | 2.44 | 10
 | C14 | 5700a | 3.5e-7 | 23
 | Be7 | 53d | 1.3e-2 | 34
 | H3 | 12a | 2.3e-6 | 22
SR @ttbar | None |  |  | 
 |  | Half-life | Air in tunnel | 
 |  |  | Specific activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | O15 | 122s | 2.7e-4 | 52
 | C14 | 5700a | 7.7e-7 | 1
 | Be7 | 53d | 1.1e-5 | 57
 | H3 | 12a | 3.5e-9 | 32
 | P32 | 14d | --- | ---
 | P33 | 25d | 1.9e-8 | 100
 | Cl36 | 3e5a | --- | ---
 | Cl38 | 37m | --- | ---
 | Ar37 | 35d | 6.1e-9 | 59
 | Ar41 | 2h | 1.4e-3 | 12
SR @ttbar | C14 | 5700a | 6.5e-6 | 2
 | Ar41 | 2h | 1.5e-2 | 20
Densities of Long half-life isotopes are lower than mandatory standard, GB18871.

## Slide 17: Radionuclides production
Only leachable isotopes are listed:
  3H, 22Na, 45Ca, 54Mn
 |  | Half-life | Water wall | 
 |  |  | Specific activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | O15 | 122s | 2e-3 | 2
 | C14 | 5700a | 5e-10 | 4
 | Be7 | 53d | 3e-5 | 5
 | H3 | 12a | 6e-9 | 3
 | F18 | 2h | 5e-6 | 52
SR @ttbar | C14 | 5700a | 2e-12 | 99
 | H3 | 12a | 1e-10 | 71
 |  | Half-life | Rock wall | 
 |  |  | Specific activity/GB18871 | Stat. error (%)
Beam losses @Z-pole | Mn54 | 312d | 6.94E-04 | 1.8
 | Ca45 | 163d | 5.49E-06 | 0.3
 | Na22 | 2.6y | 7.20E-04 | 1.4
 | H3 | 12a | 5.90E-09 | 0.9
SR @ttbar | H3 | 12a | 1e-10 | 71
Densities of Long half-life isotopes are lower than mandatory standard.
Should investigate if radionuclides would transport to drinking water.

## Slide 18: Production of toxic gases
Saturated concentrations of ozone and oxides of nitrogen. [Hoefert, 1986]
Concentration limit
  O3: 160 ug/m^3; NO2: 40 ug/m^3.
  Smaller than limits in CEPC cases.
 | Number of SR photons/ 114m | Deposited energy from photon | O3 mass [ug/m^3]
Higgs | 4.7e18 | 2.8e-8 | 1.8e-6
WW | 1.6e19 | 1.8e-9 | 1.5e-6
Z | 8.4e19 | 6.0e-9 | 9.7e-7
ttbar | 1.4e18 | 7.6e-8 | 1.1e-6

## Slide 19: outline
Introduction
Synchrotron radiation shielding
Radionuclide productions
Collider ring dump system
Linac hot spots and beam losses
Summary and outlook

## Slide 20: Collider dump
A set of kicker magnets is used to dilute the beam horizontally and vertically.
The length of transfer tunnel is about 100m The volume of hall will be determined after the design of the equipment installation.
The area of bunch distribution at dump entrance is optimized to be 6cm x 6cm (@Z mode)
Dilution kicker requirement:
Vertical kicker should periodic oscillate 12.5 times in 300 us
From Xiaohao Cui
 |  | Extraction kicker | Septum | Dilution kickers
Length (m) |  | 2 | 20 | 10
Magnetic flux density (Gauss) | Z | 280 | 2600 | 40 (Max.)
 | WW | 493 | 4700 | 
 | Higgs | 740 | 7000 | 
 | ttbar | 1110 | 10500 | 

## Slide 21: Bunch distribution: 50MW
The bunch distributions at the dump entrance is simulated.
  Bunch size:
Simulate energy deposition in dump core.
Find the maximum energy deposition. And calculate maximum temperature rise.
Optimize dump dimensions
From Xiaohao Cui
Higgs
Higgs
WW
Z pole
ttbar
Dilution kicker requirement:
2. Horizontal kicker should reduce step by step from max. to min. in 300 us

## Slide 22: Max. temperature rise: 50MW
Example: graphite core
Max. temperature rise is smaller than graphite melting point. Inert gas will be used to stop fire and chemical reaction.
Dimension (graphite + Iron): R~2.3m, L~8m; constrained by the condition that dose-eq is smaller than 5.5mSv/h.
Temperature rise @Z mode
Temperature rise @WW mode
 | Higgs | WW | Z | ttbar
Beam energy/GeV | 120 | 80 | 45.5 | 180
Ne/bunch/ | 14 | 13.5 | 14 | 20
Bunch number (50MW) | 415 | 2162 | 19918 | 58
Max. temperature rise |  |  |  | 
Max. temperature rise by one bunch |  |  |  | 
 | Higgs | WW | Z | ttbar
Beam energy/GeV | 120 | 80 | 45.5 | 180
 | 14 | 13.5 | 14 | 20
Bunch number (50MW) | 415 | 2162 | 19918 | 58
Max. temperature rise |  |  |  | 
Max. temperature rise by one bunch |  |  |  | 

## Slide 23: Radionuclides production in Dump hall
A dumping hall geometry in the below.
Assume dumping beam one time per day
The radionuclide production is simulated. Meet Chinese mandatory standard.
 | Half-life | Air in dump hall | 
 |  | Specific activity/GB18871 | Stat. error (%)
C14 | 5700a | 3.1e-9 | 7
H3 | 12a | 1.5e-11 | 49
Ar41 | 2h | 5.6e-10 | 33
 | Half-life | Concrete wall | 
 |  | Specific activity/GB18871 | Stat. error (%)
Ca47 | 4.5d | 4.9e-9 | 100
Ca45 | 163d | 3.1e-9 | 17
Na24 | 15h | 1.0e-4 | 5
Na22 | 2.6y | 1.4e-8 | 100
H3 | 12a | 1.6e-13 | 56

## Slide 24: Response time
Abort request:
  Beam loss monitors
  Synchrotron oscillation phase monitor
  Hardware components
  Manual abort
Time interval
  Device request -> local control
  Local control -> central control
  Central control -> dump system
  Extract all beam.
Collider dump response time ~ 1ms.
SuperKEKB Design Report

## Slide 25: More about dump
Abort beam in booster and collider
  For normal operations and machine tuning
Study feasibility to build extraction line from booster to dump.
Build in the straight sections. One for electron beam and one for positron beam.
Will study reliability (or alternative design).
Need absorber to protect machine elements from incorrect dumping.
Response time ~ 1ms.
Need collimators to deal with beam losses faster than 1ms.
  fault cases.
Krainer, A. et.al., EPJ Techn Instrum 9, 3 (2022)
LHC design report Ch.17

## Slide 26: outline
Introduction
Synchrotron radiation shielding
Radionuclide productions
Collider ring dump system
Linac hot spots and beam losses
Summary and outlook

## Slide 27: CEPC linac
Length: 1601.3m; 7 dumps and 1 collimator;
Dump1
Dump2
Dump3 + Collimator
Dump4
Dump5
Dump6 + dump7

## Slide 28: Linac beam losses assumptions
Angle of incidence 10mrad
Not consider EBTL & DR beam losses.
Position | Length | Beam energy | Number of bunches [s-1] | Beam loss/bunch [nC] | Number of particles [/s]
FAS | 100m | 300MeV | 200 | 0.5 | 62.5
Positron target | 15mm | 4GeV |  | 10 | 1250
PSPAS | 15m | 5~200MeV |  | 10 | 1250
SAS | 3m | 300MeV |  | 2 | 250
 | 30m | 600MeV |  | 0.2 | 25
TAS | 1163m | 1.1~30GeV |  | 0.1 | 12.5
Position | Length | Beam energy | Number of bunches [s-1] | Beam loss/bunch [nC] | 
FAS | 100m | 300MeV | 200 | 0.5 | 62.5
Positron target | 15mm | 4GeV |  | 10 | 1250
PSPAS | 15m | 5~200MeV |  | 10 | 1250
SAS | 3m | 300MeV |  | 2 | 250
 | 30m | 600MeV |  | 0.2 | 25
TAS | 1163m | 1.1~30GeV |  | 0.1 | 12.5

## Slide 29: Simulation setup
Beam pipes and concrete wall
Top/side view
Dose-eq distribution example: SAS
Thickness of Shielding wall according to upper limit 5.5mSv/h (left/right/bottom) or 2.5uSv/h(top).
Wall thickness | FAS | SAS | TAS
Left | 0.3m | 1.9m | 0.3m
Right | 0.2m | 1.9m | 0.3m
Bottom | 0.3m | 2.1m | 0.3m
Top | 1.3m | 4.1m | 2.0m

## Slide 30: Local shield design for hot spots
Carbon and iron is selected as the absorber material, surrounded by the polyethylene as local shielding.
5.5mSv/h is set as upper limit to decide the thickness of local shielding.
The thickness of shielding will be optimized combined with Linac tunnel geometry in the next stage.
Absorber geometry and local shielding:
Size for carbon and iron for different beam energy, adopt from other projects, is suitable but haven't been optimized.
Local size selection (20GeV dump as example):
2D map of dose distribution is obtained using FLUKA, the dose rate alone Z or R axis was averaged by 1x1cm^2 area, the shielding size can be selected by setting dose rate limit.
Preliminary design results for different beam energy analysis station:
Radiation level nearby each energy analysis station was figured out, also specify a roughly space for the future local shielding.
Beam energy | R/m | Length/m
60MeV | 0.7 | 1
4GeV | 1.2 | 2.6
250MeV | 0.55 | 1
1.1GeV | 0.85 | 1.7
6GeV | 1 | 2.5
30GeV | 1.3 | 3.8

## Slide 31: Summary
Have studied:
  lead shielding design,
  radionuclides productions estimation,
  Collider dump design,
  Linac hot spots and bulk shielding
Go on:
  Shielding design for experiment hall/RF hall/DR/transport line
  Reliability study for dump.
  Machine protection: fault cases.
Thank you

## Slide 32: backup