## Slide 1
Yuhui Li
Institute of High Energy Physics
Sep. 21, 2023
IAS Program on High Energy Physics (IAS-HEP 2024)
Hong Kong, China, Jan. 8-26 (2024)
CEPC Efforts Towards a Green Collider
Yuhui Li
On behalf of CEPC accelerator team

## Slide 2: Content
Brief introduction to CEPC and other accelerator facilities at IHEP
  CPEC background information
  Machine layout, Research status, energy consumption, …
  BEPCII and HEPS at IHEP
Key technology R&D for a green collider
  High-Q SRF system; High efficiency klystron; Magnets and prototypes
  Plasma acceleration; waste-heat in cooling water; solar panel and clean energy
  Novel concepts
Summary

## Slide 3: A brief introduction to CEPC
The CEPC aims to start operation in 2030’s, as a Higgs (Z / W) factory in China.
To run at ~ 240 GeV, above the ZH production threshold for ≥1 M Higgs; at the Z pole for ~Tera Z; at the W+W- pair and then pair production thresholds.
Higgs, EW, flavor physics & QCD, probes of physics BSM.
Possible pp collider (SppC) of ~ 50–100 TeV in the far future.
Higgs (Z) factory
Ring length ~ 100 km
IP 1
IP 2

## Slide 4: CEPC TDR design
4
 | Higgs | W | Z | ttbar
Number of IPs | 2 |  |  | 
Circumference [km] | 100.0 |  |  | 
SR power per beam [MW] | 50 |  |  | 
Energy [GeV] | 120 | 80 | 45.5 | 180
Bunch number | 415 | 2161 | 19918 | 59
Emittance (x/y) [nm/pm] | 0.64/1.3 | 0.87/1.7 | 0.27/1.4 | 1.4/4.7
Beam size at IP (x/y) [um/nm] | 15/36 | 13/42 | 6/35 | 39/113
Bunch length (SR/total) [mm] | 2.3/3.9 | 2.5/4.9 | 2.5/8.7 | 2.2/2.9
Beam-beam parameters (x/y) | 0.015/0.11 | 0.012/0.113 | 0.004/0.127 | 0.071/0.1
RF frequency [MHz] | 650 |  |  | 
Luminosity per IP[1034/cm2/s] | 8.3 | 27 | 192 | 0.83
Circular collider: Higher luminosity than a linear collider
100km circumference: Optimum total cost, good also for SppC
Shared tunnel: Accommodate CEPC booster &collider and SppC
Switchable operation: Higgs, W/Z, top
Common tunnel for booster/collider & SppC
Compatible Operation for Higgs W and Z
Main Parameters: High luminosity as a Higgs Factory
Luminosity comparison

## Slide 5: CEPC TDR international review and formal release
Technical review
Cost review
基建国际评审
IAC meeting
Civil construction review
International TDR reviews
2023 June 12-16 ：technical review； June 26: civil cost domestic review； September 11-15 ：cost review
2023 October: CEPC International Advisory Committee meeting
CEPC TDR -Accelerator formally released on 25. Dec. 2023
arXiv: 2312.14363

## Slide 6: Energy consumption breakdown @ 50MW SR power
The total electricity consumption is 340MW for the operation of Higgs, SR power 50MW
The major energy consumer systems:
  RF power (177MW) Magnet (58MW)  Cryogenics (11 MW)
  Auxiliary power:
    Instrumentation(2.2) + Radiation Protection(0.4) + Control(1.8) + Experimental device (4) + Utility(54.5) + General Service(19.9) = 78 MW
CEPC-TDR p967
The total power at other operation modes are listed in TDR

## Slide 7: Energy consumption breakdown @ 30MW SR power
The total electricity consumption is 262MW for the operation of SR power 30MW
The major energy consumer systems:
  RF power (109 MW) Magnet (58 MW)  Cryogenics (11.6 MW)
  Auxiliary power:
    Instrumentation(2.2) + Radiation Protection (0.4) + Control (1.8) + Experimental device (4) +Utility(44.6) +General Service(19.9) = 73 MW
CEPC-TDR p965

## Slide 8: Operation of BEPCII and performance enhancement
BEPCII
- Upgrade project of BEPC, operated since 2009
- A double-ring factory-like collider
- Collider & SR operation modes
BEPCII
BESIII
BSRF

## Slide 9: HEPS construction
Advanced 4th generation light source, promoting multi-disciplinary researches
Accumulate conventional key technologies for CEPC
- Magnet - Vacuum - Power supply - Beam instrumentation
- Alignment - Control - Mechanical system - Linac complex
- RF - Cryogenics - Utilities

## Slide 10: Motivation and obligations to pursue a green machine
China national dual-carbon strategy: CO2 emission peak before 2030 and carbon neutrality before 2060)
The modern high-performance accelerator complex consumes a significant amount of energy: LHC, ILC, CEPC…
LHC 照片
功率 200MW
HEPS 照片
功率 ？MW
BEPCII 照片
功率 ？MW
上海光源 照片
功率 ？？W
LHC
200MW
Spring 8
25MW
BEPCII
7MW
SSRF
10MW
SHINE
20MW
ESS
33.75MW
EuropeanXFEL
17.76MW
HEPS
30MW

## Slide 11: SRF cavity using Mit-T baking
Mid-T baking (O-doping) vs. N-doping: higher Eacc & Q, simple process, less EP
Excellent results obtained, exceeding requirements of CEPC, SHINE, LCLS-II, etc.
ILC-type cavities with higher Eacc is also under development

## Slide 12: Mid-temp baking SRF cavity test results
6.4E10@30MV/m, 2.3E10@41.6MV/m
Mid-T baking applied to 1.3GHz/650MHz cavities, resulting in High Q SRF cavity that meets the CEPC specification;
Completed SRF modules for both 1.3GHz and 650MHz cavities were assembled;

## Slide 13: SRF cryo-module horizontal test results
650 MHz test cryomodules including cavities, couplers, HOM absorbers, tuners..., was built and tested OK
A full eight 1.3 GHz 9-cell cavities with input couplers, tuners, SC magnet, BPM, cryostat, module cart, feed/end-cap, volve-box … was built and tested OK
Parameters | Horizontal test results | CEPC Booster Higgs | LCLS-II, SHINE | LCLS-II-HE
Average Q0 @ 21.8 MV/m | 3.6×1010 | 3.0×1010 @ 21.8 MV/m | 2.7×1010 @ 16 MV/m | 2.7×1010 @ 20.8 MV/m
Average CW Eacc (MV/m) | 23.1 |  |  | 
650MHz 2-cell
166MHz QW
1.3GHz 9-cell
1.3GHz 9-cell

## Slide 14: High Q SRF significance for a green machine
The SRF system, along with its cryogenic auxiliaries, is one of the major electricity consumers. High Q-factor SRF cryo-modules effectively reduce the heat load, resulting in lower energy consumption
Power consumption with respect to the cavity Q-factor
CEPC 50MW Higgs operation
The CEPC 1.3GHz SRF cavities adopt the mid-temp baking technology, which enhances the Q factor by 5 times compared to the EP technique.
Using the high-Q SRF in CEPC may reduce the operational power by 10MW, which could result in an electricity savings of approximately 60M kWh per year.

## Slide 15: Endeavors for a high-efficient klystron
Chart: 
| 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 576 | 460.8 | 384 | 329.1429 | 288 | 256 | 230.4
CEPC at 800 RMB/MWh and 6000 hours/year
Excessive electricity bill, M RMB
1 year
Efficiency, %
90 M RMB
130M RMB
2020
2021
2022
Save Money
Efficiency impact on operation cost (Only considering operation efficiency of 650MHz klystrons)
Klystron No. 1
Efficiency 62%
(2020)
Klystron No. 2
aiming at efficiency 77%
Klystron No. 3
Efficiency 80.5%

## Slide 16: Research status of the klystron

## Slide 17: Energy recovery by decelerating the used beams
CPI (USA) has developed multiple models of multi-stages decelerating collector klystrons
Many research institutes in Japan, UK and so on has conducted similar efforts.
CEPC first prototype H.V. 81.5kV Cur. 15.3A |  | 
Coll. Qty | Coll. Eff. | Kly. Eff.
0 | 0.00% | 58.3%
1 | 31.4% | 71.4%
2 | 50.9% | 79.5%
3 | 59.2% | 83.0%
4 | 64.3% | 85.1%
5 | 67.9% | 86.6%
CEPC high efficiency klystron prototype H.V. 113kV Cur. 9.5A |  | 
Coll. Qty | Coll. Eff. | Kly. Eff.
0 | 0.0% | 68.0%
1 | 29.8% | 77.5%
2 | 47.7% | 83.3%
3 | 55.6% | 85.8%
4 | 61.4% | 87.7%
5 | 65.2% | 88.9%
Chart: Klystron efficiency comparison
| 0 | 1 | 2 | 3 | 4 | 5
81.5整管效率 | 58.3 | 71.4 | 79.5 | 83 | 85.1 | 86.6
113kV整管效率 | 68 | 77.5 | 83.3 | 85.8 | 87.7 | 88.9
CEPC will carry out the researches as well
  Theoretical studies of efficiency v.s. collection stages for normal and high-efficient klystrons
The electric field distribution inside the three-stage depressed collector

## Slide 18
Dual aperture magnets prototypes for the CEPC Collider
  Following the proposal of dual-aperture magnets with common coils from CERN, the CEPC team has developed prototypes for dipoles and quadrupoles. Both prototypes meet the specified requirements.
  Large amount of dual-aperture magnets will be used in CEPC: 7574 sets of magnets cover about 84.67 km
  Compare to the conventional separated-aperture magnets, the dual-aperture magnets will save 50% electricity, roughly 40 MW
Combine-function dipole- sextuple design for the CEPC Booster, eliminating a lot of sextuples and resducing their energy consumption
Novel design and prototypes for the room-temperature magnet

## Slide 19: HEPS employs permanent dipole magnets
20
Longitudinal-gradient dipole takes use of the permanent magnet at HEPS, which consumes zero electricity
Equivalent single excitation energy consumption of about 1.62kW.
Equivalent cooling, power efficiency additional energy consumption of about 1.3kW
240 magnets in the whole ring
Annual running time of 8000 hours
Annual saving electricity about 5.6 million kWh

## Slide 20: R&D for Halbach type quadrupole with tunable field
Dual-rings magnets enable field tenability in a large range
Challenges:
  Movement synchronizing for ceaselessly field cancellation
  Shimming technology for good field quality at all operation modes
  Radiation shielding
The CEPC uses permanent magnets (dipole, quadruple) for
  Damping ring  Transport line

## Slide 21: Plasma wake field acceleration
High gradient: ~10-100GV/m, ~1000times higher than conventional Acc.
High energy conversion rate
High repetition rate possibility
Focus on PWFA acceleration
Driver beam
Trailer beam
Plasma wake field
1GeV accelerator in hand
Conventional linac

## Slide 22
Conventional collider Vs. plasma collider
Size:
  LWFA LC << PWFA LC << LC
  But NOT 1000 times smaller due to beam deliver section
Power consumption
  Plasma LC < LC, smaller size means smaller vacuum, magnet, SC ……
  PWFA LC < LWFA LC, due to higher ηwall plugdriver and ηdrivertrailer
  Plasma acclerator estimation is not as accurate as conventional LC, and should be overestimated / based on future technology
Construction
  Plasma accelerator cost is in a big range due to technique uncertainty
  May not be ready in the next 20 yrs
59 km
50 km
1.3 km
14 km

## Slide 23
Single stage plasma acceleration efficiency
Hosing instability
High rep. rate plasma source and lasers (for LWFA)
Right now < 10 or even < 1
AC  Driver, Driver  Wakefield, Wakefield  Trailer
50-60% for PWFA
~ 10% for LWFA
50% (exp.)
90% (sim.)
40% (exp.)
90% (sim.)

## Slide 24: CEPC drives PWFA study @ IHEP
  Backup solution for CEPC linac, conceptual design based on simulation shows that the scheme is feasible
  Main linac: 10GeV S-band
  L-band (10+ nC) and S-band (≤5nC) RF guns
  Compression and combination
  Different e+ acc. scheme
  e+ PWFA need to be cascaded
  e- PWFA with TR ~ 3.5
  Conventional technology as the baseline design:
  PWFA backup design:

## Slide 25: Test facility to be built at BEPCII
束流中心
2.5 GeV e-/e+ beamline + PW-level high performance laser system
Plasma Acc. Experimental Hall

## Slide 26: HEPS Waste Heat Sources Utilization
A heat recovery chiller unit is used to recover waste heat.
HEPS installs four heat recovery chiller units: 2 * 5500 kW and 2 * 2800 kW. In the normal operation, maximum of about 13 MW waste heat can be recovered in the form of 42°C water
The heat load of HEPS is about 10,413 kW in winter and 4,117 kW in summer. When the system is running, the recovered heat source can fully replace municipal heat sources
Installation the heat recovery condenser

## Slide 27: Advanced heat-pump technology applications for CEPC
As the rapid development of photovoltaic and heat storage technology, AHP can be served the new possible scheme to recover the waste heat.

## Slide 28: Solar panels on-top of the roof at HEPS
Photovoltaic (PV) power generation systems are installed on the roofs of HEPS building complex
Adopting 465Wp/550Wp monocrystalline silicon photovoltaic modules, the first phase has a total installed capacity of 9,950.92 kWp. The average annual power generation is expected to be 10.30766 million kWh, and the equivalent average annual utilization hours will be 10,035.85h.
Phase I was connected to the grid on 2023.10.30.
The second phase is planned to lay PV modules on the ground inside the storage ring with an installed capacity of 7314.45kWp.

## Slide 30
Full recovery/recycling of helium for sustainability operation
Helium gas is a non-renewable resource. Therefore, helium recycling is essential for sustainable operations.
IHEP has implemented a helium gas recovery system, specifically the liquid helium recovery and purification system of BEPCII(ADS)/PAPS, many years ago. This system has been operating stably.
Recovery capacity ≥210NM³/h; purification capacity ≥105NM³/h;
PAPS helium purification
and recycling system
ADS helium purification
and recycling system
BEPCII cryogenic system

## Slide 31: R&D for Iron-based HTS magnets
Iron-based superconducting materials are very promising for high-field magnets
  Isotropic
  May go to very high field
  Raw materials are cheap
  Metal, easy for production
Technology spin-off can be enormous
Major R&D goals
  High Jc: > 1000A/mm2@4.2K
  Long cable: > 1000 m
  Low cost: < 5$/kAm
A collaboration formed in 2016 by IHEP, IOP, IOEE, SJTU, etc., and supported by CAS
Chart: Applied Magnetic Field (T)
| 0 | 5 | 15 | 20 | 25 | 30
REBCO: B ∥ Tape plane | 4144.6766 | 3507.9375 | 3148.3332 | 2909.0554 | 2090.4933 | 1888.9952
REBCO: B ⊥ Tape plane, 45 μm sub | 5478.1345 | 5053.3515 | 4372.0346 | 3812.2534 | 3348.8068 | 3146.724 | 2964.7726 | 2801.365 | 2663.2305 | 2530.35 | 2415.161 | 2307.3222 | 2215.5971 | 2121.427 | 2046.7953 | 1970.1838 | 1905.1216 | 1841.6283 | 1784.4676 | 1729.8653 | 1682.3664 | 1631.1403 | 1591.3007
REBCO: B ⊥ Tape plane | 4144.6766 | 1445.8386 | 975.0997 | 767.7508 | 655.6687 | 571.6114 | 526.7777 | 481.944 | 442.7183 | 428.1462 | 403.4904 | 386.6773 | 364.2626 | 341.8457 | 328.3952 | 319.4289 | 318.3073
Bi-2212: OST NHMFL 50 bar OP | 1243.4169 | 1159.7904 | 1097.571 | 1051.5861 | 1014.8275 | 981 | 955.0755 | 928.7776 | 905.6283 | 884.9933 | 865.478 | 846.7181 | 827.3047
Nb₃Sn: Internal Sn RRP® | 1754.8557 | 1454.9349 | 1190.9814 | 1072.6374 | 957.7741 | 855.0933 | 757.6336 | 268.0143 | 190.8587 | 118.9241 | 65.5533 | 28.3097
Nb₃Sn: High Sn Bronze | 166.6431 | 137.8146 | 111.0954 | 84.3762 | 60.8212 | 40.0788 | 19.3362 | 8.0861
Nb-Ti: LHC 4.2 K | 5106.8846 | 4054.1538 | 3180.5962 | 2710.2269 | 2217.4577 | 1724.6885 | 1411.1115 | 1187.1231 | 918.3423
Nb-Ti: Iseult/INUMAC MRI 4.22 K | 393.4783 | 291.3043 | 194.203 | 104.3478
Exponential Y-axis Labels | 10 | 100 | 1000 | 10000
Nb-Ti midrange maximal | 971.9231 | 687.3077 | 448.4615 | 393.4783
2212 Fitted Line for 50bar ASC'16 | 1381.5217 | 1248.5735 | 1162.079 | 1099.1369 | 1050.2486 | 1010.6145 | 977.4929 | 949.1799 | 924.5486 | 902.818 | 883.4258 | 865.9547 | 850.0872 | 835.5764 | 777.6921 | 691.6232
YBCO B perp linear extrap | 312.7055 | 264.5487 | 240.4379
1st Iron-based Superconducting solenoid Coil at 24T
12.5T dipole with Nb3Sn and NbTi coil
World first: 1000m IBS cable, IBS coil,  magnet

## Slide 32: Novel concept of power supply based on 10kV SST
Numerous media/small magnet power supplies are needed: Quadrupole, Sextupole, corrector, … Lots of cables are needed, resulting in energy lost
SST can eliminate the need for 10kV transformer and SVG, which directly converts the AC power from 10kV to DC 200V – 1000V DC200V~1kV, with voltage tenability
Rectifier is not needed in the power supplies, reducing the cost, space occupation and power consumption

## Slide 33
The issues should be addressed in the EDR
  Radiation-resistant components- ADCs and FPGAs
  Highly reliable wireless transmission protocol
  Necessary radiation shielding
  ……
Wireless data transmission for BPM signal
Necessary modification in BPM electronics
  ADC and data process close to the detector
  Add wireless transmission module
  Improved timing system according to specific requirements

## Slide 34
Summary
CEPC has released its TDR for the accelerator
Prototypes have been developed and key technology breakthrough has been achieved, with many of them addressing green collider technologies
Power efficiency, energy recycling, and clean energy generation are addressed as comprehensive measures for sustainable operation.