## Slide 1
CEPC Booster and Damping Ring Development in EDR
Dou Wang (IHEP)
on behalf of CEPC Acc group
22-25. Jan. 2024, Hong Kong, IAS Program on High Energy Physics.

## Slide 2
CEPC injector chain
30 GeV linac provides electron and positron beams for booster.
Top up injection for collider ring ~ 3% current decay
Booster is in the same tunnel as collider ring, above the collider ring, bypass in IRs (same circumference).
Budget for transfer efficiency 90%: 95% for booster + 95% for transport lines (inj. to collider).
Beam current threshold in booster is limited by RF system.
Feedback systems (Transverse & longitudinal) are need to damp the instability at low energy.
100km
30GeV
30180GeV
2 RF stations
2 Inj. (Linac to Booster)
2 Inj. (Collider to Booster)
4 Ext. (Booster to Collider)
2 Ext. (Booster to Dump

## Slide 3: Booster TDR parameters
Injection
Extraction
*Diameter of beam pipe is 56mm for re-injection with high single bunch current @120GeV.
Injection energy: 10GeV  20GeV  30GeV
Max energy: 120GeV  180GeV
Lower emittance ─ new lattice (TME)

## Slide 4: Booster TDR optics
Arc: TME like structure (cell length=78m)
Interleave sextupole scheme
Emittance@120GeV=1.26nm
D. Wang, C. H. Yu, D. H. Ji, Y. M. Peng, X. H. Cui,…
Arc cell
Overall idea: uniform distribution for the Q
Combined magnet (B+S) scheme
Phase advance/cell: 100 (H) / 28 (V)
Dispersion sup.
Straight cell

## Slide 5
Booster error study and correction
 | Dipole | Quadrupole | Sextupole
Transverse shift X/Y (μm) | 100 | 100 | -
Longitudinal shift Z (μm) | 100 | 150 | -
Tilt about X/Y (mrad) | 0.2 | 0.2 | -
Tilt about Z (mrad) | 0.1 | 0.2 | -
Nominal field | 1e-3 | 2e-4 | 3e-4
 | Accuracy (m) | Tilt (mrad) | Gain | Offset w/ BBA(mm)
BPM(10Hz) | 1e-7 | 10 | 5% | 30e-3
D. H. Ji
dipole | quadrupole
B1/B0  210-4 | 
B2/B0  510-4 | B2/B1  310-4
B3/B0  210-5 | B3/B1  210-4
B4/B0  810-5 | B4/B1  110-4
B5/B0  210-5 | B5/B1  110-4
B6/B0  810-5 | B6/B1  510-5
B7/B0  210-5 | B7/B1  510-5
B8/B0  810-5 | B8/B1  510-5
B9/B0  210-5 | B9/B1  510-5
B10/B0  810-5 | B10/B1  510-5
Include multipole errors
(100 seeds)
(93 seeds)
DA track in AT w/o SR

## Slide 6: Booster DA results after error correction
The definition of beam stay clear region at different energies
Lattice design with TME structure, lower emittance than CDR
Sufficient Dynamic Aperture for all energies with errors
30GeV
45GeV
80GeV
120GeV
180GeV

## Slide 7: Booster Physics Study in EDR
RF Beam loading study for the bunch structure with half ring distribution (Higgs & ttbar)
Redundancy study for the BPM and correctors
Injection efficiency simulations related with the on-axis injection
Dynamic simulations during the ramping process
Booster table ramping scheme
Booster machine/beam commissioning plan is proposed.

## Slide 8: RF ramping curve
Different RF ramping curve for each energy mode (constant s )
Max RF voltage @tt determined by longitudinal quantum lifetime & DA.
s for tt: 0.14
s for Higgs: 0.094
s for W & Z: 0.088
RF: ~ 12 
VRF (180GeV)=9.8GV
W &Z
Higgs
tt
D. Wang, J.Y. Zhai
 | tt | Higgs | W | Z
VRF (GV) | 9.8 | 2.2 | 0.87 | 0.46
s | 0.14 | 0.094 | 0.088 | 

## Slide 9: CEPC Booster Ring 1.3 GHz RF Parameters
1.3 GHz 9-cell cavities
Higgs and ttbar booster are half filled for the injection timing with Collider ring.
Transient beam loading for Higgs on-axis injection tolerable (both at injection and extraction).
Increased average HOM power of HL-Z requires ERL-type 1.3 GHz cryomodule (HOM absorber at low temperature between cavities). Four cryomodules for Z with RF bypass, also to reduce impedance and increase current limit.
High gradient high Q 9-cell cavities for ttbar.
Narrow bandwidth high gradient cavity voltage ramping through the multipacting region to be studied. Counter-phasing ramp.
* The small bunch charge number before the parenthesis is for the bunches injected from the linac. The large bunch charge number in the parenthesis is for the bunches injected back from the Collider ring during the swap-out injection at Higgs energy.
30/50 MW Collider SR power per beam. 30 GeV injection. Higgs & ttbar half filled. Higgs on-axis injection with bunch swapping. Z injection from empty ring. | ttbar 30/50 MW |  | Higgs 30/50 MW on-axis | W 30/50 MW | Z 30/50 MW
 | New cavities | Higgs cavities |  |  | 
Extraction beam energy [GeV] | 180 |  | 120 | 80 | 45.5
Extraction average SR power [MW] | 0.05 |  | 0.5 / 0.67 | 0.02 / 0.04 | 0.05 / 0.1
Bunch charge [nC] | 1.1 |  | 0.78 (20.3)* | 0.73 | 0.81
Beam current [mA] | 0.12 / 0.19 |  | 1 / 1.4 | 3.1 / 5.3 | 16 / 30
Injection RF voltage [GV] | 0.761 |  | 0.346 | 0.3 | 0.3
Extraction RF voltage [GV] | 9.7 (7.53 + 2.17) |  | 2.17 | 0.87 | 0.46
Extraction bunch length [mm] | 1.8 |  | 1.86 | 1.3 | 0.75
Cavity number (1.3 GHz 9-cell) | 256 | 96 | 96 | 96 | 32
Module number (8 cavities / module) | 32 | 12 | 12 | 12 | 4
Extraction gradient [MV/m] | 28.3 | 21.8 | 21.8 | 8.7 | 13.8
Q0 @ 2 K at operating gradient | 2E10 | 3E10 | 3E10 | 3E10 | 3E10
QL | 4E7 | 4E7 | 1.2E7 | 7.3E6 / 4.4E6 | 1.2E7 / 6.3E6
Cavity bandwidth [Hz] | 33 | 33 | 110 | 178 / 296 | 111 / 208
Peak HOM power per cavity [W] | 0.5 / 0.8 |  | ~ 75 / ~ 100 | 11.8 / 19.6 | 146 / 272
Average HOM power per cavity [W] | 0.2 / 0.32 |  | ~ 10 / ~ 15 | 3.8 / 6.3 | 80 / 150
Input peak power per cavity [kW] | 8.3 / 9.2 | 5.1 / 5.9 | 22 / 32 | 10.9 / 18.1 | 17 / 32
Input average power per cavity [kW] | 0.3 | 0.2 | 6.5 / 9.2 | 0.3 / 0.5 | 2.5 / 4.5
SSA power [kW] (1 cavity / SSA) | 10 | 10 | 25 / 30 | 25 / 30 | 25 / 40
Total cavity wall loss @ 2 K [kW] | 0.36 | 0.05 | 0.5 | 0.02 | 0.08
J.Y. Zhai

## Slide 10: CEPC Booster Superconducting RF R&D in EDR
Higgs high Q 1.3 GHz cryomodule prototyping: based on the successful verification module, build two more mid-T bake module prototypes using domestic CW FEL funding. Make improvements and increase module average CW gradient to > 25 MV/m with Q0 > 3E10. Complete engineering design for CEPC Higgs booster module (without cold BPM and quadrupole as in FEL module).
Z-pole high current 1.3 GHz cryomodule design: complete conceptual design and component development in synergy of domestic ERL project R&D.
ttbar high gradient and high Q 1.3 GHz cryomodule R&D: build one ILC/XFEL type 8x9-cell module prototype using domestic pulsed XFEL funding. Achieve module average gradient > 35 MV/m with high Q.
J. Y. Zhai

## Slide 11: RF beam loading effect @ 30 GeV
Assuming a constant detuning and a consistent loaded Q optimized for the top energy in each energy mode.
The longitudinal coupled bunch mode will be effectively managed with the aid of bunch-by-bunch feedback.
However, for Z mode we might need to consider adding more power to meet the requirement.
Growth rate = 3.7 Hz
Pg = 1.14 MW
df = -752 Hz
Growth rate = 0.88 Hz
Pg = 0.61 MW
df = -216 Hz
Growth rate < 0.01 Hz
Pg = 0.095 MW
df = -19.4 Hz
Higgs
W
Z
Transient beam loading due to half filled ring in Higgs mode.
Higgs
Higgs
T. M. Xin, J. Y. Zhai

## Slide 12: Magnets Requirement
Dipole | BST-63B-Arc | BST-63B-Arc-SF | BST-63B-Arc-SD | BST-74B-IR
Number | 10192 | 2017 | 2017 | 640
Gap [mm] | 63 | 63 | 63 | 63
Dipole strength [Gs]@180GeV | 564 | 564 | 564 | 549
Dipole strength [Gs]@120GeV | 376 | 376 | 376 | 366
Dipole strength [Gs]@30GeV | 94 | 94 | 94 | 91
Sext. Strength [T/m^2]@180GeV | 0 | 16.0388 | 19.1423 | 0
Sext. Strength [T/m^2]@120GeV | 0 | 10.6925 | 12.7615 | 0
Sext. Strength [T/m^2]@30GeV | 0 | 2.67 | 3.19 | 0
Length [mm] | 4700 | 4700 | 4700 | 2350
Good field region [mm] | 45 | 45 | 45 | 45
Quadrupole | QDM-63 | QFM-63 | QM-RF-63 | QFM-ARC-63 | QDM-ARC-63 | QF-DIS-63 | QD-DIS-63
Number | 64 | 48 | 264 | 1016 | 2018 | 16 | 32
Gap[mm] | 63 | 63 | 63 | 63 | 63 | 63 | 63
Quad. Strength [T/m]@180GeV | 12.8811 | 16.3553 | 12.7248 | 12.0313 | 12.0313 | 18.0522 | 15.8575
Quad. Strength [T/m]@120GeV | 8.5874 | 10.9036 | 8.4832 | 8.0209 | 8.0209 | 12.0348 | 10.5717
Quad. Strength [T/m]@30GeV | 2.147 | 2.726 | 2.121 | 2.005 | 2.005 | 3.008 | 2.643
Length [mm] | 2000 | 2000 | 1000 | 2000 | 700 | 2000 | 1000
Good field region [mm] | 45 | 45 | 45 | 45 | 45 | 45 | 45
Dipoles (series connection) -- 14866
Quadrupoles (series connection + 3200 independent PS) --3458
Sextupoles & correctors
 | Number | Length [m]
Sextupole | 100 | 0.4
Corrector | 1200 | 0.58
D. Wang, W. Kang

## Slide 13
There are three families of dipole magnets in the CEPC booster. One family is the pure dipoles while the other two families are the dipole-sextupole combined magnets.
Introduction of the dipole magnets
W. Kang

## Slide 14
In TDR stage, a full-scale pure dipole magnet for the CEPC booster has been produced and the field performance is satisfied with the requirements.
Booster magnet R&D in TDR
W. Kang

## Slide 15
The plan of the Booster magnet production in EDR
In the EDR stage, in order to verify the magnetic field design of the dipole-sextupole combined magnet, a full scale prototype magnet will be developed and measured by a harmonic coil field measurement system.
In addition, in order to improve the production efficiency and reduce production cost, an automatic production line for the dipole magnets of the Booster will be designed and developed.
W. Kang

## Slide 16
切片、掺和、冲制、打毛刺
三坐标
涂胶（按需）
叠装
固化
焊接
尺寸测量、合铁、尺寸测量、骑缝销、尺寸测量
焊外围件
铁芯保护、铁芯喷漆
安装线圈
线圈固定
铁芯装配
整铁装配
安装电排
包绝缘带、水路安装
尺寸测量、电测、水压检测、准直测磁、出厂检查
The sketch map of the automatic production line for the dipole magnet
Dimensional measurement, electrical testing, water pressure testing, magnetic collimation measurement, factory inspection
Slice, mix, punch, deburr
Wrap insulation tape, install water channels
Install electrical outlets
assembly of magnets
Iron core assembly
coil fixation
installing the coil
Iron core protection, Iron core painting
three-coordinate
Glue application (as needed)
stacking
solidify
welding
dimension measurement, iron fitting, dimension measurement, saddle stitching, dimension measurement
Welding peripheral parts
W. Kang

## Slide 17: Mechanics plan in EDR
Magnet supports and mockup tunnel
  For the TDR design, the Booster ring is 2.4 meters higher above Collider.  Reasonable stability by optimizing the supports.
Change support height
Change support number
Change steel sections
H. J. Wang

## Slide 18: Mechanics plan in EDR
Booster magnet supports plan
  The final magnet support scheme
  The deformation and stability simulation and optimization.
  Verification of support structure, stability, installation and alignment in a mockup tunnel.
  Considering method for efficient installation and alignment: semi-automatic adjustment and high-precision alignment field.
H. J. Wang

## Slide 19: CEPC Damping Ring
Damping with reversed bending magnet
60 FODO (r /0=0.355)
4 (max. 8)-bunch storage, storage time:20 (40) ms
Emittance: 2500 166/75 (97/3) mm.mrad
DA with errors
Both the DR and trans. lines are well optimized in TDR, with lower emittance than CDR.
tt/Higgs/W
Z

## Slide 20: Damping Ring RF requirement
The total cavity voltage requirement is 2.5MV
5 cell cavity aperture is decided by impedance、HOM and instability threshold
  Taking into account the simulation results for impedance threshold and HOM power, the 5-cell cavity with a 90 mm aperture is considered the best choice

## Slide 21: Damping Ring RF cavity design
The design of the 650MHz 5 cell cavity finished
  RF cavity design
  Input coupler and doorknob design
  Vacuum design
  Mechanical design
Electromagnetic field distribution
Ion pump distribution
Parameters | Unit | Value
Operation frequency | MHz | 650
Voltage per cavity | MV | 1.25
Cell length | mm | 5230.61
Shunt impedance | M | 16
R/(Ql) | Ω/m | 430
Q factor |  | 32000
Dissipated power per cavity (20% margin) | kW | 59
Emax | MV/m | 8.5
  Mechanical design
Cavity
Tunner
Coupler
J. R. Zhang

## Slide 22: Damping Ring RF cavity R&D in EDR
Further optimize the 5 cell cavity design
We hope to process a DR normal conducting 5 cell cavity. And finished the cold test of the cavity.
After the machining of the cavity completed, use PAPS (a test bench of IHEP at Huairou) test bench to do the high-power test of the DR normal conducting 5 cell cavity
  Mechanical design
J. R. Zhang

## Slide 23: Booster lattice optimization for better polarization transmission
The TDR lattice suffers from superstrong resonances before Z energy
  Injected vertical emittance 6.5nm -> Polarization trans. ~ 50% @ Z & W, 20% @ Higgs
  Injected vertical emittance 1.5 nm -> Polarization trans. ~ 80% @ Z & W, 30% @ Higgs
Potential optimization:
  Increase vertical focusing
  Mitigation of imperfection resonances
    Reduce lattice sensitivity
    Harmonic spin matching & partial snakes
TDR bare lattice
Intrinsic resonance
TDR lattice (one seed)
Imperfection resonance
Z. Duan

## Slide 24: Positron damping/polarizing ring
Optimization of a dual-purpose design
  Bunches stay ~ 20 msec for regular refill
  Bunches stay ~ 10 min to accumulate > 20% polarization for resonant depolarization in the Colliders
Cost and benefit comparison between two schemes
  Higher beam energy without asymmetric wigglers
  Lower beam energy with asymmetric wigglers
Asymmetric wigglers
Z. Duan

## Slide 25: Summary
The CEPC booster TDR parameter and design optimizations for all four energies (Higgs, W/Z and ttbar) have been studied. The results demonstrate that the physics design satisfies the scientific goals.
CEPC booster development was reported on the TDR international review meeting and cost review meeting from June 12-16, 2023 and Sept. 11-15, 2023
R&D plan for EDR phase (2024-2027) before construction have been established, with the aim of starting the construction in “15th five-year-plan” (2026-2030) .