## Slide 1: CEPC large scale and precision control system study in EDR
Dapeng Jin
Institute of High Energy Physics, CAS, Beijing
23 January, 2024
环形正负电子对撞机
Circular Electron Positron Collider

## Slide 2: Outline
Challenges & current status
Further to do
Summary

## Slide 3: Challenges & current status
Reliability & availability & low cost on large scale (First priority). Radiation hardness of components in tunnel.
Maintainability : Flexibility : Scalability (Second priority).
Overall

## Slide 4: Challenges & current status
Fiber routing
Optical fibers as backbone to minimize cables || preliminary routing topology:
  4-arc routing, balance between total fiber length, performance, maintainability and scalability => radiation hard for those in tunnel.
  Central station at LINAC to ease the first stage beam commissioning.
MPS : Response speed is the key:
  Bidirectional loop structure in the tunnel with redundancy for both reliability and availability.
  Isolation of action and monitoring. Few and radiation-hard chips used for action.

## Slide 5: Challenges & current status
Timing system & reference line
Beam instrumentation along the whole ring with high requirements => Performance, radiation-hardness & cost.
Temperature variation induced drift compensation. Hundreds of ps for 10km optical fiber with 1 ℃ change normally.
Good experiences of development and application in the BEPCII & HEPS.

## Slide 6: Challenges & current status
Timing system & reference line
Preliminary design of the reference line (experiences in BEPCII & HEPS)

## Slide 7: Challenges & current status
Timing system & reference line
Integration of timing system and reference line under consideration.
Transmission and compensation part of the reference line in detail
(Compensation for more than 1 clock cycle needs to be tested)

## Slide 8: Challenges & current status
Data acquisition and analysis
Distributed data acquisition, online and offline analysis.
Post mortem & real-time health monitoring(Distributed Logic Analyzer) with time correlated data. Size of front end controllers’ data caches and accuracy of timestamp.
Multi-layer network : control and DAQ

## Slide 9: Challenges & current status
Control structure
Overall control & zone allocation.
Automation: development, installation, configuration, log, alarm, AI analysis, health report …
Joint development & management.

## Slide 10: Challenges & current status
Control platform
EPICS is the current selection
  Good structure and performance.
  Good toolsets to use.
  Widely used, also by us.
CWS : Client WorkStation
IOC : Input/Output Controller

## Slide 11: Challenges & current status
Control platform

## Slide 12: Challenges & current status
Tunnel inspection
Robot considered to do the inspection
  Easy to avoid strong radiation.
  Easy to install more inspection equipment.
  Low cost.
  Ground guide method to be used.

## Slide 13: Further to do
To integrate the timing system and reference line together, design and development.
For timing system and reference line, long distance, long time, large temperature variation compensation & test.
Radiation hard optical fibers and electronics test.
Design of software structure and development for data acquisition, storage, analysis and display.
Design and development of control structure and automation.

## Slide 14: Summary
Key issues have been identified till now, much work need to be done together with the related systems.
Experiences from previous and current facilities help to the design and development, radiation-hardness and long distance transmission needs to be studied thoroughly.
Thanks for your attention!