## Slide 1: Mechanical Model of the FCC e+e- MDI

## Slide 2: Table of content
Spatial constraint | 5 | Support tube | 14
MDI Mechanical Model | 4 | Assembly procedure | 19
Central Chamber | 7 | Conclusion | 20
Trapezoidal chamber | 8 |  | 
Structural analysis – chamber | 9 |  | 
Bellows | 11 |  | 
Crotch chamber | 12 |  | 

## Slide 3
10.6m
12 m
13 m
11 m
At the moment a detector concept has not been defined. The two main philosophy are based on the IDEA concept and the CLD concept,
Any design shown in this presentation for now is based on IDEA detector.
IDEA
CLD

## Slide 4
Support tube
LumiCal
Conical chamber
Central chamber
Cooling
Cryomagnet
IDEA detector
Bellows
Disks
Outer and medium tracker
Outer and medium tracker

## Slide 5: Spatial constraints - LumiCal Cones
105 mrad
50 mrad
The Lumical is centred on the outgoing beam pipe.
The device to perform properly needs an empty space between two cones, the 50 mrad cones and the 105 mrad cone.
The components integration and each component (i.e. the conical chamber) have been designed to keep everything out of this range, or the thickness has been optimized to achieve the maximum transparency possible.
Asymmetric spatial constraint

## Slide 6: Spatial constraints – Detector Cone
Another important constraint imposed over the IR from the detector is the respect of a 100 mrad cone, centered on the detector axis.
This constraint is symmetric and, therefore, is less problematic if compared with the Lumical Constraint

## Slide 7: Central chamber
Inlet/outlet
Central chamber
1st layer Inner Vertex
The central has the following characteristics:
AlBeMet 162 as main material
Three layers from 0-90 mm from IP
0.35 mm of AlBeMet162
1 mm gap for Paraffin
0.35 mm of AlBeMet162
Paraffin as coolant
Geometry studied to integrate the central chamber with the Inner Vertex (200 µm of clearance between central chamber and Inner Vertex support)
Inlet/outlet for paraffin cooling

## Slide 8: Trapezoidal chamber
The cooling is based on an asymmetric solution, using the 50 mrad cone as the cutting profile, to assure the respect of the spatial constraint due to the LumiCal requirment.
To reduce the cooling material, the design provides five couples of channels for each side; in this way is possible to use the needed quantity of coolant and reduce the material, creating a light structure.
EBW
Two halves AlBeMet pipe
Transition
Bellows
EBW
Thick copper deposition
Main characteristics:
AlBeMet162 as main material
Chamber in two halves and assembled using EBW
Copper cooling system
A
A
A-A

## Slide 9: Structural analysis – chamber
Loads, constraints, characteristic parameters, design
FEA (Ansys)
Temperature distribution, stress and displacement along the pipe
Paraffin flow (central chamber)
Flow rate
Section
Velocity
Inlet temperature
Convective coefficient
Water flow (trapezoidal chamber)
Flow rate
Section
Velocity
Inlet temperature
Convective coefficient
Heat load
From CST calculations (Alexander Novokhatski (SLAC))
Chamber design (until the bellows)
Weight
chamber
Inner Vertex first layer
Constraint
Cantilevered, simply supported configuration
RESULTS
Hypothesis:
Perfect thermal contact between the materials

## Slide 10
 | Trapezoidal chamber | Central chamber
Coolant | Water | Paraffin
Maximum chamber temperature [°C] | 47,6 | 33,1
T_out coolant [°C] | 20,5 | 20,1
Von Mises stress [MPa] |  |  |  |  | 
 |  | Trapezoidal SX | Trapezoidal DX | Central IN | Central EX
BEAM | Fixed ends | 22,07 | 21,86 | 46,8 | 38,9
 | Fixed+displ | 14,65 | 10,63 | 9,69 | 17
Maximum displacement [mm] |  |  | 
 |  | X | Y
BEAM | Fixed ends | 0,031 | 0,07
 | Fixed+displ | 0,1 | 0,29
Structural analysis - chamber - results

## Slide 11: 2nd Bellows (Double bellows)
Bellows
The use of Support Tube is designed to avoid overloads on central chamber during assembly and operation (thermal expansion). This solution has been obtained using two kind of bellows for the two sides of the support tube.
In short, in this way we can:
Protect the central chamber during the assembly procedure
Support properly the chamber bellows-to-bellows, containing the deformation
Allow the thermal deformation without compromising the chamber
1st Bellows (Single bellows)
Anchoring flange
IP SIDE
IP SIDE
CRYOSTAT SIDE
CRYOSTAT SIDE
IP SIDE
CRYOSTAT SIDE
IP SIDE
CRYOSTAT SIDE

## Slide 12: Crotch chamber
-1175 mm
Solution A:
Standard flanges
More space available for the crotch
Flanges in Helium
Solution B:
Flanges not in contact with Helium
Shorter chamber than solution A
Non standard flanges
Chart: 
| -5560 | -2500 | -90 | 0
X4 | 106.4627 | 52.5 | 10 | 10
X3 | -98.4 | -52.5 | -46.8 | -38.5 | -38.2 | -45.9 | -10 | -10
X2 | 71.1818 | 22.5 | 5 | 1 | 0.5 | 0
X1 | -71.1818 | -22.5 | -5 | -1 | -0.5 | 0
Xc | -84.7909 | -37.5 | 0
Solution A
Solution B
Work in progress
Remote vacuum connection

## Slide 13
SR MASK
Shifted flanges
Start of circular pipe at 2550 mm from IP
2550 mm
IP
Custom flanges
It is a work in progress:
Shape
Flanges geometry
Interface with Remote vacuum connection
REMOTE VACUUM CONNECTION BLOCK
Not regular shape
Very preliminary design

## Slide 14: Support tube – description
The structure is made with a multiple layer structure:
CF + HC + CF
To allow the support of the disks are necessary reinforcement ribs.
The cylinder is split in two halves to simplify the assembly procedure
The Aluminium endcaps support the LumiCal and the beampipe
The support tube aims to :
Provide a cantilevered support for the pipe.
Avoid loads on thin-walled central chamber during assembly or due to its own weight
Support LumiCal.
Support the Medium, Outer Vertex and Vertex Disks.
CF=carbon fibre
HC=honeycomb
Aluminium ribs
Aluminium endcaps

## Slide 15: Support tube – loads and constraints
The aim of this analysis is to calculate the stress and displacement in each part of the cylinder (Al reinforcement, carbon fiber, honeycomb).
It is necessary to set:
Constraint configuration  double fixed ends
Loads configuration
Chamber | 50 kg
LumiCal | 70 kg + 70 kg
Vertex Disks | 6*10 kg
Outer Vertex | 15 kg
Medium Vertex | 7 kg
First guess loads (overestimated) | 
Carbon fiber/ honeycomb creation  layered section

## Slide 16: Support tube – Structural analysis – results
 | Maximum stress [MPa]
Aluminium flanges | 2.08
Aluminium ribs | 0.20
Honeycomb | 0.02
Carbon fiber | 0.60
 | Maximum displacement X [mm]
Aluminium flanges | 1.34 e-2
Aluminium ribs | 2.62 e-2
Composite | 2.80 e-2

## Slide 17: Support tube – Rail
The support tube needs to be inserted into the main detector; the idea is to use a rail, starting from the outside of the detector to allow the sliding of the cylinder.
To assure a good precision and appropriate support it is necessary to use the linear bearings; different types are available, the choice has to be made considering:
Required positioning precision
Weight of the whole structure
Necessary degrees of freedom
SECTION
After the positioning the rail will be removed, and the support tube attached to the detector

## Slide 18
Under study:
Rail support
Rail anchoring
Rails length
Geometry of the rail section
Linear bearing type
Positioning system
To continue the design, it is necessary to know:
Allowable anchoring point from detector side
Allowable space (internal detector diameter and geometry)
Hypothesized anchoring point

## Slide 19: Assembly procedure
2) Disks 2 and 3 are installed inside the support tube
Section view
1) Outer tracker, Medium tracker and disks 1 are installed as a rigid structure inside the support tube
3) LumiCal is installed in centered position, then beam pipe with vertex detector is inserted with a dedicated tool inside disks and outer tracker, then fixed to both endcaps
4) LumiCal can be aligned in the correct position on the outgoing beams
5) Support tube can be closed

## Slide 20: Conclusion
The current central chamber design has been proposed and is compatible with the Inner Vertex design.
The design of conical chamber has been developed and is compatible with LumiCal requirements.
The preliminary design of crotch chamber has been proposed.
The concept of Support Tube has been introduced and the proposal of an assembly strategy as well.
The preliminary structural analyses have been performed and the results are compatible with the requirement in terms of allowable maximum stress and displacement.

## Slide 21: \