## Slide 1
CEPC high efficiency & high power RF sources
Zusheng Zhou
On behalf of CEPC klystron R&D team
IAS Program on Fundamental Physics (FP 2025), January 13-17, 2025

## Slide 2: Content
System design consideration
  Collider ring
  Booster ring
  Linac injector
R&D
  High efficiency (P band 800kW CW klystron/Energy recovery klystron)
  High power (C band 80MW klystron)

## Slide 3: Collider RF sources
Requirement list:
Klystron | 96 | 650MHz/800kW
PSM Power Supply | 96 | 130kV/16A and 60kV/22A
Circulator | 96 | 650MHz/800kW
Load | 96 | 650MHz/800kW
Phase shift | 96 | 650MHz/800kW
Waveguide | 96 | Power divider/directional coupler
LLRF | 96 | Phase stabilization <0.1 degree, Amplitude stabilization <0.1%
Pre-amplifier | 96 | 650MHz/100W

## Slide 4: Collider RF sources
Requirement list:
Klystron | 96 | 650MHz/800kW | Higher efficiency
PSM Power Supply | 96 | 130kV/16A and 60kV/22A | Mature product
Circulator | 96 | 650MHz/800kW | Mature product
Load | 96 | 650MHz/800kW | Mature product
Phase shift | 96 | 650MHz/800kW | Mature product
Waveguide | 96 | Power divider/directional coupler | Mature product
LLRF | 96 | Phase stabilization <0.1 degree, Amplitude stabilization <0.1% | Mature product
Pre-amplifier | 96 | 650MHz/100W | Mature product

## Slide 5: Booster RF sources
Requirement list:
SSA | 96 | 1300MHz/25kW
Circulator | 96 | 1300MHz/25kW
Load | 96 | 1300MHz/25kW
Waveguide | 96 | Directional coupler
LLRF | 96 | Phase stabilization <0.1 degree, Amplitude stabilization <0.1%

## Slide 6: Booster RF sources
Requirement list:
SSA | 96 | 1300MHz/25kW | Mature product
Circulator | 96 | 1300MHz/25kW | Mature product
Load | 96 | 1300MHz/25kW | Mature product
Waveguide | 96 | Directional coupler | Mature product
LLRF | 96 | Phase stabilization <0.1 degree, Amplitude stabilization <0.1% | Mature product

## Slide 7: Linac RF sources
The main high power RF sources components are 33 units of 80MW S-band klystron, 236 units of 50MW C-band klystron and related modulators.
Type | QTY | Freq.(MHz) | Structure type
S-band klystron | 33 | 2860 | 1 1-to-1，standard-bunch 3 1-to-2，standard acc. structure. 8 1-to-2，large aperture acc. structure 21 1-to-4, standard acc. structure.
C-band klystron | 236 | 5720 | 1-to-2，standard acc. structure.

## Slide 8: Linac RF sources
Requirement list:
S band klystron | 33 | 2860MHz/80MW
Modulator of S band klystron | 33 | 400kV/500A
C band klystron | 236 | 5720MHz/50MW
Modulator of C band klystron | 236 | 350kV/400A

## Slide 9: Linac RF sources
Requirement list:
S band klystron | 33 | 2860MHz/80MW | Mature product
Modulator of S band klystron | 33 | 400kV/500A | Mature product
C band klystron | 236 | 5720MHz/50MW | Mature product
Modulator of C band klystron | 236 | 350kV/400A | Mature product

## Slide 10
Why we need R&D?

## Slide 11: 1st-Collider RF sources
Higher efficiency
Less power consumption
CEPC annual electricity @6000 hours/year
Efficiency impact on operation electricity consumption (Only considering operation efficiency of klystrons)
Chart: Annual electricity consumption vs. Efficiency
| 0.4 | 0.5 | 0.6 | 0.7 | 0.78 | 0.8 | 0.9 | 1
60MW Power | 0.9 | 0.72 | 0.6 | 0.51429 | 0.46154 | 0.45 | 0.4 | 0.36
100MW Power | 1.5 | 1.2 | 1 | 0.85714 | 0.76923 | 0.75 | 0.66667 | 0.6
Mature product

## Slide 12: 1st-Collider RF sources
Higher efficiency
Less power consumption
CEPC annual electricity @6000 hours/year
Efficiency impact on operation electricity consumption (Only considering operation efficiency of klystrons)
Chart: Annual electricity consumption vs. Efficiency
| 0.4 | 0.5 | 0.6 | 0.7 | 0.78 | 0.8 | 0.9 | 1
60MW Power | 0.9 | 0.72 | 0.6 | 0.51429 | 0.46154 | 0.45 | 0.4 | 0.36
100MW Power | 1.5 | 1.2 | 1 | 0.85714 | 0.76923 | 0.75 | 0.66667 | 0.6
IHEP R&D

## Slide 13: 1st-Collider RF sources
CEPC annual electricity @6000 hours/year
Chart: Annual electricity consumption vs. Efficiency
| 0.4 | 0.5 | 0.6 | 0.7 | 0.78 | 0.8 | 0.9 | 1
60MW Power | 0.9 | 0.72 | 0.6 | 0.51429 | 0.46154 | 0.45 | 0.4 | 0.36
100MW Power | 1.5 | 1.2 | 1 | 0.85714 | 0.76923 | 0.75 | 0.66667 | 0.6
Higher efficiency
Less power consumption
Efficiency impact on operation electricity consumption (Only considering operation efficiency of klystrons)
Near future

## Slide 14: 1st-Collider RF sources
CEPC annual electricity @6000 hours/year
Chart: Annual electricity consumption vs. Efficiency
| 0.4 | 0.5 | 0.6 | 0.7 | 0.78 | 0.8 | 0.9 | 1
60MW Power | 0.9 | 0.72 | 0.6 | 0.51429 | 0.46154 | 0.45 | 0.4 | 0.36
100MW Power | 1.5 | 1.2 | 1 | 0.85714 | 0.76923 | 0.75 | 0.66667 | 0.6
Higher efficiency
Less power consumption
Efficiency impact on operation electricity consumption (Only considering operation efficiency of klystrons)
Future

## Slide 15: 2nd-Linac RF sources
Now
  Only C band of 50MW klystron is mature product in the world. 1 klystron only power to 2 accelerator structures (CEPC Linac baseline).
  Number of C band klystron is very large (236 set).
IF output power of C band klystron is up to 80MW, the number of klystron will be reduced by half. (1 klystron power to 4 accelerator structures). The cost of Linac RF sources will be decreased more than 30%.
CEPC Linac baseline
Higher power
Smaller number

## Slide 16
R&D Progress and Achievements

## Slide 17: 650MHz klystron R&D
3 or more klystron prototypes for klystron efficiency improvement
Step1
Step2
Step3
1st
2nd
3rd
more
Prototypes
Efficiency: 60%
70%
80%
2016 | 2017 | 2018 | 2019 | 2020 | 2021
2022
2023
2024

## Slide 18: Design scheme
Scheme 1: Traditional way for >60% efficiency
Scheme 2: With high voltage gun (110 kV/9.1 A), low perveance (HE, >75%)
Scheme 3: MBK, 54 kV/20A electron gun (8 beams) (HE, >80%)
Parameter | Scheme1(1st prototype) | Scheme2(2nd) | Scheme3(3rd)
Freq. (MHz) | 650 | 650 | 650
Voltage (kV) | 82 | 110 | 54
Current (A) | 16 | 9.1 | 20(2.5×8)
Beam No. | 1 | 1 | 8
Perveance (µP) | 0.65 | 0.25 | 1.6(0.2×8)
Efficiency (%) | 65 | ~80 | >80
Power(kW) | 800 | 800 | 800(100×8)

## Slide 19: 1st prototype
Oct. 2017 Prototype manufacture
Mar. 2020 High power test at IHEP
Parameters | Design | Test
Operating frequency (MHz) | 650 | 650
Beam Voltage (kV) | 81.5 | 80
Beam Perveance (μA/V3/2) | 0.65 | 0.7
Efficiency(%) | 65 | 62
Saturation Gain(dB) | ≥45 | 47
Output power(kW) | 800 | 800
1 dB Bandwidth(MHz) | ≥1 | 1.8

## Slide 20: 2nd prototype (HE design)
Jan. 2021: Prototype manufacture
Jul. 2022: CW 630kW with Eff. 70.5% (1st stage high power test)
Aug. 2024: CW 803kW with Eff. 78.5% (2nd stage high power test)

## Slide 21: 3rd prototype (MBK)
Dec. 2021: Klystron beam tester manufacture
Oct. 2023: Accomplishment of klystron beam tester high voltage conditioning and beam emission.
Now: Klystron prototype manufacture is in progress.

## Slide 22
C band klystron

## Slide 23: Design progress
Parameters | Value
Frequency | 5720 MHz
Output Power | 80MW
Pulsed width | 3us
Repetition rate | 100Hz
Gain | 54 dB
Efficiency | 47%
Beam voltage | 420 kV
Beam current | 403 A
Main parameters
Beam dynamics

## Slide 24: Fabrication progress
Prototype manufacture is started from August 2024.
The processing is scheduled to be completed in July this year.

## Slide 25
Energy recovery klystron

## Slide 26: 3rd-Energy recovery
CEPC annual electricity @6000 hours/year
Chart: Annual electricity consumption vs. Efficiency
| 0.4 | 0.5 | 0.6 | 0.7 | 0.78 | 0.8 | 0.9 | 1
60MW Power | 0.9 | 0.72 | 0.6 | 0.51429 | 0.46154 | 0.45 | 0.4 | 0.36
100MW Power | 1.5 | 1.2 | 1 | 0.85714 | 0.76923 | 0.75 | 0.66667 | 0.6
Higher efficiency
Less power consumption
Assuming klystron efficiency is up to 80%.

## Slide 27: 3rd-Energy recovery
CEPC annual electricity @6000 hours/year
Chart: Annual electricity consumption vs. Efficiency
| 0.4 | 0.5 | 0.6 | 0.7 | 0.78 | 0.8 | 0.9 | 1
60MW Power | 0.9 | 0.72 | 0.6 | 0.51429 | 0.46154 | 0.45 | 0.4 | 0.36
100MW Power | 1.5 | 1.2 | 1 | 0.85714 | 0.76923 | 0.75 | 0.66667 | 0.6
Higher efficiency
Less power consumption
It is difficult to increase RF conversion efficiency of the klystron itself from 80% to 85 or 90%? So we need other methods to achieve a leap in efficiency.

## Slide 28: Energy recovery klystron(ERK)
The energy recovery klystron recovers energy from the spent electron beam by multi-depressed collector, thereby reducing the power demand from the grid and significantly lowering operation.
Typical klystron
Energy recovery klystron
RF OUT

## Slide 29: Roughly theoretical analysis
Stage No. | Linear region | Saturation region
Without stage | 65% | 77.5%
Single stage | 72.9% | 84.3%
Two stages | 79.4% | 88.1%
Three stages | 83.0% | 90.1%
Based on high efficiency klystron design
Final efficiency is the whole efficiency of ERK

## Slide 30: Design progress
Parameter | Value
Operating frequency | 650 MHz
Beam Voltage | 113 kV
Efficiency | 77.5%
Output power | 800 kW
Beam perveance | 0.25 μP
Beam current | 9.5A
Efficiency (one-stage depressed collector) | 84%
The energy distribution of spent electron beams
One-stage depressed collector
PIC (Particle-In-Cell) beam simulation

## Slide 31: Preliminary mechanical design
5048mm
4200mm

## Slide 32: Conclusion
The high power test of high-efficiency klystron prototype has been successfully completed, achieving a continuous wave (CW) output of 803 kW and an efficiency of 78.5%.
The processing of C band 80MW klystron is under progress.
Processing and high-power test of the MBK will be conducted in the near future.
Development of an energy recovery klystron based on high efficiency klystron technologies is progressing.

## Slide 33
Thanks for your attention!