## Slide 1: Imaging detectors
Zdeněk Doležal
Výjezdní seminář ÚČJF 2018

## Slide 2: Particle Detector Applications in Medicine
Hartmut F.-W. Sadrozinski
SCIPP, UC Santa Cruz, CA 95064 USA

## Slide 5: Medical Applications
Low-energy instrumentation,
small systems (until commercialization..) profiting from HEP and (even more so) from Astrophysics heritage
Scintillators & Semiconductors (for WCC heritage: Peskov, Nygren talks)
Dosimetry, EH&S
Imaging: Radiography, Tomography
  Photons
  X-ray CT
  SPECT
  PET & TOF-PET & PET/MRI & PET/CT
  Hadrons (MedAustron)
  Intercation Vertex Imaging IVI
  Proton CT

## Slide 6
300 µm
1 mm
2 cm
Absorption of Photons N(x) = Noe- µ x
Photons of Medical Interest, Energies & Resolution
µ-waves: MRI (10’s µm)
10-100keV: X-ray radiography and CT (10’s µm)
500 keV: PET and SPECT (mm)
No directional information with exception of Compton
High bone contrast 1-100 keV
Larger energy reach (depends on thickness)
Shift of Compton region to higher E
reduced range of Compton electrons
reduced range of positron in PET
Advantage of high-Z detectors:

## Slide 10: Amorphous Silicon (aSi:H)
Non-crystalline form of Silicon
Worse electrical properties (leakage current, efficiency)
Cheaper than crystalline
Used at solar cells, etc.
Dangling bonds passivated by Hydrogen

## Slide 16: Detection technologies used for photons

## Slide 17: Scintillators: indirect detection

## Slide 19: CCDs as detectors

## Slide 20: CCDs as detectors
2D structure can be made
Drawback: charge coming during R/O is misidentified

## Slide 21: Hybrid Pixels
Signal transferred to special readout chip attached to the pixel chip
Typical pixel size is 50 μm ×50μm
Often digital (binary) resolution
Small pixel area Low detector capacitance
Large S/N (e.g. 150:1)
Small pixel volume: low leakage current
Drawback: many R/O channels, data, large power consumption

## Slide 22: Monolithic Active pixels
Silicon used both in a detector and in processing electronics
Why not integrated?
Using the same wafer/substrate
This is not so easy:
  Electronics needs high conductivity Si
  Detectors need high-resistivity Si (to achieve depletion) Several approaches to match these contradictions:
Monolithic Active Pixels
DEPFET Pixels

## Slide 25: High resolution X-ray radiography: Imaging of Termites
The imaging of termites as a model soft tissue organism is particularly difficult due to their poorly sclerotized cuticle making difficult to observe the anatomic structures with an optimal contrast.
Moreover, they are vulnerable to damage when they are manipulated or treated during sample preparation.
Thus, the termites represent an ideal model to optimize the accuracy and sensitivity of the developed method.

## Slide 26: High resolution X-ray radiography: Imaging of Termites
X-ray transmission image of termite worker body (left) and detail of its head (bottom). Even fine internal structure of the antennae is recognized.
(Magnified 15x, time=30s, tube at 40kV and 70mA)

## Slide 27
A. Del Guerra, RESMDD12
Positron Emission Tomography PET
Study accumulation of radioactive tracers in specific organs.
The tracer has radioactive positron decay, and the positron annihilates within a short
Distance with emission of 511 keV γ pair, which are observed in coincidence.
Resolution of detector (pitch)
Positron range
A-collinearity
Parallax (depth)
T: true event
S: Compton Scatter
R: Random Coincidence
Resolution and S/N Effects:
Perfect Picture:

## Slide 28
Reduce Accidentals & Improve Image: TOF-PET
t1
t2
Localization uncertainty:
Dd = c x Dt /2
When Dt = 200 ps
➔ Dd = 3 cm
PET
TOF-PET
@ VCI
K. Yamamoto 2012 IEEE NSS-MIC
Notes: As you know, in Time-Of-Flight Positron Emission Tomography, TOF information provides better localization of the annihilation event and improves the signal-to-noise ratio of the reconstructed image.
For example, when timing resolution is 300ps, position resolution is 4.5cm along the line of response.
In fact, timing resolution depends on the scintillation light yield, detector performance and read out noise.
Multi-Pixel Photon Counter, MPPC is a silicon photomultiplier and expected for use in PET-MR.
Timing resolution required for the MPPC is less than 200ps.

## Slide 33: SR imaging
Structural imaging
Short beam time structure allows for dynamic imaging

## Slide 37: The Neutronography
Specimen attenuating the beam
Shadow on detector
plane
Neutronogram
Parallel beam of thermal neutrons

## Slide 38: Neutronography with Medipix
Conversion of thermal neutrons to heavy charged particles in 6Li or 10B converter layer.
10B reaction (Cross section 3840 barns at 0.0253 eV):
10B+n  a (1.47 MeV) + 7Li (0.84 MeV) + g (0.48MeV) (93.7%)
10B+n  a (1.78 MeV) + 7Li (1.01 MeV) (6.3%)
6Li reaction (cross section 940 barns at 0.0253 eV) :
6Li + n  a (2.05 MeV) + 3H (2.72 MeV)
6LiF layer: 3±1 mg/cm2

## Slide 39: Sample objects – blank cartridge
Photograph
CCD
Medipix-1
Imaging
plate
Medipix-2
Neutronography
Roentgenography
Medipix-2
Medipix-1

## Slide 40: Flower behind Al plate
Seeds

## Slide 41: 3D reconstructions
3D reconstruction - neutron
3D reconstruction – X-ray

## Slide 42
Range Uncertainties
(measured with PTR)
> 5 mm
> 10 mm
> 15 mm
Alderson Head Phantom
Schneider U. (1994), “Proton radiography as a tool for quality control in proton therapy,” Med Phys. 22, 353.
RSP
H
Proton CT Basics
Proton therapy and treatment planning requires the knowledge of the stopping power
in the patient, so that the Bragg peak can be located within the tumor. X-ray CT has been shown to give insufficiently accurate stopping power (S.P.) maps in
complicated phantoms or from uncertainty in converting Hounsfield values to S.P.
The goal of Proton CT is to reconstruct a 3D map of the stopping power
within the patient with as fine a voxel size as practical at a minimum dose,
using protons (instead of x-rays) in transmission. In a rotational scan the integrated stopping power is determined for every view
by a measurement of the energy loss.

## Slide 43: Proton CT (pCT) Concept
An energetic low intensity cone beam of protons traverses the patient
The position and direction (entry & exit) and energy loss of each proton is measured
Proton histories are taken from multiple projection angles
(angular “CT scan”)
Minimal proton loss and high detection efficiency make this a low-dose imaging modality
Design of a Proton CT Scanner rotating with the proton gantry
(R Schulte et al. IEEE Trans. Nucl. Sci., 51(3), 866-872, 2004)
Low intensity proton beam
Tracking of individual protons
Measure Stopping power distribution directly (instead of converting X-ray CT scans

## Slide 44: Low Contrast in Proton CT
High contrast in absorption of Photons
N(x) = Noe- m x
with the linear absorption coefficient µ differing by a factor 10 between bone and soft tissue.
Low contrast in energy loss of Protons
with the stopping power dE/dl only 50% larger for bone than for soft tissue.
NIST Data
Bethe-Bloch

## Slide 45: pCT Challenges
D C Williams Phys. Med. Biol. 49 (2004) 2899–2911
The proton path inside the patient/phantom is not straight  the path of every proton before and after the phantom
has to be measured and its path inside
the patient reconstructed.
From deflection and displacement, calculate the “Most Likely Path MLP”
#1: Multiple Coulomb Scattering
#2: Proton Data Rate
Data Flow math: Assuming 100 protons / 1mm voxel and 180 views requires ~ 7*108 protons.
A scan with a proton rate of 2 MHz takes 6 min with a dose of 1.5 mGy. Image Reconstruction To reconstruct images with > 107 voxels using ~109 protons is NOT trivial. Our reconstruction code is already running on GPU’s in anticipation of the much higher data rates of the future.

## Slide 46: Hand Radiography: Something New (?)
Hand Phantom imaged with 200 MeV protons
at the Loma Linda Synchrotron,
using the existing pCT scanner.
Color-coded image
of the summed-up
stopping power
in terms of
water-equivalent
thickness [in mm].
Note the varying thickness of the hand
and clear structural details.

## Slide 47: A step forward into Imaging History..
Wilhelm Roentgen,
Laboratory Radiology (1895)
200 MeV Protons
X-Rays
UCSC-LLU-CSUSB 2012, T. Plautz et al., 2012 IEEE NSS-MIC
Stopping Power
Multiple Scattering

## Slide 48: Summary
Vivid field
Broad range of applications
Inspired by particle physics, but developing autonomously
Particle physics experience still useful
Companies exist also in the Czech Republic