## Slide 1: Reactor Neutrinos
Xin Qian
xqian@bnl.gov
Borrowed many materials from my colleague Dr. Chao Zhang (czhang@bnl.gov), who is traveling right now

## Slide 2: Me and Reactor Neutrinos
Physicist in the Electronic Detector Group (EDG), Physics Department, BNL
  PhD @ Duke University (2010)
    Nucleon spin structure with electron scattering
  Post-doc @ Caltech (2010-2013)
    Daya Bay experiment (China)
    LBNE  DUNE experiment
  Staff Scientist @ BNL (2013-Now): BNL | Staff | Xin Qian, Physics Department
    PROSPECT experiment (US)
    LArTPC technology development for DUNE
    PIONEER: rare decay experiment

## Slide 3: Worlds’ First Nuclear Reactor
Chicago Pile-1 (CP-1) ~ 0.5 W power
Part of the Manhattan Project
  Did you watch “Oppenheimer” last weekend?
Designed and tested by a team of 49 scientists led by Enrico Fermi at U. Chicago
Dec 2, 1942: first human-made self-sustaining nuclear chain reaction:
  Fuel: 40-ton Uranium Oxide and 6-ton Uranium Metal
  Neutron moderator: 380-ton Graphite blocks
  Control rods: Cadmium sheets
CP-1 in a squash court under the stands of Staff Field @ U. Chicago

## Slide 4: Fission and Energy Release
1 fission 0.219 AMU 200 MeV
1 g of U-235 fission = 24,000 kwh
  3.2 tons of coal
  12.6 barrel of oil
  Lightening of a small city overnight
Energy density (energy/mass) of U-235 = 28,000 times of that of coal
Key properties of fission:
Release substantial energy (mostly as kinetic energy of the fission fragments)
Release excess neutrons: possibility of chain reaction
Reactor Design Requirement
Thermal neutrons: needs “moderator” to slow down neutrinos (water, graphite etc.)
Controllable fission: engineering to make output neutron = 1
1.008 atomic mass unit (AMU)
235.044 AMU
140.883 AMU
91.926 AMU

## Slide 5
Core Heat Removal
Coolant: Heat Transfer
Safety Systems
Confinement of Radioactivity
Electricity Production
Spent fuel processing
Reactor Core Design:
Core Power Distribution
Ability to shutdown plant
No fuel failure or melting
Schematic of a Pressurized Water Reactor (PWR)

## Slide 6
Breazeale Nuclear Reactor Start up, 500kW, 1MW, and Shut Down (ANNOTATED) - YouTube
Full video with annotations:

## Slide 7
https://www.carbonbrief.org/mapped-the-worlds-nuclear-power-plants
>450 operating nuclear reactors with >50 under construction in >30 countries, contributing to ~10% of global electricity
IEA Electricity Information 2019
2015 Ranking

## Slide 8: Production of Weapon-graded Plutonium
U-235: 52 kg critical mass
Natural abundance of 0.72% (mostly U-238)
90% and above is needed for weapon graded  electromagnetic separation, diffusions, centrifuges, highly technically challenging
Pu-239: 10 kg critical mass
93% and above for weapon graded
Produced in nuclear reactors  given enough time, all U-238  Pu
Safeguards efforts (e.g. WATCHMAN: arXiv:1502.01132)

## Slide 9: Nuclear Reactor as Antineutrino Source
Pure anti-νe source with ~6 anti-νe per fission
~2 x 1020 anti-νe/sec per GigaWatt thermal power (GWth)
Low-enriched uranium (LEU) cores in Commercial reactors in Nuclear Power Plants
  Mixture of fissions: 235U (~55%), 239Pu (~30%), 238U (~10%), 241Pu (~5%)
  Large power: ~3 GWth
Highly-enriched uranium (HEU) cores with compact size in Research reactors
  235U fission fraction ~99%
  Lower power, few tens of MWth
Rep. Prog. Phys. 82, 036201
nobelprize.org
Fission process in a nuclear reactor
Notes: Explicitly state that anue are produced in beta decay of fission daughters. This is hard to see in the image. Write out GWth = GigaWatt of thermal power.

## Slide 10
https://www.bnl.gov/about/history/reactors.php
Research Reactors typically ~10 MW
BNL’s past 3 reactors
  BGRR, HFBR, BMRR

## Slide 11: Homework Problem 1
How many antineutrinos are produced per second for a typical 3-gigawatt (thermal) commercial reactor?
  Each fission releases ~200 MeV energy. How many fissions are produced per second?
  Each fission produce ~6 antineutrinos on average from the beta-decay chains. How many antineutrinos are produced per second?

## Slide 12: Neutrino and Beta Decay
1930: Pauli’s letter to physicists at a workshop in Tubingen
Dear Radioactive Ladies and Gentlemen,
“I have done a terrible thing. I have postulated a particle that cannot be detected.”

## Slide 13: The Elusive Neutrinos
An intensive neutrino source: a billion trillion (~1021) ν per second
A huge neutrino detector: tons to kilotons of target material
A distinctive method to tell “neutrino interactions” from other backgrounds
ν
ν
100 million Earths
Neutrino detection requires:
Weak nuclear force

## Slide 14: Neutrinos from the Universe
99% of the energy in a core collapse supernova explosion is carried away by neutrinos
1038 νe/s are produced by the sun
Notes: A mole of neutrino passing through your body through your lifetime

## Slide 16: Neutrinos: First Detection
Frederick Reines and Clyde Cowan first detected (anti)neutrinos using the Savanah River nuclear reactor in South Carolina in 1956. (26 years after Pauli’s proposal)
“We are happy to inform you that we have definitely detected neutrinos from fission fragments by observing inverse beta decay of protons”
Reines and Cowan’s telegram to W. Pauli (1956)
Target: Water + CdCl2
Detector: Liquid Scintillator + PMTs

## Slide 17
Chart: Energy Budget of the Universe
| Dark Energy ~73% | Dark Matter ~23% | Visible Matter ~4% | Neutrino >~ 0.3%
Sales | 73 | 23 | 4 | 1
As fundamental particles in the standard model of particle physics, neutrinos are the second most abundant (known) particles in our universe
26 free parameters
Notes: For every proton/neutron/electron the Universe contains a billion of neutrinos from the Big Bang

## Slide 18: Discoveries with Reactor Anti-ν
2000s: KamLAND
2010s: Daya Bay
1950s: Reines and Cowan
Detection of anti-v
Solving solar v problem on Earth
Measurement of non-zero oscillation angle θ13
Currently hold the best precision of
  Δm221 (KamLAND)
  θ13 (Daya Bay)
Comparable precision to accelerator-based experiments
  | Δm232 | (Daya Bay)
Courtesy of Karsten Heeger

## Slide 19: Reactor Models
Summation (ab initio) method
  Calculate the spectrum of each beta-decay branch using nuclear databases: fission yields, decay schemes
  ~10% uncertainty
Sonzogni et al
PRC 91, 011301
Conversion Method
  Measure total outgoing beta-decay electron energy spectra
  Predict corresponding anti-neutrino spectra with >30 virtual branches
  Considered to be more precise: ~2.5% uncertainty
~6000 decay branches
reactor thermal power, energy released per fission, baseline, target protons, detection efficiency, oscillation, etc.
isotope fission fraction
isotope neutrino spectra
IBD cross section
Latest update @ PRL 123, 022502

## Slide 20: Reactor Anti-νe Detection
Coincidence signal of IBD:
Thermal neutron
Rep. Prog. Phys. 82, 036201
Inverse Beta Decay (IBD)

## Slide 21: Event Rate
Depending on the power of the reactors, size of the detectors, and the distance between them
17 GW
800 /day
500 m
80 /day
1.6 km
55 GW
180 km
1000 ton
1000 ton
1000 km
0.5 /day
10 kt TNT-equivalent
< 0.001 event
20 ton
Daya Bay
KamLAND
Nuclear Bomb Test

## Slide 22: Homework Problem 2
Daya Bay’s antineutrino detector (AD) is a 20-ton liquid scintillator detector. The far ADs are placed at ~1.6 km away from reactors with a total power of ~17 GW. How many inverse beta decay(IBD) reactions are expected per day in each far AD?
  The hydrogen mass fraction in the AD is ~12%. How many free protons (from hydrogen) are there in each AD?
  How many reactor antineutrinos per cm2 per second is expected at the AD? (this is referred as the “flux”)
  The average IBD cross section is ~3x10-43 cm2 , calculate event rate = flux * cross section * number of protons, assuming 100% detection efficiency. (remember that IBD can only detect 1/3 of all reactor antineutrinos)

## Slide 23: Reactor Neutrino Experiments
Four major motivations:
  Measurement of fundamental parameters (MB, SB)
  Search for new physics (VSB, SB, MB)
  Measurement of neutrino flux, spectrum, evolution (SB, VSB)
  Technology development (MB, VSB, SB)
Courtesy of Chao Zhang

## Slide 24: Measurement of Fundamental Parameters
4 MeV
Nat. commun. 6, 6935
Prog. Part. Nucl. Phys. 83, 1
Notes: neutrino oscillation enables access to fundamental parameters.
Neutrino mass hierarchy, explain,
Explain atm, or sol

## Slide 25
Far AD
(1.6 km)
Near AD
(500 m)
Far/Near Neutrino Ratio
Detector
Target Mass
Detector Efficiency
Survival Probability (θ13)
Distance
from
Reactor

## Slide 26
Image credit: H. Murayama
Δm2 ~ 7.5 x 10-5 eV2
Chao Zhang’s Ph. D thesis
Daya Bay data
Δm2 ~ 2.5 x 10-3 eV2
My post-doc work @ Caltech
survival probability

## Slide 27
Statistics
  powerful reactors (17.4 GWth) + large detectors (80 ton at Far site)
Systematics
Reactor
  Far/Near relative measurement
Detector
  multiple functionally identical detectors (4 Near + 4 Far)
Background
  deep underground (860 m.w.e at far site)
Designed to discover sin2(2θ13) < 0.01 @90% C.L.

## Slide 28: Detection of Reactor Neutrino in Daya Bay

## Slide 29
Discovery of non-zero θ13 at 5.2 σ
  2011/12/24 – 2012/2/17 (55 days)
  6 detectors in operation first
https://indico.bnl.gov/event/9947/
BNL virtual mini-symposium: The Daya Bay Reactor Neutrino Experiment and the Discovery of Non-zero Theta13
End of operation ceremony (Dec 24, 2011 - Dec 12, 2020)
In fact, in the first 5 days we already knew that θ13 is large from the data. In the homework I’ll give you all the inputs to do a simplified analysis.
Phys. Rev. Lett. 108, 171803 (2012)

## Slide 30: Homework Problem 3
How to discover the smallest neutrino oscillation with 5 days of Daya Bay reactor neutrino data?

## Slide 31: Reactor and Detector Location
Reactor | D1 | D2 | L1 | L2 | L3 | L4
x (m) | 43.0 | -44.6 | 856.0 | 792.3 | 1143.6 | 1076.5
y (m) | -7.0 | 6.9 | 830.9 | 767.9 | 1206.1 | 1138.5
z (m) | -12.0 | -12.0 | -12.0 | -12.0 | -12.0 | -12.0
AD | 1 | 2 | 3 | 4 | 5 | 6
x (m) | 94.5 | 97.8 | 584.1 | -254.3 | -259.5 | 257.3
y (m) | 350.2 | 345.2 | 1216.2 | 1892.6 | 1889.6 | 897.8
z (m) | -20.0 | -20.0 | -16.6 | -15.4 | -15.4 | -15.4
All reactor cores operated at approximately equal power for the 5 days
  L2 was powered off during the 5 days

## Slide 32: Summary of event selection for the first 5 days
Backgrounds
Calculate the signal rate per day after efficiency correction
  EH1-AD1: (3278 - 60.9 – 43 - 6) / 0.8144 / 5.39 = 721.7 events/day
Calculate the statistical error on the signal rate
  EH1-AD1: sqrt(3278)/0.8144/5.39 = 13.0 events/day
Signal + Backgrounds

## Slide 33: Background to IBD
Accidentals: statistically calculate from uncorrelated singles
Li9 / He8: measure time distribution of after-muon events
Fast neutron: measure energy spectrum from AD/water/RPC tagged muon events
Background | Near | Far | Uncertainty
Accidentals | 1.4% | 2.3% | negligible
Li-9 / He-8 | 0.4% | 0.4% | ~30%
Fast neutron | 0.1% | 0.1% | ~30%

## Slide 34
How to discover the smallest neutrino oscillation with 5 days of Daya Bay reactor neutrino data?
  Plot the measured antineutrino signal rate of each AD vs. the expected flux, assuming each AD has the same size, and each reactor has the same power.
  Fit the data (what function to use?) with the near ADs and extrapolate to the far ADs. What do you see?
  What is the “survival probability” in the far ADs relative to the near ADs? What is the statistical significance of this observation?
  What is the size of θ13 using the oscillation formula?
Δm2 | 2.4 x 10-3 (eV2)
L | 1.66 x 103 (m)
E | 3.5 (MeV)

## Slide 35
Daya Bay
Near Hall
Ling Ao
Near Hall
Far Hall
Data taking (12/24/2011 – 12/12/2020)
  3275 days, 5.5M events largest reactor neutrino data sample in the world

## Slide 36: Precision Oscillation (1/26 free parameters in the SM)
Final results with the full data set
Phys. Rev. Lett. 130, 161802 (2023)
Likely to be the best measurement in the foreseeable future
Critical input to the current and future long-baseline experiments (DUNE)
(2.8% precision)
Daya Bay Near Hall
Ling Ao Near Hall
Far Hall

## Slide 37: Resolution of the Neutrino Mass Hierarchy (MH or NMO) with Reactors
20 kt JUNO detector with better than 3% energy resolution @ 1 MeV and better than 1% energy scale determination
~100k neutrino events with ~27 GWth  3σ MH sensitivity*
JUNO
Ann. Rev. Nucl. Part. Sci. 67, 183
PRD 87, 033005
* See PRD 86, 113011 for the statistical interpretation of MH sensitivity
Notes: 6 -7 years …

## Slide 38: Micro-Channel Plate PMT and High-Light-Yield Liquid Scintillator (LS)
3% energy resolution @ 1 MeV
PMTs:
17,600 20’’ PMT
25,000 3’’ PMT
Coverage 77.5%
LS:
104 PE/MeV
Latt > 20 m @ 430 nm
Low background
PDE: Photon Detection Efficiency
http://juno.ihep.cas.cn/
20 kT liquid scintillator
~40 m

## Slide 39: Construction Process of JUNO

## Slide 40
Questions?