## Slide 1
Atomic Clock Ensemble in Space
Luigi Cacciapuoti
16-20 October 2023
9th Symposium on Frequency Standards and Metrology
Kingscliff – Australia

## Slide 2: ACES mission concept

## Slide 3: The Columbus module

## Slide 4: The ACES payload
Volume: 1172x867x1246 mm3
Mass: 240 kg (w/o CEPA)
Power: 600 W
PHARAO (CNES): Atomic clock based on laser cooled Cs atoms
SHM: Active hydrogen maser
FCDP: Clocks comparison and distribution
MWL : T&F transfer link
GNSS receiver
ELT: Optical link
Support subsystems
  XPLC: External PL computer
  PDU: Power distribution unit,
  Mechanical, thermal subsystems
  CEPA: Columbus External PL Adapter

## Slide 5: The ACES clock signal
PHARAO accuracy ~110-16
The ACES clock signal (red curve) combines the good short-to-medium term frequency stability of the active H-maser SHM with the long-term stability and accuracy of the Cs clock PHARAO.
Two servo-loops control the clocks with two different time constants: the short-term servo-loop (PLL) steers PHARAO local oscillator on SHM (1-2 s time constant); the long-term servo-loop (FLL) corrects SHM against long term drifts (100-500 s time constant).

## Slide 6: PHARAO and ACES stability
PHARAO stability in autonomous mode
ACES stability with STSL and LTSL closed and in the presence of magnetic and thermal perturbations

## Slide 7: ACES time & frequency links
Ground clock comparisons with MWL
Common view: 1.410-15 after 300 s (ISS pass duration) and 110-17 in less than 1 day.
Non common view: 110-15 after 2700 s, 110-17 in 3-4 days (calculated assuming a deadtime of 2700 s).
MWL ground terminal
ELT detector

## Slide 8: MWL
Two-way link:
    Removal of the troposphere time delay (8.3-103 ns)
    Removal of 1st order Doppler effect
    Removal of instrumental delays and common mode effects
Additional down-link in the S-band:
    Determination of the ionosphere TEC
    Correction of the ionosphere time delay (0.3-40 ns in S-band, 6-810 ps in Ku-band)
Phase PN code modulation: Removal of 2p phase ambiguity
High chip rate (100 MChip/s) on the code:
    Higher resolution
    Multipath suppression
Carrier and code phase measurements (80 ms sampling time)
Data link: 2 kBits/s on the S-band down-link to obtain clock comparison results in real time
Up to 4 simultaneous space-to-ground clock comparisons

## Slide 9: MWL measurements and scientific products
Code and carrier phase measurements on Ku-band up/down-link
and S-band down-link
where
Scientific Products |  | …from
Space-to-ground Desynchronization |  | 
Ionosphere Total Electron Content |  | 
Range + Tropospheric Delay | & | 

## Slide 10: MWL PFM performance - Static
MWL Time deviation [s]: 2-way combination of common clock measurements under static conditions (no signal dynamics)

## Slide 11: MWL PFM performance – Signal dynamics
4 DLLs simultaneously tracking the same signal
DLLx – DLLy code and carrier phase

## Slide 12: MWL PFM performance – Signal dynamics
Time Deviation [s] of DLLx – DLLy code and carrier phase data
DLLx – DLLy code and carrier phase data after removing data containing carrier cycle slips

## Slide 13: ACES MWL network

## Slide 14: European Laser Timing (ELT)
Detector package 500 grams
0.6 Watt
CTU Prague
ACES Time Scale
(MWL)
ACES
Power
TM/TC

## Slide 15: ELT performance - Preliminary
ELT Time Stability [s]: dark counts detection events vs NPET time tagging measurements at 100 Hz gate rate
ELT detector package tested from -55C to +60C: KT=1 ps/K
ELT Calibration Campaign at Graz SLR (1 yr)

## Slide 16: ILRS network of SLR stations
ACES as official ILRS target: Wettzell (primary station), Graz, Herstmonceaux, Potsdam, and Zimmerwald SLR stations already calibrated; other stations can join provided they comply with ISS safety requirements.

## Slide 17: ACES – Fundamental Physics tests
ACES Mission Objectives | ACES performances | Scientific background and recent results
Gravitational red-shift | Absolute measurement of the gravitational red-shift to < 2∙10-6 after 10 days of integration time. | Factor 70 improvement over the GPA experiment and factor 10 over tests involving Galileo 5 and 6 satellites.
Time drifts of fundamental constants | Time variations of a constrained to a -1da /dt < 310-18 yr-1 after 3 years of mission. | Comparisons of clocks based on different atoms and atomic transitions on a worldwide scale to constrain a, me/LQCD and mq/LQCD.
Dark matter search with atomic clocks | Establish bounds on topological dark matter models based on the comparisons of clocks in the ACES network. | Comparisons via the ACES network imposing limits on the three coupling constants , , and in the model lLagrangian. Measurements over an interval between encounters of 20 d. Simultaneous observation with several clocks along different baselines providing ways to confirm any observation above the sensitivity threshold and control the measurement systematics. Screening effect on the dark matter field due to the Earth mass reduced to about 0.06 on the space clock PHARAO with respect to ground clocks (~ 10-7).
ACES Mission Objectives | ACES performances | Scientific background and recent results
Gravitational red-shift | Absolute measurement of the gravitational red-shift to < 2∙10-6 after 10 days of integration time. | Factor 70 improvement over the GPA experiment and factor 10 over tests involving Galileo 5 and 6 satellites.
Time drifts of fundamental constants | Time variations of a constrained to a -1da /dt < 310-18 yr-1 after 3 years of mission. | Comparisons of clocks based on different atoms and atomic transitions on a worldwide scale to constrain a, me/LQCD and mq/LQCD.
Dark matter search with atomic clocks | Establish bounds on topological dark matter models based on the comparisons of clocks in the ACES network. | 

## Slide 18: Gravitational redshift test
Frequency shifts | 
First order Doppler effect | 210-5
Second order Doppler effect | 310-10
Gravitational red-shift | 510-11
Sagnac effect | 710-13

## Slide 19: A network of atomic clocks to test fundamental physics
ACES as a relay satellite to transfer time and frequency on a worldwide scale.
Comparisons of ground clocks (microwave and optical) to better than 110-17.

## Slide 20: Time variations of fundamental constants
Frequency of hyperfine transitions:
Frequency of electronic transitions:
Ratios between atomic frequencies:
and depend on the QCD mass scale and thus
V.V. Flambaum, Laser Spectroscopy, pp. 49-57 (2004)
V.V. Flambaum et al., Phys. Rev. D 69, 115006 (2004)
hyperfine transitions
electronic transitions
vibrational transitions

## Slide 21: Dark matter search
Atomic clock networks can be used to search for dark matter and place boundaries on certain models, e.g. topological dark matter (TDM).
TDM is represented by a scalar field that couples to fundamental constants thus inducing fluctuations of atomic transition frequencies.
The ACES network can ensure comparisons of atomic clocks based on different atomic transitions down to 110-17, in the optical domain, in the microwave domain, and optical vs microwave.
Limits on variations for each of the three fundamental constants can be established thus testing different terms in the model Lagrangian and imposing limits on the three energy scales , , and .
The simultaneous observation with several clocks compared along different baselines will provide ways to confirm any observation above the sensitivity threshold and control the measurement systematics.
Clock comparisons can be performed continuously on 20 d intervals thanks to the ACES MWL, extending the time between encounters.
Screening effect of the dark matter field due to the Earth mass reduced to about 0.06 on the space clock PHARAO with respect to ground clocks (~ 10-7).

## Slide 22: ACES – Scientific applications
Relativistic geodesy
Relativistic geodesy: mapping of the Earth gravitational potential based on the red-shift measured between two clocks at two different locations.
ACES intercontinental comparisons of optical clocks at the 10-17 level after 4 days, corresponding to a resolution on the local height above the geoid at the 10 cm level.
The global coverage offered by ACES will complement the results of the CHAMP, GRACE, and GOCE missions.
Clocks synchronization
MWL and ELT clocks synchronization at the 100 ps and 50 ps level, respectively.
Atomic time scales (TAI)
The PHARAO clock is accurate to 1-210-16.
MWL will provide means to compare atomic clocks on a worldwide scale:
  PHARAO and primary standards on ground contributing to TAI.
  Optical clock comparisons to 110-17 will help SI second redefinition.

## Slide 23: Way-forward to the ACES launch
A first run of the ACES Integrated System Tests (IST) tests has been completed. They included:
  ACES servo-loops performance
  ACES clock signal performance evaluation
  Sensitivity under temperature and magnetic field variations
IST revealed a major anomaly: SHM getters had reached end-of-life and needed replacement.
Acceptance status of ACES:
  PHARAO clock PFM, ELT detector package, ACES GNSS system and FCDP PFM are integrated.
  SHM PFM getters have been replaced and acceptance tests completed. SHM is now integrated in the ACES payload.
  MWL PFM is completing qualification tests before final acceptance (by end 2023).
  ACES payload performance tests planned for summer 2024.
ACES PFM delivered for launch on SpaceX in end 2024 – beginning 2025.
MWL GTs deployment will start in mid 2024 (SYRTE, PTB and Wettzell); the other institutes will follow.

## Slide 24
L. Cacciapuoti1, M. Armano1, R. Jansen1, R. Much1, S. Weinberg1, P. Crescence2, A. Helm2, J. Kehrer2, S. Koller2, R. Lachaud2, T. Niedermaier2, F.X. Esnault3, D. Massonnet3, J. Pittet4, P. Rochat4, S. Liu5, W. Schaefer5, T. Schwall5, I. Prochazka6, A. Schlicht7, U. Schreiber7, P. Delva8, P. Laurent8, M. Lilley8, P. Wolf8, C. Salomon9
1European Space Agency, ESTEC, Noordwijk, The Netherlands
2Airbus Defence and Space, Friedrichshafen, Germany
3CNES, Toulouse, France
4Orolia Switzerland (Spectratime), Neuchˆatel, Switzerland
5Timetech, Stuttgart, Germany
6Czech Technical University in Prague, Prague, Czech Republic
7Technical University of Munich, Munich, Germany
8SYRTE, Observatoire de Paris-PSL, CNRS, Sorbonne Université, LNE, Paris, France
9Laboratoire Kastler Brossel, ENS, Paris, France