## Slide 1: Robust optical clocks for international timescales (ROCIT) Helen Margolis, NPL 9th Symposium on Frequency Standards and Metrology, Kingscliff, New South Wales, Australia, 18th October 2023

## Slide 2: The ROCIT consortium
8 internal partners:
NPL (UK)
CMI (Czech Republic)
GUM (Poland)
INRIM (Italy)
LNE (France)
OBSPARIS (France)
PTB (Germany)
VTT (Finland)
6 external partners:
BGU (Israel)
CNRS (France)
LUH (Germany)
POLITO (Italy)
SRC PAS (Poland)
UMK (Poland)
2 Researcher Mobility Grants:
ROA (Spain)  NPL
ROA (Spain)  OBSPARIS
2 collaborators:
AIST/NMIJ (Japan)
TiFOON consortium (Europe)
M9 consortium meeting at INRIM, February 2020
Aim:
To enable European optical clocks to contribute regularly to International Atomic Time (TAI)
– a significant milestone on the path to the redefinition of the second

## Slide 3: Roadmap for the redefinition of the second
Validation that optical frequency standards (OFS) are at a level 100  better than Cs
Continuity with the definition based on Cs
Regular contributions of OFS to TAI as secondary representations of the second
Availability of sustainable techniques for OFS comparisons
Knowledge of the local geopotential with a sufficient uncertainty level
Definition allowing future more accurate realisations
Access to the realisation of the new definition
High reliability of optical frequency standards
High reliability of ultra high stability T/F links
Continuous improvement of the realization and time scales after redefinition
Regular contributions of optical clocks to UTC(k)
Availability of commercial optical clocks
Improved quality of the dissemination towards users
arXiv:2307.14141v1
Status should be advanced, even if not completely achieved at the time of redefinition
Ancillary conditions
Must be achieved before changing the definition
Mandatory criteria
Achieved
In progress
Validation that optical frequency standards (OFS) are at a level 100  better than Cs
Continuity with the definition based on Cs
Regular contributions of OFS to TAI as secondary representations of the second
Availability of sustainable techniques for OFS comparisons
Knowledge of the local geopotential with a sufficient uncertainty level
Definition allowing future more accurate realisations
Access to the realisation of the new definition
High reliability of optical frequency standards
High reliability of ultra high stability T/F links
Continuous improvement of the realization and time scales after redefinition
Regular contributions of optical clocks to UTC(k)
Availability of commercial optical clocks
Improved quality of the dissemination towards users
arXiv:2307.14141v1
Validation that optical frequency standards (OFS) are at a level 100  better than Cs
Continuity with the definition based on Cs
Regular contributions of OFS to TAI as secondary representations of the second
Availability of sustainable techniques for OFS comparisons
Knowledge of the local geopotential with a sufficient uncertainty level
Definition allowing future more accurate realisations
Access to the realisation of the new definition
ITOC
Accuracy ~ 0.2 m2s−2 or 210-18 clock accuracy

## Slide 4: Roadmap for the redefinition of the second
Status should be advanced, even if not completely achieved at the time of redefinition
Ancillary conditions
Must be achieved before changing the definition
Mandatory criteria
High reliability of optical frequency standards
High reliability of ultra high stability T/F links
Continuous improvement of the realization and time scales after redefinition
Regular contributions of optical clocks to UTC(k)
Availability of commercial optical clocks
Improved quality of the dissemination towards users
Validation that optical frequency standards (OFS) are at a level 100  better than Cs
Continuity with the definition based on Cs
Regular contributions of OFS to TAI as secondary representations of the second
Availability of sustainable techniques for OFS comparisons
Knowledge of the local geopotential with a sufficient uncertainty level
Definition allowing future more accurate realisations
Access to the realisation of the new definition
Achieved
In progress
arXiv:2307.14141v1

## Slide 5: Robust optical clocks
Tools for on-the-fly correction of systematic frequency shifts
With sufficiently low latency for UTC(k) steering
Also useful for timely contributions to TAI and faster data analysis in international comparisons
Automatic control systems (some open source)
Robust & autonomous frequency stabilisation of laser systems
Automated optical alignment
Remote monitoring and control
Software to schedule and perform operational checks, e.g. minimisation of micromotion in trapped ion clocks, magic wavelength calibration in lattice clocks
SYRTE-Sr2, PTB-Yb1E3 and NPL-Sr1 all achieved uptimes > 80% over 2 weeks

## Slide 6: Roadmap for the redefinition of the second
Status should be advanced, even if not completely achieved at the time of redefinition
Ancillary conditions
Must be achieved before changing the definition
Mandatory criteria
High reliability of optical frequency standards
High reliability of ultra high stability T/F links
Continuous improvement of the realization and time scales after redefinition
Regular contributions of optical clocks to UTC(k)
Availability of commercial optical clocks
Improved quality of the dissemination towards users
Validation that optical frequency standards (OFS) are at a level 100  better than Cs
Continuity with the definition based on Cs
Regular contributions of OFS to TAI as secondary representations of the second
Availability of sustainable techniques for OFS comparisons
Knowledge of the local geopotential with a sufficient uncertainty level
Definition allowing future more accurate realisations
Access to the realisation of the new definition
Achieved
In progress
arXiv:2307.14141v1

## Slide 7: New optical clocks and a new fibre link
New optical clocks
88Sr+ at VTT and 115In+ at LUH were completed and operated for the first time as part of the project
88Sr at UMK joined international comparisons for the first time
Data also shared from 88Sr+ at PTB
New optical fibre link established from Paris to Turin
Robust performance with long-term fractional instability and accuracy below 1018
High-accuracy optical clock comparisons can be performed between more European laboratories
C. Clivati et al., Phys. Rev. Applied 18, 054009 (2022)
VTT 88Sr+
LUH 115In+

## Slide 8: Coordinated comparison campaigns
First campaign (March 2020) badly impacted by COVID-19 pandemic
Second campaign (March 2022) much more successful
  1 month of data
  11 optical clocks in 7 different countries
  2 link technologies (fibre, GNSS)
  27 ratios measured between remote optical clocks (20 via GNSS, 7 via fibre)

## Slide 9: March 2022 comparison campaign
Optical fibre links between INRIM, LNE-SYRTE and PTB
Local links between ultrastable lasers and lasers used for long-distance links
Optical clocks
Uptimes for comparisons via fibre links:

## Slide 10: Remote frequency ratio measurements
Offset is well within uncertainty of recommended frequency value (4.31015)
Offset is statistically significant
There is growing evidence that the problem lies with the recommended frequency value
Preliminary
3 ratios determined by both techniques
Source of discrepancy in 2 out of 3 cases is not yet understood

## Slide 11: Complete body of data
Measurements are correlated
79 ratios implies up to 3081 correlation coefficients (N.B. some will be zero)
313 non-zero correlation coefficients were calculated
  40 with magnitude ≥ 0.5
  135 with magnitude ≥ 0.1
79 new frequency ratio measurements
28 ratios between remote optical clocks
51 local frequency ratios
  33 absolute frequencies (26 referenced to Cs, 7 against TAI)
  15 optical frequency ratios
  3 optical v 87Rb frequency ratios

## Slide 12: Roadmap for the redefinition of the second
Status should be advanced, even if not completely achieved at the time of redefinition
Ancillary conditions
Must be achieved before changing the definition
Mandatory criteria
High reliability of optical frequency standards
High reliability of ultra high stability T/F links
Continuous improvement of the realization and time scales after redefinition
Regular contributions of optical clocks to UTC(k)
Availability of commercial optical clocks
Improved quality of the dissemination towards users
Validation that optical frequency standards (OFS) are at a level 100  better than Cs
Continuity with the definition based on Cs
Regular contributions of OFS to TAI as secondary representations of the second
Availability of sustainable techniques for OFS comparisons
Knowledge of the local geopotential with a sufficient uncertainty level
Definition allowing future more accurate realisations
Access to the realisation of the new definition
Achieved
In progress
arXiv:2307.14141v1

## Slide 13: Real-time validation of optical clock data
Considered the whole metrological chain connecting optical clocks to the flywheel oscillators (H masers)
  Local phase-compensated fibre links
  Frequency combs used for optical-microwave comparison
  Optical clocks
Effectiveness of different approaches compared
Cycle slip detection through dual measurements
Algorithms for detecting sudden changes in frequency measurements
Validation of atom number in a Sr lattice clock

## Slide 14: Steering algorithms
Robust algorithm developed for generation of a time scale based on steering an Active Hydrogen Maser (AHM) with an optical clock
  Can deal with low uptime and long periods of unavailability of the optical clock
  Can take advantage of high uptime periods of the optical clock
Tested on both simulated and experimental (historical) data
V. Formichella, L. Galleani, G. Signorile and I. Sesia, Metrologia 59, 015002 (2022)

## Slide 15: Optical steering of UTC(k) time scales
Phase comparator
Frequency offset generator
UTC(NPL)
HM4
Frequency steers applied 3 times a week, based on data from NPL-CsF2 and Circular T
UK time scale
Frequency steers applied hourly, based on data from Sr and Yb+ optical clocks
Frequency offset generator
UTCx(NPL)
HM6
Experimental prototype

## Slide 16: Prototype optically steered time scales
Sub-ns deviation from UTC, despite technical glitches and gaps in optical clock data (32.3%)
UTC(NPL)
UTCx(NPL)
v
GPS PPP
Offset between the two prototype optically steered time scales lower than the typical offset between the two operational UTC(k) time scales
UTC(OP)
UTCx(OP)
v

## Slide 17: Roadmap for the redefinition of the second
Status should be advanced, even if not completely achieved at the time of redefinition
Ancillary conditions
Must be achieved before changing the definition
Mandatory criteria
High reliability of optical frequency standards
High reliability of ultra high stability T/F links
Continuous improvement of the realization and time scales after redefinition
Regular contributions of optical clocks to UTC(k)
Availability of commercial optical clocks
Improved quality of the dissemination towards users
Validation that optical frequency standards (OFS) are at a level 100  better than Cs
Continuity with the definition based on Cs
Regular contributions of OFS to TAI as secondary representations of the second
Availability of sustainable techniques for OFS comparisons
Knowledge of the local geopotential with a sufficient uncertainty level
Definition allowing future more accurate realisations
Access to the realisation of the new definition
Achieved
In progress
arXiv:2307.14141v1

## Slide 18: Recommended values of standard frequencies
Importance of correlations
Must be included to avoid biased frequency values and (usually) underestimated uncertainties
Guidelines prepared on the evaluation & reporting of correlation coefficients between frequency ratio measurements (http://empir.npl.co.uk/rocit/project-outputs/)
Shared with the CCL-CCTF Frequency Standards Working Group (WGFS)
Least-squares analysis procedure
Based on the approach used by CODATA to provide a self-consistent set of recommended values of the fundamental physical constants H. S. Margolis and P. Gill, Metrologia 52, 628 (2015)
First used to update the list of recommended frequency values in September 2015
http://www.bipm.org/en/publications/mises-en-pratique/standard-frequencies-second

## Slide 19: 2021 update
105 input data points (72 absolute frequencies, 33 ratios)
Correlations included for the first time (483 correlation coefficients)
  Mostly arising through the use of the same primary or secondary frequency standard to access the SI second
  86 computed on an ad-hoc basis (common data, common coefficients …)
6 secondary representations of the second now have uncertainties 21016

## Slide 20: Optical clock contributions to TAI
Similar to the approach used for primary frequency standards
Calibrate a commercial clock for which phase comparison data is submitted on a continuous basis to the BIPM
Use the frequency of the optical clock as listed in the “Recommended values of standard frequencies”
Sr lattice clock
frep
f0
Femtosecond comb
H-maser
For first submission of a new standard
  Several calibration values must be provided (do not need to be contiguous)
  Operation of the frequency standard and its uncertainty evaluation must be described in a peer-reviewed publication
Material must be reviewed and approved by the CCTF Working Group on Primary and Secondary Frequency Standards before the clock can be used for steering of TAI

## Slide 21: Optical clock contributions to TAI
SYRTE-Sr2
5 contributions used for TAI steering (Jun – Aug 2021 and Mar – Apr 2022)
One contribution so far in 2023
IT-Yb1
First contribution in Nov 2019
9 further contributions used for TAI steering (Feb – Oct 2022)
7 more since then
Highest-weight clock in July 2022!
https://webtai.bipm.org/database/show_psfs.html
NPL-Sr1
First contribution in March 2023
3 more since then
Suitable data also gathered from other optical clocks …
12 optical clocks, 55 periods ranging from 5 – 35 days, total cumulative data acquisition period > 1000 days
Almost 40% of the “on time” contributions from optical clocks

## Slide 22: New record set in March 2022
Circular T no. 411 – 5 optical clocks contributing

## Slide 23: Summary
More robust optical clocks, achieving unattended uptimes > 80 % over a few weeks
Tools for on-the-fly evaluation of systematic frequency shifts and real-time validation of optical clock data
An extensive programme of optical clock comparisons to check performance levels
First direct comparison of two prototype optically steered time scales
Guidelines on evaluating correlations between frequency ratio measurements influenced the 2021 update to the CIPM list of recommended values of standard frequencies
3 European optical clocks now contributing to TAI as secondary representations of the second

## Slide 24: Future perspectives
Intercontinental clock comparisons using optical fibre?
Transatlantic fibre linking Halifax and Southport (5860 km long)
So far mainly used for environmental sensing
  G. Marra et al., Science 361, 486 (2018)
  G. Marra et al., Science 376, 874 (2022)
Also offers prospects for intercontinental clock comparisons
  Environmentally induced noise lower than for terrestrial fibre
International comparisons using transportable optical clocks (ICON project)

## Slide 25: Thank you for listening!
http://empir.npl.co.uk/rocit/
helen.margolis@npl.co.uk