## Slide 1
Time crystals as regenerative frequency dividers
and other time and frequency applications of low noise photonic systems
Andrey B. Matsko
Jet Propulsion Laboratory, California Institute of Technology

## Slide 2: Contents
Background on low loss systems and (some) of their uses at JPL
  JPL’s Frequency and Timing Advanced Instrument Development group: main activities and interests
Early studies of dissipative solitons and parametric instabilities in low loss photonic systems
  Low loss resonant (micro)systems
  Dissipative solitons in high-Q systems
  Use of dissipative solitons (and not only the solitons) in clocks and oscillators
Recent developments
  Fundamental limitations of spectral purity of photonic oscillators: theory and experiments
  Photonic time crystals as ideal frequency dividers and their use in clocks
Outlook

## Slide 3: Contents
Background on low loss systems and (some) of their uses at JPL
  JPL’s Frequency and Timing Advanced Instrument Development group: main activities and interests
Early studies of dissipative solitons and parametric instabilities in low loss photonic systems
  Low loss resonant (micro)systems
  Dissipative solitons in high-Q systems
  Use of dissipative solitons (and not only the solitons) in clocks and oscillators
Recent developments
  Fundamental limitations of spectral purity of photonic oscillators: theory and experiments
  Photonic time crystals as ideal frequency dividers and their use in clocks
Outlook

## Slide 4: Deep Space Network Clocks and Oscillators
H-Masers
Photonic Frequency
Distribution
Time Distribution
FTS in each DSN Cite includes:
Redundant atomic frequency standards
Redundant clocks
Signal distribution via fiber optic links
S, X, Ka phase reference combs
Performance measurement and calibration capabilities
Frequency Distribution
DSS-xx
M&C, GPS
Master Clock
Carrier Offset | DSN Requirement (dBc/Hz) | SAO H-maser + VCO (dBc/Hz) | SAO H-maser + CSO (dBc/Hz)
1 Hz | -118 | -123 to -130 -128 (typ.) | -151 to -161
10 | -129 | -147 (typ.) | 
100 | -141 | -152 (typ.) | 
Phase Noise Comparison @ 5 MHz
C. Thornton and J. Border, 2003, Radiometric Tracking Techniques for Deep Space Navigation, JPL Deep Space Communications and Navigation Series (John Wiley & Sons, New York).
This is not research but hard-core engineering
Allowed operation disruption is 8 min per year

## Slide 5: Canberra Site a Week Ago

## Slide 6: DSN Low Loss Photonics Links
JPL time and frequency group was the first one to utilize optical fibers for time and frequency transfer [G. Lutes, “Experimental optical fiber communications link,” TDA Prog. report 42-59 (Jet Propulsion Laboratory, 1980), pp. 77–85]
Stability of existing links is better than the stability of a maser.
Appl. Opt. Vol. 60, No. 12
/ 20 April 2021 / p. 3487
DT=2C
DT=15C

## Slide 7: More than 20 years history of Mercury Ion Clock development
Many people have been involved
Achievable Stability:
Local Oscillator (< 10s)
SNR*Q (~10s to 1 day)
Systematic offsets/environment (> 1 day)
  Magnetic Shifts
  Number (Doppler Shifts) – QP only
  Collision Shifts
  Light Shifts – QP only
  Please note that Q is important here
Mercury Ion Clock for a NASA Technology Demonstration Mission;
IEEE UFFC Transactions, Vol. 63, No.7, July 2016.

## Slide 8: Development of Ultrastable Fabry-Perot Cavities
Stable laser based on Fabry Perot etalon:
spacer
Laser
substrate
coating
Highly stable optical frequency is critical in a variety of advanced research direction: optical atomic clock, gravational wave detection, very long base line interferometry, geodesy…
Very long baseline
interferometry
LIGO
Laser Interferometer
Gravitational Wave Observatory
LISA
Laser Interferometer Space Antenna
Optical atomic clock
Cavity length fluctuation
Optical frequency stability
Laser frequency is referenced to cavity length
Wei Zhang et al.

## Slide 9: An Ultrastable Optical Cavity System Can Be Better Than Quantum Clocks
A JILA silicon Fabry-Perot cavity at 4 Kelvin
frequency stability 6×10-17, drift <5×10-19/s
Frequency comb
Low noise microwave reference
Cesium fountain clock (10 GHz)
Mercury clock (40 GHz)
VLBI, Radar…
Photodetector
Photonics microwave generation
LO for optical clock
Stable Optical Carrier for time keeping
vs
Typical results at 10 GHz
Cavity vs Maser over 30 days time error X10 improvement
Sr atomic optical clock
Wei Zhang et al.

## Slide 10: Development of Sapphire (DBR) Resonator
Goal: Support legacy of John Dick, Lute Maleki and others and develop RF oscillators based on low loss crystals.
An intrinsic Q-factor of 2×105 is demonstrated at 36 GHz for the lowest order TE-mode of a sapphire DBR.
An oscillator suitable for the mercury clock operation is the next step of the development.
V. Iltchenko, et. al. TBP

## Slide 11: Future Drivers of the Frequency & Timing Systems Development
Optical Communications
NASA Space Networking
Planetary Networks
Antenna arrays
t
Today’s DSN
(S, X, Ka bands)
φ
f
Reliability and SWaP are in the development focus (R. Tjoelker)

## Slide 12: Contents
Background on low loss systems and (some) of their uses at JPL
  JPL’s Frequency and Timing Advanced Instrument Development group: main activities and interests
Early studies of dissipative solitons and parametric instabilities in low loss photonic systems
  Low loss resonant (micro)systems
  Dissipative solitons in high-Q systems
  Use of dissipative solitons (and not only the solitons) in clocks and oscillators
Recent developments
  Fundamental limitations of spectral purity of photonic oscillators: theory and experiments
  Photonic time crystals as ideal frequency dividers and their use in clocks
Outlook

## Slide 13
How the modern (micro) photonics can help to push forward our time and frequency applications?
Stable and spectrally pure (UV) lasers
Stable and spectrally pure photonic oscillators

## Slide 14: Whispering Gallery Mode Resonators
*Transparency of most of the optical materials is not well documented in literature and the documented values vary by an order of magnitude
E.D.Palik, “Handbook on optical
constants of solids”, Academic, NY, 1998
For
Solid state optical resonators with dimensions ranging from 10’s of micron to a few mm, to support various applications
Extremely high Q’s (record > 1011 in CaF2) ~1x109 LiTaO3
Easy to T control/ encapsulate
Can support any broad range of wavelengths (unique feature)
A toolbox of low loss optical coupling solutions is developed
Andrey Matsko, WMB6, IMS2019
CaF2 | 3x10-7 cm-1
SiO2 (optical fiber) | 5x10-6 cm-1
Al2O3 | 1x10-5 cm-1
SiO2 (crystal) | 1x10-5 cm-1
Si (crystal) | 8x10-5 cm-1
LiNbO3/LiTaO3 | 1x10-4 cm-1
Si3N4/Hydex | 1x10-2 cm-1
Polymers | 1x10-1 cm-1
Cavities enable stable oscillators. Q-factor of a cavity is ultimately determined by the material attenuation a:

## Slide 15: Attenuation of the material
M. Sparks and L. J. Sham, Phys. Rev. B 8, 3037 (1973)
The multiphonon absorption occurs due to
unharmonicity of internal vibrational modes
of an ideal crystalline lattice
F. Urbach, Phys. Rev. 92, 1324 (1953)
The density of states is not zero at the band edge.
There are always band tails in non ideal crystals.
In the center of the transparency window the attenuation is given by the impurities and scattering
Surface scattering is the leading effect in crystalline cavities
M.L Gorodetsky et al., Opt. Lett. 21, 453 (1996);
D.W. Vernooy et al., Opt. Lett.23, 247 (1998);
L. Collot et al., Europhys. Lett. 23, 327 (1993);
V.B. Braginsky et al., Phys. Lett. A 137, 393 (1989).

## Slide 16: Variety of the solid state WGMRs (early results)
CaF2: Savchenkov et al, PRA 70, 051804 (2004); OE 15, 6768 (2007).
Grudinin et al Opt. Commun. 265, 33-38 (2006).
CaF2 Qm>105: J. Hofer, A. Schliesser, P. Del’Haye, and T. Kippenberg (CLEO’09)
LN WGM resonator,
D. Haertle, T. Beckmann, J. Schwesyg, S. Hermann, A. Zimmermann, K. Buse
Photonics West 2009
LN WGM: D.A. Cohen and A.F.J. Levi, Electron. Lett. 37 (1) , 2001.
MgF2 resonator, C. Y. Wang, T. Herr, P. Del'Haye, A. Schliesser, J. Hofer, R. Holzwarth, T. W. Hänsch, N. Picqué, T. J. Kippenberg, arXiv:1109.2716
MgF2 resonator,
OEwaves (2011)
BBO resonator,
JPL, 2012
SBN resonator,
OEwaves (2012)
Si: Appl. Phys. Lett. 85 (2004)
Fused silica: K. Vahala et al., Nature 421, 925 (2003)
Solid H2: K. Hakuta et al. OL 27 (2002)
Fused silica: Gorodetsky et al., OL 21, 453 (1996).
C. G. B. Garrett, W. Kaiser, and W. L. Bond, "Stimulated emission into optical whispering gallery modes of spheres", Phys. Rev. 124, 1807-1809 (1961).
P. Walsh and G. Kemeny, "Laser operation without spikes in a ruby ring", J. Appl. Phys. 34, 956-957 (1963).
D. Roess and G. Gehrer, "Selection of discrete modes in toroidal lasers", Proc. of IEEE 52, 1359-1360 (1964).
Please note, the first crystalline WGMRs were created well before 1996.

## Slide 17: Resonators of nearly any reasonable size can be created by mechanical polishing
Grudinin et al., Opt. Commun. 265, 33 (2006).

## Slide 18: Importance of size and Q-factor for EM mixing
Q
V
Cavity field build-up
factor and linewidth
Small size and high optical energy density
Figure of merit for nonlinear processes:
SRS and FWM: n=2
Purcell’s factor: n=1
Frequency doubling and acousto-optics: n=3
Cavities enable efficient nonlinear interaction

## Slide 19: Microcavity-based dissipative solitons: some early studies
A. B. Matsko et al., Phys. Rev. A 85, 023830 (2012)
A. B. Matsko et al., Opt. Lett. 38, 525 (2013)
Multistability
Chaos
A. B. Matsko et al. Opt. Lett. 37, 4856 (2012)

## Slide 20
Optical clocks using high-Q microcavities

## Slide 21: Optical Clocks
Trapping/cooling lasers
Atomic reference
Locking feedback
LO ultrastable laser
Optical to RF divider
Electronics and control
High power and frequency stability
Low RIN and frequency noise
Low vibration sensitivity
Low RAM
Compact
Low SWaP
High stability
High finesse
Low environmental sensitivity
Low SWaP
High stability
Low environmental sensitivity
Lasers
Reference cavities
Kerr combs
Now, using the high-Q cavities we can improve clocks
Supported by JPL, NASA, ONR, AFRL and DARPA, in collaboration with Nan Yu et al.

## Slide 22: Atomic Cell Stabilized Laser: Improved Locking Due to High-Q Cavity
W. Liang et al., Appl. Opt. 54, 3353-3359 (2015)
A frequency comb is needed to make a clock
Low relative amplitude modulaton (RAM) is essential for the accurate locking to the atomic transition.
Was supported by DARPA

## Slide 23
A microwave signal is generated by demodulating the Kerr comb with a high-frequency photodiode. (a) The signal on logarithmic scale; (b) the same signal on linear scale; (c) optical comb used in the experiment. Linear fit of the microwave line gives a 40 Hz linewidth.
Main idea: Frequency stability can be transferred from optical frequency to microwave frequency using an optical comb. The stabilization goes through the resonator stability. Does not works well because of the efficiency dips.
Atomic Transition Stabilized Kerr Frequency Comb
The idea still can work IF/WHEN a good single mode cavity will be created
Was supported by DARPA

## Slide 24
Stabilized Blue Lasers

## Slide 25
Stabilized Magenta Lasers

## Slide 26: Problem to solve
Need to create a laser at 194 nm

## Slide 27
RF oscillators based on dissipative solitons

## Slide 28: Spectrally Pure RF Oscillators
RF oscillators are needed in a variety of systems including:
Radar
Direction finding of signals of interest
Applications related to coherent operation across multiple segmented platforms
Radar operational requirements include ever-increasing demands for lower-phase noise signal and waveform generation
RF photonic oscillators are characterized with
High Spectral Purity
Low Environmental sensitivity
Small SWaP
Convenient Signal Distribution
Existing electronic technologies cannot meet these demands concurrently within environmental and tactical requirements

## Slide 29: Advantages of Nonlinear Microcavities
High transparency/Low loss materials
Low bending and radiative losses
  Allows for direct generation of high frequency
  Small size
Low vibration sensitivity
  Small size
Superior phase noise owing to high-Q
Relatively simple design
Division of the optical frequency noise
Phase noise of the 28 GHz signal generated by the packaged photonic oscillator. Inset represents Laser, Resonator and Coupling optics layout. 28 GHz resonator ~ 2.5 mm in diameter. Non-soliton regime is utilized.
The phase noise measurement is limited by performance of the phase noise measurement setup.
D Seidel et al., “Minituarized Ka-band Photonic Oscillators”, 2018 International Topical Meeting on Microwave Photonics

## Slide 30: Performance Optimization
Unit 1 produces irregular combs. Unit 2 produces symmetric multi-soliton combs.
RF phase noise is comparable -> solitons are unnecessary for good RF performance.
30
A. Matsko, et al. "Turn-key operation and stabilization of Kerr frequency combs" 2016 IEEE International Frequency Control Symposium (IFCS).

## Slide 31: Timing Jitter
Photonic oscillators are also ideal for 5G and 6G applications
KOEO – Kerr comb oscillator
COEO– Coupled Opto-Electronic Oscillator
W. Liang et al., Nature Commun. 6, Article no: 7957 (2015)
Was supported by DARPA

## Slide 32: Problem to solve
Need to reach AD~10-13 at 1s

## Slide 33: Contents
Background on low loss systems and (some) of their uses at JPL
  JPL’s Frequency and Timing Advanced Instrument Development group: main activities and interests
Early studies of dissipative solitons and parametric instabilities in low loss photonic systems
  Low loss resonant (micro)systems
  Dissipative solitons in high-Q systems
  Use of dissipative solitons (and not only the solitons) in clocks and oscillators
Recent developments
  Fundamental limitations of spectral purity of photonic oscillators: theory and experiments
  Photonic time crystals as ideal frequency dividers and their use in clocks
Outlook

## Slide 34
Fundamental limitations of spectral purity of Kerr comb oscillators: theory and experiment

## Slide 35: Analytical Theory of the Mode Locked Comb
Kerr frequency combs can be analyzed using Lugiato-Lefever (LL) equation accompanied by the standard high finesse cavity input-output equation:
or by two input-output equations, in the case of two optical couplers:
A. B. Matsko et al., “Whispering gallery mode oscillators and optical comb generators,” Proc. of 7th Symp. Frequency Standards and Metrology, ed. L. Maleki, pp. 539–558 (World Scientific, New Jersey, 2009).
A. B. Matsko et al., “Mode-locked Kerr frequency combs,” Opt. Lett. 36, 2845–2847 (2011).
A. B. Matsko and L. Maleki Optics Express 21 (23), 28862 (2013).

## Slide 36: An Analytic Solution
The solution is assumed in an autosoliton form
Then the parameters of the solution are found using perturbed Lagrange equations derived from Lagrange operator:
H. A. Haus and A. Mecozzi, “Noise of mode-locked lasers”, IEEE J. Quantum. Electron. 29, 983–996 (1993).
A. Hasegawa, “Soliton-based optical communications: an overview,” IEEE J. Sel. Top. Quantum Electron. 6, 1161–1172 (2000).
A. B. Matsko and L. Maleki Optics Express 21 (23), 28862 (2013).

## Slide 37: Steady State Formalism
Unless the pump light is filtered out the output pulses are “dark” solitons
In the case of two couplers
The peak power of the pulse is comparable with the cw pump power
A. B. Matsko and L. Maleki, OE 21, 28862 (2013)

## Slide 38: Phase Noise Limit of Kerr Comb Oscillator
Oscillators are useful for clocks as flywheels
The noise floor drops with pulse duration decrease
A. B. Matsko and L. Maleki, OE 21, 28862 (2013)
Was supported by DARPA

## Slide 39: Fundamental Stability of the Comb Oscillator Does not Depend on Q
Sidebands are always equidistant because of energy and photon number conservation, but the repetition rate of the comb can change.
A. B. Matsko and L. Maleki, OE 21, 28862 (2013)
Minimum Allan deviation for two sidebands
Minimum Alan deviation for fundamental soliton Kerr comb
A. B. Matsko, et al., Phys. Rev. A 71, 033804 (2005)

## Slide 40: Size and Power Dependence
For the same oscillation frequency the better performance has an oscillator with larger mode volume and smaller nonlinearity
The time averaged input power is equal to time averaged output power. The energy is conserved. No attenuation is present, in the global sense. The signal is generated at the photodiode that performs the measurement.
Demodulation of the modulated light on a photodiode produces spectrally pure radio frequency signal

## Slide 41: Fundamental Limitations Verified Experimentally
In collaboration with Caltech, supported by JPL/NASA

## Slide 42: Timing Jitter Correlation for Two Pulses in the Same Cavity

## Slide 43
Time crystals as ideal frequency dividers

## Slide 44: Second coherent pump for the soliton stabilization
H. Taheri et al., Optical lattice trap for Kerr solitons. The European Physical Journal D. 2017

## Slide 45: A trap for solitons
H. Taheri et al., Optical lattice trap for Kerr solitons. The European Physical Journal D. 2017
We manipulate by the pulse by tuning the second pump

## Slide 46: Discrete Time Crystals
Time symmetry breaking, similar to a high order parametric oscillator. This is not a soliton trap!
H. Taheri at al., Nature Communications 13 (1), 848 (2022).
The phase noise of the laser beat note is divided!

## Slide 47: Dichromatically Pumped Kerr Solitons (DTC-like)
A. B. Matsko and L. Maleki, Optics Letters 48, 715 (2023)
The main idea is to match the group velocity of the beat note of the two pumps and group velocity of the dissipative soliton

## Slide 48: Time Symmetry Breaking in Dual Pumped Systems
A. B. Matsko and L. Maleki, Optics Letters 48, 715 (2023)

## Slide 49: Thanks to (Recent) Collaborators
Nan Yu (JPL)
Robert Tjoelker (JPL)
Eric Burt (JPL)
Vladimir Iltchenko (JPL)
Anatoliy Savchenkov (JPL)
Wei Zhang (JPL)
Mahmood Bagheri (JPL)
Siamak Forouhar (JPL)
Lute Maleki (OEwaves)
Kerry Vahala (Caltech)
Hossein Taheri (UCR)
Misha Sumetsky (Aston University)
Scott Papp (NIST)
Chee Wei Wong (UCLA)
Sergey Vyatchanin (MSU)
Tobias Herr (Universität Hamburg)
Krzysztof Sacha (Uniwersytet Jagielloński)
Paolo De Natale (CNR-INO)
Simone Borri (CNR-INO)
Mario Siciliani de Cumis (CNR-INO)
and many others

## Slide 50: Thanks for Support
JPL/Caltech
NASA
DARPA
ONR
AFOSR/AFRL
NRO