## Slide 1: Next Generation Chip-Scale Atomic Clocks
John Kitching
Time and Frequency Division
National Institute of Standards and Technology
Boulder, CO USA

## Slide 2: Atomic Devices and Instrumentation Group
Matt Hummon
William McGehee
Ying-Ju Wang
Susan Schima
Rb 2-hv clock
Sr vapor cells
Vapor cell cQED
Atom interferometer
Chip-scale beam clock
Atomic magnetometers
Rydberg sensors
Silicon fab
Process development
Seji Kang
Isaac Fan
Gaby Martinez
Alex Staron
Safra Niyaz
Yorick Andeweg
Peter Riley
Yang Li
Post-doc positions available!
2

## Slide 3: Chip-Scale Atomic Clocks
Precision spectroscopy + MEMS + photonics
Holds 100 ms over 1 day on 120 mW
  1 s with environmental control
Commercial product – 2011
  120,000 sold as of 2020, > $100M in economic impact
30 X
From Microsemi CSAC Datasheet
J. Kitching, Applied Physics Reviews 5, 031302 (2018).

## Slide 4: Chip-Scale Atomic Clocks
Precision spectroscopy + MEMS + photonics
Holds 100 ms over 1 day on 120 mW
  1 s with environmental control
Commercial product – 2011
  120,000 sold as of 2020, > $100M in economic impact
From Microsemi CSAC Datasheet
J. Kitching, Applied Physics Reviews 5, 031302 (2018).
US Army BAA, 2020

## Slide 5: Chip-Scale Atomic Clocks
Government, academia and industry all played a significant role: lots of information exchange
Large (100 X) potential improvement over existing approaches; high-risk, innovative
Early wins: MEMS cell demonstration 1 year after program start, physics package 1.5 years
Substantial, sustained funding (~ $100M over 10 years)
Multidisciplinary teams
MEMS
Cells
DARPA/NIST: V ~ 1 cm3, P ~ 30 mW, Df/f ~ 10-11 @ 1 hr
Commercial
CSAC
Physics
Packages
Chip-scale magnetometers
VCSELs
European CSAC begins
NIST on a Chip
2nd Com. CSAC
Army MANTECH
100,000 CSACs sold
DARPA ACES (optical)
DARPA IMPACT (laser cooling)
Chip-scale optical clocks
DARPA A-Phi
1cc, 30 mW
Instruments
DARPA CSAC Program
Simple, manufacturable technical approach: VW Beetle, not Ferrari
CSAC workshop (NIST)
Thermal
suspensions
2001|2002|2003|2004|2005|2006|2007|2008|2009|2010|2011|2012|2013|2014|2015|2016|2017|2018|2019|2020|2021|2022|2023
Westinghouse/
DARPA
NIST
NIST
Draper Labs
Microsemi
Teledyne
NIST/Draper
Feasibility
NIST
Microsemi
Microsemi
Chip-scale beam clocks
NIST/Ga Tech
DARPA H6
Army LC-CSAC
5

## Slide 6: Portable Atomic Clocks
Next Generation CSACs
Better long-term stability
Beam microwave clocks
Overall better stability
Optical clocks, but at cost of needing a frequency comb
Lower cost
Wafer-level fabrication processes
D. G. Bopp et al., J. Phys: Photonics 3, 015002 (2020).

## Slide 7: NIST on a Chip
Measurement standards in chip format
Embedded, SI-traceable calibration built into instruments
Goals: flexible, useful, manufacturable, deployable
Get rid of the middle-man (us!)
Length [m]
Time [s]
Temp
Force
Volt [V]
Current [A]
Temp [K]
Force [N]
J. Kitching, et al., Journal of Physics: Conference Series 723: 012056 (2016).

## Slide 8: Integrated Photonics for Quantum Sensing
Laser/Photonics
Layer
Atomic Cell Layer:
Quantum Standard
Length [m]
Time [s]
Temp
Force
Volt [V]
Current [A]
Temp [K]
Force [N]
Time Length Temperature Current Voltage
5 base SI units!
8
Matt Hummon
Stability ~ 10-11 @ 1 hour
Accuracy ~ 10-9

## Slide 9: Two-Photon Chip-Scale Optical Standard
Two-photon Rb
optical standard
On-chip optical frequency division
Collaborators:
Scott Papp
Scott Diddams
Kerry Vahala
Kartik Srinivasan
…
Z. Newman, et al., Optica 6, 680 (2019).
10-10
10-11
10-12
10-13
10-14
Allan Deviation
10-1 100 101 102 103 104 105
Integration Time (s)
CSAC
This work
Best 2-hv clock
Rb 2-hv: Secondary representation of s

## Slide 10: Performance with a low-noise ECDL
Lower frequency noise  reduced intermodulation effect
Short-term: 1.9 x 10-13 τ-1/2
Frequency flicker floor at 2 x 10-14
Typical drift around 5 x 10-14 /day
Z. Newman, et al., Opt. Lett. 2021

## Slide 11: Stability Limits – Long Term
Main Systematics: collision shift and light shift
Z. Newman, et al., Opt. Lett. 2021
11

## Slide 12: CW Light Shift Suppression
?
?
Modulate power and use “combined” error signal
Can go to higher laser power
  Better short-term stability  intermodulation noise
V. I. Yudin, et al., Phys. Rev. Appl., 14, 024001, 2020.
M. Abdel Hafiz, et al., Phys. Rev. Appl., 14, 034015, 2020.
2 Hz2/Hz!
Technology transfer:
12

## Slide 13: Chip-Scale Atomic Beam Clocks
Stern, Gerlach, Rabi, etc.
Most accurate realization of SI second for ~ 1968 -2000s
Workhorse in atomic timing for 70 years
Microchip website
J. Vanier and C. Audoin, Metrologia 42, S31-S42 (2005).
13
Distribution Statement `A' (Approved for Public Release, Distribution Unlimited)

## Slide 14: Chip-Scale Atomic Beam Physics Package
Anodically bonded Si/glass stack
Laser-activated Rb2MoO4/AlZr pills
  Douahi, et al., 2007
Glass (0.7mm)
Glass (0.7mm)
Si channel wafer (2mm)
Si spacer wafer (0.6mm)
Machined glass (1mm)
Atomic beam signal at 90ºC
Signal  1cm
downstream
Rb2MoO4/AlZr pills
Drift region
Source region
Graphite
Getters
Microfabricated channels: C. Li et al., Nat. Commun. 10, 1831 (2019).
William McGehee
14
G. D. Martinez et al., Nat. Commun. 14, 3501 (2023).
Distribution Statement `A' (Approved for Public Release, Distribution Unlimited)

## Slide 15: CPT Beam Clock Stability
Ramsey CPT spectroscopy
  J. E. Thomas et al., Phys. Rev. Lett. 48, 867-870 (1982).
1 cm Ramsey zone
Ramsey
zones
Contrast:  16%
FWHM:  12kHz
Systematic | Sensitivity (Δf/f) | Required Control
1st Order Doppler Shift | 1 x 10-6/rad | μrad-level beam pointing stability
End-to-end Cavity Phase Shift | 1 x 10-6/rad | nm-level optical path length stability
Rb-Rb Collisional Shift | 5 x 10-5/Torr | Rb partial pressure below 20 nTorr
H2 & He Collisional Shift | 7 x 10-8/Torr | μTorr-level pressure stability
Light Shifts (R = P1/P2) | 1 x 10-9/R | RF power ratio stability of 0.1%
2nd Order Zeeman Shift | 2 x 10-7/G | ppm-level magnetic field stability
Systematic | Sensitivity (Δf/f) | Required Control
1st Order Doppler Shift |  | μrad-level beam pointing stability
End-to-end Cavity Phase Shift |  | nm-level optical path length stability
Rb-Rb Collisional Shift |  | Rb partial pressure below 20 nTorr
H2 & He Collisional Shift |  | μTorr-level pressure stability
Light Shifts (R = P1/P2) |  | 
2nd Order Zeeman Shift |  | ppm-level magnetic field stability
Projected systematics and accuracy budget (not measured yet) for
Technology transfer:
Travis Autry, PI
DARPA H6 (Jonathan Hoffman, PM):
1 s @ 1 week in 1 cm3, 150 mW
15
G. D. Martinez et al., Nat. Commun. 14, 3501 (2023).
Distribution Statement `A' (Approved for Public Release, Distribution Unlimited)
5p1/2
5s1/2
F=1
F=2

## Slide 16: Light Shifts in CPT Beam Clocks
Off-resonant level
Resonant light shift  0 for large ,
Off-resonant light shift:
Atoms
for Cs,
Control of light shifts at 10-12 level requires ~ 1% relative power control for CPT fields
Distribution Statement `A' (Approved for Public Release, Distribution Unlimited)

## Slide 17: Microfabricated Sr Vapor Cells
Alkaline earths have range of transition linewidths
  461 nm -> 31 MHz
  689 nm -> 7 kHz
  698 nm -> mHz
Al2O3 coatings protect windows
  Woetzel, et al., 2013; Karlen, et al., 2017
1S0
1P1
3P1
689 nm
7 kHz
461 nm,
31 MHz
Strontium Levels
461 nm laser
Sr Cell
Det
461 nm Spectroscopy
689 nm Spectroscopy
461 nm laser
Sr Cell
Det
698 nm laser
J. M. Pate, et al., Opt. Lett., 48, 383, 2023.
Matt Hummon
17

## Slide 18: The Future?
Ca beam clock, 9 cm Ramsey zone -> 10-16 stability
+
+
Beam clock
Sr cells
Microresonator
combs
On-chip SBS lasers
18
Chip-scale clocks with 10-15 level stability?

## Slide 19: Conclusions
CSACs now a successful commercial product: ~ $0.25B
  Underwater timing for oil and gas
Photonically-integrated wavelength references
Compact Rb 2-hv optical clocks
  Microresonator frequency combs
  10-14 stability @ 1 hr
Chip-scale atomic beam clocks
  CPT excitation
  Goal: 1 s timing error at one day
Sr vapor cells