## Slide 1
WINS2023, October 10-12, Troy
Neutron inelastic cross-sections on 40Ca
Marian Boromiza1, Catalin Borcea1, Philippe Dessagne2, Greg Henning2, Maëlle Kerveno2, Alexandru Negret1, Markus Nyman3, Adina Olacel1, Andreea Oprea3, Carlos Paradela3, Arjan Plompen3
1Horia Hulubei National Institute for Physics and Nuclear Engineering, Bucharest-Magurele, Romania 2Universitẻ de Strasbourg, CNRS, IPHC Strasbourg, France 3European Commission, Joint Research Center, Geel, Belgium
*WORK SUPPORTED BY ROMANIAN FUNDING AGENCIES THROUGH RESEARCH GRANT PN-III-P1-1.1-PD-2021-0207

## Slide 2
The content of this presentation
scientific motivation for performing the experiment
experimental setup
data analysis procedure
experimental results
WINS2023, October 10-12, Troy
The content of this presentation

## Slide 3
scientific motivation for performing the experiment
experimental setup
data analysis procedure
experimental results
WINS2023, October 10-12, Troy
The content of this presentation

## Slide 4
WINS2023, October 10-12, Troy
Scientific motivation - I
Inelastic scattering is one of the main neutron energy loss mechanisms inside a reactor
Main isotope: 40Ca makes up 96.9% of natural calcium
LiF-CaF2 melt - promising candidate for GEN IV Molten Salt Reactors (MSRs)
  fuel candidates for MSRs: fluorides of fissile (UF4) and fertile (ThF4) elements
  dissolved in carrier salts
  very good online processing capabilities of the burned fuel (via electrochemical
  separation of both uranium and thorium and most of the fission products)
Status of the experimental data prior to our experiment:
  only 3 (angle-integrated) g-production cross section points at 17 and 22 MeV
  for the main transition (3736 keV)
  no angle-integrated data below 17 MeV
  one data set of differential (measured at 90o) cross section values
  one data set with level cross section values in the low neutron energy region (4-6 MeV)
ADDRESSING NUCLEAR DATA NEEDS ON 40Ca:

## Slide 5
WINS2023, October 10-12, Troy
Scientific motivation - II
AIDING THE THEORY SIDE:
Providing reliable and very low uncertainty reaction
observables for the continuous refinement of
reaction models
reaction codes: TALYS, EMPIRE...
The incident energy range of interest for our group: few hundreds keV to 20 MeV
mainly inelastic channel

## Slide 6
WINS2023, October 10-12, Troy
Scientific motivation - III
EXPLORATORY STUDIES:
Not (really) covered in today’s talk!!!

## Slide 7
WINS2023, October 10-12, Troy
Scientific motivation - III
“Surrogate”-type approach for the inelastic channel:
A. Negret et al., Phys. Rev. C 88, 034604 (2013)
Bohr hypothesis for compound nucleus CN (which dominates at low incident energies)
TRY NO. 1:
Inferring neutron cross sections from charged particles-induced reactions
EXPLORATORY STUDIES:
28Si(n, n'γ )28Si vs 25Mg(α, nγ )28Si
29Si*
Not (really) covered in today’s talk!!!

## Slide 8
WINS2023, October 10-12, Troy
Scientific motivation - III
FIG. 5 A. Negret, et al., Phys. Rev. C 88, 034604 (2013) Gamma production cross sections in the 28Si(n, n’γ )28Si and the 25Mg(α, nγ )28Si reactions as a function of the excitation energy in the compound nucleus 29Si
TAKE AWAY MESSAGE:
The γ-production cross sections excited in the two reactions are indeed of the same order of magnitude, BUT an attempt to directly relate the (n,n’) channel and its surrogate yields uncertainties of at least 50%.

## Slide 9
WINS2023, October 10-12, Troy
Scientific motivation - III
WHY IS THIS NOT WORKING FOR THE INELASTIC CHANNEL?
Surrogate study for 95Mo(n,g)
A. Ratkiewicz, J. E. Escher, et al. PHYSICAL REVIEW LETTERS 122, 052502 (2019)
It seems that for both capture and inelastic channels one needs, on a target-by-target basis, a very detailed handling of the CN spin-parity population differences
NOT TRIVIAL!!!
Oliver C. Gorton, J. E. Escher, PHYSICAL REVIEW C 107, 044612 (2023)

## Slide 10
WINS2023, October 10-12, Troy
“Surrogate”-type approach for the inelastic channel:
Inferring neutron cross sections from proton-induced reactions
Scientific motivation - III
TRY NO. 2:

## Slide 11
WINS2023, October 10-12, Troy
“Surrogate”-type approach for the inelastic channel:
Inferring neutron cross sections from proton-induced reactions
Scientific motivation - III
TRY NO. 2:
Minimize the OMP differences

## Slide 12
WINS2023, October 10-12, Troy
“Surrogate”-type approach for the inelastic channel:
Not the same compound nucleus (as in the above study)
Now we make use of the isospin symmetry
16O(n, n’g)16O versus 16O(p, p’g)16O
CN: 17O
CN: 17F
Inferring neutron cross sections from proton-induced reactions
Scientific motivation - III
TRY NO. 2:
Minimize the OMP differences

## Slide 13
WINS2023, October 10-12, Troy
Scientific motivation - III
Partial level schemes of 17O and 17F mirror nuclei through which
the two corresponding neutron and proton reactions on 16O proceed

## Slide 14
WINS2023, October 10-12, Troy
“Surrogate”-type approach for the inelastic channel:
Inferring neutron cross sections from charged particles-induced reactions
NOT REALLY A SURROGATE!!!
TRY NO. 2:
Scientific motivation - III
EXPLORATORY STUDIES:

## Slide 15
WINS2023, October 10-12, Troy
Scientific motivation - III
Complementary to “standard” surrogate!
- very different OMPs in the input channel
- identical residual/final nuclei
- Weisskopf-Ewing limit of CN reactions MUST hold
VERSUS
- extremely similar OMPs in the input channel
- different CN => nuclear structure-induced differences
- we do not really care about the Weisskopf-Ewing approximation

## Slide 16
WINS2023, October 10-12, Troy
Scientific motivation - III
J populated in CN
Transmission coefficients populated in CN
Different reaction observables for 3 projectiles: a neutron, a proton and a proton whose Coulomb term was removed from the proton-58Ni OMP
Results for 58Ni
A. Olacel, M. Boromiza* et al., ., Phys. Rev. C 106, 024609 (2022)

## Slide 17
WINS2023, October 10-12, Troy
Scientific motivation - III
Results for 58Ni
A. Olacel, M. Boromiza* et al., ., Phys. Rev. C 106, 024609 (2022)
Different reaction contributions for 3 projectiles: a neutron, a proton and a proton whose Coulomb term was removed from the proton-58Ni OMP

## Slide 18
WINS2023, October 10-12, Troy
Scientific motivation - III
Inferring the neutron inelastic channel from proton-induced cross sections
Inspired by the surrogate reactions method
A combination of experiment & theory
Nuclei studied so far:
- 16O & 28Si: M. Boromiza et al., Phys. Rev. C 101, 024604 (2020)
58Ni: A. Olacel, M. Boromiza* et al., Phys. Rev. C 106, 024609 (2022)
UP NEXT: 40Ca!!!
WHY?
a) determining the neutron cross sections from a much simpler-to-measure reaction
b) extracting information about the isospin-dependent term & Lane consistency of the nucleon-target OMP
THE GENERAL IDEA:
Starting from a Lane-consistent proton OMP, tune this potential on proton experimental data
Construct/infer a Lane-consistent neutron-like OMP from the proton case above
  drop its Coulomb term
  invert the sign of its Lane term
  …
Calculate proton-inferred neutron-like inelastic cross sections
Compare to the experimental data actually measured at GELINA
Not (really) covered in today’s talk!!!

## Slide 19
WINS2023, October 10-12, Troy
Scientific motivation - III
Results for 58Ni
A. Olacel, M. Boromiza* et al., published in PRC (26 July, 2022)
HOW WELL DOES THIS WORK?
thus far…

## Slide 20
The content of this presentation
scientific motivation for performing the experiment
experimental setup
data analysis procedure
experimental results
WINS2023, October 10-12, Troy
Experimental setup

## Slide 21
Neutron inelastic scattering cross section measurements @ GELINA
WINS2023, October 10-12, Troy
Experimental setup

## Slide 22
Linear accelerator
    Ee ≈ 70 – 140 MeV
    Δt < 1-2 ns
Rotating depleted uranium target
0 < En < 20 MeV
Multi-user facility
Flight paths and measurement
cabins: 10 ÷ 400 m
Time-of-Flight (ToF) technique
High resolution measurements
GELINA
Geel Eelectron LiNear Accelerator
WINS2023, October 10-12, Troy
Experimental setup

## Slide 23
GAINS
Gamma Array for Inelastic Neutron Scattering
Flight path 3 @ 100 m
  good neutron energy resolution
  @ 100 m: 3 keV at 1 MeV, 80 keV at 10 MeV
12 HPGe detectors @ 110o, 150o and 125o, d=17 cm
Large volume: relative efficiency 100%
FWHM typically ≈ 3 keV @ 1332 keV (60Co)
Digital acquisition (ACQIRIS digitizers)
  12 bit amplitude resolution (4096 channels)
  420 MS/s (2.38 ns sampling period)
Fission chamber (with 235U deposits) to monitor
the neutron flux - 235U(n,f) normalization
Time of Flight (ToF) & γ-spectroscopy techniques:
  n time of flight → En
  pulse amplitude → Eγ
WINS2023, October 10-12, Troy
Experimental setup
Target: calcium fluoride compound (CaF2)

## Slide 24
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties
Target preparation: compound CaF2 (as 40Ca has a 96.9 % natural abundance):
  Weak transitions: thick target
  Keep the g self-attenuation + MSC to reasonable values
  2 mm thickness and 76 mm diameter (beam: 61 mm)
Very high energy g rays: 3736 keV (3-),
3903 keV (2+) and 5248 keV (2+):
  large volume HPGe
  tricky efficiency extrapolation up to 4 or even 5 MeV

## Slide 25
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties
40Ca HPGe efficiency

## Slide 26
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties
Target preparation: compound CaF2 (as 40Ca has a 96.9 % natural abundance):
  Weak transitions: thick target
  Keep the g self-attenuation + MSC to reasonable values:
  2 mm thickness and 76 mm diameter (beam: 61 mm)
Very high energy g rays: 3736 keV (3-),
3903 keV (2+) and 5248 keV (2+):
  large volume HPGe
  tricky efficiency extrapolation up to 4 or even 5 MeV

## Slide 27
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties
Target preparation: compound CaF2 (as 40Ca has a 96.9 % natural abundance):
  Weak transitions: thick target
  Keep the g self-attenuation + MSC to reasonable values:
  2 mm thickness and 76 mm diameter (beam: 61 mm)
Very high energy g rays: 3736 keV (3-),
3903 keV (2+) and 5248 keV (2+):
  large volume HPGe
  tricky efficiency extrapolation up to 4 or even 5 MeV
3352 keV E0-totally converted

## Slide 28
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties
40Ca

## Slide 29
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties
Target preparation: compound CaF2 (as 40Ca has a 96.9 % natural abundance):
  Weak transitions: thick target
  Keep the g self-attenuation + MSC to reasonable values:
  2 mm thickness and 76 mm diameter (beam: 61 mm)
Very high energy g rays: 3736 keV (3-),
3903 keV (2+) and 5248 keV (2+):
  large volume HPGe
  tricky efficiency extrapolation up to 4 or even 5 MeV
3352 keV E0-totally converted

## Slide 30
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties
Target preparation: compound CaF2 (as 40Ca has a 96.9 % natural abundance):
  Weak transitions: thick target
  Keep the g self-attenuation + MSC to reasonable values:
  2 mm thickness and 76 mm diameter (beam: 61 mm)
Very high energy g rays: 3736 keV (3-),
3903 keV (2+) and 5248 keV (2+):
  large volume HPGe
  tricky efficiency extrapolation up to 4 or even 5 MeV
3352 keV E0-totally converted
Additional transitions? Maybe 754 keV…

## Slide 31
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties

## Slide 32
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties
Target preparation: compound CaF2 (as 40Ca has a 96.9 % natural abundance):
  Weak transitions: thick target
  Keep the g self-attenuation + MSC to reasonable values:
  2 mm thickness and 76 mm diameter (beam: 61 mm)
Very high energy g rays: 3736 keV (3-),
3903 keV (2+) and 5248 keV (2+):
  large volume HPGe
  tricky efficiency extrapolation up to 4 or even 5 MeV
3352 keV E0-totally converted
Additional transitions? Maybe 754 keV…

## Slide 33
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties
Target preparation: compound CaF2 (as 40Ca has a 96.9 % natural abundance):
  Weak transitions: thick target
  Keep the g self-attenuation + MSC to reasonable values:
  2 mm thickness and 76 mm diameter (beam: 61 mm)
Very high energy g rays: 3736 keV (3-),
3903 keV (2+) and 5248 keV (2+):
  large volume HPGe
  tricky efficiency extrapolation up to 4 or even 5 MeV
3352 keV E0-totally converted
Additional transitions? Maybe 754 keV…
We expected Doppler broadenings of the peaks of interest: T1/2 of 41 ps (3736 keV) and 35 fs (3903 keV)

## Slide 34
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties
16O
40Ca
3736 keV (41 ps)
3903 keV (35 fs)
16O
SRIM stopping powers for 40Ca:
-> yield around 0.5-1 ps stopping time
(125 fs)
(5 fs)

## Slide 35
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties
Target preparation: compound CaF2 (as 40Ca has a 96.9 % natural abundance):
  Weak transitions: thick target
  Keep the g self-attenuation + MSC to reasonable values:
  2 mm thickness and 76 mm diameter (beam: 61 mm)
Very high energy g rays: 3736 keV (3-),
3903 keV (2+) and 5248 keV (2+):
  large volume HPGe
  tricky efficiency extrapolation up to 4 or even 5 MeV
3352 keV E0-totally converted
Additional transitions? Maybe 754 keV…
We expected Doppler broadenings of the peaks of interest: T1/2 of 41 ps (3736 keV) and 35 fs (3903 keV)

## Slide 36
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties
Target preparation: compound CaF2 (as 40Ca has a 96.9 % natural abundance):
  Weak transitions: thick target
  Keep the g self-attenuation + MSC to reasonable values:
  2 mm thickness and 76 mm diameter (beam: 61 mm)
Very high energy g rays: 3736 keV (3-),
3903 keV (2+) and 5248 keV (2+):
  large volume HPGe
  tricky efficiency extrapolation up to 4 or even 5 MeV
3352 keV E0-totally converted
Additional transitions? Maybe 754 keV…
We expected Doppler broadenings of the peaks of interest: T1/2 of 41 ps (3736 keV) and 35 fs (3903 keV)
Possible contaminants from other reaction channels, mainly 40Ca(n,p)40K

## Slide 37
The content of this presentation
WINS2023, October 10-12, Troy
Preparing the experiment: main difficulties

## Slide 38
scientific motivation for performing the experiment
experimental setup
data analysis procedure
experimental results
WINS2023, October 10-12, Troy
Data analysis

## Slide 39
The content of this presentation
WINS2023, October 10-12, Troy
Detection technique: g spectroscopy
n + AZXN
A+1ZXN+1*
CN
AZXN + g
AZXN* + n’
E*  En – En’
En=Eth  ~20 MeV
Neutron inelastic scattering reaction:
Inelastic cross section: detect outgoing neutrons or gammas
Direct access to Level cross sections
g-production cross sections
Level cross section + Total inelastic cross section
Indirect access to

## Slide 40
g-spectroscopy measurements coupled with time of flight method
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 41
g-spectroscopy measurements coupled with time of flight method
HPGe detectors
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 42
g-spectroscopy measurements coupled with time of flight method
γ yield
HPGe detectors
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 43
g-spectroscopy measurements coupled with time of flight method
Fission chamber
HPGe detectors
γ yield
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 44
g-spectroscopy measurements coupled with time of flight method
γ yield + fission chamber yield
Fission chamber
HPGe detectors
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 45
g-spectroscopy measurements coupled with time of flight method
Other corrections:
MSC coefficients
Fission chamber efficiency
- …
HPGe detector efficiency
interpolation & extrapolation
(via simulations - MCNP 6)
γ yield + fission chamber yield
Fission chamber
HPGe detectors
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 46
g-spectroscopy measurements coupled with time of flight method
Other corrections:
MSC coefficients
Fission chamber efficiency
- …
γ yield + fission chamber yield
Fission chamber
HPGe detectors
Differential γ-production cross section
HPGe detector efficiency
interpolation & extrapolation
(via simulations - MCNP 6)
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 47
g-spectroscopy measurements coupled with time of flight method
Other corrections:
MSC coefficients
Fission chamber efficiency
- …
γ yield + fission chamber yield
Fission chamber
HPGe detectors
Differential γ-production cross section
Angle-integrated γ-production cross section
HPGe detector efficiency
interpolation & extrapolation
(via simulations - MCNP 6)
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 48
g-spectroscopy measurements coupled with time of flight method
Other corrections:
MSC coefficients
Fission chamber efficiency
- …
γ yield + fission chamber yield
Fission chamber
HPGe detectors
Differential γ-production cross section
Angle-integrated γ-production cross section
HPGe detector efficiency
interpolation & extrapolation
(via simulations - MCNP 6)
Level cross section
Level scheme
(ENSDF)
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 49
g-spectroscopy measurements coupled with time of flight method
Other corrections:
MSC coefficients
Fission chamber efficiency
- …
γ yield + fission chamber yield
Fission chamber
HPGe detectors
Differential γ-production cross section
Angle-integrated γ-production cross section
Level cross section
Total inelastic cross section
Level scheme
(ENSDF)
HPGe detector efficiency
interpolation & extrapolation
(via simulations - MCNP 6)
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 50
g-spectroscopy measurements coupled with time of flight method
Other corrections:
MSC coefficients
Fission chamber efficiency
- …
γ yield + fission chamber yield
Fission chamber
HPGe detectors
Differential γ-production cross section
Angle-integrated γ-production cross section
Level cross section
Total inelastic cross section
Level scheme
(ENSDF)
HPGe detector efficiency
interpolation & extrapolation
(via simulations - MCNP 6)
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 51
g-spectroscopy measurements
WINS2023, October 10-12, Troy
Data analysis
The time-amplitude matrix of one HPGe detector

## Slide 52
The time-amplitude matrix of one HPGe detector
WINS2023, October 10-12, Troy
Data analysis
Eγ=6128 keV
Y110(Ek)
g-spectroscopy measurements

## Slide 53
g-spectroscopy measurements coupled with time of flight method
Other corrections:
MSC coefficients
Fission chamber efficiency
- …
γ yield + fission chamber yield
Fission chamber
HPGe detectors
Differential γ-production cross section
Angle-integrated γ-production cross section
Level cross section
Total inelastic cross section
Level scheme
(ENSDF)
HPGe detector efficiency
interpolation & extrapolation
(via simulations - MCNP 6)
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 54
g-spectroscopy measurements coupled with time of flight method
Other corrections:
MSC coefficients
Fission chamber efficiency
- …
γ yield + fission chamber yield
Fission chamber
HPGe detectors
Differential γ-production cross section
Angle-integrated γ-production cross section
Level cross section
Total inelastic cross section
Level scheme
(ENSDF)
HPGe detector efficiency
interpolation & extrapolation
(via simulations - MCNP 6)
we extract cross sections normalized to the very well known 235U(n, fission) cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 55
WINS2023, October 10-12, Troy
Data analysis
FC data analysis - very similar to HPGe detector’s case:
  FC time-amplitude matrix
  FC Amplitude spectrum
  FC ToF spectrum
  ….
FC efficiency determination
FC amplitude spectrum

## Slide 56
WINS2023, October 10-12, Troy
Data analysis
ToF technique or calibration in time of flight
The time-amplitude matrix of one HPGe detector

## Slide 57
ns
Figure out the neutron energy by using the
g-flash as a time reference!!!
WINS2023, October 10-12, Troy
Data analysis
The time-amplitude matrix of one HPGe detector
265
The tof spectrum of one HPGe detector
ToF technique or calibration in time of flight
g-flash
neutron events

## Slide 58
Differential g-production cross sections (at 110o and 150o)
(
WINS2023, October 10-12, Troy
Data analysis
Nota Bene! 110o and 150o are nodes (zeroes) of the 4th order Legendre Polynomials

## Slide 59
Angle-integrated g-production cross sections → our primary results
WINS2023, October 10-12, Troy
Data analysis
Angle integration based on Gaussian Quadrature Theorem
plus
Legendre Polynomials series expansion of the differential cross section

## Slide 60
γ-production cross sections (primary results)
level cross section
total inelastic cross section
WINS2023, October 10-12, Troy
Data analysis

## Slide 61
Total inelastic cross sections
Calculated based on the feeding of the ground state using the production cross section of the observed transitions.
WINS2023, October 10-12, Troy
Data analysis

## Slide 62
Total inelastic cross sections
Calculated based on the feeding of the ground state using the production cross section of the observed transitions.
WINS2023, October 10-12, Troy
Data analysis

## Slide 63
Total inelastic cross sections
Calculated based on the feeding of the ground state using the production cross section of the observed transitions.
WINS2023, October 10-12, Troy
Data analysis

## Slide 64
Total inelastic cross sections
Calculated based on the feeding of the ground state using the production cross section of the observed transitions.
WINS2023, October 10-12, Troy
Data analysis

## Slide 65
Total inelastic cross sections
Calculated based on the feeding of the ground state using the production cross section of the observed transitions.
WINS2023, October 10-12, Troy
Data analysis
Emax

## Slide 66
scientific motivation for performing the experiment
experimental setup
data analysis procedure
experimental results
WINS2023, October 10-12, Troy
Experimental results

## Slide 67
WINS2023, October 10-12, Troy
Experimental results
Two transitions in 40Ca:
3736 keV ( the main transition)
3903 keV
(maybe also 754 keV)
Most probably also 109 keV and 197 keV from 19F

## Slide 68
3736 keV: γ-production cross section
WINS2023, October 10-12, Troy
Experimental results

## Slide 69
3903 keV: γ-production cross section
WINS2023, October 10-12, Troy
Experimental results

## Slide 70
Total inelastic cross section on 40Ca
WINS2023, October 10-12, Troy
Experimental results

## Slide 71
Thank you for your attention!

## Slide 72
BACKUP SLIDES

## Slide 73
g-ray emission anisotropy
WINS2023, October 10-12, Troy
Data analysis
2+ to 0+
E2
3- to 0+
E3