## Slide 1: LHC Machine Protection
Daniel Wollmann, CERN
Acknowledgments: G. D’Angelo, R. Denz, B. Lindstroem, A. Monteuuis, Y. Nie, A. Oslandsbotn, E. Ravaioli, R. Schmidt, J. Steckert, M. Vaananen, M. Valette, A. Verweij,
J. Uythoven, J. Wenninger, C. Wiesner, A. Will, M. Zerlauth
LHC parameters for Machine Protection
Failure time scales and Machine Protection Systems
LHC Operation – a machine protection view
Machine Protection studies for the future
  Cold diode qualification
  Sc. magnet damage due to beam impact

## Slide 2: Outline
LHC parameters for Machine Protection
LHC Machine Protection Systems
LHC Operation – a machine protection view
Machine Protection studies for the future
  Cold diode qualification
  Sc. magnet damage due to beam impact

## Slide 3
LHC pp and ions
7 TeV/c – up to now 6.5 TeV/c
26.8 km Circumference
CERN Main Site
Switzerland
Lake Geneva
France
LHC Accelerator
(100 m down)
SPS Accelerator
CERN-Prevessin
CMS
ALICE
LHCb
ATLAS

## Slide 4
LHC Layout
8 sectors
8 arcs
8 long straight sections (insertions) about 700 m long
1232 sc. main dipole magnets (r ≈ 2804 m): making the circle
Injection
IR6: Beam dumping system
IR4: RF + Beam instrumentation
IR5: CMS
IR1: ATLAS
IR8: LHC-B
IR2: ALICE
Injection
IR3: Momentum Beam Cleaning (warm)
IR7: Betatron Beam Cleaning (warm)
Beam dump blocks
Courtesy R. Schmidt

## Slide 5: LHC Parameters
 |  | Nominal | 2018 | HL-LHC
Proton energy | [TeV] | 7.0 | 6.5 | 7.0
Number of particles per bunch | - | 1.15 x 1011 | ~1.15 x 1011 | ~2.2 x 1011
Number of bunches | - | 2808 | 2556 | 2760
Bunch spacing | [ns] | 25 | 25 | 25
Transvers normalized emittance | [um] | 3.75 | 2.0 - 3.0 | 2.5
b* in IP1 and IP5 | [m] | 0.55 | 0.3 … 0.25 | 0.15
Current in main dipoles | [kA] | 11.85 | 10.98 | 11.85
Stored energy per beam | [MJ] | 362 | 292 | 680
Stored energy per dipole circuit (154 dipoles) | [GJ] | 1.07 | ~0.92 (6MJ per dipole) | 1.07
Peak luminosity in IP1 & IP5 | x 1034 [cm-2s-1] | 1.0 | 2.2 | 17 (virtual) Leveled: 5
Integrated luminosity in IP1 & IP5 | [fb-1] | - | 65 | 250/year
Integrated luminosity (total) | [fb-1] | 300 | >150 (2009-2018) | 3000

## Slide 6: LHC Luminosity Production 2018
xx
Courtesy J. Wenninger

## Slide 7: Pb-Pb ion run 2018
max ~ 620 Pb bunches (~ 11 MJ - 100ns spacing)
later ~790 Pb bunches (~14 MJ - 75 ns spacing),
assuming 1.7e10 charges/bunch, i.e. 2.1e8 Pb82+/bunch

## Slide 8: LHC Stored beam energy
LHC 2018
362 MJ stored beam energy:
90 kg TNT
8 l gasoline
15 kg chocolate
Drill 30 m long hole in solid copper block

## Slide 9: Damage due to instantaneous beam impact
Beam losses lead to energy deposition in materials
The energy deposition leads to a temperature increase
Material can change its material properties, deform, melt or vaporize.
Energy deposition due to impact of 50 MeV to 40 TeV protons in copper.
Sigma 0.2mm
Courtesy F. Burkart

## Slide 10: LHC main dipoles
1238 superconducting bending magnets.
NbTi.
Operated at 1.9 K.
Beam
362 MJ
Inom = 11.85 kA (currently 10.98 kA)
Bnom = 8.33 T
Estored= 6.9 MJ (currently 6 MJ)
R ≈ 2804 m

## Slide 11: Energy stored in Magnet Powering System of the LHC
Ekin(v = 27 kn) ≈ ELHC main circuits (@6.5 TeV)

## Slide 12: Small but already dangerous
Courtesy J.B. Lallement
Damage @ Linac4 with a 3 MeV beam – vacuum leak.
Failure combination:
  Beam misaligned
  Unlucky magnet setting / disabled interlock
  Aperture limitation at bellow
Energy loss from ionization
3 MeV L4
7 TeV
LHC
At such low energies, the local energy loss per proton is very high
 Damage after some integration time

## Slide 13: SPS dipole magnet
A real case from the 2018 SPS run !
Impact on the vacuum chamber of a 400 GeV beam of 3x1013 protons (2 MJ).
Event is due to an insufficient coverage of the SPS MPS (known !).
Vacuum chamber to atmospheric pressure, downtime ~ 3 days.
3 days downtime + dose to workers
1 event / 5-10 years

## Slide 14: Release of 600MJ at the LHC
Arcing in the interconnection
The 2008 LHC incident happened during test runs without beam.
A magnet interconnect was defect and the circuit opened. An electrical arc provoked a He pressure wave damaging ~600 m of LHC, polluting the beam vacuum over more than 2 km.
1 year downtime + repair of 50 magnets + organization’s reputation 1 event / 1000? years

## Slide 15: Outline
LHC parameters for Machine Protection (MP)
LHC Machine Protection Systems
LHC Operation – a machine protection view
Machine Protection studies for the future
  Cold diode qualification
  Sc. magnet damage due to beam impact

## Slide 16
Assumptions for LHC MP systems
Ultra- Fast failures (< 3 turns):
  Beam injection from SPS to LHC.
  Beam extraction into dump channel.
  Missing beam-beam kick after dump of one beam.
Passive protection devices (TDI, TCDQ, Collimators etc.)
0.6s single turn orbit perturbation measured @4TeV  0.8s @ 7Tev
Trajectory perturbation of beam 1 after dump of beam 2, 4TeV, 0.9e11p/b, 84b, 25ns, IP5-xing=68urad, 13.12.2012 08:26:54
Courtesy T. Baer

## Slide 17
Assumptions for LHC MP systems
Ultra- Fast failures (< 3 turns):
  Beam injection from SPS to LHC.
  Beam extraction into dump channel.
  Missing beam-beam kick after dump of one beam.
Fast failures (< few milliseconds):
  Detected by: BLMs (>40us), FMCM (~100us), Beam Life Time monitor (~200-300us), …
  Equipment failure with fast effect on orbit: e.g. D1 separation dipole (IP1/5) fastest failure with circulating beam.
  UFOs.
Study new failure cases and impact of machine upgrades (e.g. HL-LHC).

## Slide 18
Assumptions for LHC MP systems
Ultra- Fast failures (< 3 turns):
  Beam injection from SPS to LHC.
  Beam extraction into dump channel.
  Missing beam-beam kick after dump of one beam.
Fast failures (< few milliseconds):
  Detected by: BLMs (>40us), FMCM (~100us), Beam Life Time monitor (~200-300us), …
  Equipment failure with fast effect on orbit: e.g. D1 separation dipole (IP1/5) fastest failure with circulating beam.
  UFOs.
Slow Failures (> few milliseconds):
  Instabilities, Magnet quenches, Moving devices, …
  Multi-fold redundancy (BLM, PC, QPS, RF, … )
Protection versus Availability!

## Slide 19: Machine Protection Systems @ the LHC
Quench Protection Systems  essential for sc. magnets
Beam Loss Monitor System (> 3600 ion. chambers)  the last safety net
Beam Position Monitors (BPMs monitor orbit)  operation + protection
Injection Protection System  delicate
LHC Beam Dumping System  never to fail
Collimation  beam cleaning and passive protection
Beam Interlocks System  links all the system
Powering Interlock System  link between magnets, PC, beam
Warm Magnet Interlock System  warm magnets
Fast Magnet Current Change Monitor  catches fastest failure
Software Interlock System  everything which is not in HW, easy to add
Beam Current Change Monitor (not yet deployed)  second safety net to be
Safe Machine Parameter  supervision of parameters, Setup Beam Flag allows for safe machine commissioning with intensity  automatic un-masking of interlocks above critical intensity

## Slide 20: LHC Machine Protection System (MPS) architecture
nQPS /
MPS architecture is constantly evolving, today many 10.000 interlock conditions can request an abort of the beams
In addition every year some 100 major changes to operational systems that require tracking and follow-up (threshold changes, maintenance/ replacement of components, R2E, operational tools, procedures,…)

## Slide 21: LHC Beam Dumping System
C. Bracco et al., LHC Performance Workshop, Chamonix, 26/01/2016
15 extraction kicker (MKD)
Beam dump (TDE)
15 DC septa magnets (MSD)
Dilution Kicker:
4 MKBH
6 MKBV
Total length (MKD to TDE): 976 m
Nominal dilution pattern
Extraction of the two circulating beams (also in case of emergency!), by a system of kicker magnets send into a dump block
3 ms gap (‘abort gap’) in the beam gives the kicker time to reach full field
Ultra-high reliability system !!

## Slide 22: Beam dump line
~ 8m carbon block at the end.
Operated in N2 overpressure

## Slide 23: LHC dump block
The dump block is the only LHC element capable of absorbing the nominal beam
Low density graphite sheets

## Slide 24: Beam dump with 648 Pb bunches

## Slide 25: Collimators
Aperture bottle necks defined by robust collimators (fibre reinforced carbon), shower absorption by tungsten collimators
Protection of critical elements like triplet magnets
about 100 moveable collimators are installed in LHC
beam
1.2 m
Courtesy R. W. Assmann

## Slide 26: Betatron beam cleaning
Cold aperture
Cleaning insertion
Arc(s)
IP
Circulating beam
Illustration drawing
Arc(s)
Primary collimator
Secondary collimators
Tertiary beam halo + hadronic showers
Shower absorbers
Tertiary collimators
SC Triplet

## Slide 27: Beam Loss Monitor System
Ionization chambers to detect beam losses:
  Reaction time ~ ½ turn (40 us)
  Very large dynamic range (> 106)
There are ~3600 chambers distributed over the ring to detect abnormal beam losses and if necessary trigger a beam abort !
Very important beam instrumentation  last safety net

## Slide 28: Magnet and Beam Interlock Systems
Custom made electronics developments for fast and reliable concentration and transmission of protection actions

## Slide 29: Next generation of Quench Detectors
8 channel quench detection system (uQDS)
Currently used to protect the new HL-LHC magnets in test stands
Frontend input channel v6.6
Redundant power supplies & digital part
Digital evaluation unit
Courtesy J. Steckert

## Slide 30: New protection systems for superconducting circuits
Prototype 2 kA electro-mechanical in-vacuum breaker based energy extraction system for HL-LHC
Coupling Loss Induced Quench systems developed @ CERN and built in industry for test stations and HL-LHC
Controls & Switches
Courtesy F. Rodriguez Mateos

## Slide 31: Outline
LHC parameters for Machine Protection (MP)
Failure time scales and Machine Protection Systems
LHC Operation – a machine protection view
Machine Protection studies for the future
  Cold diode qualification
  Sc. magnet damage due to beam impact

## Slide 32: Commissioning and re-validation of machine protection systems
Commissioning of each machine protection system is defined in detailed procedures, specifying the revalidations required after long/short stops
Commissioning with beam is followed by an intensity ramp-up
Technical stops require a partial re-validation and are followed by a fast intensity ramp-up

## Slide 33: Intensity ramp-up 2017
The plan: 3 - 12 - 72 - 300 - 600 - 900 - 1200 - 1800 - 2400 – 2550
23.05.
3/12 b
26.05.
75 b
28.05.
315 b
601 b
03.06.
06.06.
Scrubbing 07.-12.06.
12.06.
985 b
15.06.
1225 b
17.06.
1561 / 1741 b
20.06.
24.06.
2029 / 2173 / 2317 b
1225 b after 15 days (excl. scrubbing [1d], injector stop [2d], scrubbing week) – intensity ramp-up combined with beam commissioning
~2500 b after 24 days
Careful check of high energy beam dumps and documentation in 11 so-called check lists
Establish cycle
MP dominated
Intensity dominated

## Slide 34: Quench of Triplet quadrupole (RQX.R1, 03.06.2018)
Beams dumped by losses in collimators
Significant orbit movement in B1, but not B2
Quench detected only ~20 ms after beam dump
250 um
<10 um
18 ms
Offset=0.58 mm

## Slide 35: Quench of Triplet Quadrupole – Q&A
What was the source of the quench?
  Debris from the IP & regulation problems in cryogenic system, heating magnet to lambda point and leading to a very fast quench of a big part of the coil
Why was quench not detected earlier?
  Quench developed symmetrically, no symmetric quench detection for triplet magnets
Why were the beams not displaced symmetrically?
  Detailed magnetic simulations showed that the observed beam behavior / magnetic fields can be explained by current redistribution in the magnet cable during the quench, other effects are inter-filament and inter-strand coupling currents (but too small)
Magnetic field induced in aperture
Origin of kick
Temperatures in triplet
Courtesy B. Lindstroem, E. Ravaioli, A. Verweij

## Slide 36: Beam induced quench causing periodic losses in collimation region
  Periodic losses during beam induced quench (~3ms) before beam dump
  Traced back to small orbit oscillation from skew dipole field (kick of ~14.3 m*0.7 mT)  quench heater firing

## Slide 37: Quench heater discharge: Ultrafast current rise
Ultra fast effect, quench heaters reaching full current/field within less than 1/2 LHC turn
  Dipole: ~ 29 us; Triplet Quad: ~ 35 us
Spurious triggering of one QH unit cannot be excluded
Stronger effect in HL-LHC than in LHC due to more QH and larger beta functions
  Triplet (~8 km  ~21 km), D1 (~5 km  ~19 km) D2 (~1.7  ~6.4 km)
For HL-LHC
Issue beam dump before triggering QH discharges
Reduce kicks strength from QH circuits by optimizing connection schemes
Interlock spurious firing of QHs

## Slide 38: Outline
LHC parameters for Machine Protection (MP)
Failure time scales and Machine Protection Systems
LHC Operation – a machine protection view
Machine Protection studies for the future
  Cold diode qualification
  Sc. magnet damage due to beam impact

## Slide 39: Cold diodes for the new Nb3Sn HL-LHC triplet
Motivation:
Separation of cold and warm part of circuit
Fast transients do not enter the superconducting link and stay clear of the power converters
Expected total lifetime dose at foreseen position of installation in LHC tunnel:
12 kGy and
5 x 1013 cm-2 1MeV neq fluence
Courtesy F. Rodriguez Mateos, S. Yammine, F. M. Camara, A. Will

## Slide 40: Irradiation of cold diodes for triplet
Three different cold diode types (LHC reference, thin n-base width and very thin n-base width) irradiated in CERN’s CHARM facility
Two stacks of four diodes (77K, 4K), and weekly measurement of forward characteristic up to 18 kA, turn on voltage, reverse blocking voltage
Two thermal cycles to study annealing after the end of the irradiation
A total of ~12 kGy and ~2.2e14 1MeVneq/cm2 was accumulated
Very thin base width diodes chosen for HL-LHC inner triplet circuit

## Slide 41: Outline
LHC parameters for Machine Protection (MP)
Failure time scales and Machine Protection Systems
LHC Operation – a machine protection view
Machine Protection studies for the future
  Cold diode qualification
  Sc. magnet damage due to beam impact

## Slide 42: Motivation of the sc. magnet damage studies Ultra-fast failures in HL-LHC
For HL-LHC beam, peak energy deposition of 100 Jcm-3 in the D1 magnet without mask[1] and similar in Q5 are expected in case of an asynchronous beam dump[2].
Will the magnets survive?
What are the damage mechanisms and limits of superconducting magnets due to high intensity beam impact?
One such event per year in today’s LHC. No damage.
HL-LHC:
  increased bunch intensity from 1.15 x 1011 ppb to 2.2 x 1011 ppb
  reduced emittance (3.75 um rad  2.5 um rad)
  Increased stored beam energy from 360 MJ to 690 MJ
  Failures become more critical
[1] A. Lechner et al., Protection of superconducting magnets in case of accidental beam losses during HL-LHC injection, In Proceedings of IPAC15
[2] B. Auchmann et al., Quench and Damage Levels for Q4 and Q5 Magnets near Point 6, CERN EDMS 1355063, 2014

## Slide 43: Critical parts of superconducting magnets
Polyimide insulation (Nb-Ti magnets)
  Decomposition when exposed to high temperature
  Reduction of the dielectric strength
Nb-Ti strand/cables (LHC)
Nb3Sn strand/cables (HL-LHC)
  Reduction of the Jc induced by:
  High temperature (e.g. diffusion)
  Mechanical stress, deformation and cracks
Image from C. Senatore, CAS Zuerich 2018

## Slide 44: Sample holder & hotspots
Superconducting strands embedded in sheeted copper sample holder (held by vacuum grease)
Samples from one batch see the same beam
Hadronic showers cause increasing energy deposition when protons pass through the sample holder  similar to a failure case when beam-showers impact on a sc. magnet
Energy deposition and hotspots calculated with FLUKA based on measured beam parameters (intensity, beam size, offset)

## Slide 45: Beam experiment at 4 K
20 Nb-Ti short strand samples: 50 mm, Ø 0.825 mm
30 Nb3Sn short strand samples (RRP type): 50 mm, Ø 0.85 mm
40 YBCO tape samples: 60 mm x 4 mm x 0.2 mm
11 x 24 b (~3e12 p, sigmax,y= 1.1 mm) @ 440 GeV
Hotspots up to 1250 K reached in strands
p+

## Slide 46: Sample holder and samples after beam impact - visual inspection
Beam imprints clearly visible in sample holder plates
Nb-Ti strands: no deformation observed after beam impact
Nb3Sn strands:
  Beam impacted with slight offset  visible bending of samples for hotspots > ~700 K
  Breaking of copper matrix in some samples with hotspots > ~ 900 K
YBCO: de-coloration due to beam heating, copper layer damaged at high temperatures
Nb3Sn, peak ~ 730 K /760 K
B1 S6
B2 S8
B3 S6
Nb3Sn, peak ~ 950 K
hot spot ~1200 K
YBCO tape, hot spot ~ 1100 K
YBCO tape, hot spot ~ 1030 K

## Slide 47: Key results of cryogenic beam experiment: Nb-Ti
No degradation of critical current (Ic) observed
Measurements indicate significant reduction of RRR at beam impact position
  Reduced minimum quench energy (MQE)  potentially causing thermal instability of the strands / magnets
  RRR locally reduced below 100 for samples with hot spots > 800 K

## Slide 48: Nb3Sn: Ic degradation after beam impact
Significant Ic degradation from Sample S4 with peak temperatures > 460 K
No measurable transport current for peak temperatures > 890 K  samples S9 and S10 destroyed
Inversion of degradation order (S4, S7, S5, S6, S8) due to effect of different sample holder design around sample S7 (thin copper sheets versus thick copper blocks)  reproduced in thermo-mechanical simulations
Similar behaviour observed in all three batches of strands (within the uncertainty of the experimental setup and the measurements)

## Slide 49: Thermo-mechanical simulations
Simulation of stresses within the strand cross-section due to
thermal gradients and expansion caused by beam heating
the sample holder impacting on the strand due to its thermal expansion
Derive expected Ic for each strand based on literature scaling laws (Uni Twente Model, filament breaking limit, etc.)
Results:
Measured Ic degradation can be explained by the residual strain in the strands and the breaking of filaments.
Filament breaking can be observed for hotspots > 450 K (from sample S4) and is dominating the Ic degradation with increasing hotspot temperature
Bc2 distribution from microscopic theory
Local lattice strain
Jc distribution from microscopic theory + cracked filaments
Axial strain
Scaling laws

## Slide 50: Conclusion
LHC has been a game changer in respect to machine protection for particle colliders due to stored energy in magnet system and beams
Highly sophisticated and reliable machine protection system, which requires careful re-commissioning after long stops
High intensity dumps are carefully analyzed, criticality of failures is evaluated and extrapolated to HL-LHC beam intensities and operational conditions
Experimental studies have been performed to test damage limits of cold diodes and superconducting magnets