## Slide 1: Korean participation in ALICE Upgrade Ⅱ
In-Kwon Yoo
Pusan National University
Heavy Ion Meeting 2013-06

## Slide 2: Outline
ALICE & Inner Tracking System
ALICE upgrade Strategy
  ITS Physics Motivation
New ITS design
  Goals
  Upgrade options
Physics Performance Study
Korean contribution

## Slide 3: ALICE Detector
Current ITS
6 concentric barrels, 3 different technologies
2 layers of silicon pixel (SPD)
2 layers of silicon drift (SDD)
2 layers of silicon strips (SSD)

## Slide 4: ALICE Upgrade Strategy
☐ High precision measurements of rare probes at low pT, which can not be selected with a trigger, require a large sample of events.
Target
Gain a factor 100 in statistics over approved program.
  Pb-Pb recorded luminosity ≥ 10 nb-1  8 x 1010 events
  pp (@5.5 TeV) recorded luminosity ≥ 6 pb-1  1.4 x 1011 events
Significant improvement of vertexing & tracking capabilities.
Goals
Upgrade the ALICE readout system & online system
Improve vertexing & tracking at low pT  New ITS

## Slide 5: ITS performance - Tracking and vertex determination
ALICE ITS (present detector)
K-
π+
D0 flight line
D0 reconstructed
momentum
Primary vertex
Pb
Pb
d0k
d0π
secondary
vertex
Pointing
Angle θ
~ 100 μm
Example: D0 meson
ALI-PERF-12878
Analysis based on decay topology and invariant mass technique
Particle | Decay Channel | c (m)
D0 | K + (3.8%) | 123
D+ | K + + (9.5%) | 312
 | K+ K + (5.2%) | 150
 | p K + (5.0%) | 60
Open charm

## Slide 6: What determines the impact parameter resolution
detector layer 1
detector layer 2
pointing resolution = (13  22GeV/pc) m
from
detector
position
error
from
coulomb
scattering
r2
r1
true vertex
perceived
vertex
x
x
v
r2
r1
true vertex
perceived
vertex
v
m
current ITS 
first pixel layer
What determines the impact parameter resolution?
Vertex projection from two points: a simplified approach (telescope equation)
For higher Pointing resolution,
Smaller pixel size
less material budget
Add layers
Reduce distance between layers

## Slide 7: New ITS Design goals
1. Improve impact parameter resolution by a factor of ~3
- Get closer to IP (position of first layer) : 39mm 22mm
- Reduce material budget (X/X0 /layer) : ~1.14%  ~ 0.3% (for inner layers)
- Reduce pixel size : currently 50mm x 425mm
monolithic pixels  20 mm x 20 mm
hybrid pixels  state-of-the-art , 50 mm x 50 mm
2. Improve tracking efficiency and pT resolution at low pT
- Increase granularity: 6 layers  7 layers , reduce pixel size
- Increase radial extension: 39-430 mm  22– 430 (500) mm
3. Fast readout
readout of Pb-Pb interactions at > 50 kHz and pp interactions at ~ several MHz
4. Fast insertion/removal for yearly maintenance
possibility to replace non functioning detector modules during yearly shutdown

## Slide 8: Upgrade options
Two design options have being studied
7 layers of pixel detectors (baseline)
3 inner layers of pixel detectors and 4 outer layers of strip detectors
7 layers of pixels
Option A
3 layers of pixels
4 layers of strips
Option B
Pixels: O(20x20µm2 – 50 x 50µm2)
Pixels: O( 20x20µm2 – 50 x 50µm2)
Strips: 95 µm x 2 cm, double sided
700 krad/ 1013 neq
Includes safety factor ~ 4

## Slide 9: New ITS (baseline)
Inner Barrel: 3 layers
Outer Barrel: 4layers
Detector module (Stave) consists of
Carbon fibber mechanical support
Cooling unit
Polyimide printed circuit board
Silicon chips (CMOS sensors)
25 G-pixel camera, 10 m2
Complementary Metal-Oxide-Semiconductor

## Slide 10: ITS Barrel Layers
3 innermost layers at r= 22, 28 and 36 mm
Same z-length: 27 cm
Assumed chip size: 15 mm x 30 mm
9 chips/module
X/X0≤ 0.3%
 | Modules | Chips
Layer 1 | 12 | 108
Layer 2 | 16 | 144
Layer 3 | 20 | 180
Total | 48 | 432
4 outermost layers at r= 48, 52, 96, 102 mm
84 cm < z-length < 150 cm
Double chip rows per module
X/X0≤ 0.8%
 | Modules | Chips
Layer 4 | 48 | 2688
Layer 5 | 52 | 2912
Layer 6 | 96 | 9600
Layer 7 | 102 | 10200
Total | 298 | 25400
Inner Barrel layers
Middle & Outer Barrel layers

## Slide 11: Hybrid Pixel Detector – ‘Expolrer-0/1’
Assembly layout
Hybrid Pixel Layout
Assumed chip size: 15 mm x 30 mm
9 chips/module
X/X0 ≤ 0.3%
Ionizing Particle
CMOS Pixel Sensors

## Slide 12: Physics Performance Study
Option A: 7 pixel layers
Resolutions: srf = 4 mm, sz = 4 mm for all layers
Material budget: X/X0 = 0.3% for all layers
Option B: 3 layers of pixels + 4 layers of strips
Resolutions: srf = 4 mm, sz = 4 mm for pixels srf = 20 mm, sz = 830 mm for strips
Material budget: X/X0 = 0.3% for pixels X/X0 = 0.83% for strips
radial positions (mm): 22, 28, 36, 200, 220, 410, 430
Same for both layouts
Simulations for two upgrade layouts
x 3
x 5
Key !!
Motivation : Improvement of impact parameter resolution

## Slide 13: Physics Performance Study
An Example : Impact parameter distribution for,
Dielectron and Dalitz electrons
electrons from B meson
Current
Upgraded
Current
Upgraded
PbPb
pp
work with Prof. M.Kweon
K.Choi, K,Oh
Notes: 그림에 대한 간단한 설명을 드리면 앞의 그림은,
- pp와 PbPb 2.76 TeV 충돌에서의 0.8~6.0 GeV의 Dielectron and Dalitz electrons의 impact parameter 분포입니다.
- 그림에서 블루는 업그레이드 전, 레드는 업그레이드 후입니다.
- 총 4개의 그래프가 2개씩 겹쳐 있는데, 위의 그래프 두개가 PbPb 결과이고 아래의 결과가 권민정 교수님께서 하셨던 pp에서의 결과입니다.
- 왼쪽위의 블루 시그마는 업그레이드 전의 PbPb 결과의 가우시간 피팅의 시그마 값이고 레드는 업그레이드 후입니다.
- 그림의 X축은 impact parameter over impact parameter resolution으로 업그레이드 전/후 같은 값이 나오기를 기대하였고, 결과도 그러합니다.
두번째 그림은,
- B 메존에서 붕괴된 전자의 분포입니다.
- 업그레이드 후 피크가 더 브로드 해지길 기대하였고, 그렇게 되는 것을 시물레이션을 통해서 확인하였습니다.

## Slide 14: Task Organization of Asian groups
Activity | Participants | Comments
Detector simulation and reconstruction, physics performance | Inha, SUT, CCNU (?) | WP physics (A. Dainese) WP simul. and rec. (M. Masera, J. Belikov)
Design of pixel chip | CCNU, Yonsei, TMEC | WP chip design (W. Snoeys)
Characterization of pixel chip (radioactive source, test beam) | CCNU , Inha, Pusan, SLRI | WP characterization and qualification (M. Mager)
Characterization of pixel chip (laser) | Yonsei | WP characterization and qualification (M. Mager)
Pixel chip mass test | CCNU, Yonsei, TMEC | WP wafer pp and test (P. Riedler)
Assembly and qualification of hybrid structures | CCNU, Pusan, Inha | WP middle/outer layers (other institutes involved: Berkeley/INFN-Nikhef)

## Slide 15: Outlook : PNU Task for ITS upgrade
2013/15 : Characterization & Qualification of pixel chips.
  This July/August : Learn Test System (Procedure, Device)
  In advance : Build a Test System in Pusan
: Physics Performance study (with Inha Univ.)
2015/2017 : Assembly and qualification of hybrid structures (pixel chips + kapton printed circuit board)
  Test environment preparation:
    Probing (including mechanical tooling, probe-card design, …) Visual inspection system Define test areas (clean room)
  Automatisation of test-system: movements, pattern recognition.
  Define Database for test-results
  Component tracking – investigate technical options

## Slide 16: Back Up

## Slide 17
Project Coordination
(PL, DPL, SPL, TC, RC,
Upgrade Tasks Coordinators)
Institute Board
(PL, DPL, SPL, TC, Team Leaders)
3. Pixel chip design
4. Wafers post-processing and testing
5. Characterization and Qualification
6. Inner Layers Module
7. Middle Layers Module
8. Outer Layers Module
10.Readout Electronics
11. Mechanics and Cooling
12. DCS and Database
2. Simulation and Reconstruction
1. Physics
PROJECT
ORGANIZATION
ITS Operation
(RC, PL, DPL, SPL, TC, QAC, CC,
experts)
9. Layers Integration/Commissioning
UPGRADE
Conveners nominated

## Slide 18: ALICE ITS Upgrade layout
Current Layout (SPD)
Inner Radius
R 50
R 78.89
R 157.4

## Slide 19: ALICE ITS Upgrade layout
Current Layout (SPD)
Upgrade Layout (Inner)
Mean Radius
R 39.04
R 31.32
R 23.35
Inner Radius
R 50
R 78.89
R 157.4

## Slide 20: CMOS Pixel Sensors
Ionizing Particle
COLUMN DISCRIMINATORS
SCANNER & ENCODER
Row Address Decoder
Address
Generator
Pixel Array
Res Addr
ROLLING SHUTTER

## Slide 21
Inner Barrel (IB): 3 layers pixels
Radial position (mm): 22,28,36
Length in z (mm): 270
Nr. of modules: 12, 16, 20
Nr. of chips/module: 9
Nr. of chips/layer: 108, 144, 180
Material thickness: ~ 0.3% X0
Throughput: < 200 Mbit / seccm2
Outer Barrel (OB): 4 layers pixels
Radial position (mm): 200, 220, 410, 430
Length in z (mm): 843, 1475
Nr. of modules: 48, 52, 96, 102
Nr. of chips/module: 56, 56, 98, 98
Nr. of chips/layer: 2688, 2912, 9408, 9996
Material thickness: ~ 0.8% X0
Throughput: < 6 Mbit / seccm2

## Slide 22
CLAMP
PROTOTYPE
Carbon clamps
Silicon
Bus

## Slide 23
Chip aligner and gluing machine