Strain Data in KAGRA
Chai-Jui Chou
National Yang Ming Chiao Tung University, Taiwan
2021/12/23

---
The Archival Data in KAGRA
The Archival Data in KAGRA
Full bulk data including all channels: 1023586336 ~ 1324257664
  - K-K1_C-1144890112-32.gwf: 18984 channels.
  - K-K1_C-1270299936-32.gwf: 142518 channels.
- Low latency merged file: 1246261248 ~ 1271414784
  - KAGRA's low latency data is C10, 1sec frame size, exists on shared memory and spool files of data exchange server, and also is distributed to LIGO, Virgo and some KAGRA servers which for pipeline analysis in low latency.
  - Users cannot use this in m31-01,-02 servers.
  - Also, LIGO, Virgo low latency data is same as KAGRA's.

---
The Archival Data in KAGRA
The Archival Data in KAGRA
Full bulk data including all channels: 1023586336 ~ 1324257664
  - K-K1_C-1144890112-32.gwf: 18984 channels.
  - K-K1_C-1270299936-32.gwf: 142518 channels.
- Calibrated strain:
  - C00 level: 1142824000 ~ 1145700000
  - C20 level: 1270281600 ~ 1271462432
- Variation of h(t):
  - C00: generated in the ditital control
  - C10: generated by real time pipeline of calibration (Finite Impulse Response (FIR) filters using gstlal)
  - C20: generated by offline calibration several months after the data acquisition (gstlal)

---
Strain Data: 1144890112 (2016/04/17-01:01:35 UTC)
Strain Data: 1144890112 (2016/04/17-01:01:35 UTC)
Here are two 32-second frame files start at 1144890112:
- K-K1_C-1144890112-32.gwf (18984 channels are recorded)
- K-K1_PROC_C00-1144890112-32.gwf

---
Strain Data: 1144890112 (2016/04/17-01:01:35 UTC)
Strain Data: 1144890112 (2016/04/17-01:01:35 UTC)
Channel Name: “K1:DMG-PROC_C00_STRAIN”

---
O3GK run
O3GK run
O3GK run:
  - 2020/04/07-06:00:00 (1270274418) ~ 2020/04/20-00:00:00 (1271376018) UTC
- Target range of frequencies for C20 calibration: 30 ~ 1500 Hz.
- KAGRA detector was operated at cryogenic temperatures (20K).

---
Strain Data: 1270299936 (2020/04/07-13:05:18 UTC)
Strain Data: 1270299936 (2020/04/07-13:05:18 UTC)
Here are two 32-second frame files start at 1144890112:
- K-K1_C-1270299936-32.gwf (142518 channels are recorded)
- K-K1_HOFT_C20-1270299936-32.gwf

---
Strain Data: 1270299936 (2020/04/07-13:05:18 UTC)
Strain Data: 1270299936 (2020/04/07-13:05:18 UTC)
Channel Name: “K1:CAL-CS_PROC_C00_-STRAIN_DBL_DQ”

---
Strain Data: 1270299936 (2020/04/07-13:05:18 UTC)
Strain Data: 1270299936 (2020/04/07-13:05:18 UTC)
Channel Name: “K1:DCS-CALIB_STRAIN_C10”

---
Strain Data: 1270299936 (2020/04/07-13:05:18 UTC)
Strain Data: 1270299936 (2020/04/07-13:05:18 UTC)
Channel Name: “K1:DAC-STRAIN_C20”

---
Physical Environmental Monitors
Physical Environmental Monitors
- Seismometers, Accelerometers, Microphones, Magnetometers, Voltmeters, Thermometers, Weather station, Lightning sensor
- Known noises: 17.2Hz, 44Hz, 160Hz, 280Hz, 360Hz
- Geophysics interferometer (GIF):
  - Unique features in KAGRA to measure the ground motions along the arms.

---
Other Denoising method in KAGRA: ICA
Other Denoising method in KAGRA: ICA
Independent Component Analysis (ICA) on the accoustic noise:
  - 363Hz, 372Hz, 402Hz
- Power main noise:
  - 60Hz, 120Hz
- From the slides of F2F meeting on 2020/12/19.
- The channel used: “K1:DAC-STRAIN_C20”, ”K1:PEM-MIC_PSL_TABLE_PSL4_Z_OUT_DQ”
- Kume, Itoh, Yokoyama, Washimi, Yokozawa

---
Discussions:
Discussions:
1. Access of C10 (low latency data).
2. Test of DeepClean using C20 (or C10) strain with injected noise.
3. Correlation analysis of the channels?
4. Comparison with other denoising method: Wiener filter, Independent Component Analysis, etc.
5. DeepClean on the low frequency noise such as ground motions?