Triton Server:
Get Access to ldas-grid.ligo-la.caltech.edu (LLO) and http://ldas-grid.ligo.caltech.edu/ (LHO) so we can download the frame files for the data replay and client scripts to send inference jobs to triton server.

Deepclean:
1. Subtraction of 60Hz power main noise:
  1. The comparison of 5-parameter PE and 15-parameter PE to the O3 event GW191216 shows that the strain after the noise subtraction using Deepclean gives the similar result to the strain released by GWOSC.
  2. We should consider the subtraction of the 60Hz noise up to the 5th harmonics.
  3. We should also do the PE to the GDS_CALIB_STRAIN and compare it to the PE result from the DC_STRAIN and the GWOSC_STRAIN.
  4. Suggestion on applying Deepclean to KAGRA’s strain data: we can inject simulated CBC GW to KAGRA’s strain and test if we can improve the ability to localize the events after the noise subtraction using Deepclean.
2. Subtraction of low frequency noise (10Hz ~ 30Hz). The following is quoted from Saleem’s message from Slack:
  1. There is a low frequency subtraction achieved with the NonSENS pipeline (Vajente et al). The original analysis can be found in this repo https://git.ligo.org/gabriele-vajente/nonsens-asc-lsc-o3/-/tree/master which was performed as a two-layer analysis with first layer done using the configurations shown here https://git.ligo.org/gabriele-vajente/nonsens-asc-lsc-o3/-/blob/master/lho_sub_asc_dither_parameters.py and the output being further cleaned with the configuration here https://git.ligo.org/gabriele-vajente/nonsens-asc-lsc-o3/-/blob/master/lho_sub_isc_parameters.py
  2. We can do the minimal test by changing the config file and chanlist.ini of the 60Hz subtraction. Do the first layer subtraction and set the frequency band to 10Hz ~ 30Hz.
  3. chanlist of the first layer subtraction:
'ASC-INP1_P_INMON',
'ASC-INP1_Y_INMON',
'ASC-MICH_P_INMON',
'ASC-MICH_Y_INMON',
'ASC-PRC1_P_INMON',
'ASC-PRC1_Y_INMON',
'ASC-PRC2_P_INMON',
'ASC-PRC2_Y_INMON',
'ASC-SRC1_P_INMON',
'ASC-SRC1_Y_INMON',
'ASC-SRC2_P_INMON',
'ASC-SRC2_Y_INMON',
'ASC-DHARD_P_INMON',
'ASC-DHARD_Y_INMON',
'ASC-CHARD_P_INMON',
'ASC-CHARD_Y_INMON',
'ASC-DSOFT_P_INMON',
'ASC-DSOFT_Y_INMON',
'ASC-CSOFT_P_INMON',
'ASC-CSOFT_Y_INMON',
'H1:ASC-ADS_PIT10_DEMOD_I_OUT16',
'H1:ASC-ADS_YAW10_DEMOD_I_OUT16',
'H1:ASC-ADS_PIT10_DEMOD_Q_OUT16',
'H1:ASC-ADS_YAW10_DEMOD_Q_OUT16',
'H1:ASC-ADS_PIT2_DEMOD_I_OUT16',
'H1:ASC-ADS_YAW2_DEMOD_I_OUT16',
'H1:ASC-ADS_PIT2_DEMOD_Q_OUT16',
'H1:ASC-ADS_YAW2_DEMOD_Q_OUT16',
'H1:ASC-ADS_PIT3_DEMOD_I_OUT16',
'H1:ASC-ADS_YAW3_DEMOD_I_OUT16',
'H1:ASC-ADS_PIT3_DEMOD_Q_OUT16',
'H1:ASC-ADS_YAW3_DEMOD_Q_OUT16',
'H1:ASC-ADS_PIT4_DEMOD_I_OUT16',
'H1:ASC-ADS_YAW4_DEMOD_I_OUT16',
'H1:ASC-ADS_PIT4_DEMOD_Q_OUT16',
'H1:ASC-ADS_YAW4_DEMOD_Q_OUT16',
'H1:ASC-ADS_PIT5_DEMOD_I_OUT16',
'H1:ASC-ADS_YAW5_DEMOD_I_OUT16',
'H1:ASC-ADS_PIT5_DEMOD_Q_OUT16',
'H1:ASC-ADS_YAW5_DEMOD_Q_OUT16'
  1. chanlist of the second layer subtraction:
'ASC-DHARD_P_OUT_DQ',
'ASC-DHARD_Y_OUT_DQ',
'ASC-CHARD_P_OUT_DQ',
'ASC-CHARD_Y_OUT_DQ',
'ASC-DSOFT_P_OUT_DQ',
'ASC-DSOFT_Y_OUT_DQ',
'ASC-CSOFT_P_OUT_DQ',
'ASC-CSOFT_Y_OUT_DQ',
'ASC-MICH_P_OUT_DQ',
'ASC-MICH_Y_OUT_DQ',
'ASC-PRC1_P_OUT_DQ',
'ASC-PRC1_Y_OUT_DQ',
'ASC-PRC2_P_OUT_DQ',
'ASC-PRC2_Y_OUT_DQ',
'ASC-SRC1_P_OUT_DQ',
'ASC-SRC1_Y_OUT_DQ',
'ASC-SRC2_P_OUT_DQ',
'ASC-SRC2_Y_OUT_DQ',
'LSC-MICH_OUT_DQ',
'LSC-PRCL_OUT_DQ',
'LSC-SRCL_OUT_DQ'