## Slide 1: Deepclean: Offline and Online Tests
Chia-Jui Chou
National Yang Ming Chiao Tung University, Taiwan
2022/03/10

## Slide 2: Deepclean: Denoising using PEM and Auxiliary Channels
w(t): witness channels that record the data from the auxiliary sensors and PEM.
p(t): predicted noise in strain.
Both w(t) and p(t) are 8-second long timeseries with the same sampling rate.
Ref: 2005.06534, 2108.12430
Conv1d
Conv1d
Conv1d
Conv1d
TransposeConv1d
TransposeConv1d
TransposeConv1d
TransposeConv1d
w(t)
latent vector
p(t)
Encoder (down-sampler)
Decoder (up-sampler)
Conv1d

## Slide 3: Deepclean: Training and Inferencing
h(t): raw strain data.
r(t) = h(t) - p(t): residual.
Loss function:
h(t)
-
r(t)
Conv1d
Conv1d
Conv1d
Conv1d
TransposeConv1d
TransposeConv1d
TransposeConv1d
TransposeConv1d
w(t)
latent vector
p(t)
Encoder (down-sampler)
Decoder (up-sampler)
Conv1d

## Slide 4: Offline Test
Data used: LIGO Hanford and Livingston data from 2019/04/01 ~ 2019/06/01.
Target noise:
  power-line noise at 60Hz and its side-bands (55 ~ 65 Hz, 8th-order Butterworth filter),
  low-frequency band (8~22Hz).
Strain channel: GDS-CALIB_STRAIN.
Sample rate: 16384Hz downsampled to 4096Hz.
Loss function: ASD loss function only.

## Slide 5: Metric of Performance: Improvements in Detection Range
BNS merger in 20~1024Hz band,
IMBBH merger in 20~80Hz band.
Improvements of IMBBH range should be seen in cleaned strain.
Evaluation of detection range?
Other metric: SNR, GstLAL?

## Slide 6: Safety Check: PE on Injected CBC Events
128 events are injected in a 4096-second segment, one injection inevery 32-second segments in this 4096-second segment.
Estimated parameter: chirp mass, mass ratio, luminosity distance.
PE shoud be done on both cleaned and uncleand data to show that noise subtraction does not destroy the astrophysical signals.

## Slide 7: Online Deployment
Cleaning 1-second long strain written in frame files.
Edge effect: Quality Degrading of the noise prediction happens at the edge of the 8s-kernels (around 0.5s from the edge). It’s caused by the windowing the data.
Edge effect becomes serious when cleaning 1s data.
Bad Predictions
Windowed Kernel

## Slide 8: Working Model for 1s latency
By taking 6s before and 1s after the target 1s to form a 8s kernel, we can avoid the edge effects.
Only the green segment will be extracted after cleaning.
Windowed Kernel

## Slide 9: Training Optimizations
There are Hyper Parameters of Neural Network to be tuned for better performance.
In this work, the following parameters are focused:
  the duration of the data,
  selection of segments and the frequency of training (the cadence for re-training),
  choice of loss function weighting
Further Hyper Parameter Tuning can be done with the help of the Inference as a Service (IaaS) model.
For the online test, we need pre-trained models.

## Slide 10: Performance Evaluation and Safety check for Online Test
PE for CBC events
Stochastic signals