## Slide 1: JOREK modelling of Runaway Electron beam benign termination in JET
L.Singh, E. Nardon, V. Bandaru, H. Bergström, M. Hoelzl, C. Sommariva, JOREK Team and JET contributors
European Fusion Theory Conference, Aix en Provence, 23-26 September 2025

## Slide 2: Motivation
Runaway electrons (RE) pose a serious threat in high-current tokamaks, such as ITER, where they can reach tens of MeV and damage plasma-facing components
Damage caused by the RE beam in JET #86801
L. Chen, 5th Asia Pacific Conference on Plasma Physics, 26 Sep-1 Oct 2021
Main strategies:
RE avoidance, challenging in large machines like ITER [1]
Sacrificial limiters (EU-DEMO)
Benign RE beam termination (ITER)
[1] Vallhagen et al 2024 Nucl. Fusion 64 086033

## Slide 3: Outline
Introduction
  What are Runaway Electrons?
  What is benign termination?
JET pulse #95135: a famous case of RE benign termination
  Experiment Description
  Numerical Modelling
  Past Results
New Results
  Scan in resistivity
  Scan in viscosity
  Comparsion between the RE transport mechanism
  Moving towards a self-consistent evolution
Conclusions

## Slide 4: Introduction
1

## Slide 5: What are Runaway Electrons?
Generated during a disruption: TQ CQ Possible Runaway Plateau
Drop in plasma temperature
Increase in plasma resistivity
Plasma current decay and rise in inductive electric field
Acceleration of electrons due to overcoming RE generation
M. Hoppe. PhD thesis, Department of Physics, Chalmers University of Technology, Goteborg, 2021
As the RE beam evolves (e.g. runs into the wall) an MHD instability can occur RE deconfinement and possible damage

## Slide 6: What is benign termination?
MHD instability
Magnetic field stochastization
RE beam broad deposition on the PFC
No reavalanching and conversion from magnetic to kinetic energy
BENIGN TERMINATION [1, 2]
Bergström et al 2024 Plasma Phys. Control. Fusion 66 095001
[1] Reux et al 2021 Phys. Rev. Lett. 126, 175001
[2] Paz-Soldan et al 2021 Nucl. Fusion 61 116058

## Slide 7: JET pulse #95135
2
A famous case of RE benign termination

## Slide 8: JET #95135: experiment description
Bandaru et al, 2021 PPCF 63
Generation of RE
At , SPI
Plasma recombination and Argon flush out
Drop in the effective resistivity
RE current increases
Disruption (#95135) triggered by Argon MGI
Fast loss of RE with no wall damage

## Slide 9: JOREK Modelling
Using JOREK RE fluid model [Bandaru et al, 2021 PPCF 63 ]:
RE current density
Advection term
Diffusion term

## Slide 10: JOREK simulation setup
The initial current (and safety factor) profile derived from a comparison between the Infrared synchrotron image and SOFT [1] :
Bandaru et al, 2021 PPCF 63
2 q=4 surfaces (Double Tearing Mode)
[1] Hoppe et al, 2018, Nuclear Fusion, 58(2), 026032.

## Slide 11: Past results
Evolution of a DTM
Full magnetic field stochastization
Loss of REs within 200
Bandaru et al, PPCF 63 (2021)

## Slide 12: New Results
2

## Slide 13: Aim: more realistic simulations
Bandaru et al found a fast and complete loss of REs (consistent with benign termination), but:
  In reality, is probably since recombines
  (too high (?))
  RE transport through diffusion instead of advection
  Initial equilibrium highly MHD unstable (not self consistent). Start from a stable equilibrium and evolve it to termination
Notes: Improving the results from Vinodh which has some limitations. Spitzer resistivity corresponding to 𝑻_𝒆= 𝟏𝟎 𝒆𝑽 since there is no clear information about the background temperature. In reality, the 𝑻_𝒆 might be much lower due to Deuterium recombination (happening at 𝑇_𝑒<2 𝑒𝑉 )
A viscosity of 𝝁=𝟒𝟖 𝒎^𝟐/𝒔 taken into consideration. It might an effect on the overall dynamics.
RE transport modelled through numerical diffusion instead of advection due to heavy computational requirements

## Slide 14: Scan in background resistivity with advection
Higher faster dynamics, shorter loss timescale BUT higher final
High
Medium
Low
High
Medium
Low
Notes: Axis label too small. Indicate on the figure the resistivty As expected, the higher resistivity case (plain curves) grow much faster since the linear growth rate of the n=1 mode scales as 𝜂^(3/5) as shown in the figure with the magnetic energy growth of the 𝑛=1−5 toroidal harmonics
increasing resistivity → decreasing 𝐽_𝑅𝐸 loss time of the RE current due to a slower dynamics as shown in the figure. BUT, the fraction of current lost increases

## Slide 15: Higher final at higher , why?
, 0.82 MA
At high REs don’t have enough time to escape before the reformation of the flux surfaces
loss timescale of

## Slide 16: Faster dynamics leads to larger wetted area
RE footprint determined by MHD
growth rate
amplitude
Similar amplitude for all , but high has the highest growth rate
LARGEST FOOTPRINT
 | High | Medium | Low
Area | 3.2 | 2.7 | 1.4
 | 3.2 | 2.7 | 1.4
REs losses occur as stochasticity develops.
Large MHD needed for large wetted area

## Slide 17: Viscosity effects on modes growth
, , @
Lowest viscosity fastest linear growth rate, but lowest amplitude
High
Medium
Low
Notes: In the second figure add rescaled. I am not doing Rutherford scaling I am just shifting in time to match the Rutherford phase for n=1. Instead of rescaling write shifted. Indicate on the figure the viscosity (high, middle, small) The viscosity values used are 𝝁=𝟒𝟖 𝒎^𝟐/𝒔, 𝝁=𝟒.𝟖 𝒎^𝟐/𝒔, 𝝁=𝟎.𝟒𝟖 𝒎^𝟐/𝒔 with a resistivity of 𝜂=3.3∗10^(−5) Ω𝑚:
A lower viscosity leads to faster linear growth rates due to a lower energy dissipation
At the lowest viscosity the relaxation phase is smoother

## Slide 18: Viscosity Effects on RE current losses
Faster dynamics with lower viscosity faster RE loss timescale in the initial phase
But, smallest amplitude reduced loss timescale

## Slide 19: Moving towards a self-consistent evolution
Bandaru et al, PPCF 63 (2021)
Previous simulations started from unstable MHD equilibrium. Now, start from a stable equilibrium and evolve it to termination

## Slide 20: Current ramp up
Start from an equilibrium with a and
Ramp up the RE current by applying a loop voltage through Central Solenoid

## Slide 21: 2D preliminary output
In 2D, current ramp up leads to
I

## Slide 22: 3D preliminary output
MHD activity during the irregular ramp up. In particular, in the core region cannot reach (numerical issues)
I

## Slide 23: Initial MHD instability: mainly 5/1 DTM
t= 0.074 ms, 0.69 MA
t= 0.163 ms, 0.64 MA
t= 0.131 ms, 0.68 MA
5/1 islands as observed in experiment. But, afterwards MHD only in the core

## Slide 24: Summary and Outlook
High faster but incomplete RE loss and larger wetted area
Low slower but complete RE loss and smaller wetted area
Interpretation: MHD dynamics and RE advection timescales govern REs losses and footprint
In the model, is not T dependent. In experiment, initialy high, but then, due to ohmic heating, gets lower fast and complete RE loss (speculation)
Stable equilibrium 5/1 island initially, but later MHD only in core. Currently, under investigation
Notes: A higher resistivity -> faster RE loss rate but no complete loss A resistivity of 𝜂=6,1∗10^(−4) causes the RE loss to occur on the time scale seen in the experiment. However, differently from the experiment, a complete loss of RE does not take place. In the model, we do not have a self consistent evolution of resistivity. Therefore, in reality the resistivity might be high at the starting of the loss phase, but then due to ohmic heating, it gets reduced. This would allow for faster and complete loss of RE. This is for future work.
Footprint larger at larger resistivity. At higher resistivity the MHD dynamics are faster and maybe that’s why:
1, I loose less Res at high resistivty. Flux surface come back quicker and RE don’t have to escape
21, The footprint has more time to grow with respect to the loss time of RE. The footprint is governed by the combination of how fast and how large you grow.

## Slide 26: Higher final amplitude, Why?
The growth of the toroidal harmonics for and rescaled through Rutherford scaling [1]
Rutherford phase similar for n=1 mode, but non linear dynamics sensitive to
At lower resistivities n > 1 grow faster higher RE losses
[1] E. Nardon et al. Phys. Plasmas, 30:092502, 20
Notes: As always, too much text. Explain the figures thoroughly. We scale the time with Rutherford scaling because this is how the tearing mode grows But then there are differences due to the interaction between the different modes nonlinearly. Nonlinear dynamlics sensitivite to resitivire The growth of the toroidal harmonics for 𝜂=1.84×10^(−4) Ωm is plotted as a function of a rescaled time t′ =t/3.3+0.07 ms where factor 3.3 comes from the resistivity ratio. For 𝜂=3.3×10^(−5) Ωm t′ = t/18.51+0.1 ms. This is consistent with the theory as the dynamics during the Rutherford phase should be invariant by a transformation of the type t → αt, η → η/α [1]
The growth of the toroidal harmonics for 𝜂=1.84×10^(−4) Ωm is plotted as a function of a rescaled time t′ =t/3.3+0.07 ms where factor 3.3 comes from the resistivity ratio. For 𝜂=3.3×10^(−5) Ωm t′ = t/18.51+0.1 ms. This is consistent with the theory as the dynamics during the Rutherford phase should be invariant by a transformation of the type t → αt, η → η/α [1]
The Rutherford phase is similar for the n=1 mode but as the resistivity decreases, the secondary modes (n > 1) grow faster causing the relaxation phase to become violent. This leads to higher RE losses

## Slide 27: Faster dynamics leads to larger wetted area
In all cases, the primary mode n=1 which dominate the dynamics both linearly and non linearly
The dominance of the primary mode is directly linked to the wall area on which the RE energy deposition occurs.
The heat loads are computed using the JOREK particle tracing module
Since the MHD simulations provide no information about the RE distribution in the momentum space, each RE particle is assumed to have a kinetic energy of 10 MeV and a pitch angle of ζ =v∥/v⊥ =−0.99.
For (with highest growth n=1) the largest area of energy deposition among all the simulated cases take place as reported in the table

## Slide 28: Advection vs diffusion: modes growth (I)

## Slide 29: Advection vs diffusion: modes growth (II)

## Slide 30: Advection vs diffusion: modes growth (II)

## Slide 31: Faster dynamics leads to larger wetted area
High
Medium
Low
RE footprint determined by
Growth rate
n=1 maximum amplitude
Similar max values for all , but high has the highest growth rate
LARGEST FOOTPRINT

## Slide 32: Viscosity effects on modes growth
, , @
Lowest viscosity fastest linear growth rate, but lowest amplitude Smallest Footprint
 |  | 4.8 | 
Area | 1.4 | 0.9 | 0.8
 | 1.4 | 0.9 | 0.8
High
Medium
Low
Similar max as high and faster rates, but lower footprint (?)
Notes: In the second figure add rescaled. I am not doing Rutherford scaling I am just shifting in time to match the Rutherford phase for n=1. Instead of rescaling write shifted. Indicate on the figure the viscosity (high, middle, small) The viscosity values used are 𝝁=𝟒𝟖 𝒎^𝟐/𝒔, 𝝁=𝟒.𝟖 𝒎^𝟐/𝒔, 𝝁=𝟎.𝟒𝟖 𝒎^𝟐/𝒔 with a resistivity of 𝜂=3.3∗10^(−5) Ω𝑚:
A lower viscosity leads to faster linear growth rates due to a lower energy dissipation
At the lowest viscosity the relaxation phase is smoother
With resistivity the scaling of the growth rate is faster therefore I see an effect on the footprint

## Slide 33: Advection vs diffusion
, , @
Lowest viscosity fastest linear growth rate, similar amplitude
High
Medium
Low

## Slide 34: Advection vs diffusion: RE current loss
Larger RE loss rate due to faster growth of the modes and clear scaling with viscosity
Notes: With diffusion the RE loss rate is higher due to faster growth of the modes. Morevoer, there is a clear trend with viscosity since the relaxation is not smoothned with 𝜇=0.48 𝑚^2/𝑠 as with advection.
All this has an effect on the RE loss phase. If we look ony at the diffusion curves (dashed), we see a scaling with viscosity. Higher viscosity leads to higher loss time due to slower dynamics. If compared with advection cases we can see difference due to slower dynamics and smoother non linear phase

## Slide 35: Moving towards a self-consistent evolution
Bandaru et al, PPCF 63 (2021)
Previous simulations started from unstable MHD equilibrium. Now, start from a stable equilibrium and evolve it to termination