## Slide 1
Matt Pyle
UC Berkeley
University of Michigan
25/05/04
Solving the Fundamental Challenges of meV-GeV Dark Matter Searches with Calorimeters

## Slide 2: Light Mass DM Direct Detection Design Drivers

## Slide 3: Light Mass DM: Nuclear Recoil Direct Detection Constraints
?
There are basically no Direct Detection constraints. Why?
2203.08297
Typical Neutrino cross section

## Slide 4: Kinematics: 2 Body Elastic Nuclear Scattering
Transfer of DM kinetic energy to nucleus is really inefficient for elastic 2 Body Scatters when Mn >> MDM
DM
When Mn>> MDM

## Slide 5: Light Mass Dark Matter: Elastic Nuclear Scattering
Design Driver #1: Energy Sensitivity
1 meV
<v> -
Vesc --

## Slide 6: It’s not quite this daunting …

## Slide 7: DM- Coherent Vibrational Interactions
For DM interactions with small momentum and energy transfers, we need to start thinking about DM interactions producing coherent crystal excitations!
- <E>
-- <E>
Coherent Vibrational Excitations in Si
1712.06598, 2205.02250
Scalar Nuclear Interaction: Detectable Energy [eV]

## Slide 8: Light Mass DM: Detector Design Driver #1: Energy Sensitivity
2203.08297
Typical Neutrino cross section
1. Energy Sensitivity

## Slide 9: Mysterious Low Energy Excess
CRESST III
2207.09375
CRESSTIII Background Studies
Expected Radiogenic Backgrounds
Seen in all calorimeter experiments to varying degree
?
Si 0.35g
LiAlO2 11g
Al2O3 16g
Al2O3 16g
CaWO4 24g
CaWO4 24g

## Slide 10: Light Mass DM: Detector Design Drivers
2203.08297
Typical Neutrino cross section
1. Energy Sensitivity
2. Detector
Backgrounds

## Slide 11: Superconducting Athermal Phonon Detectors
2410.16510: you can read today … a bit out of date
Most plots shown are coming from our newest athermal phonon pixel detector paper. Going up on arXiv next week!

## Slide 12: Athermal Phonon Detectors
TES (W or IrPt)
Athermal Phonon
Collection Fins (Al)
Substrate (Si,Ge,GaAs,SiO2,Al2O3)
1 cm
1 cm
R
T

## Slide 13: Measured Phonon Collection Efficiency
Phonon detectors optimized for maximum phonon collection / energy sensitivity
Single Photon Sensitivity!
Easy to Calibrate with IR/Optical Photons
1cm2x1mm Silicon 1% coverage

## Slide 14: Unexplained Low Energy Excess (LEE) Background(s)

## Slide 15: 1. Variation with time since cooldown
Warm up to 11K and 19K due to fridge issues
E. Queguiner
Thesis
Rate partially reset with thermal cycling
2 distinctive decay time constants
Ge, epoxy, Au
EDELWEISS/RICOCHET

## Slide 16: 2) Low Energy Excess is Non-Ionizing
From J. Gascon /EDELWEISS
EDELWEISS interleaved detectors measure both phonons (NTD) and ionization production
Large no ionization background of unknown origin out to pretty high energies
Ge, NTD,
epoxy, Au

## Slide 17: Low Energy Excess Fact Summary
 | SPICE/CDMS | EDELWEISS | CRESST
1) Variation with time since cooldown (and/or time since fabrication) | Yes | Yes | Yes
2) Non-Ionizing | Yes | Yes | 
3) Same above /below ground | In 10-80eV range | mostly | 
These facts are incredibly restrictive!

## Slide 18: Stress Relaxation?
Detector
Detector
Detector under stress due to thermal contraction,manufacturing, etc.
Detector relaxes releasing phonon energy
arXiv:physics/0504151

## Slide 19: Stress Related Relaxation: 1st Low Energy Evidence
Glued Down with GE varnish
(High Stress)
Hanging (low stress)
2 orders of magnitude difference in rate between high stress (glued) and low stress (hanging) device
2208.02790
GE varnish (and rubber cement) significantly increase <38eV backgrounds

## Slide 20: Mitigation for Stress Relaxation Events: GET RID OF ALL STRESS
Support Structure
Sensor Films
Crystal Surface Relaxation
Bulk dislocation(s) relaxation

## Slide 21: Understanding Relaxation Events: 2 Channel Devices
We see both shared and single channel relaxation events
1% 2 Channel Device

## Slide 22: Single Events in Photon Calibration too
Calibration photons have single and shared events too!
Shared = substrate absorption
Singles = Al fin absorption
1 Al fin photon + 3 substrate photons

## Slide 23: Single Relaxation Event Pulse Shape
Single LEE background source is Al film relaxation!
LEE single pulse shapes and Al fin calibrations photons have pulse shapes consistent with a dirac delta energy pulse that saturates a single phonon sensor in the channel
As LEE energy drops, pulse shape looks more like a dirac-delta energy deposition (known from dIdV)

## Slide 24: Source Shared LEE Relaxation?
Substrate Volume?
Dicing Saw Sidewall Surface?
Polished z face?
Wirebond support interface?
Test hypotheses with different substrate geometries

## Slide 25: Shared LEE Rates
First Evidence that LEE seems to scale largely with substrate mass/volume not surface area …
76mm diameter x1mm thick

## Slide 26: Tension with CRESST Measurements?
2207.09375
CRESSTIII Background Studies
Si 0.35g
LiAlO2 11g
Al2O3 16g
Al2O3 16g
CaWO4 24g
CaWO4 24g

## Slide 27: Energy Sensitivity

## Slide 28: Current Performance: Sensitivity
On Day 12, Phonon baseline energy resolution is 259meVrms
  World leading by x4
Sensitivity continues to improve pretty rapidly with time cold. @40days, we expect 180meVrms !

## Slide 29: Measured Noise
Excess nominated splits into 2 pieces:
- Correlated noise whose pulse shape -> shot noise from substrate phonon events
- Uncorrelated white power noise -> shot noise from localized sensor events

## Slide 30: Light Mass DM LEE Design Driver
2203.08297
Typical Neutrino cross section
LEE Mitigation

## Slide 31: Low Energy Excess Discrimination

## Slide 32: GaAs
GaAs has very high scintillation yield (1802.09171)
We now have the capability to tag single IR photons at 5 !
ER DM and NR DM interactions can be distinguished from non-ionizing LEE Backgrounds!

## Slide 33
Superfluid Helium: it’s a liquid … no stress microfractures
Multiple Pixel Coincidence for He DM events discriminates DM from pixel microfractures
Pulse Shape Discrimination: Helium is slow!
Surface
Underground
Stretch
Goal
Goal
Required
Al2O3
He

## Slide 34: Light Mass DM LEE Design Driver
2203.08297
Typical Neutrino cross section
LEE Mitigation
Discrimination
Huge Progress
GaAs Single IR Sensitivity

## Slide 35: Backup

## Slide 36: The TES Challenge: Environmental Noise
Lowering Tc and decreasing Vtes, doesn’t just increase sensitivity to DM, it drastically increases sensitivity to all environmental power sources
To increase your sensitivity by x10, you need to decrease your susceptibility to environmental DC backgrounds by x100!

## Slide 37: External EMI suppression
300K
50K
4K
750mK
10mK
Russian Doll of Faraday Cages
3.2 MHz Pi, conductive gaskets at 300K
Wire heatsinks feedthroughs encase twisted pairs in ”coppercast” for > O(10GHz) filtering
  Martinis, Devoret, Clarke (PRB 35.4682 1987)
Tested with external 900MHz modulated @200Hz source … Nothing
SQUIDS
John Clarke’s Lab

## Slide 38: Black Body IR: QUBITs Decoherence & Resonator Losses
1105.4642
1105.4642
Black Body Radiation emitted from higher temperature thermal cans leaks through a single 10mK thermal shield and dominate the loss mechanisms in resonators and QUBITs (R. Barends et al 1105.4642,Baselmans et al, AIP 1185 2009)
Box + mm Absorber (eccosorb or coppercast) + Box minimizes IR transmission
How do the photons get in? Why isn’t a single light tight box enough?
Notes: Martinis paper 1105.4642

## Slide 39: 4 Photon Bend Flanges
Original Plan: With a “4 photon bend” flange, we won’t need a copper cast absorber!
Backup: slather on some coppercast
Inner Can
Outer Can
Coppercast Feedthrough

## Slide 40: Black Body Leakage Through Flange
TES Bias Power [fW]
Still Temperature [mK]
Publishing Soon!
4 photon bend double box (no absorber) had 30fW of ~1K IR leakage!
Adding coppercast absorber dropped it to unmeasureable levels (Martinis was right)
How: HFSS simulations suggest 4 photon bend completely transparent above TE cutoff!

## Slide 41: Impedance Mismatch Flange
2mm
Modify the 4 photon bend to have a mismatched optical cavity
TES Bias Power [fW]
Still Temperature [mK]
~ x6 decrease in IR absorption compared to
Standard flange (no absorber)
~ x10 expected from HFSS
Publishing Soon!

## Slide 42: Future: Multiple Impedance Mismatched Cavities
Create a flange with multiple (2-3) impedance mismatched cavities with offset resonances
>-40dB suppression
Significant suppression even at low frequencies

## Slide 43: Environmental IR still dominate
Liu et al (2203.06577) finds that their residual charge parity switching rate varies enormously with the geometry of the charge island
Propose this is due to coupling of environmental photons in the 100GHz to THz
Mismatched flange could significantly improve background rates!

## Slide 44: Current TES Sensitivity
1cm2x1mm Si chip with
  4% athermal phonon detector with
  25umx25umx60nm W TES
  25umx100umx60nm W TES
  200xumx800umx60nm W TES
Thicker TES used to maximize photon collection in TES electronic system
Tc = 50mK
Publishing Soon
Sensitivity limited by 2x1019 W/rtHz of unknown origin
  Doesn’t scale with TES size
100% collection … expect 7meVrms sensitivity

## Slide 45: Future: IR calibration
450nm (2.75eV) photons badly saturate the 25umx25umx60nm TES
need IR photons to linearly calibrate
Can piece together collection efficiencies from the 200x800 and 100x400 devices and we can get 8-12meV rms