## Slide 1
Dr. Kimberly Tkalčec
ket36@cam.ac.uk
30th January 2025
The Atom Interferometry and Observational Network (AION)
AION-10 Planning

## Slide 2
AION-10 Plans
Oxford Physics Department
Beecroft Building
https://www.hawkinsbrown.com/projects/beecroft-building-university-of-oxford

## Slide 3
AION-10 Plans: Modules
The modules encased in their aluminium support frames
space for attachments such as cold atom sources as well as stability support
The modules will be lifted into the building and lowered into place using a dedicated crane system.

## Slide 4
AION-10 Plans: Modules
Top Module:
Telescope
2 m long
Houses telescope and ion pumps

## Slide 5
AION-10 Plans: Modules
Upper/Lower main module:
Each 4.6 m long
Module houses vacuum pipe and the magnetic shields.
Levelling mechanism is present to correct any skewness.

## Slide 6
AION-10 Plans: Modules
Inter module:
2D MOT
3D MOT
Interconnect chamber
  Bespoke support structure around the interconnect chamber for the optical elements.
Active Vibration Isolation Platforms for camera stability

## Slide 7
AION-10 Plans: Stability Requirements
Inter Module
(Interconnect chamber
Attached to Cold Atom Source)
BR Mirror
Base Module:
Passive Vibration Isolation Platform at base of tower

## Slide 8
AION-10 Structure
Structural Stability
Support Structure: Connection Points on Walls and Ground
Modal frequency analysis
Evaluation of stability of lenses and camera
 Translational RMS (Root mean square) or End-To-End values of response points

## Slide 9
Stability requirement: The two camera assemblies are ∼ 5 m apart and must be fixed within 100 nm relative to each other during measurements.
Example: Translational motion of camera
AION-10 Structure

## Slide 10
Baseline L
atom
cloud
atom
cloud
Laser beam
Gradiometer Configuration:
Two atom interferometers along a baseline
for differential measurements
Intrinsic laser phase noise then becomes common mode
if one interferometry laser beam used for the entire vertical baseline.
That requires single-photon transitions between the laser pulses and the atoms
Differential readout
AION-10 Configuration

## Slide 11
Large Momentum Transfer (LMT)
PRX QUANTUM 3, 030348 (2022)
Required beam power levels calculated:
For clock interferometry @ 698 nm
AION 100 m (beam waist ~1cm)  ~102 W
AION 1km (beam waist ~3 cm)  ~103 W
(assuming pulse length of ~1 us (LMT : 10^4),
Rabi Frequ.> 10kHz, Laser Linewidth stabilised to 1 Hz )
Example
Strontium clock transition @698 nm
for pulse separation = 1us,
pulse length = 1 s
Increasing AI sensitivity with π pulses

## Slide 12
AI Readout – Phase Noise
To achieve high fringe visibility, phase noises in the interference pattern must be minimised.
Phase noise in the readout arise from laser-induced phase shifts:
  Inhomogeneous intensity distribution
𝛑
𝛑/2
𝛑/2
atom cloud
AI Readout:
Simulation
M. Abe et al, Quantum Sci. Technol. 6 044003 (2021)
Uniform intensity distribution on lengthscale of atom cloud
 Telescope designed to maximise beam size
  Laser wavefront aberrations

## Slide 13
AI Readout – Phase Noise
Optical Path Difference (OPD)
Wavefront aberration results in OPD across the beam.
Δφ = Δφcurv+ Δφsurf+ Δφmech + Δφscatt
Laser Wavefront Aberrations:
Phase shift of a wavefront curvature

## Slide 14
AI Readout – Phase Noise
Optical Path Difference (OPD)
Wavefront aberration results in OPD across the beam.
Δφ = Δφcurv+ Δφsurf+ Δφmech + Δφscatt
Laser Wavefront Aberrations:
Phase shift of a wavefront curvature
Beam Delivery to AI pipe:
Vacuum pressure calculation:
OPD due to refractive index (n>1) –
Refractive indices as a function of air pressure calculated
(Theory in Appl. Opt. 35, 1566-1573 (1996))
pressure p = 10-5 mbar  Phase shift dphi = 0.038 mrad
(n(p) = 1+2.6745*10-12, T = 20 deg C, path length = 10 m, lambda = 698 nm)

## Slide 15
AI Readout – Phase Noise
Optical Path Difference (OPD)
Wavefront aberration results in OPD across the beam.
Δφ = Δφcurv+ Δφsurf+ Δφmech + Δφscatt
Laser Wavefront Aberrations:
Phase shift of a wavefront curvature
 Analysis in telescope design

## Slide 16
AI Readout – Phase Noise
Optical Path Difference (OPD)
Wavefront aberration results in OPD across the beam.
Δφ = Δφcurv+ Δφsurf+ Δφmech + Δφscatt
Laser Wavefront Aberrations:
Including aspheric first lens could cancel out the OPD around the optical axis
Phase shift of a wavefront curvature
 Analysis in telescope design

## Slide 17
AI Readout – Phase Noise
Phase shift of imperfect optical surfaces
 feasibility studies on surface tolerances
Δz
OPD Requirement ~ Δz < 1/1000 λ
Δφ = Δφcurv+ Δφsurf+ Δφmech + Δφscatt
Laser Wavefront Aberrations:

## Slide 18
AI Readout – Phase Noise
Phase shift due to
mechanical instabilities
Δφ = Δφcurv+ Δφsurf+ Δφmech + Δφscatt
Laser Wavefront Aberrations:
Optical path difference between clouds
L
δL
Phase shear
Laser wavefront curvature
L
x
Beam Pointing instabilities
Beam pointing angle < 35 nrad!
(Assuming 1% fluctuation in
horizontal phase gradient)

## Slide 19
AI Readout – Phase Noise
Δφ = Δφcurv+ Δφsurf+ Δφmech + Δφscatt
Laser Wavefront Aberrations:
Phase shift of a scatterer
Numerical analysis of dust particle size:
Fourier propagation of a beam propagating through a dust particle.
Motivation:
What dust size can we tolerate?
What are cleanliness requirements?

## Slide 20
AI Readout – Phase Noise
Δφ = Δφcurv+ Δφsurf+ Δφmech + Δφscatt
Laser Wavefront Aberrations:
Phase shift of a scatterer
What dust size can we tolerate?
Aberrations still >> 0.5 mrad after 0.5 m propagation
Dust particle size: 200 um

## Slide 21
AI Readout – Phase Noise
Δφ = Δφcurv+ Δφsurf+ Δφmech + Δφscatt
Laser Wavefront Aberrations:
Phase shift of a scatterer
Aberrations <5 mrad for distances >0.03 m
Dust particle size: 10 um
What dust size can we tolerate?

## Slide 22
M1
M2
BR Mirror
Lens 2
Lens 1
Atom
cloud 1
Atom
cloud 2
Bottom figure: Abe et al 2021 Qu. Sci. Technol. 6 044003
Galilean Telescope
Simulation:
 Removing transverse wavevectors
AION 10 - Beam Cleaning

## Slide 23
Large Mode Area Photonic Crystal Fibre (PCF)
Beam simulation
at 3.3 m after PCF:
Option: Coupling via Large Mode Area Photonic Crystal Fibre (PCF)
M1
M2
BR Mirror
Lens 2
Lens 1
Atom
cloud 1
Atom
cloud 2
AION 10 - Beam Cleaning

## Slide 24
Large Mode Area Photonic Crystal Fibre (PCF)
Beam simulation
at 3.3 m after PCF:
Stimulated Brillouin Scattering does not limit the PCF input power level up to ~3.5 Watts
(test: 698 nm laser of ~100 kHz linewidth).
Future tests with higher power and narrower linewidth.
Option: Coupling via Large Mode Area Photonic Crystal Fibre (PCF)
M1
M2
BR Mirror
Lens 2
Lens 1
Atom
cloud 1
Atom
cloud 2
AION 10 - Beam Cleaning