## Slide 1: SuperCDMS … and Beyond
Miriam Diamond & Ziqing Hong, University of Toronto
2025 Canadian Astroparticle Physics Community Meeting

## Slide 2: The Super Cryogenic Dark Matter Search
~ 100 researchers at 28 institutes across 6 countries
Canada taking the lead!
A direct detection search experiment employing an array of ultra-pure silicon and germanium detectors to search for low-mass (< 10 GeV/c2) DM candidates
Canadian PIs:
Miriam Diamond, Ziqing Hong, Pekka Sinervo (UofT)
Wolfgang Rau (TRIUMF)
Scott Oser (UBC)
Andy Kubik, Matt Stukel, Jodi Cooley (SNOLAB)
Alan Robinson (UdeM)

## Slide 3
Science goals
Experiment layout & detector technology
Installation & integration
Schedule
Tower testing in CUTE
Simulations & background modeling
Sensitivity projections
HVeV R&D program
Far-future R&D initiatives
  HONEYCOMB
  SPLENDOR
  Underground detector fabrication
Outline
Highly Qualified Piggies (HQPs)

## Slide 4: Science Goals

## Slide 5: SuperCDMS @ SNOLAB Experiment Layout

## Slide 6: SuperCDMS @ SNOLAB Experiment Layout
Facility:
6000 m.w.e. overburden
15 mK base temperature
Initial Payload: ~30 kg total
Electron Recoil Backgrounds:
External and facility: O(0.1 /keV/kg/d)
Det. setup: O(0.1(Ge)-1(Si) /keV/kg/d)
Total: O(0.1-1 /keV/kg/d)
Designed to be dominated by solar neutrinos in NR background
Vibration isolation:
Seismic: spring loaded platform
Fridge on active vibration damper
Cryo coolers: soft couplings
  Braids, bellows
Copper cans: hanging on Kevlar ropes

## Slide 7: Cryogenic Calorimeter SuperCDMS Detector Technology
Absorber
Thermal Bath
Weak Thermal Link
Cryogenically cooled in dilution fridge
Transition-Edge Sensor (TES)
web.mit.edu/figueroagroup
Temperature [mK]
Resistance [mOhm]
TES
Energy
Response of TES
Current
Time

## Slide 8: SuperCDMS Detector Technology
iZIP Detector:
Prompt phonon and ionization signals allow for discrimination between nuclear and electron recoil events
HV detector:
Drifting electrons/holes across a potential (Vb) generates a large number of phonons (Luke phonons).
  Enables very low thresholds!
  Trade-off: No event-by-event NR/ER discrimination
Discriminating
Low Threshold

## Slide 9: SuperCDMS Detector Technology
Detectors made of high-purity Ge and Si Crystals
  Si (0.6 kg each): sensitivity to lower DM masses
  Ge (1.4 kg each): sensitivity to lower DM cross-sections
Low operation temperature: ~15mK
  Athermal phonon measurement with TESs
  Ionization measurement (iZIP) with HEMTs
Multiple channels per detector to identify event position
Initial payload: 4 “towers” of 6 detectors each
  2 iZIP : 10 Ge / 2 Si
  2 HV : 8 Ge / 4 Si
iZIP
HV

## Slide 10
Dilution fridge on temporary stand
Thermometry installation
SuperCDMS Installation & Integration
Lower portion of shield

## Slide 11
50K Cooler installation
ETank scaffolding
SuperCDMS Installation & Integration
E-stem cabling completion

## Slide 12
Detector Readout Cables connection
CP Stem insertion
SuperCDMS Installation & Integration
Vacuum vessel installation
DAQ connection

## Slide 13
Dilution Fridge Tails installation
Cryostat purge
SuperCDMS Installation & Integration
Calibration system assembly

## Slide 14: SuperCDMS Schedule

## Slide 15: Cryogenic Underground TEst facility (CUTE)
Friendly neighbour
Taking on critical mission of detector testing
  Exercise & debug detectors before SuperCDMS cryostat in place
Same environment, same electronics → similar challenges expected
Small science exposure - mostly to exercise the analysis tools
WE ARE VERY CUTE!

## Slide 16: SuperCDMS Tower Testing at CUTE
Tower-3 (HV detectors) installed & operated at CUTE
Oct 2023 - March 2024
First time operating HV detectors in deep underground low-background facility!

## Slide 17: SuperCDMS Tower Testing at CUTE
1.3 keV
Si calibration using Compton step features
Ge calibration using activation lines
151 days of operation:
  ~ 2 months of calibration data
  ~ 2 months of low background data
  Several weeks for detector characterization (e.g. noise performance, HV testing)
Stay tuned!
HV amplification
Phonon pulses

## Slide 18: Understanding Detector Response: Simulations
GEANT4 + G4CMP based simulation
  GEANT4 for energy depositions
  G4CMP for charge and phonon propagations in crystals (NIM A 1055 168473 (2023))
Deriving detector response modeling from first principle
Validation with existing calibration data ongoing
Time (samples)
Voltage (arbitrary unit)

## Slide 19: Background Modeling
Background: extensive material cleaning, tracking and screening
eTraveller: Bookkeeping tool to keep track of material movement
  Precision accounting for cosmogenic activations
BGExplorer: Background estimate based on material assay results
https://github.com/bloer/bgexplorer-demo

## Slide 20: SuperCDMS Sensitivity Projection : NRDM
Current constraints
(Already excluded)
Current constraints
(Already excluded)
SuperCDMS SNOLAB
(Initial payload)
SuperCDMS SNOLAB
(Initial payload)
I
II
Ge 10 cm3
Si 10 cm3
Si 1 cm3
Si 1 cm3
Si 10 cm3
Ge 10 cm3
10 cm3 Ge iZIP
10 cm3 Ge piZIP x20 mass
10 cm3 piZIP Si/Ge
No ionization
Pushing the sensitivity to lower DM mass
Future Improvement in phonon resolution: 0V Si/Ge 1 cm3, 10 cm3
At lower DM masses, DM spectrum steeply rises whereas ER bkg is flat
  Improved 𝜎phonon allows bkg subtraction statistically with PLR
  NB: LEE not taken into consideration
Pushing the sensitivity into the neutrino-fog : three avenues
HV-SNOLAB-sized detectors : improved 𝜎phonon → spectral discrimination
10 cm3 iZIP detectors: improved 𝜎ionization → better ER/NR discrimination
10 cm3 piZIP detectors: measure phonons from ER and Neh separately → ionization-yield discrimination
I : with in-hand detector technology upgrade
II : with significant technology upgrade & x20 mass
Upgrade scenario
Neutrino Fog
Neutrino Fog
arXiv:2203.08463
arXiv:2203.08463

## Slide 21: Exploring the Sensor Limits: HV → HVeV Detectors
HVeV: Prototype HV detector
Gram scale
eV level resolution
(“Run 4”: low-energy calibration using Compton steps in Si
https://arxiv.org/abs/2508.02402 )
HVeV

## Slide 22: Background Challenges in Low-Mass DM Searches
Sub 1-eh peaks
Hypothesized from unpolished sidewalls
Will attempt sidewall etching/polishing
1-eh peak
Could be from electrode leakage, light leakage, etc.
Attempting electrode blocking materials for mitigation
Also building better light tight enclosures
Low energy excess
Evidence hints different ionization from ER and NR
  “Heat only”
Unpacking ER/NR/Heat Only components by operating with different NTL gains
What are these?

## Slide 23: HVeV “Run 5” @ CUTE
New light tightness standard
More sensitive TES sensors
  Lower Tc, requires lower noise
Quieter electronics
SiO2 insulating layer for charge injection
Lower background
Operating detector at multiple voltages to model non-ionizing backgrounds

## Slide 24
0V data in hand to help model this
HVeV “Run 5” @ CUTE

## Slide 25: R&D: HVeV with more targets
Try HVeV with different target materials: Germanium, SiC, Diamond, maybe others
Better low-mass WIMP sensitivity with Carbon
Exploring arts of fabrication
Coming to SNOLAB soon!

## Slide 26: HONEYCOMB
Scaling up HVeV concept
A few grams each
“Dicing” wafer with Deep Reactive Ion Etching trenches
  Leave a small “bridge” for thermal conduction
  Smooth dicing reduces sidewall charge injection
  Stress-free mounting, hope to reduce/remove low energy excess
Multiplexing readout with uMUX
  With multi-stage cryogenic amplifiers
10 cm

## Slide 27: HONEYCOMB
Stacking multiple wafers for O(10 kg) payload
Aiming for eV level threshold
Multiple chips serve as active veto for each other
Perfect match for recent RF readout upgrades for the CUTE facility

## Slide 28: SPLENDOR Narrow bandgap materials
Slides from Taylor Aralis

## Slide 29: SPLENDOR Two-stage charge readout
7.2 electron resolution achieved!
Best in class! (arXiv:2311.02229)
Slides from Taylor Aralis

## Slide 30: Far Future: Underground Detector Fabrication?
With all detectors/technology under control, circle back to backgrounds
Background budget dominated by Tritium (cosmogenic activation)
Solution: Keep the whole detector fabrication cycle underground!
Also benefit from electroformed copper underground

## Slide 31: Conclusions
SuperCDMS is well suited for low mass DM searches
Low threshold enables low mass NR searches
  iZIP provides background rejection
  HV pushes down threshold further
SNOLAB commissioning well underway
  Lab provides critical resources for all aspects
HVeV detectors achieve sub-1 eV resolution
  More varieties of HVeV coming soon!
Two more future experiments on the horizon
  HONEYCOMB -- extreme phonon sensor
  SPLENDOR -- charge readout with nano-gap materials

## Slide 32: Bonus Slides

## Slide 33: QET Design and Transport

## Slide 34: SuperCDMS Detectors & Dark Matter Mass Scales
Dark Matter Mass Ranges
  "Traditional" Nuclear Recoil: Full discrimination, ≳ 5 GeV
  Low Threshold NR: Limited discrimination, ≳ 1 GeV
  HV Detector: HV, no discrimination, ∼0.3 – 10 GeV
  Migdal & Bremsstrahlung: no discrimination, ∼0.01 – 10 GeV
  Electron recoil: HV, no discrimination, ∼0.5 MeV – 10 GeV
  Absorption (Dark Photons, ALPs): HV, no discrimination, ∼1 eV – 500 keV (“peak search”)