## Slide 1: Light Sources Update I. Martin
JAI Advisory Board Meeting
24th April 2025

## Slide 2
Talk Outline
Updates on Diamond-II:
Project status / procurement update
Injection magnet prototyping
Beam loss management
Timeline
Updates from JAI members:
Feasibility Studies of Cherenkov Diffraction Radiation BPMs (A. Clapp, RHUL/DLS)
Application of machine learning for improving operational performance of storage ring light sources (S. Preston, UO/DLS/ALC)
Fast Beam Loss Monitor System for Diamond-II and Machine Learning Applications (C. Lehmann, UO/DLS)
Conclusions
Ian Martin, Light Sources, JAI AB, 24/04/2025

## Slide 3
Diamond-II: Project Status
Procurement for Diamond-II machine well underway:
38 major orders placed, totalling £58.3m. Overall 53% of the machine budget has been committed.
All major Magnet contracts placed (other than pulsed magnets).
All major Vacuum vessel contracts placed.
Contracts placed for SR Girders and magnet supports.
Booster girder contracts placed.
All major RF contracts placed (NC cavities, SC 3rd harmonic cavity, Solid-State Amplifiers, platforms...).
Items brought back in scope:
Approval for purchase, and contracts placed, for additional HOM-damped cavity and Solid-State Amplifier.
Successful Final Design Reviews held with Suppliers for most of the vacuum vessels, dipoles, quadrupoles, octupoles, SC 3rd harmonic cavity, HOM-damped cavities, Booster girder assemblies.
Still a lot of procurement ahead: pulsed magnets and power supplies, front-ends, vacuum equipment for straights, APPLE-type Insertion Devices, etc.
Ian Martin, Light Sources, JAI AB, 24/04/2025
Courtesy R Walker

## Slide 4
Diamond-II: Extension Building (DEB)
Girder assembly
Bakeout
Vessel assembly
Magnet Lab.
Beamline assembly
Ian Martin, Light Sources, JAI AB, 24/04/2025
Diamond-II Extension Building nearing completion
Will be used for:
Magnet measurement
Vacuum bakeout
Girder, beamline assembly
Girder storage ahead of dark period
Additional office and lab space
Initial handover delayed Feb’25 => July’25 (TBC)
Feb’24
Mar’25
Courtesy P Coll

## Slide 5
Diamond-II: Extension Building (DEB)
Courtesy P Coll
Ian Martin, Light Sources, JAI AB, 24/04/2025
Parking area in front of DEB
20 Tonne crane installed in DEB2
DEB1 Vacuum Assembly Lab
DEB1 Ground Floor partitioning works
Link bridge to synchrotron building

## Slide 6
Diamond-II: Injection Scheme
Straight I01
Straight K01
Turn = -3
Turn = 0
Injected bunch
Stored bunch
Kick from striplines
Septum plate
I01
K01
septum
striplines
magnets
Δμx ~ 90 deg
‘Kick-and-cancel’ top-up injection scheme
Improved overall transparency - only perturbation to users is the injected bunch oscillating at large amplitude
Reduced transverse wakefields / interaction with TMBF compared to aperture-sharing (stored bunch is back on-axis)
Upgrade path for future high-brightness lattices: can move to kick-and-aperture-sharing injection
Key components
6 × short stripline kickers
±20 kV, 3 ns pulsers, >2 kicks per 5 Hz injection cycle
Timing system with tuneable delay (2-8 turns; 1.5-15.0 µs)
Septum magnet(s) with low leakage field:
  PM main septum (7.4 degrees)
  EM final thin septum (1.1 degrees)
Ian Martin, Light Sources, JAI AB, 24/04/2025

## Slide 7
Diamond-II: Stripline Pulsers
To ensure only a single bunch is kicked, require:
Prototype pulsers developed by Kentech Ltd.
Stage 1: +2.5kV, <15 ns, 4 pulses/cycle
Stage 2: ±4 kV, <4 ns, >10 pulses/cycle
Stage 3: ±20 kV, <4 ns, >10 pulses/cycle
Specification
Amplitude adjustment: 5:1 (best effort for 10:1)
Post-pulse noise: <±5% for 15 ns, <±2% thereafter (over 2:1 tuning range)
Amplitude / timing jitter: <±5% / <±0.1 ns
# Striplines | Nominal bend angle | Nominal Stripline Voltage | Power Supply Peak Voltage*
6 | 124 µrad | 11.7 kV | 20.0 kV
*includes contingency for 12% cable losses, +20% tuning range and only 5 out of 6 operational
3 ns
1.5 µs
2 ns
<1 ns
>1 ns
<1 ns
22.7 kV
Ian Martin, Light Sources, JAI AB, 24/04/2025

## Slide 8
Diamond-II: Prototype Injection Striplines
Prototype striplines have been installed to validate D-II design choices and test individual components:
Stage 1 and 2 – 5 kV testing (Feb-April 2025; Lab and BTS)
S-parameter / pulser / cabling / feed-throughs successfully tested
Kick amplitude, timing adjustment
Stage 3 – 20 kV tests (Summer/Autumn 2025; Lab and SR)
hardware testing, impedance effects, beam dynamics, KC demonstration
Prototype striplines in BTS transfer line
Ian Martin, Light Sources, JAI AB, 24/04/2025
Initial kick
Timing adjustment
Courtesy A Morgan
Kick angle ~60 µrad @ 5 kV

## Slide 9
Thin electromagnetic septum (1 mm, in-vacuum)
0.6 T, 400 mm long, 10 μsec full sine, iron powder core
Targeting 10 µTm integrated leakage field for transparency
Prototype mock-up
120 mm long, full cross-section
Tested shielding configuration examples:
  0.5 mm copper
  0.5 mm copper + 0.1 mm iron layers
  0.5 mm copper + 0.05 mm mumetal layers
  0.5 mm copper + 0.05 mm nanocrystalline layers
Issues with power supply output (repurposed kicker PS)
  noise in the measurements
  clean full-sine pulse not possible
Believe end leakage might be dominating, even in the centre of the magnet (no end shielding in mock-up)
SmCo
Iron
Trigger
Search coil
Magnet voltage
Diamond-II: Pulsed Thin Septum Magnet
Ian Martin, Light Sources, JAI AB, 24/04/2025
Courtesy C Bailey

## Slide 10
Diamond-II storage ring contains six collimators to collect lost particles (3H + 3V)
Collect losses during injection, lifetime, beam dumps
Provides protection for permanent magnet devices (DL dipoles, IDs)
Collaboration with RHUL to construct BDSIM model of sensitive region
Engineering STEP file used to construct BDSIM model
  Materials: Cu, Al, W, Fe, Stainless Steel, Sm2Co17
OPERA field maps for all the magnets included
Field alignment with magnet yoke checked.
Iron
Diamond-II: Beam Loss Management
Ian Martin, Light Sources, JAI AB, 24/04/2025
Beam direction
Diamond-II Girder
collimator
Sm2Co17 PM blocks in DL dipoles
Insertion device
Diamond-II Quadrupole and Sextupole with OPERA Field Map
Courtesy W Shields

## Slide 11
Risk of long-term damage to collimators after beam trip identified from ANSYS FEA studies, even if decoherence/fan-out kickers are used to spread the beam across the blades
High e- energy density could cause surface melting or cracking from fatigue
Strain range is 0.57% (above the fatigue strength at 100 cycles)
Max tensile stress ~1200MPa (fracture stress ~550MPa in Tungsten)
Crack nucleation is expected above 838°C
SmCo
Diamond-II: Beam Loss Management
Ian Martin, Light Sources, JAI AB, 24/04/2025
Tungsten blade ~2000 °C (below melting point)
Peak strain range ~0.57%
Neutron fluence at PM dipoles over 30 years expected to remain below damage threshold
RF ON + FK
RF OFF
Demagnetisation vs neutron fluence
Courtesy H Ghasem, J Linde Cerezo
Neutron population per electron in module #1
B. Shepherd, CLIC note 1079

## Slide 12
To avoid risk of damage to the collimators, a dedicate beam dump in mid-straight K24 is under consideration.
Initial concept:
Single-turn kicker at upstream end of straight
Copper beam dump at downstream end (fixed aperture)
SmCo
Iron
Diamond-II: Beam Loss Management
Ian Martin, Light Sources, JAI AB, 24/04/2025
Kicker
Beam dump
Beam dump controller
Beam Interlocks
Fast (<100 µs)
Low Level RF
Slow (<1 ms)
Orbit
Magnets
Vacuum
Temps
Doors
EPICS Interface
Beam Abort
Fire abort kicker
Inhibit injection
Inhibit linac gun
Turn off RF
Post-Mortems
Low Level RF
BPMs
Multibunch feedback
Fast Loss Monitors
Beam dump controller to manage process

## Slide 13
Diamond-II Timeline
Milestone | Planned date
Approval for the Diamond-II Project and start of funding | July 2023
Completion of the Diamond Extension Building | July 2025
Girder assembly complete | September 2027
Start of the dark period | December 2027
Start of storage ring beam commissioning | December 2028
Start of regular beamline X-ray commissioning | June 2029
First phase of beamlines become operational | September 2029
End of the Diamond-II project | March 2030

## Slide 14
L. Bobb, 07/04/2024
PhD Student: Alec Clapp (started 2021; writing thesis)
“Feasibility study on the use of incoherent Cherenkov Diffraction Radiation to develop a non-invasive BPM”
Cherenkov Diffraction Radiation (ChDR) occurs when a charged particle moves in the vicinity of a dielectric medium.
Photon yield depends on the distance between particle and medium
Enables beam position measurement using purely light signals (quartz target + glass fibres; no metal)
Dual pick-up ChDR BPM using two targets installed and first beam tests completed on 3-4th April 2024
 Demonstration of a 1D ChDR BPM using pick-ups at visible wavelengths presented at IBIC 2024
Electron beam passes between targets
ChDR is emitted by target and collected by collimators
Light is propagated out of vacuum by fibre optic feedthroughs and PMT
A. Clapp et al, Proc. of IBIC’2023, MOP032
A. Clapp et al., Proc. of IBIC’2024, TUP33
ChDR Position
Supervisors: P. Karataev and L. Bobb

## Slide 15
DPhil Student: Shaun Preston (started 2023)
Main topic of study has been developing a Gaussian Process Optimiser (GPO), specifically targeting online tasks:
  Compensation for ‘Heteroscedastic’ measurement errors
  Compensation for magnet hysteresis effects
  Coping with strictly positive objective functions
Applied to varying numbers transfer line magnet strengths, aiming to improve injection efficiency
Possible test at ISIS to reduce beam halo formation at target station
Supervisors: P. Burrows and I. Martin
“Application of Machine Learning for Improving Operational Performance of Storage Ring Light Sources”
Ian Martin, Light Sources, JAI AB, 24/04/2025
Varying 4 steerer currents
Increase in efficiency
Single GPO
Double GPO
Gun charge fluctuations
Sensor noise
Non-physical negative value

## Slide 16
L. Bobb, 07/04/2024
DPhil Student: Corey Lehmann (started 2023)
“Fast Beam Loss Monitor System for Diamond-II and Machine Learning Applications”
Current Status:
4 fast BLMs (13 BLDs) have been calibrated in the lab and deployed around the Diamond storage ring (in cells 1, 4, 13 and 23)
Data characterising typical beam losses in Diamond under user beam conditions has been acquired, including with regular ID gap changes
Linear regression and neural network models have been developed to match loss patterns against known ID states
Starting shifts to purposefully introduce “faults” to the machine to assess sensitivity of ML anomaly detection using the measured beam losses
Calibration set-up in the lab
Beam Loss Detector (i-Tech)
Fast BLDs deployed on storage ring
Supervisors: P. Burrows and L. Bobb
Anomaly from movement of I21

## Slide 17
Conclusions
JAI is active in many areas of light source design and operation:
Enhanced performance / special operating modes / facility design
Photon / electron beam diagnostics
Exploitation of machine learning and related techniques
Directly supports and well-integrated with Diamond-II Project. Collaborations / synergies with ISIS, ILC and Ada Lovelace Centre
Providing training and expertise in light sources for next generation of accelerator physicists:
Four PhD/DPhil Studentships (RHUL and Oxford)
Joint Diamond / JAI PDRA working on Diamond-II – to be readvertised pending confirmation of JAI grant renewal and availability of Diamond funding
Ian Martin, Light Sources, JAI AB, 24/04/2025