## Slide 1
IEEE NPSS Student Branch Chapter
Universidad Simón Bolívar
BEIS 2026
Protontherapy – Technology for the benefit of the patient
Martin Grossmann
Center for Protontherapy, Paul Scherrer Institute, Switzerland
Barranquilla, Colombia · June 2026
BEIS 2026 – Barranquilla EduCom International School
Notes: 1

## Slide 2: Agenda
Why radiotherapy with protons?
Irradiation techniques
PSI’s clinical program
FLASH with protons
Why technology is important

## Slide 4: Paul Scherrer Institute
590 MeV proton cyclotron
250 MeV proton cyclotron
Proton therapy
Synchrotron light source
SwissFEL 

## Slide 6: About myself…
Study physics in Münster & Lausanne
Master thesis CERN
PhD thesis PSI
Protontherapy since 1995
Control and Safety Systems

## Slide 7
Why radiotherapy with protons?

## Slide 8: Why Radiotherapy with Protons?
Conventional therapy (LINAC)
Proton therapy
Mass: ~200 tons
Diameter: ~8 m
Varian Gantry

## Slide 9: Why Protons?
Dose burden - photons
Dose burden - protons
0
10
20
30
40
0.0
0.2
0.4
0.6
0.8
1.0
depth [cm]
effect (dose)
Bragg-Spitze
Tumor
Photons (X-ray)
Protons - Sum
Protons

## Slide 10: Main parts of a particle treatment facility
Accelerator – charged particles source
Beam transfer lines to treatment areas
Fixed beam line
Gantry – rotating beam line
©IBA

## Slide 11: Superconducting Cyclotron COMET (Accel/Varian)
90 tons, 300 kW
Closed He system 4 cryostats @ 4K
Protons source
Superconducting coils 2.4 – 3.8 T
4 RF cavities 72 MHz @ 80 kV

## Slide 12: Superconducting Cyclotron COMET (Accel/Varian)

## Slide 14
Irradiation Techniques

## Slide 15: Irradiation technique - classical
Scattering foil
collimator
Tumor
protons

## Slide 16: Irradiation technique - classical
Treating Eye Melanoma
Collaboration with eye clinic in Lausanne (Hôpital Ophtalmique Jules Gonin, Prof. L. Zografos)

## Slide 17: Irradiation technique - classical

## Slide 18: PSI’s OPTIS program

## Slide 19: OPTIS

## Slide 20: OPTIS – a success story
Since 1984: treated more than 10’000 patients
98% cure (local tumor control)
Conservation of vision 100% for small tumors 90% for big tumors
Protons are the standard!
5 J., retinoblastoma, left eye, 18 months after treatment

## Slide 21: Irradiation technique – «pencil beam scanning» (PBS)
Tumor
magnet
Range shifter plates
protons

## Slide 22: Gantry 1: A compact system for PBS
Conformal scanning
a Rotation
b Rotation
First implementation of PBS
Start patient operation 1996
During 12 years the only PBS gantry worldwide
Due to eccentric design still the most compact system, r = 2m
Single pencil beam
Lateral scanning
Depth scanning
Design by Eros Pedroni
Patient table ■
Sweeper magnet ■
Range shifter ■

## Slide 23: Scanning-Technology is today’s standard
Chart: Start of treatment
| 1984 | 1989 | 1990 | 1991 | 1993 | 1994 | 1995 | 1996 | 1998 | 1999 | 2001 | 2002 | 2003 | 2004 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2015 | 2016 | 2017 | 2018 | 2018
n | 0 | 0 | 3 | 3 | 3 | 3 | 3 | 3 | 5 | 5 | 10 | 10 | 13 | 15 | 20 | 22 | 24 | 26 | 30 | 35 | 35 | 40 | 40 | 41 | 41 | 42 | 42 | 42 | 42
y | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 3 | 7 | 12 | 12 | 19 | 26 | 38 | 51 | 51 | 54 | 54 | 56 | 58
1st scanning patient
Source: S. Psoroulas, D. Meer PSI
scanning

## Slide 24: Gantry 2: next generation spot scanning
Scanner Magnete
Easy access to patient at all times
  Rotation limited to 210°
  Patient table rotatable 180° ( still full flexibility)
  No pit
Fast scanning in 2 dimensions
  Re-scanning possible
  Parallel Scanning
  Field size 12 x 20 cm
  Fast energy change  3rd dimension
  Energy step < 100 ms
  Re-scanning possible in 3 dimensions

## Slide 25
2006 - Delivery of mechanical structure
2008 - Beam line with innovative 90O dipole
2013 - 1st patient treated
2011 – Interior fittings and imaging
2008 - Beam line with innovative 90O dipole
Gantry 2: next generation spot scanning

## Slide 26: Video: Virtual Tour of PSI Protontherapy
https://youtu.be/sJOUdAd6QYk

## Slide 27
PSI’s clinical program

## Slide 28: Treating small children
Since 2004 treatments of small children  anesthesia team from children’s hospital in Zurich
Ca. 1000 patients

## Slide 31: Base of the skull Chordoma

## Slide 32: Medulloblastoma

## Slide 33: Patient treatments
Per year 400-500 patients
80% Switzerland
  We do accept patients from abroad!
Eye treatments 8’000 EUR, Gantry treatments 50’000 EUR
Types of cancer treated at PSI:
  Meningioma
  Low-grade glioma
  Head & Neck tumors
  Sarcoma
  Chondrosarcoma and chordoma
  ALL pediatric tumors
Covered by basic health insurance
  Switzerland and EU
Prostate is a good indication for protons
  But we don’t treat for economic reasons

## Slide 34
FLASH with protons

## Slide 35: FLASH radiotherapy
FLASH: application of therapeutic dose in very short time
 extremely high dose rates (1000 higher than standard)
“FLASH-effect”: for a given dose, sparing of healthy tissue is better if dose is applied in very short time
V. Favaudon et al., “Ultrahigh dose-rate FLASH irradiation increases the differential response between normal and tumour tissue in mice”, Science Translational Medicine 6, 2014
Control 17Gy CONV (0.03 Gy/s) 17Gy FLASH (60 Gy/s)
electrons

## Slide 36: FLASH protontherapy
Most (important) protontherapy vendors have demonstrated they can reach FLASH dose rates
  IBA: Groningen, Dresden
  Varian: Cincinatti
Biological experiment performed in Dresden
  Published October 2019
  No FLASH effect observed 
   More experiments required!
E. Beyreuther et al., “Feasibility of proton FLASH effect tested by zebrafish embryo irradiation”, Radiotherapy and Oncology 139, 2019

## Slide 37: Beamline Transmission

## Slide 38: FLASH @ Gantry1
We CAN operate at high energies with full transmission
Gantry 1 is designed to transport high energies (250 MeV)
Gantry 1 can provide energy modulation
 bring full current from cyclotron (800 nA) to isocentre
 Dose rate >1000 higher as in standard operations
Gantry 1 “resurrection”: restart after 10 months shutdown
  Everything still working 
First experiments with high-transmission beam tunes Nov 2019
  We are very close to 100% transmission
Input current from cyclotron 0.2 nA
X&Y profile monitor on Gantry 1, integrated current

## Slide 39: Flash @ Gantry 1
Demo experiment January 2020  reach dose rates up to 9’000 Gy/s
Nesteruk et al., Medical Physics 2021 https://doi.org/10.1002/mp.14933
Togno et al., Physica Medica 2022 https://doi.org/10.1016/j.ejmp.2022.10.019

## Slide 43: Results
Dose rate effect for electrons, but not so much for protons
Kacem et al., Radiotherapy and Oncology, in press https://doi.org/10.1016/j.radonc.2022.07.011
Notes: Gerade = gut, gekrümmt = schlecht.
Protonen-Bild ist ziemlich enttäuschend, man sieht keinen Unterschied CONV und UHDR

## Slide 44: Zebrafish embryos: Morphological analysis
Protons have minimal impact on growth and survival
Kacem et al., Radiotherapy and Oncology, in press https://doi.org/10.1016/j.radonc.2022.07.011
1
2
Notes: 1: we want to see how much damage wihout killing the embryos
2: length of fish after 5 days. Strong effect with photons, little with e CONV, no difference for protons CONV or UHDR -> disappointed (similar to Dresden result, although embryos older)

## Slide 45: Proton FLASH irradiations of mice
Experiments at PSI ongoing since 2021

## Slide 46: Proton FLASH irradiations of mice

## Slide 48: Clinical Trial: Cats

## Slide 52: 03.06.2024 12.06.2024

## Slide 53
Why technology is important

## Slide 54: A new idea: pencil beam scanning
Ugo Amaldi CERN
Eros Pedroni PSI

## Slide 55: From the idea to the implementation
Pencil beam scanning requires:
  Fast magnets
  Fast position-sensitive detectors
  Fast electronics
  Fast control systems
  Medical Imaging (CT, MRI)
  Fast computers (preparation of therapy plans)
All these technologies became available in the 1970s/1980s
Proton therapy is applied particle physics!

## Slide 56: Demonstration experiment at PSI 1989

## Slide 57: It worked!

## Slide 58: 1994

## Slide 59: «Machine Ready» Signal
Pencil beam scanning proceeds spot by spot
Between spots individual «devices» are modified:
  configuration of dose monitor units
  Setting of scanning magnets
  Energy setting
  Patient table motion
«Ready» Signal ok when all devices reached nominal value
New signals can easily be added
  Gating for organ motion: automatically pause therapy when patient is breathing

## Slide 60: Optimizing a pencil beam scanning system using tools from high energy physics
HEP: Detector  Single event  Analysis of many events
Pencil beam scanning: Gantry  Single spot  Analysis of many spots
 Write logfiles with per-spot-data

## Slide 61: CERN: HBOOK  PAW  ROOT
https://ep-news.web.cern.ch/content/interview-rene-brun

## Slide 62: Logging information per spot
/****************************************************
contents of output buffer:
index contents
0 spotnumber
1 Preset Monitor 2
2 delay_to_add for Preset Monitor 2
3 Monitor1 single gated
4 Monitor2 single ungated
5 dose measured by U strip chambers
6 dose measured by T strip chambers
7 U center nominal
8 U center actual
9 T center nominal (should always be 0)
10 T center actual
11 U FWHM nominal
12 U FWHM actual
13 T FWHM nominal
14 T FWHM actual
15 sweeper hall probe nominal
16 sweeper hall probe actual
/****************************************************
contents of output buffer:
index contents
17 gantry position X
18 gantry position Y
19 gantry position Z
20 actual range shifter plate settings plate 01...24
21 actual range shifter plate settings plate 25...40
22 10 kHz clock ungated single
23 10 kHz clock gated single
24 ADG3 hallprobe nominal value [0.1 mV]
25 ADG3 hallprobe actual value [0.1 mV]
26 10 kHz clock summed gated
27 10 kHz clock summed ungated
. . .
128 parameters per spot

## Slide 63: Pencil beam scanning needs to control dose AND position
Position sensitive IC (Kapton foil with 4mm aluminium strips)
Measure beam position and shape

## Slide 64: Use HEP tools to analyze proton therapy data
During commissioning of Gantry 1: interlocks due to spot position error
(difference nominal/actual position out of tolerance)
Spot dose [MU * 104]
Position error [mm]
 Introduce dose dependent tolerance!

## Slide 65: A useful tool for Quality Assurance
Logfiles proved to be a valuable tool for Patient Specific Quality Assurance
Back calculation of dose and dose distribution from monitor units, table position, beam settings etc. (PhD thesis; now a routine tool)
Current project: retrospective analysis of PSI Gantry treatments
  «Modeling of proton RBE variations in patients: Retrospective analysis of 20 years of treatment of chordoma and chondrosarcoma cancer patients”
RBE is hypothesized to be affected by numerous factors, among which dose averaged LET. Other, more "exotic" quantities that have sparked interest in the last years are Dose rates … Thanks to the logfiles we can reconstruct all these quantities and get as close as possible to the actual delivered physics quantities.
We can approximate the dose rate because the timings of the spots were recorded (timestamps and durations)
Bastien Golomer, PSI PhD student