## Slide 1
Determination of partial prompt gamma-ray cross-sections induced by fast neutron inelastic scattering using the FaNGaS instrument
Iaroslav Meleshenkovskii, Eric Mauerhofer, Niklas Ophoven
Forschungszentrum Jülich
The 7th edition of the International Workshop On Nuclear Data Evaluation for Reactor Applications (WONDER-2026)
Aix-en-Provence, France, 2026

## Slide 2: PRESENTATION OUTLINE
FaNGaS instrument
Analytical equations
Measurement campaign 2016-2020
    22 Elements study
    CaCO3 example
Results and summary
Outlook & future research

## Slide 3: Aim & Scope of FaNGaS Instrument
Chemical analysis of small to large samples using prompt gamma radiation induced by fast-neutron reactions: (n,n´γ), (n,p), (n,α), (n,2n)
Complementary method to PGNAA (cold/thermal neutrons), exceeding its limits
PGAINS method: Prompt Gamma Analysis based on Inelastic Neutron Scattering
Non-destructive elemental analysis for
large objects
Industry
Geology & Arctic
Environmental research
Archaeology
Fundamental
research
: Comprehensible (n,n´g) data catalogue with state of the art equipment
1
2
Two major aims:
Need of reliable nuclear data of (n,n´g) reactions
"Demidov Atlas"[3-5] (1978) must be validated!
[3]A.M. Demidov et al., NIMA (1974)
[4]A.M. Hurst et al., NIMA (2021)
[5]A.M. Demidov et al., Atomizdat, Moscow (1978)

## Slide 4: PGNAA vs PGAINS: Thermal vs Fast Neutrons
Neutron
10-16-10-12 s
Target
Nucleus
n
*
Compound
Nucleus
Prompt γ-ray
Delayed γ-ray
10-6-102 s
PGNAA
(DG)NAA
β particle
[1]Shahabinejad et al., PROG NUCL ENERGY (2020, modified)
Incoming neutron:
E0
Scattered neutron: E
Inelastic scattering angle:
ϑinelastic
Inelastic prompt
γ-rays
Nucleus
*
(Compound Nucleus)
[2]Chen, PhD thesis (2015, modified)
PGNAA
Prompt Gamma Neutron Activation Analysis
PGAINS
Prompt Gamma Analysis based on Inelastic Neutron Scattering
Radiative capture dominates at low energies, whereas inelastic scattering in the high energy region around a few MeV and is a threshold reaction!
Advantages:
Analysis of larger and denser samples
Higher sensitivity for some elements like to C, O, Ce, Pb
Less sample activation

## Slide 5: Typical Excitation Functions
ENDF/B-VIII.0 reaction data processed with NJOY for 139La
(n,γ)
(n,n´γ)
(n,p)
(n,α)

## Slide 6: FaNGaS Instrument
FRM-II (Forschungs-Neutronenquelle Heinz-Maier-Leibnitz) reactor:
Swimming-pool type
Extraction channel: SR10 (Strahlrohr 10)
Mauerhofer et al., 2021
Convertor plate containing 498 g of enriched uranium (93% 235U)
Bench filters bunker (FaNGaS collimator)
Multi-leaf-collimator of MEDAPP facility
FaNGaS spectrometer (measuring position)
MEDAPP facility bunker
NECTAR facility bunker (radiography)
FaNGaS location
Neutron beam axis
FaNGaS supported by the German Federal Ministry of
Education and Research (BMBF) under the Project number 02S9052A

## Slide 7: FaNGaS Instrument Specifications
Multi-leaf neutron beam collimator (beam size: 6x6 cm2)
BPE front shielding (d= 30 cm)
Detector collimator (= 6 cm)
Teflon (CnF2n) sample holder
Steel support frame
3
4
5
2
1
Source: J. Feil, MLZ
n-type HPGe detector
50% relative efficiency
Energy resolution: 2.1 keV @ 1.33 MeV
Sample-to-detector distance: 67 cm
Gamma/Neutron attenuator: 1 - 10 cm BPE
Possible to analyze samples of up to 400 cm3 volumes

## Slide 8: FaNGaS Instrument
Neutron spectrum @ sample position
Obtained by foil activation method and spectrum unfolding with software STASYL PNNL
Reevaluation of thermal and epithermal component due to multi-leaf-collimator of MEDAPP
Fast
(~97.5%)
Epithermal
(~ 2.5%)
Thermal
(~ 0.003%)
Thermal neutron flux (10-10 ≤ En ≤ 1.4 10-7 MeV):
φth= (3.2± 1.3) 103 cm-2 s-1
Epithermal neutron flux (1.4 10-7 ≤ En ≤ 0.06 MeV):
φepi= (2.94 ± 0.77) 106 cm-2 s-1
Fast neutron flux(0.06 ≤ En ≤ 20 MeV):
φfast= (1.13 ± 0.04) 108 cm-2 s-1
Z. Ilic et al., JRNC (2020)
N. Ophoven et al. JRNC (2024)
Mean neutron E ~ 2.2 MeV

## Slide 9: Analytical Equations
Quantification of partial cross-sections
Parameters:
: Fast-neutron spectrum-averaged partial cross section
: Net count in the gamma-ray peak (HYPERMET-Pc)
: Molar mass (g mol-1)
: Element mass (g)
: Avogadro number (6.022 1023 mol-1)
: Isotopic abundance
: Full-energy-peak (FEP) efficiency
: Gamma-ray self-absorption factor
: Neutron self-shielding factor
: Integral fast-neutron flux at sample position
: Counting live time (s)
: Integral cross section
: Absolute γ-ray intensity
: Angular-distribution correction factor
: Background below gamma line (HYPERMET-Pc)
: Net area of interfering peak
Anisotropic γ-ray emission:
Detection limit (DL)
(Without interference)
(With interference)
c= 0.5, i.e. 50% uncertainty using beam background spectrum

## Slide 10: Measurement Campaign 2016-2020
Experimental protocol
Goal: Energies Eg, relative intensities IR and partial cross section ⟨𝝈_𝑬𝜸 (𝟗𝟎°)⟩ of gamma lines for 23 elements: C, O, Al, Cl, Ca, Cl, Ti, Fe, Ni, Cu, Zr, In, La, Ce, Pr, Nd, Sm, Tb, Dy, Na, Si, K and S.
Element (Sample) | Form | Mass (g) | ti (h) | tc (h)
C (CaCO3) | Powder | 0.288 | 8.6 | 6.5
O (CaCO3) | Powder | 1.152 | 8.6 | 6.5
Al | Foil | 0.343 | 9.7 | 8.0
Cl (CeCl3) | Powder | 1.146 | 3.4 | 2.7
Ca (CaCO3) | Powder | 0.962 | 8.6 | 6.5
Ti | Foil | 0.772 | 8.2 | 6.5
Fe | Foil | 1.282 | 10.0 | 7.6
Ni | Foil | 2.809 | 10.0 | 7.0
Cu | Foil | 0.583 | 11.8 | 9.5
Na (Na2Co3) | Powder | 2.875 | 6.3 | 4.4
Si (SiO2) | Powder | 1.665 | 10.1 | 8.1
Element (Sample) | Form | Mass (g) | ti (h) | tc (h)
Zr | Foil | 1.109 | 14.5 | 11.4
In | Foil | 1.334 | 9.9 | 7.5
La (LaCl3·7H2O) | Powder | 0.566 | 13.1 | 10.9
Ce (CeCl3) | Powder | 1.509 | 3.4 | 2.7
Pr (PrCl3·7H2O) | Powder | 0.561 | 7.6 | 6.3
Nd (NdCl3) | Powder | 1.074 | 3.1 | 2.5
Sm (SmCl3·7H2O) | Powder | 0.739 | 3.6 | 2.8
Tb (TbCl3·6H2O) | Powder | 0.872 | 9.7 | 7.7
Dy (DyCl3·6H2O) | Powder | 0.804 | 3.1 | 2.5
K (K2Co3) | Powder | 1.863 | 6.9 | 5.6
S | Foil | 0.317 | 12.7 | 11.2

## Slide 11: Analysis of Calcium Carbonate
Measurement configuration
Mass m: 2.40 g (Ca: 0.96 g, C: 0.29 g, O: 1.15 g)
Main isotopes: 40Ca (96.9%), 12C (98.9%), 16O (99.8%)
Thickness d: powder, compressed to ~ 1 mm
Tilted by 45° relative to neutron beam
Measuring time tm: 8.60 h
Counting (live) time tc: 6.46 h
25% deadtime
On the right: ENDF/B-VIII.0 reaction data
processed with NJOY for all observed reactions
N. Ophoven et al., JRNC (2022)

## Slide 12: Analysis of Calcium Carbonate
Measurement of active background
Acquired during 15.7 h measuring time and 14.3 h counting (live) time
Element | Source material
Hydrogen | BPE shielding
Nitrogen | Air
Iron | Iron support frame
Germanium | HPGe crystal
Indium | Detector electronics
Lead | Inner lead shielding

## Slide 13: Measured Gamma-ray Spectrum
Measurement of calcium carbonate (CaCO3)
- Background (14.3 h)
- CaCO3 (6.5 h)
Black and bold: (n,n´g) reactions
Black: (n,pg) and (n,αg) reactions on 40Ca
4.44 MeV 12C Doppler-broadened
Lifetime of excited state ~ 40 fs

## Slide 14: Analysis of Measured Gamma-ray Signatures
Identified gamma-lines in calcium carbonate (CaCO3)
Element | Isotope | Reaction | nγ |  | 
 |  |  | This work | Demidov Atlas | New
C | 12C | 12C(n,n´γ)12C | 1 | 1/1 | 0
O | 16O | 16O(n,n´γ)16O | 1 | 1/1 | 0
O | 18O | 18O(n,n´γ)18O | 1 | 1/1 | 0
Ca | 40Ca | 40Ca(n,n´γ)40Ca | 7 | 5/9 | 2
Ca | 40Ca | 40Ca(n,p)40K | 20 | 16/16 | 4
Ca | 40Ca | 40Ca(n,α)37Ar | 3 | 3/3 | 0
Ca | 42Ca | 42Ca(n,n´γ)42Ca | 1 | 1/1 | 0
Ca | 44Ca | 44Ca(n,n´γ)44Ca | 4 | 4/4 | 0
Σ= |  |  | 38 | 32/36 | 6
nγ: Number of gamma rays
6 new gamma-lines were observed

## Slide 15: Analysis of Measured Gamma-ray Signatures
Consistency check for Identified gamma-lines in calcium carbonate (CaCO3)
Between our data set and that of Demidov et al.:
Indices:
R: FaNGaS intensity
RD: Demidov Atlas intensity
Indices:
1: FaNGaS
2: Demidov Atlas
1.2σ

## Slide 16: Results of Measurement Campaign 2016-2020
Identified gamma-lines, partial cross-sections and detection limits (DL)
DL: smallest amount of pure element detectable for a measurement time of 12 h
 | Number of g lines |  |  | Detection limits |  | 
El. | This work | Demidov Atlas | New | AZ, Eγ (keV) | σEγ (mb) | DL (mg)
C | 1 | 1/1 | 0 | 12C, 4441.1 | 14.4 | 13
O | 2 | 2/2 | 0 | 16O, 6129.3 | 2.2 | 62
Al | 22 | 21/25 | 1 | 27Al, 1013.9 | 136 | 1.0
Cl | 29 | 19/27 | 10 | 35Cl, 1763.1 | 70 | 1.8
Ca | 35 | 29/35 | 6 | 40Ca, 29.8 | 157 | 4.8
Ti | 72 | 53/63 | 19 | 48Ti, 982.9 | 627 | 0.4
Fe | 81 | 48/69 | 33 | 56Fe, 846.9 | 586 | 0.5
Ni | 163 | 80/85 | 83 | 58Ni, 1453.6 | 338 | 0.7
Cu | 120 | 83/91 | 37 | 63Cu, 961.5 | 410 | 0.9
Na | 19 | 19/18 | 1 | 23Na, 439.4 | 507 | 0.1
Si | 13 | 13/12 | 1 | 28Si, 1778.8 | 189 | 0.6
 | Number of g lines |  |  | Detection limits |  | 
El. | This work | Demidov Atlas | New | AZ, Eγ (keV) | σEγ (mb) | DL (mg)
Zr | 101 | 52/54 | 49 | 92Zr, 933.8 | 1068 | 1.4
In | 94 | 79/92 | 15 | 115In, 933.1 | 222 | 1.3
La | 53 | 43/51 | 10 | 139La, 165.7 | 574 | 0.6
Ce | 58 | 31/45 | 27 | 140Ce, 1596.0 | 666 | 0.7
Pr | 69 | 56/77 | 13 | 141Pr, 145.3 | 889 | 0.4
Nd | 112 | 39/44 | 73 | 144Nd, 696.0 | 354 | 2.1
Sm | 147 | 64/73 | 83 | 150Sm, 333.4 | 967 | 0.7
Tb | 122 | 49/60 | 73 | 159Tb, 57.9 | 445 | 1.2
Dy | 148 | 75/92 | 73 | 162Dy, 184.8 | 289 | 1.6
K | 48 | 48/30 | 17 | 39K, 2814.1 | 27.2 | 4
S | 20 | 20/15 | 5 | 32S, 2230.5 | 79 | 1

## Slide 17: Summary Measurement Campaign 2016-2020
Energies Eg, relative intensities IR and partial cross section of gamma lines for 23 elements:
C, O, Na, Al, Si, S, Cl, K, Ca, Cl, Ti, Fe, Ni, Cu, Zr, In, La, Ce, Pr, Nd, Sm, Tb, Dy, Na, K, Si and S.
1529 g-rays in total from 23 elements (~ 20% of Demidov Atlas)
624 new g-rays (Higher , better energy resolution & resolving of doublets)
159 g-rays from Demidov Atlas not observed (Interferences, detection limit, tentative or misattributions)
Agreement level of data sets (this work/ Demidov Atlas): 0.7 ≤ σ ≤ 1.7
Several intense g-rays not on NuDat: Expansion of level/decay schemes (in particularly Tb)
Data for C, O, Al, Ca, Ti, Fe, Cu, In compiled in EXFOR (Experimental Nuclear Reaction Database, IAEA)
Detection limits (12 h) ~ 1 mg, except C (13 mg), O (64 mg), Ca (4.8 mg) and K (4 mg)
[1] E. Mauerhofer et al., J. Radioanal. Nucl. Chem. 2020, 325.
[2] E. Mauerhofer et al., J. Radioanal. Nucl. Chem. 2022, 331.

## Slide 18: Outlook & Future Research
Measurement of Sc, V, Co, Zn, Y, Eu, Gd, Ho, Er, Tm and Lu (for gamma-ray catalogue)
Determination of partial cross sections for the FaNGaS neutron spectrum from the Demidov´s data
Characterization of permanent magnets for industrial sorting/recycling using fast neutrons
Coupling of FaNGaS with Fast Neutron Imaging and Transmission techniques (ongoing R&D)
Development of advanced ML-based analysis software (in collaboration with RWTH and University d’Evri)

## Slide 19: Outlook & Future Research
Measurement of Sc, V, Co, Zn, Y, Eu, Gd, Ho, Er, Tm and Lu (for gamma-ray catalogue)
Determination of partial cross sections for the FaNGaS neutron spectrum from the Demidov´s data
Characterization of permanent magnets for industrial sorting/recycling using fast neutrons
Coupling of FaNGaS with Fast Neutron Imaging and Transmission techniques (ongoing R&D)
Development of advanced ML-based analysis software (in collaboration with RWTH and University d’Evri)
Irradiation at 0o
Irradiation at 45o
MC simulations of the precise FANGAS configuration

## Slide 20: Outlook & Future Research
Measurement of Sc, V, Co, Zn, Y, Eu, Gd, Ho, Er, Tm and Lu (for gamma-ray catalogue)
Determination of partial cross sections for the FaNGaS neutron spectrum from the Demidov´s data
Characterization of permanent magnets for industrial sorting/recycling using fast neutrons
Coupling of FaNGaS with Fast Neutron Imaging and Transmission techniques (ongoing R&D)
Development of advanced ML-based analysis software (in collaboration with RWTH and University d’Evri)
FRMII reactor planned restart 2027
Open call for FaNGaS Beam Time

## Slide 21: Questions? Interested in fast neutron analytics R&D? i.meleshenkovskii@fz-juelich.de e.mauerhofer@fz-juelich.de