## Slide 1: Random-matrix approach for generating cross sections and probability table in the unresolved resonance region
K. Fujio, T. Kawano, A. E. Lovell, D. Neudecker, N. A. W. Walton
WONDER 2026
LA-UR-26-24913

## Slide 2
Cross section in theoretical approaches
RRR
URR
Fast.
Resolved resonance region (RRR)
Unresolved resonance region (URR)
Fast energy region
・Individual resonances can be seen
・Expressed in R-matrix formalism by using resonance parameters
・Resonances overlap and cannot be separated from one another
・No commonly used theoretical model
・Calculated by Hauser-Feshbach theory
・Smooth cross section because resonance width is bigger than the spacing
?

## Slide 3
Importance of URR and probability table
Self-shielding: Neutrons are easily captured at resonance peaks, and the neutron flux decreases at resonance energies. → Impacts on reaction rate
We need to take into account resonances in URR as well !
・A probability table which represents the probabilistic distribution of cross sections is employed in Monte-Carlo approaches
L. L. Carter et al., LA-UR-98-0026 (1998).
[b]
[b]
[b]
[b]
・Assume Wigner and chi-square distributions for the resonance spacing and width, respectively
A theoretical approach is required to calculate the cross sections in URR without these kinds of assumptions

## Slide 4
Research objective and approach
Eigenvalue distribution
Matrix dimensions: 100 x 100
The number of simulations: 0.1 M
Distribution of spacing of each eigenvalue
Random-matrix approach
Gaussian Orthogonal Ensemble (GOE)
・Matrix elements are Gaussian distributed random numbers
Develop a theoretical model to obtain cross sections in URR and employ them to create the probability table
・Real symmetric matrix

## Slide 5
S matrix calculated using GOE
: Random matrix
J. J. M. Verbaarschot et al., Phys. Rep. 129, 367 (1985).
T. Kawano et al., Phys. Rev. C92, 044617 (2015).
E : energy in units of λ
(Does not represent incident neutron energy!)
Input parameters
・The number of levels
・The number of channels
・Neutron, photon, and fission transmission coefficients
N
Λ
Tn, Tγ, Tf
- The number of inelastic scattering channels is determined by possible number of neutron partial waves and the corresponding excited levels
Notes: To calculate cross sections, we need S matrix. The approach is established by Verbaarschot et al.

## Slide 6
How to smoothly connect 2 regions
The S matrix smoothly connects between RRR and fast energy regions
1. Obtain the energy-averaged R matrix in RRR (ENDF/B-VIII.0)
2. Determine the optical model parameters to reproduce
Between RRR and URR
Between URR and fast energy regions
✅ We can consistently use the same treatments as those used in the Hauser-Feshbach model and (coupled-channel) optical model in CoH3
Transmission coefficients
Key input parameters:

## Slide 7
Calculated cross sections
(at 150 keV)
Single-level Breit-Wigner formula (unitarity is not guaranteed)
GOE-S-matrix model (unitarity is guaranteed!)
Smoothly connected
2 regions!
Phys. Rev. C112, 064608 (2025).
Notes: EXPLAIN LAMBDA!

## Slide 8
Selected energy range
・The eigenvalue distribution corresponds to the level density.
・The convergence behavior depends on the level density.
We restrict the energy range to Eλ = ー λ/2 to λ/2.
・Compared the convergence of the cross sections using the full Eλ range and the quarter Eλ range.

## Slide 9
Calculated probability tables
The number of ladders: 10000
J. Nucl. Sci. Technol. (published)
・No significant differences are observed between the GOE calculation and the single-level Breit-Wigner result.
・Small ladder average of cross sections are seen in the SLBW results due to the negative cross sections.

## Slide 10
Conclusions
・We developed a new theoretical model to obtain cross sections in URR and employ them to create the probability table.
・The input transmission coefficients are determined that the S matrix smoothly connects between RRR and higher energy regions.
Future work
・The average cross sections converge to evaluate data by restricting the range to Eλ = ー λ/2 to λ/2.
・ The main difference in probability table between our new approach and the SLBW comes from the unitarity condition.
・Introduce the temperature effect (Doppler broadening)

## Slide 11
Acknowledgements
・Research reported in this presentation is supported by the U.S. Department of
Energy LDRD program at Los Alamos National Laboratory.
・This work was supported by the Nuclear Criticality Safety Program, funded and managed by the National Nuclear Security Administration for the Department of Energy.
・This work was carried out under the auspices of the National Nuclear Security Administration of the U.S. Department of Energy at Los Alamos National Laboratory under Contract No. 89233218CNA000001.
Notes: This research is supported by the US department of energy LDRD program at Los Alamos National Laboratory.