## Slide 1
Final results of the 239Pu capture and fission cross section measurements at n_TOF (CERN)
A. Sanchez-Caballero1, V. Alcayne1, J. Andrzejewski2, D. Cano-Ott1, J. García-Pérez1, E. Gónzalez-Romero1, J. Heyse3, T. Martínez1, E. Mendoza1, J. Perkowski2, J. Plaza del Olmo1, A. Plompen3, P. Schillebeeckx3, G. Sibbens3, and the n_TOF collaboration.
1CIEMAT, Spain
2University of Lodz, Poland
3JRC-Geel, Belgium

## Slide 2: Contents
Overview of the 239Pu measurement at n_TOF.
Summary of the data analysis.
Fission results.
Capture results.
Conclusions.

## Slide 3
1
Overview of the 239Pu measurement at n_TOF
Experimental setup

## Slide 4: 1.1 n_TOF: neutron time-of-flight at CERN
Experiment performed at n_TOF EAR1 (~185 m flight path) in Sep-Nov 2022.
Around 8 times larger flight path than in previous 239Pu measurements, which enables higher energy resolution.
n_TOF features
25 years operation, with relevant measurements for nuclear technology, nuclear astrophysics, medical science and basic research.
Neutron beam by spallation of 20 GeV protons into a lead target.
Pulses of about 1 Hz repetition rate → no overlapping pulses.
8·1012 protons per pulse, 7 ns RMS, with option for lower intensities.
Three experimental areas for different purposes (EAR1, EAR2 and NEAR).
EAR1: moderated neutrons with a layer of borated water.

## Slide 5: 1.2 Detectors
Neutron Beam Monitor (SiMon)
Four silicon detectors to monitor neutron beam intensity using 6Li(n,α)3H standard reaction.
Proton Beam Monitors
Wall Current Monitor (WCM).
Beam Current Transformer (BCT).
239Pu-specific detectors at EAR1
FFD[1] Fission Fragment Detector
Detection of charged particles.
Fast pre-amplifiers.
Filled with Ar + (10%)CF4 gas.
TAC[2] Total Absorption Calorimeter
To detect capture and fission γ-rays.
Composed of 40 BaF2 crystals operated in coincidence.
Events characterized by Esum (total deposited energy from contributing crystals) and mcr (crystal multiplicity).
[1] Perkowski et al., Nucl. Instrum. Methods Phys. Res. A 1067, 169649 (2024)
[2] Guerrero et al., Nucl. Instrum. Methods Phys. Res. A 608(3), 424 (2009)

## Slide 6: 1.3 Experimental configurations and samples
Experimental campaign divided into two different configurations:
1. FC config.
- 10 thin Pu samples (<10 mg total mass) within fission chamber.
- Use FFD + TAC simultaneously.
- Measure fission and capture (up to ~1 keV), and the α-ratio.
2. TS config.
- 1 thick sample (~100 mg).
- Use only TAC.
- Measure capture above 1 keV.
- Sample inside dummy chamber to have similar bkgds.
Both setups share similar beam line configuration:
Isotopes | Abundance (%)
239Pu | 99.90
240Pu | 0.06
241Pu | 0.02
242Pu | 0.01
Plutonium base material
Produced by JRC-Geel and SCK CEN.
Plutonium dioxide PuO2.
99.9% purity of 239Pu.
From the same base material, two different type of samples were prepared.

## Slide 7: 1.3 Experimental configurations and samples
Experimental campaign divided into two different configurations:
1. FC config.
- 10 thin Pu samples (<10 mg total mass) within fission chamber.
- Use FFD + TAC simultaneously.
- Measure fission and capture (up to ~1 keV), and the α-ratio.
2. TS config.
- 1 thick sample (~100 mg).
- Use only TAC.
- Measure capture above 1 keV.
- Sample inside dummy chamber to have similar bkgds.
Both setups share similar beam line configuration:
Isotopes | Abundance (%)
239Pu | 99.90
240Pu | 0.06
241Pu | 0.02
242Pu | 0.01
Plutonium base material
Produced by JRC-Gel and SCK CEN.
Plutonium dioxide PuO2.
99.9% purity of 239Pu.
From the same base material, two different type of samples were prepared.

## Slide 8: 1.3 Experimental configurations (mounting)
Pictures of the mounting procedure at n_TOF EAR1 during the experimental campaign in 2022.
UPSTREAM VIEW
1. The FFD is placed within the TAC
2. The TAC+FFD assembly is carefully align with the neutron beam
3. A neutron absorber is placed around the FFD.
Li-doped polyethylene
4. Neutron absorber closed.
5. TAC closed

## Slide 9
2
Summary of the Data Analysis

## Slide 10: 2.1 Fundamentals of the data analysis
Neutron fluence crossing the sample
Depends on sample diameter.
Common for the same setup.
Count rate due to background events
Measured through dedicated background measurements…
or by simulations.
Detection efficiency
Can be determined experimentally or by simulations.
Only required for 239Pu(n,γ).
Comparison of TAC Esum spectra between experimental and MC simulations.
MC
Data reduction (thresholds)
FFD: α-FF discrimination using amplitude threshold in the FFD signals.
TAC: energy and multiplicity thresholds to improve signal-to-background ratio.

## Slide 11: 2.1 Fundamentals of the data analysis
Neutron fluence crossing the sample
Depends on sample diameter.
Common for the same setup.
Count rate due to background events
Measured through dedicated background measurements…
or by simulations.
Detection efficiency
Can be determined experimentally or by simulations.
Only required for 239Pu(n,γ).
Comparison of TAC Esum spectra between experimental and MC simulations.
MC
Data reduction (thresholds)
FFD: α-FF discrimination using amplitude threshold in the FFD signals.
TAC: energy and multiplicity thresholds to improve signal-to-background ratio.
Normalization
The fission yield was normalized to the recommended evaluated 239Pu(n,f) cross section integral (9-20 eV) by I. Durán et al. (https://doi.org/10.1016/j.nds.2024.01.004).
Absolute value of , sample mass, and efficiency not needed → significantly reduce uncertainties.
Automatically determines the norma-lization for the capture yield.

## Slide 12: 2.2 Summary of backgrounds for capture
FC setup (FFD + TAC)
TS setup (TAC)
Background contributions in both setups: some components share similar approaches but others (fission) required completely different procedures.
TAC count rates as a function of neutron energy
TAC count rates as a function of neutron energy

## Slide 13: 2.2 Summary of backgrounds for capture
FC setup (FFD + TAC)
TS setup (TAC)
Background contributions in both setups: some components share similar approaches but others (fission) required completely different procedures.
TAC count rates as a function of neutron energy
TAC count rates as a function of neutron energy
Fission subtraction: Fission Tagging1,2,3
FFD+TAC event coincidences used as veto to suppress fission background.
coincidence window
Fission subtraction in the TS setup
Use the results from the FC setup.
FC-TS overlap region below 200 eV → fit of capture and fission yields on selected resonances (resonance parameters from SAMMY fit).
Resonances included in the fit
Resonances NOT included in the fit
[1] C. Guerrero et al., Eur. Phys. J. A 48, 29 (2012).
[2] J. Balibrea-Correa et al., Phys. Rev. C 102, 044615 (2020).
[3] M. Bacak et al., EPJ Web of Conferences 211, 03007 (2019).

## Slide 14: 2.3 Resonance parameters: SAMMY fit
To obtain a final set of resonance parameters (RPs) combining the three measured datasets:
Fission yield (FC setup).
Capture yield (FC setup).
Capture yield (TS setup).
10-1
1
10
102
103
104
105
106
107
0.02
eV
239Pu(n,f)
239Pu(n,γ) FC setup
239Pu(n,γ) TS setup
Combine capture data from both setups:
FC data for En < 200 eV.
TS data for En > 200 eV and some low-statistics resonances below 200 eV (overlap region).
(overlap region)
The resonance analysis obtained the resonance parameters for 1000 resonances up to 2.5 keV:
Neutron energy En, neutron width Γn, capture width Γg, and fission width Γf.

## Slide 15
3
Fission results

## Slide 16: 3.1 Fission results: uncertainties and integrals
Low-uncertainties were achieved due to the excellent properties of samples and fission chamber, which did not require additional corrections apart from neutron fluence shape.
 | I1 (0.02-0.06 eV) | I3 (9-20 eV) | I3/I1 | IHE (8-10 MeV)
n_TOF / I. Durán et al. | 1.011(1)(29) | 1.0 | 0.989(2)(20) | 1.014(8)(46)
n_TOF / ENDF/B-VIII.1 | 1.014(1)(29) | 1.010(1)(20) | 0.995(2)(20) | 1.007(8)(46)
n_TOF / ENDF/B-VIII.0 | 1.013(1)(29) | 1.007(1)(20) | 0.994(2)(20) | 1.016(8)(46)
n_TOF / JEFF-3.3 | 1.015(1)(29) | 1.010(1)(20) | 0.995(2)(20) | 1.011(8)(46)
Excellent compatibility with well-known 239Pu(n,f) cross section integrals, from thermal to fast energy regimes.
Data | SACS
Derived, this work | 1802±65 (3.6%)
Derived, IAEA standard 20171 | 1798±23 (1.3%)
Mannhart evaluation2 | 1812±25 (1.4%)
Capote et al. evaluation3 | 1826±19 (1.0%)
239Pu(n,f) spectrum-averaged cross section (SACS) in the 252Cf(sf) reference neutron field. Total SACS uncertainties are reported.
1Carlson et al., Nucl. Data Sheets 148, 143–188 (2018).
2Bersillon et al., IAEA TRS 452 (2006).
3Capote et al., EPJ Web Conf. 281, 00027 (2023)
Our results are compatible with the 239Pu(n,f) cross section reference (0.15-200 MeV) from the 2017 IAEA’s Neutron Data Standards (NDS).
1.5% unc. from eval.
n_TOF sys. uncertainties
statistical
systematic
Excellent agreement with evaluations in the regions where the cross section is very well known → confidence in our data to improve regions where it is not so well-known.

## Slide 17: 3.2 Fission results: comparison with evaluations
239Pu fission dataset with the broadest neutron energy range to date, covering almost 9 orders of magnitude, from thermal to fast region.
Ratios of our data to different 239Pu(n,f) evaluations from major libraries. With broader bins, differences are not larger than 3% (within uncertainties).
First 239Pu resonance at 0.3 eV, of relevance for nuclear reactor technology.
n_TOF about 4% above ENDF/B-VIII.0, and closer to ENDF/B-VIII.1
Ratios calculated relative to ENDF/B-VIII.0
ENDF/B-VIII.1 evaluation taken from INDEN, with an increase around 1 keV not compatible with n_TOF data.
New JEFF-4.0 evaluation improves the large discrepancies observed with JEFF-3.3 in the low energy region according to n_TOF data.
Great interest on n_TOF data shown by international evaluators (INDEN, JEFF-4.0, and IAEA’s Neutron Data Standards).
JEFF-3.3 ↔ JEFF-4.0

## Slide 18: 3.2 Fission results: comparison with evaluations
Some examples of fission yield resonances
Discrepancies in the shape of some resonances
Resonances and structures are observed even at relatively high neutron energies, surpassing the limit of the resolved resonance region of some libraries (up to 2.5 keV).
Residuals calculated relative to ENDF/B-VIII.0

## Slide 19: 3.3 Fission results: comparison with experimental data
Energy resolution
The longer flight path of n_TOF (185.6 m) allows obtaining a higher neutron energy resolution, which is visible in the shape of some resonances.
Weston 1992 data
Good compatibility with Weston 1992 data in intermediate energy range resonances, with similar energy resolution.
High energies
Our data may help extend physical fluctuations in evaluations above 20 keV (limit of Weston 1992 data).
n_TOF data provides the broadest dataset in neutron energy with high resolution and contained uncertainties, providing valuable information in low, intermediate and high energy regions up to 10 MeV.

## Slide 20
4
Capture results

## Slide 21: 4.1 Capture results: uncertainties
FC setup
TS setup
Overall uncertainty between 3-4%
Important:
Dummy uncertainties are overestimated in this plot, especially above 100 eV. Final values in the cross-section will be lower.
Valley between resonances
Target region of the TS setup
5 bins per decade
5 bins per decade
Overall uncertainty between 4-5%

## Slide 22: 4.2 Capture results: comparison with evaluations
Some examples of capture yield resonances (FC setup)
Large discrepancies with evaluations (and among themselves) in the shape of some resonances.
10 bins per decade
Great compatibility with ENDF/B-VIII.0 at the first 0.3 eV resonance.
Residuals and ratios calculated relative to ENDF/B-VIII.0
JEFF-3.3 ↔ JEFF-4.0

## Slide 23: 4.2 Capture results: comparison with evaluations
TS setup data at high energies
The capture yield from the data with the larger mass sample enables preforming SAMMY analysis up to higher neutron energies with reasonable energy resolution and statistics.
Ratio of integrated yield from TS data above 1 keV: n_TOF data remains 5-10% systematically above evaluations with best agreement to the ENDF/B-VII.1 evaluation.
10 bins per decade
ENDF/B-VIII.0 and VIII.1 may be influenced by Mosby 2018 data for this region.

## Slide 24: 4.3 Capture results: comparison with experimental data
Scarcity of high-resolution 239Pu(n,γ) cross-section measurements. Two datasets in EXFOR (Gwin 1971, Mosby 2014/2018) mainly used for all evaluations.
Energy resolution
First resonance @ 0.3 eV
Good compatibility within uncertainties with Gwin 1971 dataset in the shape and size of the first, large resonance at 0.3 eV. Both slightly below evaluation at peak.
High neutron energies
At higher neutron energies, from 1 keV to 10 keV (TS setup), the n_TOF cross section integrals generally stays slightly above Mosby 2018 data.
Our capture data exhibit the highest neutron energy resolution among the existing experimental data.

## Slide 25: 5. Summary and Conclusions
Successfully accomplished the 239Pu measurement of fission and capture cross sections (and α-ratio) for the first time at n_TOF (CERN), through a collaboration between CIEMAT, JRC-Geel, SCK CEN and University of Lodz. The excellent properties of the facility, samples, and the detection systems, along with the experienced acquired through previous n_TOF fission-tagging measurements, have resulted in new high-quality experimental data for 239Pu, providing valuable input for future evaluations.
Fission
Capture
Broad energy coverage (20 meV to 10 MeV) and low-uncertainties.
Data submitted to EXFOR data bank at the end of 2025.
Publication in Physics Letters B: 10.1016/j.physletb.2025.140070
Good candidate to become a reference dataset for future evaluations.
Successful combination of thin and thick sample measurements to cover a wider energy range from 0.1 eV to 10 keV.
High-resolution dataset to contribute to the scarcity of measurements for evaluations.
Draft paper will be submitted this year.
All details in my PhD Thesis: 10.17181/179rm-jc146

## Slide 26: Acknowledgments
This project has received funding from the Euratom research and training programme 2011-2018 under grant agreement No 847595 (ARIEL)
This activity is part of the scientific program approved by the European Commission H2020 Supplying Accurate Nuclear Data for energy and non-energy Applications – SANDA project (WP2, Task 2).
2021-1-RD EUFRAT-GELINA project funding for the stay at JRC-Geel.
This work was supported by the European Union NextGenerationEU/PRTR project C17.I02.P02 – SGI_GICS, subproject C17.I02.P02.S01 CIEMAT_CERN.
Spanish national projects PGC2018-096717-B-C21, PID2021-123100NB-I00 and PDC2021-120828-I00.
This work has been supported by the ENRESA-CIEMAT agreement 2023-2026 “Tecnologías Disponibles para la Transmutación de Radionucleidos de Vida Larga”.
 | EUROPEAN COMMISSION JOINT RESEARCH CENTRE Directorate G - Nuclear Safety and Security Standards for Nuclear Safety, Security and Safeguards

## Slide 27
THANK YOU!

## Slide 28: Backup slides

## Slide 29: 2.3 239Pu samples
Samples were produced in the Target Preparation laboratory at JRC-Geel in collaboration with SCK CEN institute.
Thin samples
10 samples deposited by molecular plating on 10 µm thickness aluminum foils.
20 mm diameter.
2 MBq and 950 µg each, expect for a ~10 times thinner sample with 0.3 MBq and 120 µg.
Placed inside the FFD chamber, parallel and opposite-oriented (facing up- and down-stream).
High homogeneity.
Plutonium base material
Plutonium dioxide PuO2.
Purified from 241Am.
99.9% purity of 239Pu.
From the same base material, two different type of samples were prepared.
Isotopes | Abundance (%)
239Pu | 99.90
240Pu | 0.06
241Pu | 0.02
242Pu | 0.01

## Slide 30: 3.1 Neutron fluence
The Neutron fluence (shape) for the full beam is known from the SiMon monitoring data and the n_TOF evaluated flux. However, corrections are required to take into account the smaller sizes of the samples (Beam Interception Factor, BIF).
Curves normalized at around 1 eV
SiMon for 0.02 eV < En < 1 keV
The transmission through different dead-materials (aluminum, mylar) and the LiF foil of SiMon was taken into account (effect of about 1%), using FLUKA simulations.
EAR1 evaluated neutron fluence for En > 1 keV
Shape taken from the neutron beam commissioning at EAR1, using several detectors based on standard reactions:
6Li(n,t)4He
10B(n,α)7Li
235U(n,f)
(Normalized) Beam Interception Factor
BIF correction from 197Au(n,γ)
The correction for the sample diameters below 1 eV was performed using ancillary measurements with gold samples of the same diameter.
197Au(n,γ) cross section is smooth and well-known in this region.
BIF from simulations
For En>1 eV, the BIF was de-termined from simulations with FLUKA.

## Slide 31: 3.2 Extraction of fission yield
Once the energy dependence of the neutron fluence for 2 cm samples, , is known, and the detectors are characterized (thresholds, calibrations…) the extraction of the fission reaction yield Yf(En) is straightforward.
0
Fission Fragment count rate
Zero background
No background in the fission yield was observed after the α-FF separation.
(previous slide)
Nf
Normalization constant Nf
The fission yield was normalized to the recommended evaluated 239Pu(n,f) cross section integral (9-20 eV) by I. Durán et al. (https://doi.org/10.1016/j.nds.2024.01.004).
εFF replaced by normalization factor Nf.
Absolute value of , sample mass, and efficiency not needed → significantly reduce uncertainties.
No dependence on En.
Automatically determines the norma-lization for the capture yield.
Obtained yield compared with evaluation (ENDF/B-VIII.0)
n_TOF data below evaluations in the valleys between resonances
↓
Indication of no residual background

## Slide 32: 3.3 TAC background subtraction: fission (FC)
Fission subtraction in the FC setup
Fission tagging
Coincidences between FFD and TAC
Prompt Fission Coincidence window:
±20 ns
It covers practically the full prompt-fission peak while minimizing the probability of tagging non-fission events (<<1%). Consistent with previous fission tagging mea-surements.
PFB
Post-Fission Background
Fission-related counts with ΔT>20 ns up to 3 us.
Attributed primarily to fission neutrons.

## Slide 33: 4.3 TAC background subtraction: fission (FC)
Fission subtraction in the FC setup
Fission tagging
Coincidences between FFD and TAC
Fission tagging coincidence window
±20 ns
It covers practically the full prompt-fission peak while minimizing the probability of tagging non-fission ev-ents (<<1%). Consistent with previous fission tagging measurements.
Esum prompt fission spectrum under different mcr cuts
PFB
Post-Fission Background
Fission-related counts with ΔT>20 ns up to 3 us.
Fission tagging enables the extraction of the PFB Esum and count rate distribution.
Attributed primarily to fission neutrons.

## Slide 34: 3.3 TAC background subtraction: fission (TS)
Fission subtraction in the TS setup
Followed approach:
Subtract all known non-fission backgrounds (excluding also PFB) and divide by the neutron fluence to obtain a quasi-yield Y*.
This quasi-yield can be reasonably interpreted by a linear combination of the capture and fission yields:
General idea: to use the results of fission and capture that were accurately measured in the FC setup below 200 eV.
Measured in the TS setup
Coefficients related with capture and fission detection efficiencies
We know
We want to know
Yields derived with SAMMY using RPs from the FC setup
Restricted below 200 eV at selected resonances
and can be determined by matching the experimental and expected capture yields in these resonances.
Extrapolate to the rest of neutron energies using the found and (constant) values.
is taken from the FC setup:
Derived from the RPs for the resonance region.
Directly from the measured yield with the FFD above 2.5 keV.

## Slide 35: 3.3 TAC background subtraction: fission (TS)
Fission subtraction in the TS setup
Results for the optimal coefficients
Resonances included in the fit
Resonances NOT included in the fit
Result on the fitted yield resonances
Result on the fitted yield resonances
Excellent compatibility between TS and FC capture yield even in resonances not used for the optimization problem with large fission → obtained fission bkgd. for higher energies.

## Slide 36: 4.3 TAC background subtraction: fission (TS)
Fission subtraction in the TS setup
Obtained fitted scaling factors (change from the expected values for the efficiencies taken from simulations and FC data):
Results for the X2 function (to be minimized)
Result on the fitted yield resonances
Resonances included in the fit
Resonances included in the fit
Result in Esum, using shapes from FC data
Fission count rate
Obtained scaling the fission shape from FC setup (SAMMY). The PFB is then determined from the obtained prompt-fission using the FC results.

## Slide 37: 3.5 Pile-up correction
Observed pile-up effects that depend on the time-of-flight (neutron energy) within the same pulse, reproducible with artificial data buffers with sample signals. Same method as in previous measurements with the TAC[1].
Validation with experimental data
Able to reproduce gain shifts and data losses.
Comparison of Esum prompt-fission spectra between experimental data and pile-up model at 1-3 keV.
TS setup
Significantly larger corrections than in the FC setup, especially for En>2 keV (up to 15%).
Low intensity pulses: corrections below 2.5% up to 10 keV.
TS capture yield was measured using only low-intensity pulses to minimize pile-up corrections.
Efficiency curves with high and low intensity pulses.
[1] E. Mendoza et al. Nucl. Instrum. Methods Phys. Res. A 768, 55 (2014).

## Slide 38: 4.4 α-ratio: comparison with evaluations (and exp. data)
Better agreement with ENDF/B-VIII.1 at 0.3 eV, and 3-4% below the other libraries.
This deviation is driven by the difference in the fission cross section.
Comparison with experimental data
Residuals and ratios calculated relative to ENDF/B-VIII.0
Regions with large errors due to counting statistics (valleys in fission and/or capture). No valuable informa-tion there.
First resonance @ 0.3 eV
New dataset for α-ratio with smaller uncertainties for the 0.3 eV resonance. Compatible with Brooks 1967 data in the tails but with more precision.
Energy resolution and discrepancies
Where the comparison is possible, n_TOF data show slightly higher energy resolution than Mosby 2014 data (starting at 10 eV). There are regions with agreement but also regions with significant discrepancies be-tween both datasets.