## Slide 1: Data-driven evaluation of Fe-56 elastic-scattering angular distributions and covariances
PSN-RES/SNC/LN
Juan Antonio Monleon
(phd student)
WONDER26 – JUNE 2026
Mariya Brovchenko (ASNR)
Dimitri Rochman (Nagra)

## Slide 2: MOTIVATION AND BACKGROUND
01

## Slide 3: Why angular-distribution covariances for Fe-56
Fe-56 is the dominant isotope in the structural steel between core and pressure vessel. It controls how fast neutrons are attenuated and in which direction they are scattered.
For deep-penetration RPV fluence the scattering angle decides the outcome: forward scattering carries neutrons outward, backward scattering returns them.
Focus on the fast neutrons MeV, because they contribute most significantly to deep-penetration shielding concerns and radiation damage in the RPV.
A propagated uncertainty is only as good as the covariance it rests on
For Fe-56 elastic angular distributions, those covariances are sparse and inconsistent across libraries.
THE PREMISE

## Slide 4: The State of MF34 in the major libraries
LIBRARY | MF34 CONTENT | ENERGY STRUCTURE | NOTE
JEFF-3.3 | Orders | 13 groups · no energy correlation | Inherited from JEFF-3.0 (2005); not consistent with current MF4
JENDL-5 | Orders only | 4 broad groups · strong + correlation | Single-order representation (2021)
LIBRARY | MF34 CONTENT | ENERGY STRUCTURE | NOTE
JEFF-3.3 |  | 13 groups · no energy correlation | Inherited from JEFF-3.0 (2005); not consistent with current MF4
JENDL-5 |  | 4 broad groups · strong + correlation | Single-order representation (2021)
The nominal MF4 grid holds more than 1,000 pointwise energies in this window.
The covariance resolution is far coarser than the data it acts on.
For MeV, evaluations are based on experimental data from EXFOR Kinney (1976) & Smith (1980)
For this energy region:

## Slide 5: Coarse, inconsistent energy structure
JEFF-3.3 (orders 1–3) — 13 energy groups, block-diagonal: no correlation between them.
JENDL-5 (order 1) — 4 broad groups with strong positive energy correlation throughout.

## Slide 6: Single-order covariances drive unphysical bands
JEFF-4.0* — ℓ = 6 contribution at 2.8 MeV. Large high-order variance produces an oscillatory, lobed band
JENDL-5 — ℓ = 1 only at 1.57 MeV. The band is dipolar and collapses to zero at cos θ = 0
*covariance from JEFF-3.3

## Slide 7: How well do libraries fit the data?
Χ²/N ON THE FULL EXFOR DATABASE
67 experiments · ≈ 47,000 angular points
≫1
Both libraries sit far above unity even after their own MF34 is folded in.
Their agreement is carried by the Kinney & Smith calibration anchors. Removing them degrades both by ≈ 1.4×. Campaigns are internally consistent but mutually offset by more than their declared uncertainties.
Motivates an independent evaluation built from the full database.
Library |  | 
JEFF-4.0 | 33.3 | 20.5
JENDL-5 | 33.6 | 25.4

## Slide 8: The evaluation pipepline
02

## Slide 9: Pipeline overview
A nominal fit sets the central coefficients; two Monte Carlo passes supply the variances and the full correlation structure; assembly and an adaptive collapse produce the MF34.
1,738
energy bins
526
final multigroups
No prior knowledge
FOUR INPUTS
EXFOR database
Uncertainty manifest
TOF parameters (opt)
Reference ENDF

## Slide 10: The experimental database
67
experiments
Drawn from EXFOR over 847 keV–4 MeV
Points from different experiments are taken as uncorrelated; the full data covariance is block-diagonal in experiment.
From the EXFOR ERR-ANALYSIS
Kish effective sample size

## Slide 11: Nominal fit: ridge-GLS
Points from different experiments are taken as uncorrelated; the full data covariance is block-diagonal in experiment.
measured cross sections at the scattering cosine
Legendre polynomial of order
The coefficient we solve for
Highest order kept
Ridge-regularized Generalized Least-Square
ENDF-style shape normalized

## Slide 12: Nominal fit: order selection
Points from different experiments are taken as uncorrelated; the full data covariance is block-diagonal in experiment.
Akaike weights

## Slide 13: Nominal fit: tau bands
Points from different experiments are taken as uncorrelated; the full data covariance is block-diagonal in experiment.
We Fix !

## Slide 14: Variance calculation – mc pass 1
Points from different experiments are taken as uncorrelated; the full data covariance is block-diagonal in experiment.
Fixed !

## Slide 15: correlation calculation – mc pass 2
Points from different experiments are taken as uncorrelated; the full data covariance is block-diagonal in experiment.
Same procedure as Pass 1 but now considering points from nearby energy bins
Apply weighting factor according to their distance and the energy resolution of the experiment
Fixed !

## Slide 16: Covariance assembly and mf34 format
Points from different experiments are taken as uncorrelated; the full data covariance is block-diagonal in experiment.
1
Per-bin variances
→ marginal σ(aℓ ) per bin, carrying the diagonal of the covariance matrix
2
Kernel-weight correlation
→ the full R: cross-order within a bin and cross-energy between bins.
ASSEMBLY
C = diag(σ) · RKW · diag(σ)
GROUP COLLAPSE
Energy bins with high correlations are combined to reduce the size of the matrix
1738 → 526 groups

## Slide 17: Results and validation
03

## Slide 18: Central values agree; covariance differs
Points from different experiments are taken as uncorrelated; the full data covariance is block-diagonal in experiment.

## Slide 19: Example at 1.40 mev
Points from different experiments are taken as uncorrelated; the full data covariance is block-diagonal in experiment.
This work
JEFF-4.0
JENDL-5

## Slide 20: Lower χ² across the database (exfor + mf34 covariance)
Points from different experiments are taken as uncorrelated; the full data covariance is block-diagonal in experiment.
Full pool · χ²/N
This work
8.5
JEFF-4.0
20.5
JENDL-5
25.4
Excluding Kinney & Smith· χ²/N
This work
7.8
JEFF-4.0
27.7
JENDL-5
35.2

## Slide 21: Out-of-sample test: Gkatis 2025
Χ²/N ON G. GKATIS (2025)
A 784-point double-differential measurement (1.01–3.93 MeV)
For this work, Gkatis is in-sample experiment
so direct comparison should be taken with caution
Library |  | 
JEFF-4.0 | 728.9 | 591.7
JENDL-5 | 639.0 | 623.4
This work | 323.0 | 245.1

## Slide 22: conclusions
WHAT THIS WORK DELIVERS
✓
A reproducible, purely data-driven MF4 + MF34, between [0.85 – 4 MeV]
✓
Uncertainty spread across orders smooth, interpretable bands.
✓
Better performance on the χ²/N metrics compared to JEFF and JENDL libraries
LIMITATIONS & OUTLOOK
—
χ²/N still > 1 for all three. Uncertainties may still underestimate the spread although MF33 covariances are not considered here
—
Many bins rest on only 1–2 experiments (often Kinney alone).
—
Check for continuity issues function of energy
Shape and magnitude decoupled
✓

## Slide 24: Lower χ² across the database (only exfor covariance)
Points from different experiments are taken as uncorrelated; the full data covariance is block-diagonal in experiment.
Full pool · χ²/N
This work
16.8
JEFF-4.0
33.3
JENDL-5
33.6
Excluding Kinney & Smith· χ²/N
This work
17.0
JEFF-4.0
44.9
JENDL-5
46.7