## Slide 1: 50Cr and 53Cr (n,γ) cross section measurements at n_TOF and HiSPANoS
P. Pérez-Maroto, C. Guerrero, a. casanovas,
B. Fernández & the n_TOF Collaboration.
Wonder 2026, aix-en-provence. 30/06/2026

## Slide 2
I. Introduction
II. 50Cr activation measurement at HiSPANoS
III. 50,53Cr time-of-flight measurement at EAR1-n_TOF
IV. Summary & Conclusions
Seville
Geneva
P. Pérez-Maroto PhD: “Measurement of 50Cr and 53Cr neutron capture
cross sections for nuclear technology at CERN n_TOF and HiSPANoS”
Index
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026

## Slide 3
I. Introduction
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026

## Slide 4
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Stainless Steel → structural material in nuclear reactors.
Contains 11-26% of chromium.
Criticality benchmarks sensitive to chromium → dominated by
50,53Cr (n,γ)
~30% discrepancies in 50Cr and 53Cr cross sections → 1% change in keff †.
Why 50,53Cr neutron capture?
†A. Trkov, “On the Benchmarking of New Evaluated Nuclear Data Libraries”, INDC (NDS)-0751 (2018)

## Slide 5
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Stainless Steel → structural material in nuclear reactors.
Contains 11-26% of chromium.
Criticality benchmarks sensitive to chromium → dominated by
50,53Cr (n,γ)
~30% discrepancies in 50Cr and 53Cr cross sections → 1% change in keff †.
Why 50,53Cr neutron capture?
†A. Trkov, “On the Benchmarking of New Evaluated Nuclear Data Libraries”, INDC (NDS)-0751 (2018)
↓
NEA High Priority Request List (HPRL):
50,53Cr σ(n,γ) within 8-10% from 1 to 100 keV

## Slide 6
Previous measurements and evaluations
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Experiment | Stieglitz (1971) | Beer (1975) | Kenny (1977) | Brusegan (1986) | Guber (2011)
Facility | RPI | FZK | ORELA | GELINA | ORELA
Detector | Scin.tank | Scin.tank | C6F6 | C6D6 | C6D6
Thickness 50Cr (10-3 at/barns) | 8 | 18 | 5/8 | 7 | -
Thickness 53Cr (10-3 at/barns) | 14 | 14 | 8/12 | 12/60 | 14
Several measurements have been performed during the 70s and 80s, and a more recent one in ORELA by Guber et al. (2011) †.
†K. H. Guber et al., “Neutron cross-section measurements on structural materials at ORELA”, J. Korean Phys. 59, nº 2(3) (2011)
Goal: as many resonances as possible, even at high energies.
Very thick samples were used → large neutron multiple-scattering effects.
Guber improves the neutron sensitivity → Issues with sample characterization.
Notes: Very thin -> 1-15 keV. The first resonance affects the most to the criticality safety calculations
Thin -> 15-100 keV. Thanks to the very intense neutron flux at n_TOF
natCr -> (50,52,53,54) = (4.3, 83.8, 9.5, 2.4)% (50Cr half-life = 2E17 years = 0.2 trillones de años)

## Slide 7
Previous measurements and evaluations
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Evaluated data
JEFF-3.3, ENDF/B-VIII.0 & JENDL-5 → Same XS, mainly based on Guber et al (2011).
CENDL-3.2 → Uses data from the 70’s and 80’s.
INDEN → Careful re-evaluation of multiple-scattering effects at Guber et al. data.
ENDF/B-VIII.1, JEFF-4.0 → Has adopted INDEN.
40%
100%
50Cr
53Cr
Notes: Very thin -> 1-15 keV. The first resonance affects the most to the criticality safety calculations
Thin -> 15-100 keV. Thanks to the very intense neutron flux at n_TOF
natCr -> (50,52,53,54) = (4.3, 83.8, 9.5, 2.4)% (50Cr half-life = 2E17 years = 0.2 trillones de años)

## Slide 8
II. 50Cr activation measurement
at HiSPANoS@CNA
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026

## Slide 9
The HiSPANoS facility at CNA
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
†M. Macías et al., “The first neutron time-of-flight line in Spain: …”, Rad. Phys. and Chem. 168 (2020)
‡M. A. Millán-Callado et al., “Continuous and pulsed fast neutron beams at the CNA HiSPANoS facility”, Rad. Phys. and Chem. 217 (2024)
HiSPANoS is the neutron facility of CNA †‡.
Thermal (eV) → moderation
Epithermal (keV) → Li(p,n)
Fast (MeV) → 2H(d,n) and Be/Li(p/d,n)
  Continuous: activations/irradiations
  Pulsed: ToF measurements

## Slide 10
Experimental set-up. Activation sample
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
94.6(4)% enriched 50Cr2O3
723(3) mg of material
Inside a PEEK capsule
Measured relative to two 197Au foils (standard cross section)
20 mm
50Cr
197Au
12 mm collimator
~23 mm Li target

## Slide 11
Neutron activation analysis
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
 | 50Cr (%) | 197Aufront(%) | 197Auback(%)
 | 0.1 | 0.6 | 
 | 3.3 | 1.8 | 
 | 1.3 | 1.7 | 1.5
 | 0.01 | 0.08 | 0.07
 | 0.01 | 0.01 | 
 | 0.2 | 0.2 | 
Overall | 3.6 | 2.6 | 2.4
 | 50Cr (%) | 197Aufront(%) | 197Auback(%)
 | 0.1 | 0.6 | 
 | 3.3 | 1.8 | 
 | 1.3 | 1.7 | 1.5
 | 0.01 | 0.08 | 0.07
 | 0.01 | 0.01 | 
 | 0.2 | 0.2 | 
Overall | 3.6 | 2.6 | 2.4
 | (106)
 | 79(3)
 | 434(11)
 | 425(10)
 | 79(3)
 | 434(11)
 | 425(10)
Efficiency is the main source of uncertainty

## Slide 12
MACS30(50Cr) determination
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
If is a Maxwellian distribution at a temperature of kT (keV)

## Slide 13
MACS30(50Cr) determination
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
If is a Maxwellian distribution at a temperature of kT (keV)
SimLiT + GEANT4
↓
MACS30(50Cr) relative to MACS30(197Au):

## Slide 14
MACS30(50Cr). Comparison with previous data
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
First 50Cr neutron activation measurement.
Agreement with CENDL-3.2 and JEFF-3.3 (and therefore, ENDF/B-VIII.0 and JENDL-5).
20% lower than INDEN.
MACS30(50Cr) |  | 197Auback
JEFF-3.3 | 37.9 mb | 38.5 mb
INDEN | 35.7 mb | 36.4 mb
MACS30(50Cr) |  | 197Auback
JEFF-3.3 | 37.9 mb | 38.5 mb
INDEN | 35.7 mb | 36.4 mb
MACS30 (50Cr) = 37.1(20) mb
→ <6% unc.
P. Pérez-Maroto et al., “Neutron activation as benchmark for cross section evaluations: Demonstration through the MACS of 50Cr for nuclear technology applications”, Physics Letters B, 2025, vol. 862, p. 139360

## Slide 15
III. 50,53Cr time-of-flight measurement at EAR1-n_TOF@CERN
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026

## Slide 16
The neutron Time-Of-Flight facility at CERN
n_TOF@CERN
In operation since 2001
2026: ~150 researchers from 42 institutes
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026

## Slide 17
The neutron Time-Of-Flight facility at CERN
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
https://ntof-exp.web.cern.ch
By N. Colonna
NEAR
↓Flux
↑En resolution
↑ Flux
↓En resolution
185 m
19 m
3 m

## Slide 18
The neutron Time-Of-Flight facility at CERN
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
https://ntof-exp.web.cern.ch
By N. Colonna
NEAR
↓Flux
↑En resolution
↑ Flux
↓En resolution
185 m
19 m
3 m

## Slide 19
Experimental set-up. C6D6 TED detectors
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
†R. Plag et al.,“An optimized C6D6 detector for studies of resonance-dominated (n,γ) cross-sections”, Nucl. Inst. & Meth. in Phys. Res. A 496 (2003)
4 C6D6 TED detectors† at 8 cm and 125° from the sample.
Developed specifically for n_TOF.
Made of carbon fiber.
Main advantages:
  Very low neutron sensitivity
  Very fast response and time resolution
TED → Pulse Height Weighting Technique.

## Slide 20
Experimental set-up. Samples
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
The strategy is to use two samples for each isotope.
94.6(4)% of 50Cr and 97.7(2)% of 53Cr.
Thinnest samples ever measured
Thin samples (1-10 keV) → MS effects under control
Thick samples (10-100 keV) → Better statistics
neutrons
C6D6
sample
C6D6
C6D6
C6D6
Plus ancillary samples…
42 days long campaign
750·103 protons pulses
Experiment | Stieglitz (1971) | Beer (1975) | Kenny (1977) | Brusegan (1986) | Guber (2011) | This work (2024)
Thickness 50Cr (10-3 at/barns) | 8 | 18 | 5/8 | 7 | - | 0.6/1.9
Thickness 53Cr (10-3 at/barns) | 14 | 14 | 8/12 | 12/60 | 14 | 1.2/5.9
x0.1
x0.1

## Slide 21
Capture yield determination
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026

## Slide 22
Capture yield determination
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Background weighted counts
Total
weighted counts
Evaluated neutron flux
Beam Interception Factor (SRM)
Efficiency (PHWT)
Threshold correction factor
Ethr = 150 keV

## Slide 23
Capture yield systematic uncertainties
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Contribution | Syst. Unc. (%) | 
 | 50Cr | 53Cr
Sample thickness | 0.4 | 0.2
Monitor norm. | 2.5 | 2.5
Neutron flux shape | 2 | 2
Saturated res. norm. | 1.5 | 1.5
Sample alignment | 2 | 2
PHWT implementation | 1.7 | 1.7
Cr cascades fthr | 1 | 1
RWF statistics | 2.3 - 7.7 | 2.1 - 7.8
Overall (1-10 keV) | 4.5 | 4.5
Overall (10-100 keV) | 5.1 - 9.0 | 5.0 - 9.0
Contribution | Syst. Unc. (%) | 
 | 50Cr | 53Cr
Sample thickness | 0.4 | 0.2
Monitor norm. | 2.5 | 2.5
Neutron flux shape | 2 | 2
Saturated res. norm. | 1.5 | 1.5
Sample alignment | 2 | 2
PHWT implementation | 1.7 | 1.7
 | 1 | 1
 | 2.3 - 7.7 | 2.1 - 7.8
Overall (1-10 keV) | 4.5 | 4.5
Overall (10-100 keV) | 5.1 - 9.0 | 5.0 - 9.0
50Cr
53Cr
A new methodology to apply the PHWT was implemented, which adds a source of uncertainty associated to the resonance total counts.
In overall, the uncertainty remains below 9%, thus fulfilling the NEA requirements.

## Slide 24
Resonance analysis with SAMMY (50Cr)
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Main resonance → in agreement with JEFF-3.3 (even also similar to CENDL-3.2).
Overestimation by INDEN.
Previous energy shifted: from keV to keV →
50Cr-thin
Multiple-scattering effects
52Cr

## Slide 25
Resonance analysis with SAMMY (50Cr)
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
For keV, INDEN adopts the same parameters than JEFF-3.3
33 resonances described.
3 of them removed from JEFF-3.2, but visible in our data (for example at 64 keV).

## Slide 26
Resonance analysis with SAMMY (53Cr)
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
The MS effects are very large → ~7mm thickness.
SAMMY fails to accurate evaluate the very strong MS effects.
53Cr-thin
53Cr-thick

## Slide 27
Resonance analysis with SAMMY (53Cr)
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
The MS effects are very large → ~7mm thickness.
SAMMY fails to accurate evaluate the very strong MS effects.
Our data is much closer to CENDL-3.2 (still with differences).

## Slide 28
Resonance analysis with SAMMY (53Cr)
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
More differences between evaluations than in 50Cr.
A total of 51 resonances have been described.
Some of them (included in JEFF-3.3 and INDEN) are not visible in our data.
In general, INDEN seems to overestimate the capture cross section.

## Slide 29
50,53Cr(n,γ) at EAR1 results
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Results for 50Cr and 53Cr are 20% and 70% lower than INDEN, respectively.
50Cr → MACS30 from HiSPANoS and n_TOF are compatible within uncertainty.
MACS30 extracted from n_TOF (En<100 keV) + evaluations above 100 keV.
This work (n_TOF)
This work (HiSPANoS)
This work (n_TOF)
P. Pérez-Maroto et al., “New measurement 50Cr and 53Cr (n,γ) cross sections at n_TOF: a call for chromium nuclear data revision ”, The European Physical Journal A, 2026, vol. 62(1), p. 5

## Slide 30
IV. Summary & Conclusions
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026

## Slide 31
Summary & Conclusions
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
This work (n_TOF)
This work (HiSPANoS)
This work (n_TOF)
A clear goal: improving the 50,53Cr(n,γ) cross section to 8-10% accuracy at 1-100 keV.
Two experiments:
  50Cr activation at HiSPANoS@CNA.
  50,53Cr ToF at n_TOF@CERN.
Uncertainties within the objective.
Both cross sections clearly lower than INDEN.
Both experiments are compatible.

## Slide 32
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Thank you for your attention
Pablo Pérez Maroto - pperezma@cern.ch
Acknowledgements: Euroatom research and training programme 2014-2018 under grant agreement No 847594 (ARIEL). Spanish national projects RTI2018-098117-B-C21, PID2019-104714GB-C22, PID2021-123879OB-C21 and PID2022-138297NB-C22 funded by MCIN/AEI/10.13039/501100011033 and by "ERDF A way
of making Europe". FPI national Grant No PRE2019-089678. Recovery & Resilience Facility (Spain). The European Union – NextGenerationEU.

## Slide 33
Backup. Why the discrepancies?
The main problem for measuring Cr(n,g) is the large neutron multiple-scattering effects
In the previous measurements thick samples were used, aiming for good statistics in a very wide energy range
(n,el)
(n,el)
(n,el)
(n,el)
(n,el)
(n,γ)
(n,γ)
(n,γ)
Y0
Y1
Y4
Capture yield
(captures/neutron)
Analytical
(accurate)
Numerical
(aproximate)
x100
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 34
Backup. MB spectrum: ToF characterization
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
A 30 keV quasi-Maxwellian spectrum can be produced by 7Li(p,n) with Ep=1912 keV†.
6Li-glass
505 mm
†W. Ratynski & F. Käppeler, “Neutron capture cross section of 197Au: A standard for stellar nucleosynthesis”, Physical Review C 37(2) (1988)
Protons
(1912 keV)
Neutrons (1-120 keV)
Li target
Li-glass detectors → based on the 6Li(n,α)3H reaction
γ-flash
neutrons
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 35
Backup. MB spectrum: ToF characterization
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
The neutron field was characterized by time-of-flight + simulations.
Ep = 1912 keV
σ = 3.5 keV
The neutron field was characterized by time-of-flight + simulations.
SimLiT → Neutron production
GEANT4 → Neutron transport
Li-glass detectors → based on the 6Li(n,α)3H reaction
γ-flash
neutrons
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 36
Backup. Neutron activation analysis
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Counts → Gaussian + linear fit
Decay during irradiation → current measurement
Decay during transport and measurement
Efficiency
4.7 h
24min/
300min
270 min/
20min
4.7 h
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 37
Backup. Ancillary samples
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Some ancillary measurements were performed during the experimental campaign
Sample |  | nat (10-3at/b)
Dummy (2) | 22 | -
197Au | 20 | 0.583
197Au | 80 | 0.644
natC | 20 | 8.702
Sample |  | nat (10-3at/b)
Dummy (2) | 22 | -
197Au | 20 | 0.583
197Au | 80 | 0.644
natC | 20 | 8.702
Dummy (empty PEEK capsule)
Empty (empty aluminum ring)
1 mm natC (neutron-scattering)
100 μm 197Au (two diameters)
→ Background
→ Normalization
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 38
Backup. Background determination
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
The background affecting the measurement can be divided in:
Sample independent
Sample related
→ Neutron-scattering and capture outside the sample: Dummy & Empty
→ Neutron-scattering inside the sample: natC
50Cr
Sample | 
50Cr-thin | 0.25
50Cr-thick | 0.72
53Cr-thin | 0.59
53Cr-thick | 2.91
Sample | 
50Cr-thin | 0.25
50Cr-thick | 0.72
53Cr-thin | 0.59
53Cr-thick | 2.91
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 39
Backup. Background determination
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Some background is still visible below the main resonance in the thick samples → Region not used.
The residual background is included in the yield analysis.
50Cr-thin
53Cr-thin
50Cr-thick
53Cr-thick
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 40
Backup. Capture yield normalization: SRM
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
†R. L. Macklin, “Absolute neutron capture yield normalization”, Nuclear Instruments and Methods 164(1) (1979)
The final step to obtain the capture yield is the normalization factor FBIF → 197Au sample
Saturated Resonance Method (SRM) †
FBIF = 0.645(9)
FBIF = 1.003(3)
20 mm
100 μm thick 197Au sample → the 4.9 eV resonance saturates.
80 mm sample to validate the analysis methodology.
80 mm
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 41
Backup. Capture yield analysis
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
The WF enhance the natural statistical fluctuations → Limited statistics bin-by-bin.
~ 16 counts
~ 18 counts
~15 counts
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 42
Backup. Capture yield analysis
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
The WF enhance the natural statistical fluctuations → Limited statistics bin-by-bin.
Solution: Average Weighting Factor (AWF).
Used at n_TOF to extend the energy range.
  J = 0+
  Heavy nuclei
Same de-excitation pattern for every resonance
~ 197 counts
~ 197 counts
~261 counts
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 43
Backup. Capture yield analysis
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
The WF enhance the natural statistical fluctuations → Limited statistics bin-by-bin.
Same de-excitation pattern for every resonance
~ 197 counts
~ 197 counts
~261 counts
Solution: Average Weighting Factor (AWF).
Used at n_TOF to extend the energy range.
  J = 0+
  Heavy nuclei
New technique proposed:
Resonance Weighting Factor (RWF)
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 44
Backup. Capture yield analysis
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
The WF enhance the natural statistical fluctuations → Limited statistics bin-by-bin.
Same de-excitation pattern for every resonance
Solution: Average Weighting Factor (AWF).
Used at n_TOF to extend the energy range.
  J = 0+
  Heavy nuclei
New technique proposed:
Resonance Weighting Factor (RWF)
Thin samples (1-10 keV)
Thick samples (10-100 keV)
Thick samples (10-100 keV)
Analysis strategy
Very good statistics (6) → PHWT
Good statistics (42) → RWF
Bad statistics (24) → AWF
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 45
Backup. Resonance analysis with SAMMY (50Cr)
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
Main resonance → in agreement with JEFF-3.3 (even also similar to CENDL-3.2).
Overestimation by INDEN.
Previous energy shifted: from keV to keV.
Resonance deformed in the thick sample.
Multiple-scattering effects
50Cr-thin
50Cr-thick
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 46
Backup. Resonance analysis with SAMMY (53Cr)
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
53Cr-thin
53Cr-thick
The MS effects are very large → ~7mm thickness.
SAMMY fails to accurate evaluate the MS effects.
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio

## Slide 47
Backup.50,53Cr(n,γ) at EAR1 results
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
The radiative kernel Kγ gives information resonance by resonance.
50Cr → 7% lower than JEFF-3.3 and CENDL-3.2, 40% lower than INDEN.
53Cr → 35% higher than JEFF-3.3, 10% and 60% lower than CENDL-3.2 and INDEN, respectively.
50Cr
53Cr

## Slide 48
Backup. 50,53Cr (n,γ) at EAR1 results
Pablo Pérez Maroto || WONDER 2026 || 30/06/2026
 | 50Cr MACS (mb) | 53Cr MACS (mb)
JEFF-3.3 (2017) | 38.2 | 25.9
CENDL-3,2 (2020) | 37.7 | 31.5
INDEN (2023) | 45.0 | 51.7
HiSPANoS(2025) | 37.1(20) | -
n_TOF (2025) | 35.0(24) | 30.9(22)
This work (n_TOF)
This work (HiSPANoS)
This work (n_TOF)
Notes: After scattering the neutron get captured at the same time, but with a different energy, therefore affecting the yield -> cross section
Multiple scattering increases with thickness and XS_t/XS_g ratio