## Slide 1: JEFF-4.0 g-production evaluations and integral validation of g-heating in ZPR/EOLE
D. Bernard, O. Litaize, A. Chebboubi, O. Serot
CEA, DES, IRESNE, DER, SPRC, Cadarache, Physics Studies Laboratory, 13108 Saint-Paul-lès-Durance, France
david.bernard@cea.fr

## Slide 2: Outline
JEFF-4.0/GP capture-g overall analysis
New JEFF-4.0 Prompt Fission & Capture Gamma Spectra & Multiplicities
Benchmarking and Validation of g-heating in ZPR/LWR/EOLE core using JEFF-3.1.1 and JEFF-4.0
Conclusions & perspectives

## Slide 3: Outline
JEFF-4.0/GP capture-g overall analysis
New JEFF-4.0 Prompt Fission & Capture Gamma Spectra & Multiplicities
Benchmarking and Validation of g-heating in ZPR/LWR/EOLE core using JEFF-3.1.1 and JEFF-4.0
Conclusions & perspectives

## Slide 4: JEFF-4.0/GP capture-g overall analysis
2010 (!): many MF3-MT102/Q-value were not correct in JEFF-3.1.1
JEFF-4.0 (593 files) corrected almost all of them (<1%):

## Slide 5: JEFF-4.0/GP capture-g overall analysis
Since JEFF-4.0/MF3-MT102/Qvalues are correct,
the completeness of g-spectra+multiplicities is tested by PSYCHE tool (thanks to NEA processing Docker files):
MF6 discrete (527 files): 29 041 g-lines@thermal
MF6 continuum only (37 files)
or composite files MF5-12-13-15 (22 files)
No g-production files (7 files: 113,115In, 18O, 13C…)

## Slide 6: JEFF-4.0/GP capture-g overall analysis
Incomplete MT102 g-production files
52,53,54Cr: -12.1%, -2.0%, -4.7% resp.
55Mn: -3.7%
54,56,57Fe: -11.2%, -2.0%, -5.1% resp.
108Pd: -12.3% 93mNb: +1.2%
109Ag: -1.6% 100,102Ru: +1.0%, +1.4%
114Sn: -1.2% 134Xe: +1.1%
139La: -2.0%
232Th: -1.3%
233, 236,238U: -14.0, -1.1%, -2.8% resp.
240Pu: -3.3%
JEFF-3.1.1/56Fe(MF12-14-15): -1.3%
JEFF-3.2/56Fe(MF6): -4.3% (ICC corrected)

## Slide 7: Outline
JEFF-4.0/GP capture-g overall analysis
New JEFF-4.0 Prompt Fission & Capture Gamma Spectra & Multiplicities
Benchmarking and Validation of g-heating in ZPR/LWR/EOLE core using JEFF-3.1.1 and JEFF-4.0
Conclusions & perspectives

## Slide 8: JEFF-4.0 Prompt Capture Gamma Spectra & Multiplicities
FIFRELIN calculations in decay mode at thermal point and 150 keV
U238 : LDM (CTM), PSF (MGLO 2xE1 + 3xM1 + 1xE2) adapted to better reproduce <Gg>, <D0> and
multi-step gamma-ray energy spectra measured at nTOF.
Pu240 : LDM, PSF from default models (CGCM/EGLO)
Conversion electrons accounted for but not stored in the g-section of the evaluation (slight Q value difference, ~ 100 keV)
JEFF-3.1.1
(MF12-14-15)
JEFF-3.3
(MF6, discrete + cont’)
JEFF-4.0
(MF6, histog)
J. Moreno-Soto et al., Phys. Rev. C 105, 024618 (2022)

## Slide 9: JEFF-4.0 Prompt Fission Gamma Spectra & Multiplicities
R. Billnert et al., Phys. Rev. C87, 024601 (2013)
FIFRELIN calculation validated on PFGS and PFGM of 252Cf(sf) measured by Billnert

## Slide 10: JEFF-4.0 Prompt Fission Gamma Spectra & Multiplicities
A. Gatera et al. PRC 95, 064609 (2017)
Example 239Pu(nth,f) reaction
 | g-multiplicity | <eg> | <Eg>
Gatera et al. 2017 with EThres= 100 keV and TCoinc= 3 ns | 7.35 ± 0.12 | 0.85 ± 0.02 | 6.27 ± 0.11
FIFRELIN simulation : with EThres= 100 keV and TCoinc= 3 ns | 7.24 | 0.93 | 6.69
FIFRELIN simulation: with EThres= 0 keV and TCoinc= | 8.40 | 0.86 | 6.99
 | g-multiplicity | <eg> | <Eg>
Gatera et al. 2017 with EThres= 100 keV and TCoinc= 3 ns | 7.35 ± 0.12 | 0.85 ± 0.02 | 6.27 ± 0.11
FIFRELIN simulation : with EThres= 100 keV and TCoinc= 3 ns | 7.24 | 0.93 | 6.69
 | 8.40 | 0.86 | 6.99

## Slide 11: Outline
JEFF-4.0/GP capture-g overall analysis
New JEFF-4.0 Prompt Fission & Capture Gamma Spectra & Multiplicities
Benchmarking and Validation of g-heating in ZPR/LWR/EOLE core using JEFF-3.1.1 and JEFF-4.0
Conclusions & perspectives

## Slide 12: Experimental set-up
Sub-critical approach
10 W x 604s critical and
few minutes of cooling
Neutron dose correction (ASTM)

## Slide 13: TRIPOLI-4® Calculation scheme
100,000 h.cpu
EPDL-97 (photon transport)
EEDL&Mott (electron transport) + EADL (atomic relaxation)…
Neutron+photon+electron+positon
keff(JEFF-3.1.1)= 1.00 222
keff(JEFF-4.0) = 1.00 077
s0.4pcm

## Slide 14: PERLE prompt-g-spectra

## Slide 15: PERLE prompt-g-spectra

## Slide 16: PERLE prompt-g-spectra

## Slide 17: PERLE g-spectra

## Slide 18
Complete scoring TRIPOLI-4.12.1® (JEFF-3.1.1)

## Slide 19: Detailed Results:
Absolute dose
The Stainless-Steel prompt heating is increasing by (+4.5±0.9)% !
Probably due to:
The increase of the total capture rates by +1.5% : 53Cr(n,g) responsible for +1.1% (only 1/3rd on the 5 keV multiplet), 55Mn for +0.6%, 52Cr for +0.4%, 56Fe for -0.4%, 58+60Ni for -0.5%...with respect of total capture in the reflector
The modification of g-production files for probably 3%...
Relative dose

## Slide 20: Outline
JEFF-4.0/GP capture-g overall analysis
New JEFF-4.0 Prompt Fission & Capture Gamma Spectra & Multiplicities
Benchmarking and Validation of g-heating in ZPR/LWR/EOLE core using JEFF-3.1.1 and JEFF-4.0
Conclusions & perspectives

## Slide 21: Conclusion
JEFF-4.0/prompt g-production at thermal (29 041 discrete lines!) seems correct for most of nuclides (Atomic Mass Evaluation + PSYCHE), except:
    Qvalues: 23Na, 148mPm, 247Bk
    Spectra & Multiplicities: Ag-113,115In-Cd, Fe-Cr-Ni, Mn, Gd…, fission products, actinides…
JEFF-4.1:
  How to manage low nrj conversion emission ? And consecutive X-rays+Auger… (GNDS ?)
  Account for IAEA/EGAF and extend the incident energy range (cf. the IAEA initiative).
EOLE/PERLE interpretation shows a clear increase in g-heating in ZPR. This partially addresses the OECD/NEA/HPRL requests #4&5 that were submitted exactly 20 years ago (May, 12, 2006) !
All these results will guarantee the reliability of JEFF-4.0 -heating calculations for the nuclear industry.

## Slide 22
MERCI !
Questions ?

## Slide 23: 52Cr(nth,g)
JEFF-4.0: 0.854(28)b n-XS
IAEA/PGAA: 0.857(15)b reconstructed g+ production XS

## Slide 24: 56Fe(nth,g)
IAEA/PGAA: 2.48(2)b reconstructed g+ production XS
JEFF-4.0: 2.59(13)b n-XS

## Slide 25: 157Gd(nth,g)
IAEA/PGAA
JEFF-4.0: 254.6(0!)kb n-XS
IAEA/PGAA: 63.0(4)kb reconstructed g production XS

## Slide 26: 238U(nth,g)
IAEA/PGAA

## Slide 27: PERLE/KERMA-g

## Slide 28: PERLE/cumulative(KERMA-g)