## Slide 1: GEANT4 simulation of a monoenergetic neutron source
CEA/DES/IRESNE/DER/SPRC/LEPh
M. Boissier, P. Leconte, K. Kessaci
Workshop WONDER-2026, 29th June – 3rd July 2023, Aix-en-Provence

## Slide 2: Outline
Introduction
Accelerator Based Neutron Sources (ABNS)
GEANT4 simulation of ABNS
Results
Conclusions and outlooks

## Slide 3: Introduction
1

## Slide 4: The ALDEN collaboration
Objective :
Accurate measurement of delayed neutron macroscopic data.
2018
2019
2020
2021
ILL
235U
ILL
235U
ILL
233U + 239Pu
2022
2023
PTB
238U
PTB
238U
2024
2025
2026
2027
JRC
238U
?? JRC
239Pu
ILL
241Pu
ILL
241Pu
thermal
thermal
fast
fast
2018 : Launch of the ALDEN framework (Average Lifetime of DElayed Neutrons)
ILL (Grenoble, France)  thermal fission
PTB (Germany)  fast fission 238U (1 MeV – 20 MeV)
Aim of the PhD fast fission 239Pu (1 MeV – 20 MeV) at JRC Geel
Energy dependance of delayed neutrons data
+
GEN-IV needs

## Slide 5: The 239Pu case – Delayed neutrons yield
Rare recent experimental data
No data between 5 MeV and 14 MeV
No data between over 15 MeV
Inconsistencies between evaluations

## Slide 6: Experiments for delayed neutrons energy dependance
Incident neutrons energy
Monoenergetic spectrum (MONNET facility)
Need for a better understanding
Accurate simulation
Difficulties in PTB campaigns analysis:
Inconsistencies between different flux estimation techniques (crucial parameter)
Secondary reactions
T(p,n)3He  1 MeV – 6 MeV
D(d,n)3He  4 MeV – 7,5 MeV
T(d,n)4He  14 MeV – 20 MeV

## Slide 7: Accelerator Based Neutron Source
2

## Slide 8: Accelerator Based Neutron Source (ABNS)
Associated issues:
Tritium decay (T1/2 = 12,32 years)  3He accumulation
Deuterons implantation  secondary source D(d,n)3He
Deuteron/Titanium reactions  secondary source
Deuteron
Tritium
Titanium
Neutron
4He
Process:
Deuteron beam
Energy loss
Reaction with tritium T(d,n)4He
Example: TiT target, deuteron beam

## Slide 9: ABNS simulation tools
NeuSDesc
Developped in JRC Geel (2009)
Stopping power tables from 1977
Used in ALDEN-4&5
NEBOAS
Developped in JRC Geel (2024)
Stopping power tables more recent (SRIM-2013+NIST)
Deterministic approach
+ : Fast
- : Difficult to update, not flexible, possibility to omit physical processes
Stopping power table  energy profile
Cross section data  neutron yield

## Slide 10: ABNS simulation tools
Monte Carlo approach
Requirements:
Transport of charged particles
Accurate simulation of energy loss
Accurate simulation of light ion induced nuclear reaction
+ : Takes into account any physics process considered by the code, easy to maintain and update
- : Higher computing time
Choice: GEANT4
Modular
Open source
Neutron physics
Use of a Monte Carlo code to simulate the transport of ions and neutrons in the target

## Slide 11: GEANT4 simulation of ABNS
3

## Slide 12: GEANT4 model for ABNS
Geometry / Composition
Nuclear Data
Variance reduction
Scoring
Target + 4 detectors
Target’s composition
Deuterons Interactions
TENDL-2019
QGSP_BIC_AllHP
Deuteron energy loss
EM_option4
Bethe-Bloch + Bragg
Cross section biasing
Increase of the statistical weight of non-reacting deuterons
Decrease of neutrons weight
Reaction rate
Fluence rate

## Slide 13: Accuracy check
Stopping power
Agreement with SRIM over 100 keV
Minimal impact for thin targets
Stopping power vs Energy
Energy vs Depth in the target

## Slide 14: Accuracy check
T(d,n)4He reaction
Excellent agreement with ENDF for the whole energy range of interest
Cross section
Angular distribution
T(d,n)4He reaction

## Slide 15: Results
4

## Slide 16: Results – Comparison to NeuSDesc and NEBOAS
Differences :
Energy range  different stopping power data
Intensity differences  potential composition differences
Impacts :
Energy range: not significant (regarding fission cross-section)
Intensity: rescaled with flux monitors
Fluence rate 0°,

## Slide 17: Results – Tritium decay
Tritium decay  Intensity decrease
Absolute fluence rate 0°
Normalized fluence rate 0°
Study case : ALDEN-8 target
Helium accumulation  Stopping power increase  Small influence on final spectrum
Age = 16 years (T1/2 = 12,32 years)
T:Ti ratio = 1,5
Thickness = 932 µg/cm2

## Slide 18: Results – Secondary sources
“Problematic” case : 3 MeV deuteron beam on 10 years old target with deuterium implanted (2,55 C)
“Expected” fission rate spectrum
239Pu
Target

## Slide 19: Results – Secondary sources
Fission rate spectrum with secondary sources consideration
ATi(d,n) 53%
D(d,n)3He
16%
T(d,n)4He
31%

## Slide 20: Conclusion
5

## Slide 21: Conclusion
We developed a simulation tool for ABNS, following an alternative approach compared to existing tools (full Monte-Carlo with GEANT4 toolkit)
The model already gives promising results and allows to tackle some of the problematics encountered with ABNS
Outlooks
Extension (oxygen and carbon secondary reactions) and experimental validation (thanks to TOF from MONNET (JRC) and AMANDE (ASNR) teams)
Development perspective : extension to deuterium targets with breakup reaction (9 MeV – 14 MeV)
Important topic for all past and future experiments using ABNS
Chemical analysis of targets (SEM)

## Slide 22: Thank you for your attention ! Questions ?

## Slide 23
References
[1] P. Leconte & al., Eur. Phys. J. A, 2024
[2] D. Belverge, Theses, Université Grenoble Alpes [2020-....], 2024.
[3] R. Böttger & al., Nucl. Instrum. Methods Phys. Res. Sect. Accel. Spectrometers Detect. Assoc. Equip., 1989.
[4] S. Agostinelli & al., Nucl. Instrum. Methods Phys. Res. Sect. Accel. Spectrometers Detect. Assoc. Equip., 2003.
[5] J. F. Ziegler & al., Nucl. Instrum. Methods Phys. Res. Sect. B Beam Interact. Mater. At., 2010.
[6] C. R. Kleinfeldt & al., Nucl. Instrum. Methods Phys. Res. Sect. B Beam Interact. Mater. At., 2025.
[7] E. Birgersson & G. Lövestam, « NeuSDesc – Neutron Source Description Software Manual », JRC Report, 2008
[8] M. Macías & al., Comput. Phys. Commun., 2024.
[9] E. Mendoza & al., Nucl. Instrum. Methods Phys. Res. Sect. Accel. Spectrometers Detect. Assoc. Equip., 2020

## Slide 24: Secondary reactions
No detector efficiency correction
TOF from Varignon & al. NIM B. 2006

## Slide 25: Deuteron BreakUp
D + d  n +p +d
Tree bodies  neutron energy continuum

## Slide 26: Fission Cross Section

## Slide 27: Reactions on Titanium
neutron yield
neutron yield
Observations :
Negligible contribution at low incident energies
Dominant for few MeV incident energies  Problematic for 18,5 MeV to 20 MeV neutron fields

## Slide 28: Deuterium implantation
Secondary peak position reproduction
Relative intensities still unknown
Absolute fluence rate 0°,
Time of flight measurements (Jarosik & al.)