## Slide 1: PICO Bubble Chambers
EIEIOO 2025
Emily Adams 16ela1@queensu.ca

## Slide 2
Agenda
Bubble chamber introduction
Working principle
Data acquisition
PICO-40L detector
  Particle identification
PICO-500 detector
  New features
  Construction update
PICO-40L uncovered water tank at SNOLAB

## Slide 3: Check out picoexperiment.com/learn !
“Boiler”
“Bubbles”

## Slide 4: Before the Bubble Chamber… The Cloud Chamber
Incoming particle ionizes supersaturated vapour (usually water or alcohol) inside the chamber
Vapour condenses around the resulting ions, creating misty tracks of liquid droplets
Trails of particles visible with the naked eye!
Uranium nugget decaying in a cloud chamber

## Slide 5: Early Bubble Chambers
Target
  Saturated vapour  superheated fluid
  Denser target  greater interaction probability
Operating conditions
  Pressure and temperature conditions more feasibly attainable than in cloud chamber
Gargamelle
Designed to detect neutrinos
First evidence of Z0 boson
10 tonnes of liquid
2T magnet
Operated 1970-1976 at CERN

## Slide 6: Early Bubble Chambers
6
Superheated target fluid
Trails of tiny bubbles created by energy depositions from charged particles
Visualize particle trails
  Validation of physical models
    Pair production, annihilation
    Weak neutral current
  Discovery of new physics
    Meson
 | First photograph of the weak neutral current by the Gargamelle Bubble Chamber in 1973 [CERN]
Notes: Innovation on cloud chamber
Visualize particle interactions
Validated Weak neutral current
DM – strategically chosen threshold

## Slide 7: Bubble Formation & Growth
WIMP collision with nuclei in target medium causes a nuclear recoil
Recoil energy, , is deposited into the surrounding target fluid
Causes localized boiling creating microscopic proto-bubbles
target
A proto-bubble will continue to grow if
Deposition length scale:
7
Surface Tension
Expansion of Vapour
Phase Transition
(3.1)
[2]
Notes: r_c is the critical bubble radius. Radius at which E_r = Q_Seitz

## Slide 8
Warm Region ()
Cold Region)
At SNOLAB 2km below surface
“Right-Side-Up” Design
  Bellows on bottom
  Removed buffer fluid (PICO 60)
Cold region prevents superheating the target fluid in contact with stainless steel bellows
8
PICO-40L

## Slide 9
9
PICO-40L
Warm Region ()
Cold Region ()
Target:

## Slide 10: Pressure Control
Target fluid inside nested silica jars
  Pressure is controlled by changing volume at fixed temperature
  Bellows move to compensate pressure differential across jars
= constant =
Bellows
Pressure Vessel
Outer Jar
Inner Jar
10

## Slide 11: Compression Cycle
neutral
11
Detector state: compressed
Target state: liquid

## Slide 12: Compression Cycle
12
Detector state: expanded
Target state: superheated
neutral

## Slide 13: Compression Cycle
13
Detector state: expanded
Target state: superheated – bubble!
neutral

## Slide 14: Compression Cycle
Detector state: compressed
Target state: liquid
neutral
14

## Slide 15: Data Acquisition
15
Optical position reconstruction
Acoustic signal (piezometric transducers)

## Slide 16: Bubble Types
16

## Slide 17: Acoustic Acquisition
17
Bubble
Valves Open
Recompression

## Slide 18
18
18
For each nucleation, a resonant energy, , is calculated from the frequency spectrum
>
Used to generate AP (Acoustic Parameter) histogram
Acoustic Particle Discrimination

## Slide 19
232-Thorium Series
238-Uranium Series
Gaseous Radon

## Slide 20
Acoustic Parameter (AP)
Region of interest: SS neutron calibration, WIMP
High AP: alpha decay region

## Slide 21
PICO Detectors
Insensitive to electron recoil
Alpha rejection using acoustics
Ability to change active fluid
  Use different target nuclei
  Current target: (SD WIMP-proton)
Tunable nucleation thresholds
  WIMP has a large range of possible masses and unknown interaction mechanism

## Slide 22
PICO program has significant SD reach.
Complementary to other DM experiments with SI interactions and higher mass reach.
Lower neutrino floor opens unique search region to PICO
PICO Detectors

## Slide 23: Agenda
PICO-500
Coming soon

## Slide 24
PICO-500
Major New Features
260L target
Vacuum jacket
Muon Veto
Degassing Tank
Improved Heater design
Fully Connectorized
Engineering Design Reviews
84” OD

## Slide 25: PICO Exposure Forecast
Spin-Independent Spin Dependent

## Slide 26
Water Tank
background shielding

## Slide 27: Base Flange Assembly Table

## Slide 28: Pressure Vessel

## Slide 29
Pressure Vessel welding now!

## Slide 33
Hello from inside the PV

## Slide 34
E. Adams, M. Bai, K. Clark, J. Corbett,
D. Cranshaw, M. Dean, K. Dering,
G. Giroux, H. Herrera, A. Mir
C. Moore, N. Moss, A. Noble, M. Robert
I. Arnquist, C.M. Jackson,
B. Loer
C.E. Dahl
E. Behnke, C. Cripe,
I. Levine,
J. Basu, M. Das,
V. Kumar
P.S. Cooper, M. Crisler, A. Sonnenschein
I. Brooklyn Varela, L. Desmmarais,
P. Frédérick, M. Laurin, V. Monette,
H. Nozard, A. Robinson, J. Savoie,
N. Starinski, V Zacek, C. Wen Chao
R. Filgas, D. Mamedov,
E. Rukhadze, I. Stekl
M. Baker,S. Fallows,
C. Krauss, Q. Malin, S. Miller,
M. Rangen, C. Rethmeier,
P. Welingampola
R. Castilloux, R. Fournier, P. Grylls, A. Mathewson,
I. Lawson, M. Ralph, S. Sekula
D. Priya, S. Priya, Y. Yan
R. Neilson
A. Acevedo-Rentería, A. García-Viltres, E. Vázquez-Jáuregui
J. Farine, A. Le Blanc,
C. Licciardi, U. Wichoski
O. Harris
J.I. Collar
Notes: 34

## Slide 35
Thank You!
35

## Slide 36: References
[1] | https://home.cern/news/news/physics/forty-years-neutral-currents
[2] | https://doi.org/10.1103/PhysRevD.100.082006
[3] | https://lss.fnal.gov/archive/2017/slides/fermilab-slides-17-012-ae-e.pdf

## Slide 37: Alpha
Credit: Stephen Sekula
What do bubbles sound like?
Neutron

## Slide 38
PICO TDR, Internal Documentation

## Slide 39: Superheat Principle
As pressure decreases, minimum free energy appears at vapor state μv .
Energy barrier keeps system at metastable liquid state μl – liquid is “superheated”.
Sufficient energy deposition within a small radius can overcome the energy barrier and form a bubble.
*Plots from Eric Dahl

## Slide 40
Particles with higher stopping power are more likely to nucleate bubbles
Major advantage of bubble chambers: electron recoils are extremely inefficient at nucleating bubbles due to low stopping power
Detectors are designed to budget less than 1 gamma event in their dark matter search periods
P. Mitra (2018). PhD thesis
Stopping Power
Notes: Neutrons come from:
  Radioactive impurities in detector materials
  Induced by high energy gammas emitted after neutron or alpha captures in rock
  Induced by cosmic muons – muon spallation, muons start EM showers and photons get absorbed by nuclei causing them to decay, hadronic cascades induced by muon
In order to achieve deposition of the threshold energy within a short enough track, the interacting particle needs to have a high enough stopping power – it must lose a certain amount of energy per unit length. This plot shows the stopping power for various particles of different energies. What we don’t want to see in our detector is gammas or electrons, and one of the main advantages about bubble chambers is that they are intrinsically nearly insensitive to electron recoils because of the low stopping power of electrons. We use a very very hot gamma source to probe those extremely rare electron recoil events to characterize the gamma rejection of the detector, and choose a threshold that is as sensitive as possible to wimps and as insensitive as possible to gammas.
Great, but you might notice we have a problem up here, especially with 222-Rn alphas, given that radon likes to settle to the floor, and we happen to be operating in the deepest underground physics lab on the planet.