## Slide 1: An ion spectrometer for the identification of molecular bound states with positronium
Florian Sterkl
SMI Seminar
27.03.2025

## Slide 2: Overview and outlook
Positron Beamline
Motivation: Positronium containing molecules
Beam line overview
Spectrometer
Spectrometer magnets
Conclusion
Outlook
Notes: Magnets
Potential divider
Pulser
Parts of my spectrometer mit unterpunkten oda so lol
Mochs so afoch wie möglich 
Simulations
Construction
Measurements and Results

## Slide 3: What is positronium (Ps)?
Positron Beamline
Positronium is the bound state of e+ and e-.
Similar energy level structure to hydrogen,
but with energy levels halved.
Short lifetime due to self annihilation.
para-Ps
ortho-Ps
Can this exotic atom bind to other atoms?
Notes: Short lifetime
Matter antimatter bound system exotic atom
Spin anti parallel or parallel

## Slide 4: Motivation to measure Ps bound states
Positron Beamline
Molecular bound states of positronium
(PsA) predicted in numerous quantum calculations [e.g. Cheng 2012, Ludlow Gribakin 2010].
No precision binding energy
measurement has been performed.
Ps interactions important for related fields like material physics (e+ annihilation spectroscopy) or biomedicine (PET scans).
X. Cheng, D. Babikov, and M. Schrader. Binding-energy predictions of positronium. Phys. Rev. A 85, 012503 (2012).
Notes: Cheng semi empirical model Ps binding energy to basic atomic properties. Used known Ps binding energies from theoretical calculations to a limited set of neutral atoms.
Solid and Surfaces relevant positronium interactions because in porous materials positrons can bind and form positronium

## Slide 5: Measurement technique and goal
Positron Beamline
One experiment observed PsH by colliding methane gas with positrons (Schrader 1992).
Measured EB = (1.1 ± 0.2) eV from ion yield thresholds.
Limited by energy spread of the beam ∆E ~ 1 eV.
The onset energy of CH3+gets reduced by the binding energy of PsH.
-> The goal is to measure B_PsH by detecting CH3+ below 7.55 eV.
Appearance energies for methane ions.
Notes: Schrader Energy spread same order than the energy measurement. ->
Need precision to distinguish between different mass ions found in the same energy range.

## Slide 6: Overview and outlook
Positron Beamline
Motivation: Positronium containing molecules
Beam line overview
Spectrometer
Spectrometer magnets
Conclusion
Outlook
Notes: Magnets
Potential divider
Pulser
Parts of my spectrometer mit unterpunkten oda so lol
Mochs so afoch wie möglich 
Simulations
Construction
Measurements and Results

## Slide 7: Positron beamline
Positron Beamline
source
deflection coils
positron trap
spectrometer

## Slide 8: Source and deflection coils
Positron Beamline
source
deflection coils
positron trap
spectrometer

## Slide 9: Slow positron beam
Positron Beamline
Fast positron production by 22Na-source.
Collisions with solid neon ice reduce energy
from 300 keV down to ~ 1 eV.
Maximum efficiency ~ 1%.
Deflector coils remove line of sight between
the source and the trap.
22Na Source
Slow beam without trapping
on the MCP.
Notes: Sodium Chloride source.
Fast particles don’t follow the magnetic guiding field and hit the wall. Slow beam follows trajectory.
Reduces systematic effects by fast particles.
Positrons frozen on the cone shaped neon form a circle.

## Slide 10: Positron trap
Positron Beamline
source
deflection coils
positron trap
spectrometer

## Slide 11: Buffer gas positron trap
Positron Beamline
The trapping process of the slow beam has several stages:
Radial confinement by the solenoid B-Field.
Axial confinement by three regions of decreasing electrical potential.
Energy loss due to collisions
with buffer gas N2 and
vibrational energy loss to SF6.
z (mm)
mbar
mbar
mbar
1
2
3
potential (V)
N2
SF6
Notes: Differential pumping is used: the trap has smaller radius at the start and thus higher pressure.
It gets wider and the pressure decreases. Last stage also gets SF6 for rotational energy loss as a cooling gas.

## Slide 12: Rotating wall method and energy spread
Positron Beamline
90° phase shifted AC signal applied to a 4-segment
electrode.
Rotating electric field compresses the ion cloud.
Beam energy spread in trap ∆E = 5 1 meV (Schrader: ∆E ~ 1 eV).
Notes: Beam intensity sinks as the blocking electrode voltage gets too high for the beam to pass
This drop is used for the beam energy measurement and the green area for the energy spread.

## Slide 13: Overview and outlook
Positron Beamline
Motivation: Positronium Containing Molecules
Beam Line Overview
Spectrometer
Spectrometer Magnets
Conclusion
Outlook
Notes: Magnets
Potential divider
Pulser
Parts of my spectrometer mit unterpunkten oda so lol
Mochs so afoch wie möglich 
Simulations
Construction
Measurements and Results

## Slide 14: Spectrometer
Positron Beamline
source
deflection coils
positron trap
spectrometer

## Slide 15: Time of flight (ToF) working principle
Positron Beamline
Charged ions gaining kinetic energy in an electric
field and fly towards a detector with a fixed velocity v.
The flight time tdrift is
proportional to.
Different mass ions
have different flight
times, resulting in a ToF spectrum.
Notes: different mass-to-charge ratios yield different flight times, and the width of the peak (FWHM, Δ𝑡) when compared to the flight time 𝑡 directly provides the mass resolution.

## Slide 16: ToF spectrometer setup
Positron Beamline
Methane gas gets induced in the spectrometer through a capillary array (1mm thick glas plate, 50µm pores).
The slow positron beam hits the gas
jet and forms gas ions.
Time variable high voltage pulse applied to the electrodes.
Accelerate the ions towards the MCP.
The magnets confine the beam
radially and guide it.
Gas inlet CH4
Field free drift region
MCP
Notes: The experimental clear superiority of a capillary array source over a single tube source, of similar overall dimensions, in producing a well collimated molecular beam.
[Buckman et al. 1993].
plate ∅: 1mm
pore size: 50µm, 50% open area
thickness: 1mm
das sind die daten fürs capillary array
MCP: mikro channel plate which acts as an electron multiplier. Charged particles hit the wall and knock out secondary electrons. They get hv accelerated across the plate and produce an avalanche easy to detect as large fast pulse at the output.
used for good sensitivity and wide range of particles
Positron beam and ion beam are confined in the 500 Gauss Field. This mimics the trap field which is also at 500 Gauss.

## Slide 17: Electric and magnetic field simulations
Positron Beamline
Simion was used to calculate the electric
and magnetic field and ion trajectory.
E-field: Discretizes 10-ring electrodes
with finite-difference grid.
Iteratively solves the Laplace / Poisson
equation to obtain the field E = −∇ϕ.
Notes: (like a fourth-order Runge–Kutta method) to compute the trajectories of the ions (as set up in your fly2 file), with custom ion-creation and processing routines defined in Lua.

## Slide 18: Ion trajectory simulations
Numerical integration of ion trajectory.
Ions get customized initial conditions
at birth.
Expansion in a constant potential for time t_wait.
Extraction by time varying high voltage pulse.
Ion trajectory simulation
Notes: Constant potential to block the positrons out

## Slide 19: Time bunching ToF mechanism
Positron Beamline
Spectrometer electrodes coated with colloidal graphite.
Meshes at the exit / entrance define electrostatic boundary for field uniformity.
Gas ions have random motion at birth.
Particles further away from MCP receive stronger acceleration fields.
Uniform extraction better mass resolution.
Gas inlet CH4
Notes: Colloidal graphite reduce patch potentials, chemical stability in vacuum does not gas out.
Field leakage = fringing fields reduced by mesh.
Ramp potential to extract the ions more evenly than just apply 100 Volt at each electrode

## Slide 20: Time of flight spectra and wait time limits
Positron Beamline
Simulations suggest an upper limit of <1.5µs for high mass resolution.
1.5µs wait time, sharp peaks, lower FWHM
5µs wait time, broader peaks
Notes: How long can we wait before we extract the ions?
Overlap harder to separate them.
Ratio t/delta t for resolution
Below 1.5 us all wait times have approximately the same resolution.

## Slide 21: Overview and Outlook
Positron Beamline
Motivation: Positronium Containing Molecules
Beam Line Overview
Spectrometer
Spectrometer Magnets
Conclusion
Outlook
Notes: Magnets
Potential divider
Pulser
Parts of my spectrometer mit unterpunkten oda so lol
Mochs so afoch wie möglich 
Simulations
Construction
Measurements and Results

## Slide 22: Spectrometer magnets
Positron Beamline
Coil 1
Coil 2

## Slide 23: Spectrometer magnet setup
Positron Beamline
Helmholtz setup: 2 identical coils separated by distance ~ coil radius and same current direction.
Nearly uniform magnetic field in center between them.
About 1.43 times stronger B field than single coil.
Coil 1
Coil 2
Notes: Perfect because there are our ions produced.
Extra slide for this calculation

## Slide 24: Spectrometer magnetic field and heat curve
Positron Beamline
Two water cooling coil electromagnets, permanently running.
First z direction magnetic field measurements and heat curve without water cooling at low current.
Notes: Helmholtz setup bigger magnetic field than a single coil with 1.431 times as strong as just one

## Slide 25: Spectrometer Coil Magnets
Positron Beamline
T
Outside connection and cutout to not
intersect with chamber.
2 coil magnets, 44 kg / 1400 windings of wire each.
Notes: Dissipate heat generated from the running magnets.
I connected 2 * 22 kg of wire on one magnet, winded with 29 and 28 windings per layer resulting in about 1400 turns of wire.

## Slide 26: Watercooling pipes and copper plates
Positron Beamline
Copper plates for better heat dissipation and water cooling pipes soldered on top.
Notes: Dissipate heat generated from the running magnets.

## Slide 27: Conclusion
Positron Beamline
Time bunching Time of Flight spectrometer has been build to precisely measure the binding energies of molecules containing Ps.
The positron beam line is built up again.
Ion Trajectory Simulations with Simion have been made to simulate the extraction pulse and how long we can wait to apply it.
Magnets have been wound, water cooling copper plates have been soldered and heat curve measurements look promising.
Notes: Magnets
Potential divider
Pulser
Parts of my spectrometer mit unterpunkten oda so lol
Mochs so afoch wie möglich 
Simulations
Construction
Measurements and Results

## Slide 28: Outlook
Positron Beamline
HV pulser prototype tests to apply extraction potential.
Build a potential divider prototype for AC and DC components.
Assemble the gas line and cut the metal pipe.
Integrate the whole spectrometer setup into the beamline.
When everything comes together:
-> Measurement of molecular bound states with positronium.
Notes: Magnets
Potential divider
Pulser
Parts of my spectrometer mit unterpunkten oda so lol
Mochs so afoch wie möglich 
Simulations
Construction
Measurements and Results

## Slide 29: THANK YOU FOR YOUR ATTENTION!
Many thanks to everybody who supported this project:
Matti Cerwenka
Eric Hunter
Andreas Lanz
Martin Simon
Eberhard Widmann
Johann Zmeskal
Fabian Duringer
Manuel Friedrich
Gerhard Kaiser
Lukasz Paszkowski
Leopold Stowasser
SMI Positron Group
Daniel Murtagh
Ross Sheldon
Alina Weiser
Florian Sterkl
Follow us online:
Instagram
Website

## Slide 30: Back UP SLIDES 
Positron Beamline
Notes: Magnets
Potential divider
Pulser
Parts of my spectrometer mit unterpunkten oda so lol
Mochs so afoch wie möglich 
Simulations
Construction
Measurements and Results

## Slide 31: Schrader
Positron Beamline
Notes: The threshold energy at which the PsH formation cross section becomes non-zero corresponds to the sum of the ionization energy of the ion product and the binding energy of PsH.

## Slide 32: Electrode Voltage ramp up
Positron Beamline
Constant potential at the start for time period t_wait.
Linear ramp up to the extraction potential
t_wait
Notes: (like a fourth-order Runge–Kutta method) to compute the trajectories of the ions (as set up in your fly2 file), with custom ion-creation and processing routines defined in Lua.
The linearly falling extraction potential at each electrode effectively creates a time bunching tof spectrometer

## Slide 33: Time of flight spectra and wait time limits
Positron Beamline
Notes: d/delta t large separation relative to their widths easier to distinguish. Measure of how sharp the peak is

## Slide 34: Helmholtz B field calculation
Positron Beamline
B field in center between the coils.
N Number of turns on each coil.
R radius of the coil.
I current.
µ magnetic vacuum permeability.
Notes: 43% B field increase than single coil.

## Slide 35: B Field z direction measurement
Probeguide and probe.
Heat probe on magnet.

## Slide 36: Potential Divider SECTION

## Slide 37: Ltspice potential divider simulations
Positron Beamline
Necessary in our setup to divide a high voltage pulse to the electrodes for the extraction while not dividing the constant potential at the electrodes.
I used 10 times the same resistor for a 10 Volt drop at each intersection.
Works as a high pass filter -> high frequency components pass, low frequency ones get blocked.
Notes: Magnets
Potential divider
Pulser
Parts of my spectrometer mit unterpunkten oda so lol
Mochs so afoch wie möglich 
Simulations
Construction
Measurements and Results

## Slide 38: Ltspice potential divider simulations
Positron Beamline
Potential divider with output signal at each electrode.
Notes: Magnets
Potential divider
Pulser
Parts of my spectrometer mit unterpunkten oda so lol
Mochs so afoch wie möglich 
Simulations
Construction
Measurements and Results

## Slide 39: Potential divider test measurements
Positron Beamline
10 * 1kOhm resistors in series, 10 * 220 pf capacitors to couple in AC and 1MOhm resistors to couple to DC.
Measured with an oscilloscope probe.
10 Volt pulses from pulse
generator gets divided.
Divider output knots | Voltages V | Pulse rise time [ns]
0 | 9.5 V | 26
1 | 8.5 V | 64
2 | 7.5 V | 87
3 | 6.5 V | 87
4 | 5.6 V | 91
5 | 4.6 V | 91
6 | 3.8 V | 100
7 | 2.9 V | 101
8 | 1.7 V | 80
9 | 0.9 V | 90
Notes: Magnets
Potential divider
Pulser
Parts of my spectrometer mit unterpunkten oda so lol
Mochs so afoch wie möglich 
Simulations
Construction
Measurements and Results

## Slide 40: High Voltage Pulser
We want a sharp, nanosecond risetime pulse to extract the ions.
Simple mosfet-based high voltage pulser circuit. (Chaney 2004)

## Slide 41: Measurements Divider

## Slide 42: Spectrometer chamber
Positron Beamline
Notes: Magnets
Potential divider
Pulser
Parts of my spectrometer mit unterpunkten oda so lol
Mochs so afoch wie möglich 
Simulations
Construction
Measurements and Results

## Slide 43: Meshes and electrodes
10 Ring electrodes with mesh at the entrance.
Colloidal graphite reduces patch potentials which can distort electric fields.

## Slide 44
PsH formation:

## Slide 45: Soldering station