## Slide 1
Activities of the
Tandem Laboratory of NCSR “Demokritos”
A. Lagoyannis
Institute of Nuclear and Particle Physics, NCSR “Demokritos”

## Slide 2
The Group
2 permanent researchers
A. Lagoyannis, M. Axiotis (S. Harissopulos retired)
PhD Students
M. Peoviti, K. Preketes-Sigalas, E. Taimpiri, A. Ziagova
Technicians
A. Andrianis (Head operator), V. Andreopoulos, E. Tsopanakis

## Slide 3
FUNDING
Cluster of Accelerator Laboratories for Ion-Beam Research and Applications - CALIBRA
ΕΣΠΑ, S. Harissopulos, Ends 2024, 3.440 MEuro +500 kEuro
IFIGENEIA
HORIZON-WIDERA-2023-ACCESS-07, Partner, A. Karydas, Ends 2029, 6 Meuro (200 kEuro)
EuroFusion – Tandem Lab
Partner, Started in 2021 , 9000 kEuro
Access to Ion and Neutron Beams at NCSR “Demokritos”
IAEA, A. Lagoyannis, Ends 2024 , Budget: 15 kEuro
Differential Cross Section Measurement of proton reactions on fusion related light elements
IAEA, M. Axiotis, 4 years, Budget: 16 kEuro
ARENA
ELIDEK, S. Harissopulos, Ends 2025, 188 kEuro

## Slide 4
ToF ERDA
SSB Detector
Time detectors
Heavy Ion beam impinges on sample with incident angle θ1 < 90o
Recoiled (and/or scattered) atoms are extracted and detected at forward exit angles with respect to the beam axis φ ~ 25ο - 45ο
Correlation between the time-of-flight and the energy of the recoil ion is:
ERDA (Elastic Recoil Detection Analysis) - TOF-ERDA (Time Of Flight – ERDA) – detection of the recoiled elements
Heavy Ion beam – I, Cu, Cl,.
Based on the detection of charged particles/recoils
ToF - ERDA : suitable for detection of light/medium elements lighter of the beam mass

## Slide 5
ToF ERDA
Start timing gate
Stop timing gate
SSB Detector
Mirror grid (-4.0kV)
Foil holder (-3.0kV)
MCP detector
(-1.8 kV)
Drift region (-2.0 kV)
Detection system consists of:
Two timing detectors (MCPs) for the detection of the recoiled ions. Distance between them: L = 540mm
One Silicon Surface Barrier Detector (SSB) placed 5mm away of the second MCP detector
MCP detectors: 2 CFD modules are receiving the signal from the MCPs and provide a start and stop signal for the Time to Amplitude Converter
SSB detector: the signal passes through a pre-amplifier & an amplifier
Electronics:

## Slide 6
ToF ERDA
Energy (Channel)
Time of flight (channel)
Scattered Iodine
Zn
O
H
23 MeV Iodine beam on a ZnO target
20MeV 127I on Aluminum thin foil
Al
O
C
H
Scattered Iodine
Energy (Channel)
Time of flight (channel)
Time of flight (channel)
Counts
Energy (Channel)
Counts

## Slide 7
ToF ERDA
100% for energy detector - Varies with respect to the ion type and energy / Less than 100% for ions due to different energy loss values in MCP foils
Different ion beams are scattered from thick Au target
Relative detection efficiency for each ion type is given by:
increase of the setup detection efficiency over 40% for Hydrogen in low energy region and ~ 10% for higher energies

## Slide 8
450 kV Accelerator
Proton energy range: 140 – 340 keV
Proton energy range: 300 – 1000 keV
Detection systems
Five backscattering detection angles
3 SSB detectors placed at 130°, 140° and 160°
2 PIPS detectors placed at 150° and 170°
~ 7.5 cm far from the targets
~ ± 1.5° angular uncertainty
4 MV Dynamitron Accelerator
130°
140°
150°
160°
170°
targets
goniometer chamber diameter: 50 cm
11B(p,a0)8Be and 6Li(p,3He)4He low energy range

## Slide 9
Peak integration via the TV code
natB target
11B(p,a0)8Be
Auel
Cuel
Oel
Cel
Bel
11B(p,a0)8Be

## Slide 10
11B(p,a0)8Be
Comparison with present work’s results at 140 and data of total cross-sections from the literature by H. W. Becker and C. Spitaleri et al. (divided with )
150°
140°

## Slide 11
Nuclear Astrophysics
See M. Peoviti presentation

## Slide 12
Nuclear Astrophysics

## Slide 13
Nuclear Astrophysics

## Slide 14
Thank you for your attention